## Slide 1: Enhancements to Enablement Procedure
Date: 2010-11-02
Authors:

## Slide 2: Contact Verification Signal
Motivation: FCC in its latest Order (10-174) requires:
  Every 60 sec, a mode I device must obtain over-the-air an encoded contact verification signal (CVS) that validates that mode I device is within reception range of enabling (mode II/fixed) device
  Current 802.11af D0.06 signaling doesn’t meet the above requirement
    Current design proposes ‘list of available channels’ sent unencrypted in a Beacon which is not allowed by FCC.
Design of CVS:
  Information element that contains a Map Identifier.
    White Space Map Identifier Information Element (WSMIIE).
Advantages of the Designed CVS
  Broadcast over the air (Required)
  Encoded: Enabled STAs can verify if the list of available channels they have is still valid while those not enabled can not obtain that list
    Broadcasting WSM is not allowed
  Has a small overhead. Transmitting the entire white space map will incur high overhead.

## Slide 3: Design of Contact Verification Signal
Contact Verification Signaling is performed using an information element that carries a White Space Map ID (WSMIIE)
  The WSMIIE may be carried in the beacon or in a broadcast/multicast Management frame.
WSMIIE has following structure:
  Information Element Consists of
    Element ID: Identifies that it is a contact verification signal
    MAP ID: Has the White Space Map ID (as defined 8.4.2.af1.1 in TGaf Draft 0.05) of the currently valid White Space Map
A dependent STA matches the MAP ID in WSMIIE to the MAP ID received during enablement
  If the MAP ID has not changed, the STA can continue using the channel
  If the MAP ID has changed, then STA shall either
    Restart enablement (using existing enablement procedures) or
    Request a new White Space Map to check if the channel it is using is still available

## Slide 4: CVS with BIP
WSMIIE may be sent in a robust broadcast/multicast management frame that includes broadcast integrity protection (BIP: 802.11w)
  Ensures that receiver of the WSMIIE can verify that the transmitter of the WSMIIE is indeed the STA that provided the enablement.
WSMIIE

## Slide 5: Recovery Procedure when WSMIIE Map ID changes
Motivating Scenario:
  STA1 has not been de-enabled, however current map version in the WSMIIE of the beacon has changed.
  Wasteful for STA1 to restart enablement procedure if the channel it uses has not changed its status.
Requirement:
  Signaling that allows STA1 to obtain the new white space MAP and check if the channel it is operating on is still valid.
Proposal:
  Use RLQP messaging to retrieve this new white space map.

## Slide 6: WSM Recovery Procedure
Enabling AP
Dependent
STA
Request Enablement
Obtain Enablement
STA Enabled
Monitor WSMIIE
WSMIIE with WSM ID change
Request new WSM
Obtain new WSM
STA Enabled
Monitor WSMIIE
STA not Enabled
STA initiates new WSM retrieval

## Slide 7: Message Format for WSM Request
WSM Request RLQP IE sent by STA when the WSMIIE in the beacon or broadcast management frame indicates a new WSM ID
Field Settings:
  Info ID is set to “request for new WSM” - (TBD)
  Enablement Identifier: Set to the value received when STA was enabled
Possible response Message from Enabling STA
  De-enablement message.
  A response message with the new WSM.
Protected dual of the RLQP action frame may be used if the message is to be sent with encryption

## Slide 8: Response Message to WSM Request
RLQP IE used to respond to a WSM Request.
Fields
  Info ID code is set to “response to WSM retriever” (TBD)
  Enablement identifier set to the value obtained during last enablement
    Enablement identifier allows the enabler to verify that the STA is indeed enabled and was enabled by the said enabling STA before it sends a new white space map
    More efficient than FCC Id verification
  WSM: WSM shall contain current channel reported by STA if available.
STA Operation
  WSM included in the Response message contains latest Map ID to be used for contact verification
  STA may switch channels to channels indicated as available in WSM or change power levels according to the power indicated in the WSM
Protected dual of the RLQP action frame may be used if the message is to be sent with encryption.

## Slide 9: Appendix

## Slide 10: Action Frames for WSM Request and Response
DSE (Dynamic Station Enablement) Action frame formats for WSM request and response are shown.
  These Action frames may be used instead of RLQP information elements.
DSE WSM Request frame body format
DSE WSM Response frame body format