## Slide 1: Frame Format for GroupID Management
Date: 2010-11-08
Authors:
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 2: Abstract
Downlink (DL) Multi-user (MU) MIMO is identified as a key technology to improve the overall network performance
  GroupID concept is essential to specify spatial stream allocation in an efficient manner [1]
Spec framework document [2] already specifies 6 bits of groupID in VHT-SIG-A
This document proposes a groupID management frame which is simple, has low overhead and is fixed length
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Unicast GroupID management is needed
A groupID assignment needs to be ACKed before that groupID can be used
  More complicated error handling for broadcast messages
We do need an approach which allows us to manage MU group membership on a per-STA basis
  Most events in the network will happen independently across STAs
Efficiency improvement with broadcast is not significant
  The same number of frames need to be transmitted for broadcast and unicast
We propose to adopt a unicast format for groupID management
  Whether or not to adopt an additional broadcast format is still TBD

## Slide 4: Unicast GroupID Assignment Frame
Above frame can be transmitted at association or anytime MU group assignment of an STA needs to be updated
  1 bit “membership status” specifies whether the STA is a member of the group or not
  2 bit STA position specifies spatial stream position of STA in the corresponding group
Fixed payload of just 24 octets
  Remains same even if all groupIDs are being updated
Classification as “robust” action frame is TBD
SU GID field in the table is always hardcoded to
  STA membership as 1
  STA position as 1
Robust or Not Robust is TBD

## Slide 5: Pre-Motion 1
Do you accept unicast messaging for groupID assignment ?

## Slide 6: Pre-Motion 2
Do you accept the fixed length frame shown on slide 3 of this document (Robust or not robust is TBD) for groupID assignment (exact location of fields TBD) and agree to add the following text to the spec framework document?
“Group ID Management
The Group ID Management frame is used to assign or change STA positions corresponding to one or more Group IDs. The frame body in such frames shall consist of a 24 octet Group ID Assignment field, which contains 3 bits for each one of the 64 group IDs. The 3 bits for each group ID consist of the following:
  1 bit “membership status” which specifies whether or not the STA is a member of the corresponding group ID
  2 bit STA position which specifies spatial stream position of the STA in the corresponding group ID
The classification of this action frame as “robust” is TBD. The exact location of the above fields within the frame body is also TBD.”
Y- N - A-

## Slide 7: References
[1] 10/582r1, “GroupID in VHT-SIG Field”
[2] 09/0992r15, “Specification Framework for TGac”