IEEE P802.11
Wireless LANs

| Link metric comment resolution text |
| --- |
| Date: 2010-11-25 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |

## Summary of the intention of this document

- Clarify the link metric request/report functions and relative MLME-SAP interface

## Suggested changes to the draft spec

Apply the following changes.
Corresponding changes to D7.03 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor. Please update the part indicated by the “Track Changes” only.

- Management frame body components

- Information elements

- Mesh Link Metric Report element

The Mesh Link Metric Report element is transmitted by a mesh STA to a neighbor peer mesh STA to indicate the quality of the link from the neighbor peer mesh STA to the transmitting mesh STA.

The contents of the element are shown in Figure s7-95o134 (Mesh Link Metric Report element).

| Element ID | Length | Link Metric |
| --- | --- | --- |
| Octets: 1 | 1 | 1-255 |
| Mesh Link Metric Report element |

The Element ID is set to the value given in Table 7-26 (Element IDs) for this element.

The Length field indicates the number of octets in the Information field (fields following the Element ID and Length fields).

The Link Metric field indicates the value of the link metric associated with the mesh link from the neighbor peer mesh STA (the recipient of the Mesh Link Metric Report) to the local mesh STA. The length and the format of the Link Metric field are determined by the active path selection metric identifier (see 7.3.2.96.3 (Active Path Selection Metric Identifier)). When Airtime Link Metric is used, the length of the field is 4 octets, and the format described in 11C.8 (Airtime Link Metric) is applied.

- Mesh Action frame details

- Mesh Action fields

Several Action frame formats are defined for mesh BSS operation. A Mesh Action field, in the octet field immediately after the Category field, differentiates the formats. The Mesh Action field values associated with each frame format are defined in Table s7-57v30 (Mesh Action field values).

| Mesh Action field values |
| --- |
| Mesh Action field value | Description |
| 0 | Mesh Link Metric Request |
| 1 | Mesh Link Metric Report |
| 2–63 | Reserved |
| 64 | HWMP Mesh Path Selection |
| 65–127 | Reserved |
| 128 | Gate Announcement |
| 129–191 | Reserved |
| 192 | Congestion Control Notification |
| 193 | MCCA Setup Request |
| 194 | MCCA Setup Reply |
| 195 | MCCAOP Advertisement Request |
| 196 | MCCAOP Advertisements |
| 197 | MCCA Teardown |
| 198 | TBTT Adjustment Request |
| 199 | TBTT Adjustment Response |
| 200–255 | Reserved |

- Mesh Link Metric Request frame format

The Mesh Link Metric Request frame is transmitted by a mesh STA autonomously providing its metric information and requesting metric information from its neighbor peer mesh STA. This frame is transmitted to the neighbor peer mesh STA using an individually addressed frame. The format of the Mesh Link Metric Request frame Action field is shown in Table s7-57v31 (Mesh Link Metric Request frame Action field format).

| Mesh Link Metric Request frame Action field format |
| --- |
| Order | Information | Notes |
|  | Category |  |
|  | Mesh Action |  |
|  | Mesh Link Metric Report element |  |

The Category field is set to the value in Table 7-24 (Category values) for category Mesh Action.

The Mesh Action field is set to the value in Table s7-57v30 (Mesh Action field values) representing Mesh Link Metric Request.

The Mesh Link Metric Report field is set as described in 7.3.2.98 (Mesh Link Metric Report element).

- Mesh Link Metric Report frame format

The Mesh Link Metric Report frame is transmitted by a mesh STA in response to a Mesh Link Metric Request frame or by a mesh STA autonomously providing its metric information. This frame is transmitted to a neighbor peer mesh STA using an individually addressed frame. The format of the Mesh Link Metric Report frame Action field is shown in Table s7-57v32 (Mesh Link Metric Report frame Action field format).

| Mesh Link Metric Report frame Action field format |
| --- |
| Order | Information | Notes |
|  | Category |  |
|  | Mesh Action |  |
|  | Mesh Link Metric Report element |  |

The Category field is set to the value in Table 7-24 (Category values) for category Mesh Action.

The Mesh Action field is set to the value in Table s7-57v30 (Mesh Action field values) representing Mesh Link Metric Report.

The Mesh Link Metric Report field is set as described in 7.3.2.98 (Mesh Link Metric Report element).

- Layer management

- MLME SAP interface

- Mesh link metric

- Introduction

This set of primitives supports the measurement of link metric and the signaling of link metric reporting.

- MLME-MeshLinkMetricMeasure.request

- Function

This primitive requests a measurement of link metric value between the local MAC entity and a specific peer MAC entity.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshLinkMetricMeasure.request(

peerMAC,

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity for which the link metric value is measured |

- When generated

This primitive is generated by the SME to order the measurement of link metric value for the specified peer MAC entity.

- Effect of receipt

On receipt of this primitive, the MLME commences the measurement of the link metric value. The MLME subsequently issues an MLME- MeshLinkMetricMeasure.confirm that reflects the results of this request.

- MLME-MeshLinkMetricMeasure.confirm

- Function

This primitive reports the results of a link metric measurement request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshLinkMetricReport.confirm(

ResultCode,

ForwardLinkMetricValue,

ReverseLinkMetricValue

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| ResultCode | Enumeration | SUCCESS, INVALID_FWLINK_METRIC, INVALID_RVLINK_METRIC, INVALID_PARAMETERS, or NOT_SUPPORTED | Indicates the result of the link metric measurement request. SUCCESS indicates that both forward and reverse link metrics are available. INVALID_FWLINK_METRIC indicates that only reverse link metric has a valid value. INVALID_RVLINK_METRIC indicates that only forward link metric has a valid value. INVALID_RVLINK_METRIC, Either INVALID_PARAMETERS or NOT_SUPPORTED indicates that the request was not processed properly. |
| ForwardLinkMetricValue | Link Meteric | As defined in 7.3.2.98 (Mesh Link Metric Report element) | A metric value reported from the specified peer MAC entity previously. |
| ReverseLinkMetricValue | Link Metric | As defined in 7.3.2.98 (Mesh Link Metric Report element) | A metric value computed for the corresponding link. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshLinkMetricMeasure.request primitive to request a link metric measurement.

- Effect of receipt

The SME is notified of the results of the link metric measurement request.

- MLME-MeshLinkMetricReport.request

- Function

This primitive requests to submit a link metric report  to the specified peer mesh STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshLinkMetricReport.request(

peerMAC,

ReverseLinkMetricRequestFlag,

MeshLinkMetricReport,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity to which the Mesh Link Metric Request/Report is sent. |
| ReverseLinkMetricRequestFlag | Enumeration | REPORT_ONLY, or REPORT_AND_REQUEST | Indicates if the STA requests a reverse link metric value from its peer MAC entity. When set to REPORT_ONLY, the Mesh Link Metric Report frame transmission is requested When set to REPORT_AND_REQUEST, the Mesh Link Metric Request frame transmission is requested. |
| MeshLinkMetricReport | Mesh Link Metric Report element | As defined in 7.3.2.98 (Mesh Link Metric Report element) | A metric value computed for the corresponding link. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the SME to request that a Mesh Link Metric Request frame or a Mesh Link Metric Report frame to be sent to a peer entity to report a link metric value.

- Effect of receipt

On receipt of this primitive, the MLME constructs a Mesh Link Metric Request frame or a Mesh Link Metric Report frame depending on the parameter given by the ReverseLinkMetricRequestFlag. This frame is then scheduled for transmission. The MLME subsequently issues an MLME-MeshLinkMetricReport.confirm that reflects the results of this request.

- MLME-MeshLinkMetricReport.confirm

- Function

This primitive reports the results of a link metric report request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME- MeshLinkMetricReport.confirm(

ResultCode,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS , or UNSPECIFIED_FAILURE | Reports the outcome of a request to submit a link metric report. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshLinkMetricReport.request primitive to indicate the result of that request.

- Effect of receipt

The SME is notified of the results of the link metric report request.

- MLME-MeshLinkMetricReport.indication

- Function

This primitive indicates that a Mesh Link Metric Request frame or a Mesh Link Metric Report frame has been received from a peer entity. This management report can be in response to an earlier measurement request (e.g., MLME-MeshLinkMetricReport.request primitive with ReverseLinkMetricRequestFlag equal to REPORT_AND_REQUEST) or can be an autonomous report.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME- MeshLinkMetric.indication(

peerMAC,

ReverseLinkMetricRequestFlag,

MeshLinkMetricReport,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity from which the Mesh Link Metric Request/Report frame was received. |
| ReverseLinkMetricRequestFlag | Enumeration | REPORT_ONLY, or REPORT_AND_REQUEST | Indicates if the peer MAC entity requests a reverse link metric value. When a Mesh Link Metric Report frame is received, set to REPORT_ONLY. When a Mesh Link Metric Request frame is received, set to REPORT_AND_REQUEST. |
| MeshLinkMetricReport | Mesh Link Metric Report element | As defined in 7.3.2.98 (Mesh Link Metric Report element) | A metric value reported from the specified peer MAC entity. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the MLME as a result of the receipt of a Mesh Link Metric Request/Report frame from a specific peer MAC entity.

- Effect of receipt

The SME is notified of the receipt of the link metric report from the specified peer MAC entity. When the ReverseLinkMetricRequestFlag is REPORT_AND_REQUEST, the mesh STA received this primitive subsequently computes the metric value on the corresponding link as specified by its active path selection metric and respond with Mesh Link Metric Report frame.

- Mesh path selection and metric framework

- General

The term “mesh path selection” is used to describe selection of multi-hop paths between mesh STAs at the link layer. Mesh path selection creates forwarding information that is utilized for MSDU/MMPDU forwarding as described in 9.22 (Mesh forwarding framework).

- Extensible path selection framework

This standard allows for alternative and flexible implementations of path selection protocols and metrics.

A mesh STA may include multiple protocol implementations (that is, the default protocol, vendor-specific protocols, etc.) as well as multiple metric implementations, but only one path selection protocol and only one path selection metric shall be used by a mesh STA at a time.

As described in 11C.2.3 (Mesh profile) and 11C.2.7 (Candidate peer mesh STA), mesh STAs use the Mesh Configuration element (7.3.2.96 (Mesh Configuration element)) to announce the active path selection protocol and active path selection metric of the MBSS. This allows a neighbor mesh STA to identify if it should become a member of the MBSS and how it should establish mesh peerings with its members. This standard does not force an existing MBSS that is using a protocol other than the default protocol to switch to the default protocol when a new mesh STA requests mesh peering establishment. While it is possible, in principle, to implement such behavior, an algorithm to coordinate such reconfiguration is beyond the scope of this standard.

(CID230)Path selection protocol and path selection metric are identified by a unique identifier as defined in 7.3.2.96.2 (Active Path Selection Protocol Identifier) and 7.3.2.96.3 (Active Path Selection Metric Identifier), respectively. Also, each path selection protocol and each path selection metric specifies the following:

- Data type of metric values

- Length of the metric field

- Operator for aggregation of link metrics to a path metric; the symbol  is used to identify an arbitrary operator for aggregation

- Comparison operator for determining a better or worse path; how this is performed depends on the actual comparison operator

- Initial value of the path metric (path selection metric only)

The standard defines a default mandatory path selection protocol (HWMP, 11C.9 (Hybrid Wireless Mesh Protocol (HWMP))) and a default mandatory path selection metric (Airtime Link Metric, 11C.8 (Airtime Link Metric)). Both shall be implemented on all mesh STAs to ensure interoperability.

- Link metric reporting

Each peer mesh STA computes the link metric value for each neighbor peer mesh STA. The link metric value computed at the mesh STA is applied to the corresponding link from its neighbor peer mesh STA to the local STA. Depending on the active path selection protocol, the computed metric value is useful for its neighbor peer mesh STA. In such case, each mesh STA should submit a link metric report to its neighbor peer mesh STA autonomously using the Mesh Link Metric Request frame or the Mesh Link Metric Report frame. When sending these frames, the mesh STA shall set the Link Metric field in the Mesh Link Metric Report element to the latest link metric value computed for the corresponding link.

A mesh STA may request a link metric report from its neighrbor peer mesh STA by transmitting a Mesh Link Metric Request frame. The frame is used to submit a link metric report while requesting link metric information from its neighbor peer mesh STA. A mesh STA receiving a Mesh Link Metric Request frame shall reply with a Mesh Link Metric Report frame containing the computed metric value for the corresponding link.

A mesh STA shall transmit a Mesh Link Metric Report frame, when it submit a link metric report without requesting a link metric report from its neighbor peer mesh STA.

Upon reception of a Mesh Link Metric Request frame or a Mesh Link Metric Report frame, the mesh STA shall update its local link metric information using the link metric information received.

- Airtime Link Metric

This subclause defines a default link metric that may be used by a path selection protocol to identify an efficient radio-aware path. The extensibility framework allows this metric to be overridden by any path selection metric as specified in the mesh profile.

Airtime reflects the amount of channel resources consumed by transmitting the frame over a particular link. This measure is approximate and designed for ease of implementation and interoperability.

The airtime for each link is calculated as:

Where O and Bt are constants listed in Table s11C-3 (Airtime cost constants), and the input parameters r and ef are the data rate in Mb/s and the frame error rate for the test frame size Bt respectively. The rate r represents the data rate at which the mesh STA would transmit a frame of standard size Bt based on current conditions and its estimation is dependent on local implementation of rate adaptation. The frame error rate ef is the probability that when a frame of standard size Bt is transmitted at the current transmission bit rate r, the frame is corrupted due to transmission error; its estimation is a local implementation choice. Frame failures due to exceeding Mesh TTL should not be included in this estimate as they are not correlated with link performance.

The Airtime Link Metric shall be encoded as an unsigned integer in units of 0.01 TU.

| Airtime cost constants |
| --- |
| Parameter | Recommended value | Description |
| O | Varies depending on PHY | Channel access overhead, which includes frame headers, training sequences, access protocol frames, etc. |
| Bt | 8192 | Number of bits in test frame |

Table s11C-4 (Parameters of the Airtime Link Metric for extensible path selection framework) gives the parameters of the Airtime Link Metric for the extensible path selection framework.

| Parameters of the Airtime Link Metric for extensible path selection framework |
| --- |
| Path Selection Metric ID | See Table s7-43bs (Path selection metric identifier values) in 7.3.2.96.3 (Active Path Selection Metric Identifier) |
| Data type | Unsigned integer, 0 metric value< 4 294 967 296 |
| Length of metric field | 4 octets |
| Operator for metric aggregation | addition (+) |
| Comparison operator | less than, equal to, greater than as used with integers metric a is better than metric b iff a < b metric a is equal to metric b iff a = b metric a is worse than metric b iff a > b |
| Initial value of path metric | 0 |

An example of the Airtime Link Metric is shown in Annex Y.5 (Airtime Link Metric usage example).

- Mesh protocol capabilities

- General mesh support

| Item | Protocol capability | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| *MP1 | Support of mesh capability | 5.2.13 (Mesh BSS: IEEE 802.11 wireless mesh network) | PC39:M | Yes No N/A  |
| MP1.1 | Announcement of mesh profile and supplemental information for the mesh discovery | 11C.2.3 (Mesh profile), 11C.2.5 (Supplemental information for the mesh discovery) | MP1:M | Yes No N/A  |
| MP1.2 | Candidate peer mesh STA determination | 11C.2.7 (Candidate peer mesh STA) | MP1:M | Yes No N/A  |
| MP1.3 | Becoming a member of a mesh BSS | 11C.2.8 (Establishing or becoming a member of a mesh BSS) | MP1:M | Yes No N/A  |
| *MP1.4 | Mesh Peering Management | 11C.4 (Mesh Peering Management) | MP1:M | Yes No N/A  |
| MP1.4.1 | Processing of Mesh Peering Open frame | 11C.4.3.2 (Mesh Peering Open frames) | MP1.4:M | Yes No N/A  |
| MP1.4.2 | Processing of Mesh Peering Confirm frame | 11C.4.3.3 (Mesh Peering Confirm frames) | MP1.4:M | Yes No N/A  |
| MP1.4.3 | Processing of Mesh Peering Close frame | 11C.4.3.4 (Mesh Peering Close frames) | MP1.4:M | Yes No N/A  |
| MP1.4.4 | MPM finite state machine | 11C.4.4 (Mesh Peering Management finite state machine (MPM FSM)) | MP1.4:M | Yes No N/A  |
| *MP1.5 | Authenticated Mesh Peering Exchange | 11C.5 (Authenticated Mesh Peering Exchange) | MP1:O | Yes No N/A  |
| MP1.5.1 | Protected Mesh Peering Management frame processing | 11C.5.3 (Construction and processing AES-SIV-protected Mesh Peering Management frames) | MP1.5:M | Yes No N/A  |
| MP1.5.2 | AMPE finite state machine | 11C.5.6 (Authenticated Mesh Peering Exchange finite state machine) | MP1.5:M | Yes No N/A  |
| MP1.5.3 | MGTK distribution | 11C.5.4 (MGTK distribution) | MP1.5:M | Yes No N/A  |
| *MP2 | Mesh Control field | 7.1.3.6.3 (Mesh Control field) | MP1:M | Yes No N/A  |
| MP2.1 | Address Extension recognition | 7.1.3.6.3 (Mesh Control field) | MP2:M | Yes No N/A  |
| MP2.2 | Decrement of Mesh frame TTL | 7.1.3.6.3 (Mesh Control field) | MP2:M | Yes No N/A  |
| MP3 | Mesh STA beaconing | 11C.12.3 (Beaconing) | MP1:M | Yes No N/A  |
| *MP4 | Mesh STA synchronization | 11C.12.2 (Extensible synchronization framework) | MP1:M | Yes No N/A  |
| MP4.1 | Neighbor Offset Protocol | 11C.12.2.2 (Neighbor Offset Protocol) | MP4:M | Yes No N/A  |
| *MP4.2 | Mesh Beacon Collision Avoidance | 11C.12.4 (Mesh Beacon Collision Avoidance (MBCA)) | MP4:O | Yes No N/A  |
| MP4.2.1 | Beacon timing advertisement | 11C.12.4.2 (Beacon timing advertisement) | MP4.2:M | Yes No N/A  |
| MP4.2.2 | TBTT selection | 11C.12.4.3 (TBTT selection) | MP4.2:M | Yes No N/A  |
| MP4.2.3 | TBTT adjustment | 11C.12.4.4 (TBTT adjustment) | MP4.2:M | Yes No N/A  |
| MP4.2.4 | Frame transmission across reported TBTT | 11C.12.4.5 (Frame transmission across reported TBTT) | MP4.2:O | Yes No N/A  |
| MP4.2.5 | Delayed beacon transmission | 11C.12.4.6 (Delayed beacon transmission) | MP4.2:O | Yes No N/A  |
| *MP5 | MCCA | 9.9a.3 (MCF coordinated channel access (MCCA)) | MP1:O | Yes No N/A  |
| MP5.1 | MCCAOP Advertisement | 9.9a.3.8 (MCCAOP advertisements) | MP5:M | Yes No N/A  |
| MP5.2 | Neighbor MCCAOP Recognition | 9.9a.3.4 (Neighborhood MCCAOP times at a mesh STA) - 9.9a.3.6 (MCCA Access Fraction (MAF)) | MP5:M | Yes No N/A  |
| MP5.3 | MCCAOP Setup | 9.9a.3.7 (MCCAOP setup procedure) | MP5:M | Yes No N/A  |
| MP5.4 | Access during MCCAOPs | 9.9a.3.11 (Access during MCCAOPs) | MP5:M | Yes No N/A  |
| *MP6 | Intra Mesh Congestion Control | 11C.11 (Intra-mesh congestion control) | MP1:O | Yes No N/A  |
| MP6.1 | Local congestion monitoring and detection | 11C.11 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP6.2 | Congestion Control signaling | 11C.11 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP6.3 | Local rate control | 11C.11 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP7 | MBSS channel selection | 11.9.7 (Selecting and advertising a new channel), 11.9a.3 (Selecting and advertising a new channel and/or operating class) | MP1:M | Yes No N/A  |
| *MP8 | Mesh power save operation (operation in light or deep sleep mode) | 11C.13 (Power save in a mesh BSS) | MP1:O | Yes No N/A  |
| MP8.1 | Mesh power modes | 11C.13.2 (Link-specific mesh power modes), 11C.13.9 (Operation in link-specific mesh power mode) | MP8:M | Yes No N/A  |
| MP8.2 | STA power state transitions | 11C.13.4 (Mesh power mode indications and transitions) | MP8:M | Yes No N/A  |
| MP8.3 | Mesh Awake Window and frame transmission | 11C.13.7 (Mesh Awake Window) | MP8:M | Yes No N/A  |
| *MP9 | Mesh power save support | 11C.13 (Power save in a mesh BSS) | MP1:M | Yes No N/A  |
| MP9.1 | TIM transmission | 11C.13.5 (TIM transmissions in an MBSS) | MP9:M | Yes No N/A  |
| MP9.2 | Link-specific mesh power modes | 11C.13.2 (Link-specific mesh power modes) | MP9:M | Yes No N/A  |
| MP9.3 | Non-peer power modes | 11C.13.3 (Non-peer mesh power modes) | MP9:M | Yes No N/A  |
| MP9.4 | Frame transmission to mesh STA in light sleep mode | 11C.13.8 (Power save support), 11C.13.10 (Mesh peer service periods) | MP9:M | Yes No N/A  |
| MP9.5 | Frame transmission to mesh STA in deep sleep mode | 11C.13.8 (Power save support), 11C.13.10 (Mesh peer service periods) | MP9:M | Yes No N/A  |
| MP10 | Airtime Link Metric computation | 11C.8 (Airtime Link Metric) | MP1:M | Yes No N/A  |
| *MP11 | Link metric reporting | 11C.7.3 (Link metric reporting) | MP1:M | Yes No N/A  |
| MP11.1 | Link metric request | 11C.7.3 (Link metric reporting) | MP11:M | Yes No N/A  |
| MP11.2 | Link metric report | 11C.7.3 (Link metric reporting) | MP11:M | Yes No N/A  |
| MP12 | Proxy operation | 11C.10.4 (Proxy protocol) | MP1:O | Yes No N/A  |
| MP13 | Gate announcement | 11C.10.2 (Gate announcement protocol) | MP1:O | Yes No N/A  |
| *MP14 | MSDU/MMPDU forwarding | 9.22 (Mesh forwarding framework) | MP1:O | Yes No N/A  |
| MP14.1 | Individually addressed MSDU forwarding | 9.22.2.2 (Addressing of individually addressed Mesh Data frames and data forwarding) | MP14:M | Yes No N/A  |
| MP14.2 | Group addressed MSDU forwarding | 9.22.2.3 (Addressing of group addressed Mesh Data frames and data forwarding) | MP14:M | Yes No N/A  |
| MP14.3 | MMPDU forwarding | 9.22.2.4 (Addressing of Management frames and MMPDU forwarding) | MP14:M | Yes No N/A  |

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D7.03, November 2010.

# Comments

Remove the XXX.response

# Text boxes

Abstract

This document provides suggested text changes in accordance with the resolutions to CID 82 and CID 237 from the initial sponsor ballot.