## Slide 1: GCMP Restriction
Date: 2011-01-11
Authors:

## Slide 2: Summary
GCMP is tentatively added to the baseline by Tgad
  Increased PHY rates of Tgad suggest the need for a more efficient encryption algorithm
GCMP is not needed for Tgac
  While PHY rates for Tgac are higher than say, 802.11n, CCMP is still adequate for these rates
Propose adding an explicit connection between GCMP and Tgac
  I.e. explicitly disallow GCMP use with Tgac STA

## Slide 3: Motion
Move to make the following changes in the Tgac draft specification:
  Editor: add the following text to the end of the 3rd paragraph of REVmb D6.0 11.4.3 RSNA policy selection in an ESS
  Within an ESS, A VHT STA shall eliminate TKIP and GCMP as choices for the pairwise cipher suite if CCMP is advertised by the AP or if the AP included either an HT Capabilities element or a VHT Capabilities element in its Beacon and Probe Response frames. The elimination of TKIP and GCMP as choices for the pairwise cipher suite may result in a lack of overlap of the remaining pairwise cipher suite choices, in which case the VHT STA shall decline to create an RSN association with that AP.
  Editor: add the following text after the 3rd paragraph of REVmb D6.0 11.4.5 RSNA policy selection in an IBSS and for DLS:
  A VHT STA that is in an IBSS or that is transmitting frames through a direct link shall eliminate TKIP and GCMP as choices for the pairwise cipher suite if CCMP is advertised by the other STA or if the other STA included either an HT Capabilities element or a VHT Capabilities element in any of its Beacon, Probe Response, DLS Request, or DLS Response messages.
  NOTE—The elimination of TKIP and GCMP as choices for the pairwise cipher suite might result in a lack of overlap of the remaining pairwise cipher suites choices, in which case the STAs will not exchange encrypted frames.