## Slide 1: Dimension Reduction for MU-MIMO
Date: 2011-01-17
Authors:

## Slide 2: Abstract
The following motions passed in TGac [10/1265r1]
  Move to accept enabling the beam-former to control the explicit feedback dimension for each user in MU-MIMO operation, and to update the specification framework document accordingly
  Move to add TBD dimension reduction information per user in MU-MIMO operation to the NDPA frame, and update the Specifications Framework document accordingly
This document attempts to build on the ideas in 10/1256r1, resolve the TBDs above, and converge on this topic in TGac

## Slide 3: Dimension indication in NDPA
Have it only for the clients which are being requested an MU type feedback
  For SU, this keeps the beamformee in control
  Allows AP to be in control for MU
    E.g. Doesn’t want to get 3 ss feedback from an MU client if it’s always going to transmit 1 ss to it
Prefer exact dimension indication (for MU)
  Useful from scheduler point of view as further reduction can “surprise” the AP
    Allows AP to prepare in advance and allocate internal resources accordingly
      No need to react quickly after the last STA sent “reduced” feedback
    Also, further reduction by one recipient can hurt other users in MU-MIMO and reduce overall efficiency
      E.g. Consider a 4 antenna AP, and user A with 2 antennas and user B with 1 antenna. AP has users A and B in an MU group, and user A needs to get 2 times the data of user B. AP decides to achieve this by allocating 2 streams to user A and 1 stream to user B. If user A returns just 1 dimension in feedback, both users will get 1 stream and most likely, there will be a lot of “dead air” in the MU transmission because user A’s data will be twice as long..

## Slide 4: Current NDPA
Current NDPA text in spec framework [1]
  NDPA is a new control frame that contains the following fields:
    a 1 octet sequence number
    a STA Info field including a list of STA IDs
    when used for MU-MIMO, TBD per user dimension reduction information [10/1265r1]
    other TBD information

## Slide 5: Proposed STA Info Field
SU/MU bit per STA in NDPA to convey the type of feedback requested
  Allows AP to optimize feedback overhead per STA
  Also allows SU STAs to pick rank (see rules of operation below)
Nc indication
  Meaningful only when MU/SU bit is set to MU
    The field is present always so that each STA Info element is always the same length
Rules for operation
  STA shall send a feedback frame with the “MU type” bit in the VHT MIMO control field set to the same value as the MU/SU bit in the corresponding STA’s Info field in NDPA
  STA shall send a feedback with the Nc field value in the VHT MIMO control field equal to the Nc field value in the corresponding STA Info element in NDPA when MU/SU bit is set to MU
  When an STA’s MU/SU bit is set to SU, STA can feed back any dimension (Nc bits in STA info can be reserved)
STA ID | MU/SU | Nc
Bits: 12 | 1 | 3
STA Info element 1 | … | STA Info element N
Bytes: 2 |  | 2
STA Info Field
STA Info Element
(2 Bytes)
Any additional fields in STA Info
element are TBD

## Slide 6: Capability Exchange
Capabilities needs a new field
  “Compressed Steering Max Number of Columns Supported” to tell the beamformer, the max Nc it can request from a beamformee for MU
Exact details of this are TBD

## Slide 7: Conclusion
We proposed a dimension reduction design using NDPA
  MU/SU bit per user in NDPA
  Dimension reduction only for MU
    Exact dimension specification per user in NDPA

## Slide 8: Pre-Motion 1
  Do you accept the following rule for sounding feedback:
  STA shall send a feedback frame with the “MU type” bit in the VHT MIMO control field set to the same value as the MU/SU bit in the corresponding STA’s Info field in NDPA

## Slide 9: Pre-Motion 2
  Do you accept the following rule for dimension reduction in MU-MIMO:
  When the Feedback Type field is set to MU, the STA shall send a feedback with the Nc field value in the VHT MIMO Control field equal to the Nc field value in the corresponding STA Info field in the NDPA provided the Nc requested is not larger than the number of currently active receive antennas

## Slide 10: References
        [1] IEEE 802.11 document 09/0992r18 , “Proposed Specification Framework for TGac”, Robert Stacey et al
        [2] IEEE 802.11 document 10/1265r1 , “Explicit feedback dimension reduction procedures”, Nir Shapira