## Slide 1: Error Recovery for TXOP Sharing
Date: 2011-01-16
Authors:

## Slide 2: Outline
Motivation
Error recovery rule for TXOP sharing

## Slide 3: Error recovery rules for MU MIMO TXOP sharing need to be clarified
MU MIMO TXOP sharing allows multiple secondary ACs to be piggybacked with a primary AC
The TXOP is obtained using EDCA parameters of the primary AC
In the following example:
  AC_VI is the primary AC
  AC_VO and AC_BE are secondary ACs
If traffic from multiple ACs are transmitted in one burst, which EDCAF should perform exponential backoff if there is a transmission failure?
AC_VI (STA1)
AC_BE (STA3)
BA
AC_VO (STA2)
BA
BA
BAR
BAR
SIFS
SIFS
SIFS
SIFS
SIFS
AP
STA1
STA2
STA3

## Slide 4: Error recovery procedure for an MU MIMO multi-AC TXOP is a simple extension of the existing error recovery procedure
If a valid response to the initial frame of a TXOP is not received, the AP shall initiate an exponential backoff for the primary AC and resume the backoff procedure for the secondary ACs without changing their CWs
The reason is that only the primary AC’s EDCA parameters are relevant in a shared TXOP
AC_VI (STA1)
AC_BE (STA3)
AC_VO (STA2)
AckTimeOut
Doubles CW for AC_VI , no change to AC_VO and AC_BE
Backoff
AC_VI backoff

## Slide 5: Pre-motion 1
Do you support updating the TGac spec framework to include the following protocol rule?
For MU MIMO TXOP sharing:
  If a valid response to the initial frame of a TXOP is not received, the AP shall initiate an exponential backoff for the primary AC