## Slide 1
Date: 2011-01-17
Authors:
Downlink TXOP Power Save
Notes: 1

## Slide 2: Introduction
Presented the downlink MU TXOP power save concept during November F2F[1].
This presentation provides the protocol details
  MU TXOP power save capability
  MU TXOP Power Save mode
  TXOP PS indication by AP
  Extend downlink MU TXOP power save to downlink MU SU TXOP power save
Notes: 2

## Slide 3: MU TXOP Power Management Capability/Mode
A bit for MU TXOP Management Capability/Mode in VHT capabilities Info of the VHT capabilities element[2].
  Indicates whether or not AP allows STAs in BSS to enter TXOP power save mode when transmitted in Beacon/Probe response
  Indicates whether the STA is in MU TXOP PS mode or not in Association/Re-Associations frame .
    1 indicates STA in MU TXOP PS mode , 0 indicates STA not in MU TXOP PS mode
Notes: 3

## Slide 4: TXOP power save indication
A bit for AP to indicate STAs during downlink TXOP whether or not they are allowed to enter Doze state.
  Using B22 bit of VHT-SIG-A1 in downlink MU frames
  The value of this bit is same in all the PPDUs in downlink MU TXOP
RSVD | NO TXOP PS | NSTS | Group ID | STBC | RSVD | BW
1: TXOP PS not allowed
0: TXOP PS allowed
Notes: 4

## Slide 5: Extend TXOP Power Save to SU
The proposed scheme can be extended for power save during SU-MIMO TXOP.
  Change the signals from MU MIMO TXOP Power Save to VHT Power Save.
STAs can enter doze state
  If the received Partial AID in VHT-SIG-A does not match the partial AID of STA
  If the partial AID in VHT-SIG-A matches the partial AID of STA but the frame is not destined to it.
  After sending appropriate acknowledgement to AP in response to frame received with ‘More Data’ bit set to 0.
Notes: 5

## Slide 6: Pre-motion 1
Do you agree to indicate the MU TXOP power Management Capability by AP and the MU TXOP Power Save Mode by STA as described in slide #3?
The exact bit on slide #3 in VHT capabilities info field is TBD.
Y
N
A
Notes: 6

## Slide 7: Pre-motion 2
Do you agree to indicate the TXOP power save by AP during downlink MU TXOP as described in slide #4?
Y
N
A
Notes: 7

## Slide 8: Pre-motion 3
Do you support to extend the MU TXOP power save for SU TXOP as mentioned in slide #5?
Y:
N:
A:
Notes: 8

## Slide 9: References
11-10-1302-00-00ac-DL-MU-TXOP-Power-Save.doc
IEEE 802.11-09/0992r18 Proposed Specification frame work for Tgac
Notes: 9