IEEE P802.11
Wireless LANs

| Indication of Group Address in PLCP Header |
| --- |
| Date: 2011-01-17 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Jarkko Kneckt | Nokia Corporation | Itämerenkatu 11 – 13 00180 Helsinki, Finland |  | Jarkko.Kneckt@nokia.com |
| Mika Kasslin | Nokia Corporation | Itämerenkatu 11 – 13 00180 Helsinki, Finland |  | Mika.Kasslin@nokia.com |

##### 3.2.3.2.2 VHT-SIG-A definition

Instructions to editor: Incorporate the changes as shown with track changes.

R3.2.1.H: VHT-SIG-A includes the fields listed in Table 1.

Table 1 - VHT-SIG-A fields

| Bit Index | Field | Bit allocation | Description |
| --- | --- | --- | --- |
| VHT-SIG-A1 |
| 0-1 | BW | 2 | Set to 0 for 20 MHz, 1 for 40 MHz, 2 for 80 MHz, 3 for 160 MHz and 80+80 MHz mode |
| 2 | Reserved | 1 | Reserved for possible expansion of BW field. Set to 1. |
| 3 | STBC | 1 | Set to 1 if all streams use STBC, otherwise set to 0. When STBC bit is 1, an odd number of space time streams per user is not allowed. |
| 4-9 | Group ID [10/0582r1] | 6 | A value of [1,1,1,1,1,0] indicates a transmission to FMSID stream and needs to bypass a group (e.g. broadcast) A value of [1,1,1,1,1,1] indicates [10/0382r2]: A single user transmission A transmission where the group membership has not yet been established A transmission that is not assigned to FMSID stream and needs to bypass a group (e.g. broadcast) |
| 10-21 | NSTS [10/0582r1] | 12 | For MU: 3 bits/user with maximum of 4 users Set to 0 for 0 space time streams Set to 1 for 1 space time stream Set to 2 for 2 space time streams Set to 3 for 3 space time streams Set to 4 for 4 space time streams When Group ID is set to [1,1,1,1,1,0]: first 3 bits contain stream allocation, set to 0 for 1 space time stream, set to 1 for 2 space time streams, etcetera up to 8 streams. The next 8 bits contain FMSID. The last bit is reserved. When Group ID is set to [1,1,1,1,1,1]: first 3 bits contain stream allocation, set to 0 for 1 space time stream, set to 1 for 2 space time streams, etcetera up to 8 streams. Remaining 9 bits contain partial AID: being the 9 LSB bits of AID. For Broadcast and multicast that are not assigned to FMSID stream, these 9 bits are set to 0. For STA-to-AP, these 9 bits are set to a special value (TBD). |
| 22-23 | Reserved | 2 | All ones |
|  | Total | 24 |  |
| VHT-SIG-A2 |
| 0-1 | Short GI | 2 | Set B0 to 0 for Long GI, set to 1 for Short GI Set B1 to 1 when Short GI and Nsym%10 == 9 |
| 2-3 | Coding | 2 | For SU: Set B2 to 0 for BCC, set to 1 for LDPC For MU: [10/1277r0] Set B2 to 0 for BCC, set to 1 for LDPC for 1st user If user 1 has 0 Nsts value, then B2 is reserved and set to 1 B3 is defined as Nldpc-ext (see 3.2.4.2.2) |
| 4-7 | MCS | 4 | For SU/Broadcast/Multicast: MCS index For MU: [10/1277r0] B4: Set to 0 for BCC, 1 for LDPC for the 2nd user B5: Set to 0 for BCC, 1 for LDPC for the 3rd user B6: Set to 0 for BCC, 1 for LDPC for the 4th user If user 2, 3, or 4 has 0 Nsts value, then corresponding bit is reserved and set to 1 B7: Reserved and set to 1 |
| 8 | SU-Beamformed | 1 | Set to 1 when packet is a SU-beamformed packet Set to 0 otherwise For MU: Reserved, set to 1 |
| 9 | Reserved | 1 | All ones |
| 10-17 | CRC | 8 | CRC calculated as in 11n Section 20.3.9.4.4 with C7 in B10 |
| 18-23 | Tail | 6 | All zeros |
|  | Total | 24 |  |

Note that the fields are transmitted in the order shown in and LSB first.

[10/1052r0]

References:

[1] 	Draft 802.11v_D 15.0, September 2010

# Text boxes

Abstract

The document describes means to carry the group address information in PLCP header. The group address information is compatible with Flexible Multicast Service (FMS) as defined in 802.11v [1].

The presentation for this normative text is 11-11-0096-00-00ac-Indication-of-Groupaddress.doc