IEEE P802.11
Wireless LANs

| M-BS comment resolution text |
| --- |
| Date: 2011-01-20 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |
| Dan Harkins | Aruba Networks | 1322 Crossman ave, Sunnyvale, CA., USA | +1 408 227 4800 | dharkins at arubanetworks dot com |

## Summary of the intention of this document

- Resolve some of the comments in M-BS category as shown in 11-11-0099 (M-BS comment resolution xls)

## Suggested changes to the draft spec

Apply the following changes.
Corresponding changes to D8.0 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor. Please update the part indicated by the “Track Changes” only.

- Management frame body components

- Fields that are not information elements

- Status Code field

Insert the following rows into Table 7-23 (Status codes) and change the last row (Reserved) as shown.

| Status codes |
| --- |
| Status code | Meaning |
| 76 | Authentication is rejected because an Anti-Clogging Token is required. |
| 77 | Authentication is rejected because the offered finite cyclic group is not supported. |
| 78 | The TBTT adjustment request unsuccessful because the mesh STA could not find an alternative TBTT. |
| 7976–65 535 | Reserved |

- Management frame body components

- Information elements

- Mesh Configuration element

- General

The Mesh Configuration element shown in Figure 7-95o130 (Mesh Configuration element format) is used to advertise mesh services. It is contained in Beacon frames and Probe Response frames transmitted by mesh STAs, and is also contained in Mesh Peering Open and Mesh Peering Confirm frames.

| Element ID | Length | Active Path Selection Protocol Identifier | Active Path Selection Metric Identifier | Congestion Control Mode Identifier | Synchronization Protocol Identifier | Authentication Protocol Identifier | Mesh Peering Protocol Identifier | Mesh Formation Info | Mesh Capability |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Octets:1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Mesh Configuration element format |

The Element ID is set to the value given in Table 7-26 (Element IDs) for this element.

The Length field is set to 8.

The remainder of the fields are described in the following subclauses.

- Synchronization Protocol Identifier

The Synchronization Protocol Identifier field indicates the synchronization protocol that is currently activated in the MBSS. Table 7-43bu (Synchronization Protocol Identifier values) provides the synchronization protocol identifier values defined by this standard.

| Synchronization Protocol Identifier values |
| --- |
| Value | Meaning |
| 0 | Neighbor Offset Protocol defined in 11C.12.2.2 (Neighbor Offset Protocol) (default synchronization protocol) |
| 1–254 | Reserved |
| 255 | Vendor specific (The active synchronization protocol is specified in the Vendor Specific element) |

The Neighbor Offset Protocol is defined as the default synchronization protocol among mesh STAs. The details of the Neighbor Offset Protocol are described in 11C.12.2.2 (Neighbor Offset Protocol).

When the Synchronization Protocol Identifier field is 255, the active synchronization protocol is specified by the Vendor Specific element that is present in the frame. The content of the Vendor Specific element is beyond the scope of this standard. (See 7.3.2.26.)

- Mesh Capability

The Mesh Capability field comprises a set of values indicating whether a mesh STA is a possible candidate for mesh peering establishment. The details of the Mesh Capability field are shown in Figure 7-95o132 (Mesh Capability field).

| B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Accepting Additional Mesh Peerings | MCCA Supported | MCCA Enabled | Forwarding | MBCA Enabled | TBTT Adjusting | Mesh Power Save Level | Reserved |
| Bits: 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Mesh Capability field |

The Accepting Additional Mesh Peerings subfield is set to 1 if the mesh STA is willing to establish additional mesh peerings with other mesh STAs and set to 0 otherwise (i.e., the Accepting Additional Mesh Peerings subfield is set in accordance with dot11MeshAcceptingAdditionalPeerings).

The MCCA Supported subfield is set to 1 if the mesh STA implements MCCA and set to 0 otherwise (i.e., the MCCA Supported subfield is set in accordance with dot11MCCAImplemented).

The MCCA Enabled subfield is set to 1 if the mesh STA is using the MCCA and set to 0 otherwise (i.e., the MCCA Enabled subfield is set in accordance with dot11MCCAActivated).

The Forwarding subfield is set to 1 if the mesh STA forwards MSDUs and set to 0 otherwise (i.e., the Forwarding subfield is set in accordance with dot11MeshForwarding).

The MBCA Enabled subfield is set to 1 if the mesh STA activates MBCA, and is set to 0 otherwise (i.e., the MBCA Enabled subfield is set in accordance with dot11MBCAActivated). (See 11C.12.4 (Mesh Beacon Collision Avoidance (MBCA)).)

The TBTT Adjusting subfield is set to 1 whilethe TBTT adjustment procedure is ongoing, and is set to 0 otherwise. (See 11C.12.4.4.3 (Adjustment procedure).)

The Mesh Power Save Level field and the Power Management field in the Frame Control field indicate the non-peer mesh power mode of the mesh STA. The Power Management subfield set to 1 and the Mesh Power Save Level field set to 0 indicate that the mesh STA is operating in light sleep mode for non-peer mesh STAs. The Power Management field set to 1 and the Mesh Power Save Level set to 1 indicate that mesh STA is operating in deep sleep mode for non-peer mesh STAs. The Mesh Power Save Level field is reserved, if the Power Management subfield is set to 0. (See 11C.13.3 (Non-peer mesh power modes).)

- Beacon Timing element

The Beacon Timing element is used to advertise the beacon timing information of neighbor STAs (mesh STAs, APs, or STAs in an IBSS). The format of the Beacon Timing element is shown in Figure 7-95o141 (Beacon Timing element format).

| Element ID | Length | Report Control | Beacon Timing Information #1 | ... | Beacon Timing Information #N |
| --- | --- | --- | --- | --- | --- |
| Octets: 1 | 1 | 1 | 5 | ... | 5 |
| Beacon Timing element format |

The Element ID is set to the value given in Table 7-26 (Element IDs) for this element.

The Length field indicates the number of octets in the Information field (fields following the Element ID and Length fields).

The Report Control field is used to signal information about the beacon timing information tuple contained in the Beacon Timing element. The structure of the Report Control field is defined in Figure 7-95o142 (Report Control field).

| Status Number | Beacon Timing Element Number | More Beacon Timing Elements |
| --- | --- | --- |
| Bits: 4 | 3 | 1 |
| Report Control field |

The Status Number subfield is set to the status number of the beacon timing information set. The status number is managed as described in 11C.12.4.2.1 (Maintenance of the status number).

The Beacon Timing Element Number subfield is an unsigned integer that indicates the index of the beacon timing information tuple contained in this Beacon Timing element. The Beacon Timing Element Number is set to 0 in the Beacon Timing element for the first or only tuple of the beacon timing information and is incremented by one for each successive tuple of the beacon timing information. The beacon timing information tuples are managed as described in 11C.12.4.2.3 (Transmitter’s procedure).

The More Beacon Timing Elements subfield is set to 1 if a successive tuple of beacon timing information exists, and set to 0 otherwise.

The Beacon Timing Information field contains the beacon timing information of a neighbor STA When the mesh STA reports multiple beacon timing information, multiple Beacon Timing Information fields are included in the Beacon Timing element. The structure of the Beacon Timing Information field is defined in Figure 7-95o143 (Beacon Timing Information field).

| Neighbor STA ID | Neighbor TBTT | Neighbor Beacon Interval |
| --- | --- | --- |
| Octets: 1 | 2 | 2 |
| Beacon Timing Information field |

The Neighbor STA ID subfield is an unsigned integer that indicates the identification of the neighbor STA corresponding to this beacon timing information. When a mesh peering is established with this neighbor STA, the MSB of this field is set to 0, and the rest of this field is set to the last 7 digits (7 LSBs) of the AID value assigned to this neighbor mesh STA. When a mesh peering is not established with this neighbor STA, the MSB of this field is set to 1, and the rest of this field is set to the last 7 digits (7 LSBs, taking the I/G bit as the MSB) of the 48-bit MAC address of this neighbor STA.

NOTE—Since the Neighbor STA ID subfield is provided in abbreviated form, it is possible that the same Neighbor STA ID value appears in multiple Beacon Timing Information fields.

The Neighbor TBTT subfield is an unsigned integer that indicates a TBTT of the corresponding neighbor STA, measured in the local TSF timer of the mesh STA. When the active synchronization protocol is the Neighbor Offset Protocol, the TBTT is calculated as described in 11C.12.4.2.2 (Calculation of neighbor STA’s TBTT). The 2nd and 3rd least significant octets of the calculated TBTT are contained in this subfield representing the TBTT in units of 256 µs.

The Neighbor Beacon Interval subfield is an unsigned integer that indicates the beacon interval being used by the corresponding neighbor STA. The unit of the Neighbor Beacon Interval subfield is TU.

Detailed usage of the Beacon Timing element is described in 11C.12.4.2 (Beacon timing advertisement).

- Action frame format details

- Mesh Action frame details

- TBTT Adjustment Request frame format

The TBTT Adjustment Request frame is used to request a particular neighbor peer mesh STA to adjust its TBTT. This frame is transmitted using individual addresses. The format of the TBTT Adjustment Request frame Action field is shown in Table 7-57v40 (TBTT Adjustment Request frame Action field format).

| TBTT Adjustment Request frame Action field format |
| --- |
| Order | Information | Notes |
|  | Category |  |
|  | Mesh Action |  |
| to (N_Info+2) | Beacon Timing element | Repeated N_Info times (N_Info is a number of beacon timing information tuples as described in 11C.12.4.2.3 (Transmitter’s procedure)). |

The Category field is set to the value in Table 7-24 (Category values) for category Mesh Action.

The Mesh Action field is set to the value in Table 7-57v30 (Mesh Action field values) representing TBTT Adjustment Request.

The Beacon Timing element is set as described in 7.3.2.103 (Beacon Timing element). When the number of beacon timing information exceeds 50, multiple Beacon Timing elements are present. The elements are present in the order of Beacon Timing Element Number field value in the Report Control field of the Beacon Timing element.

- TBTT Adjustment Response frame format

The TBTT Adjustment Response frame is used to respond to a TBTT adjustment request. This frame is transmitted using individual addresses. The format of the TBTT Adjustment Response frame Action field is shown in Table 7-57v41 (TBTT Adjustment Response frame Action field).

| TBTT Adjustment Response frame Action field |
| --- |
| Order | Information | Notes |
|  | Category |  |
|  | Mesh Action |  |
|  | Status Code |  |
| to (N_Info+3) | Beacon Timing element (optional) | Repeated N_Info times (N_Info is a number of beacon timing information tuples as described in 11C.12.4.2.3 (Transmitter’s procedure)). |

The Category field is set to the value in Table 7-24 (Category values) for category Mesh Action.

The Mesh Action field is set to the value in Table 7-57v30 (Mesh Action field values) representing TBTT Adjustment Response.

The Beacon Timing element is set as described in 7.3.2.103 (Beacon Timing element). It is present only if the Status Code is set to 78 (i.e., when the request is not successful due to the neighbor constraint). When the number of beacon timing information exceeds 50, multiple Beacon Timing elements are present. The elements are present in the order of Beacon Timing Element Number field value in the Report Control field of the Beacon Timing element.

- MCF

- MCF coordinated channel access (MCCA)

- Interaction with time synchronization

If a mesh STA adjusts its TBTT, e.g., in response to a TBTT Adjustment Request, it shall adjust the Reports accordingly by modifying the MCCAOP Offset of each of the reported MCCAOP reservations. If a mesh STA adjusts its timing offset value with respect to a neighbor mesh STA, as specified in 11C.12.2.2 (Neighbor Offset Protocol), it shall adjust the Reports accordingly by modifying the MCCAOP Offset of each of the reported MCCAOP reservations for which this neighbor mesh STA is the owner.

- MLME SAP interface

- Start

- MLME-START.request

- When generated

Change the first and second paragraph in 10.3.10.1.3 as follows:

This primitive is generated by the SME to start either an infrastructure BSS (with the MAC entity within an AP), an IBSS (with the MAC entity acting as the first STA in the IBSS), or an MBSS (with the MAC entity acting as the first mesh STA in the MBSS), or to become a member of an existing MBSS. In an MBSS, this primitive starts the process of mesh beaconing.

- In an infrastructure BSS or an IBSS, the MLME-START.request primitive must be generated after an MLME-RESET.request primitive has been used to reset the MAC entity and before an MLME-JOIN.request primitive has been used to successfully join an existing infrastructure BSS or IBSS.

In a mesh BSS, the MLME-START.request primitive must be generated after an MLME-RESET.request primitive has been used to reset the MAC entity and before any synchronization and mesh peering have been established. When the mesh STA uses the default synchronization protocol and the default mesh peering protocol, the MLME-START.request primitive must be generated before an MLME-MeshNeighborOffsetSync.request primitive and MLME-MeshPeerigManagement.request have been used.

- Mesh Neighbor Offset Synchronization

- Introduction

This mechanism supports the Neighbor Offset synchronization status with a targeted neighbor mesh STA.

- MLME-MeshNeighborOffsetSyncStart.request

- Function

This primitive requests to maintain the Neighbor Offset Synchronization with a specific neighbor mesh STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetSyncStart.request(

peerMAC

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to start the Neighbor Offset Synchronization. |

- When generated

This primitive is generated by the SME to start the Neighbor Offset Protocol with the specified neighbor mesh STA.

- Effect of receipt

On receipt of this primitive, the MLME commences the Neighbor Offset Synchronization and the calculation of the TSF timer offset value. The MLME subsequently issues an MLME-MeshNeighborOffsetSyncStart.confirm that reflects the results of this request.

- MLME-MeshNeighborOffsetSyncStart.confirm

- Function

This primitive reports the results of a mesh Neighbor Offset Synchronization request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetSyncStart.confirm(

ResultCode,

peerMAC,

TSFOffsetValue

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the Mesh Neighbor Offset Synchonization is requested. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, TOO_MANY_NEIGHBORS, or NOT_SUPPORTED | Indicates the result of the mesh Neighbor Offset Synchronization request. |
| TSFOffsetValue | Integer | –263 to (263–1) | Indicates the TSF offset value with the specified neighbor mesh STA, expressed in twos complement in µs. Valid only if the ResultCode is SUCCESS. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshNeighborOffsetSyncStart.request and report the TSF offset value.

- Effect of receipt

The SME is notified of the results of the mesh Neighbor Offset Synchronization request.

- MLME-MeshNeighborOffsetMeasure.request

- Function

This primitive requests a measurement of TSF timer offset value for a specific neighbor mesh STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetMeasure.request(

peerMAC

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to measure the TSF offset value. |

- When generated

This primitive is generated by the SME to order the measurement of TSF timer offset value with the specified neighbor mesh STA.

- Effect of receipt

On receipt of this primitive, the MLME commences the measurement and the calculation of the TSF timer offset value. The MLME subsequently issues an MLME-MeshNeighborOffsetMeasure.confirm that reflects the results of this request.

- MLME-MeshNeighborOffsetMeasure.confirm

- Function

This primitive reports the results of a mesh neighbor offset measurement request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetMeasure.confirm(

peerMAC,

ResultCode,

TSFOffsetValue

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the Mesh Neighbor Offset Measure is requested. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, or NOT_SUPPORTED | Indicates the result of the mesh neighbor offset measurement request. |
| TSFOffsetValue | Integer | –263 to (263– 1) | Indicates the TSF offset value with the specified neighbor mesh STA, expressed in twos complement in µs. Valid only if the ResultCode is SUCCESS. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshNeighborOfsetMeasure.request to report a measurement result.

- Effect of receipt

The SME is notified of the results of the mesh neighbor offset measurement request.

- MLME-MeshNeighborOffsetSyncStop.request

- Function

This primitive requests to stop the Neighbor Offset Synchronization with a specific neighbor mesh STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetSyncStop.request(

peerMAC

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to stop the Neighbor Offset Synchronization. |

- When generated

This primitive is generated by the SME to stop the maintenance of the Neighbor Offset Synchronization with the specified neighbor mesh STA.

- Effect of receipt

On receipt of this primitive, the MLME stops the Neighbor Offset Synchronization with the specified peer. The MLME subsequently issues an MLME-MeshNeighborOffsetSyncStop.confirm that reflects the results of this request.

- MLME-MeshNeighborOffsetSyncStop.confirm

- Function

This primitive reports the results of a mesh neighbor offset synchronization stop request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshNeighborOffsetSyncStop.confirm(

peerMAC,

ResultCode

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the Mesh Neighbor Offset Synchonization Stop is requested. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, or NOT_SUPPORTED | Indicates the result of the mesh neighbor offset synchronization stop request. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshNeighborOffsetSyncStop.request.

- Effect of receipt

The SME is notified of the results of the mesh neighbor offset synchronization stop request.

- Mesh TBTT Adjustment

- Introduction

The following primitives describe how a mesh STA requests TBTT adjustment of its neighbor peer mesh ST.

- MLME-MeshTBTTAdjustment.request

- Function

This primitive requests transmission of a TBTT Adjustment Request frame.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshTBTTAdjustment.request(

peerMAC,

BeaconTiming,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity to which the TBTT Adjustment Request is sent. |
| BeaconTiming | A set of Beacon Timing element | As defined in 7.3.2.103 (Beacon Timing element) | A set of beacon timing information of the mesh STA. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the SME to request that a TBTT Adjustment Request frame be sent to a peer entity to request the adjustment of the peer entity’s TBTT.

- Effect of receipt

On receipt of this primitive, the MLME constructs a TBTT Adjustment Request frame containing the Beacon Timing elements. This frame is then scheduled for transmission. The MLME subsequently issues an MLME-MeshTBTTAdjustment.confirm that reflects the result of this request.

- MLME-MeshTBTTAdjustment.confirm

- Function

This primitive reports the result of a mesh TBTT adjustment request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshTBTTAdjustment.confirm(

peerMAC,

ResultCode,

BeaconTiming,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity from which the TBTT Adjustment Response is received. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, TIMEOUT, CAN_NOT_FIND_ALTERNATIVE_TBTT, or UNSPECIFIED_FAILURE | Indicates the result of the TBTT adjustment request. |
| BeaconTiming | A set of Beacon Timing element | As defined in 7.3.2.103 (Beacon Timing element) | A set of beacon timing information of the responding mesh STA. Present only when such an element was present in the TBTT Adjustment Response frame. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MeshTBTTAdjustment.request primitive to indicate the result of that request.

- Effect of receipt

The SME is notified of the result of the mesh TBTT adjustment request.

- MLME-MeshTBTTAdjustment.indication

- Function

This primitive indicates that a specific peer MAC entity is requesting to adjust the TBTT.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshTBTTAdjustment.indication(

peerMAC,

BeaconTiming,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity from which the TBTT Adjustment request was received. |
| BeaconTiming | A set of Beacon Timing element | As defined in 7.3.2.103 (Beacon Timing element) | A set of beacon timing information of the requesting mesh STA. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the MLME as a result of the receipt of a TBTT Adjustment Request frame from a specific peer MAC entity.

- Effect of receipt

The SME is notified of the receipt of the TBTT adjustment request by the specified peer MAC entity. The mesh STA received this primitive subsequently processes the TBTT scanning and adjustment procedure described in 11C.12.4.4.3 (Adjustment procedure), and responds with the MLME-MeshTBTTAdjustment.response.

- MLME-MeshTBTTAdjustment.response

- Function

This primitive is used to send a response to a specific peer MAC entity that requested a TBTT adjustment to the mesh STA that issued this primitive.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MeshTBTTAdjustment.response(

peerMAC,

Status Code,

BeaconTiming,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| peerMAC | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity to which the TBTT Adjustment Response is sent. |
| Status Code | As defined in frame format | As defined in frame format | Indicates the result response to the TBTT adjustment request from the peer mesh STA. |
| BeaconTiming | A set of Beacon Timing element | As defined in 7.3.2.103 (Beacon Timing element) | A set of beacon timing information of the mesh STA. Present only when Status Code is set to 78. |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 | Zero or more elements. |

- When generated

This primitive is generated by the SME of a mesh STA as response to an MLME-MeshTBTTAdjustment.indication primitive.

- Effect of receipt

This primitive initiates the transmission of a TBTT Adjustment Response frame to the specific peer MAC entity that requested the TBTT adjustment.

On receipt of this primitive, the MLME constructs a TBTT Adjustment Response frame. When the Status Code is set to 78, the frame contains the Beacon Timing element. This frame is then scheduled for transmission.

- MLME

- Synchronization

- General

Change the first paragraph in 11.1.0a as follows:

- the following text is based on the amendment by IEEE 802.11p

In infrastructure BSSs or in IBSSs, Aall STAs within a single BSS are synchronized to a common clock using the mechanisms defined herein. A STA for which dot11OCBEnabled is true is not a member of a BSS, and therefore is not required to synchronize to a common clock or use these mechanisms.

In mesh BSSs, STAs use a synchronization protocol as defined as a part of the extensible synchronization framework. The synchronization in MBSS is described in 11C.12 (Synchronization and beaconing in MBSSs).

- 11.1.1  Basic approach

Insert the following new subclause after 11.1.1.2:

- 11.1.1.3  TSF for MBSSs

A mesh STA shall initialize its TSF timer depending on its active synchronization protocol. The mesh STA shall periodically transmit Beacon frames that contain a copy of its TSF timer to announce its local time reference to its neighbor mesh STAs. Mesh STAs receiving a Beacon frame may use the timing information in the Beacon frame depending on their active synchronization protocol.

- Synchronization and beaconing in MBSSs

- TSF for MBSSs

A mesh STA shall initialize and update its TSF timer depending on its active synchronization protocol. Each mesh STA shall maintain a TSF timer as described in 11.1.2, and conform to the TSF timer accuracy as described in 11.1.2.4.

- Extensible synchronization framework

- General

This standard introduces an extensible framework to enable the implementation of multiple synchronization protocols for mesh STAs. Within the extensible synchronization framework, the Neighbor Offset Protocol is defined as the default mandatory protocol in order to enable minimal synchronization capabilities and interoperability between mesh STAs that use MCCA, MBCA, or operate in power save mode. However, to accommodate various application needs, the framework allows flexibility to integrate future synchronization protocols for MBSSs. A vendor can implement any synchronization protocol using this framework to meet special application needs.

Mesh STAs shall announce the active synchronization protocol using the Synchronization Protocol Identifier field in the Mesh Configuration element in their Beacon and Probe Response frames. Although a mesh STA may include multiple implementations of synchronisation protocols, only one synchronization protocol shall be used by a mesh STA at a time and all the mesh STAs in an MBSS use the same synchronisation protocol.

- Neighbor Offset Protocol

- General

When dot11MeshActiveSynchronizationProtocol is 0 (Neighbor Offset Protocol), the mesh STA shall use Neighbor Offset Protocol as its active synchronization protocol, and maintain the timing offset value between its own TSF timer and the TSF timer of each neighbor mesh STA with which it synchronizes. The mesh STA shall maintain synchronization with all of its neighbor peer mesh STAs. The mesh STA should maintain synchronization with up to the dot11MeshNbrOffsetMaxNeighbor neighbor mesh STAs that are in the same the MBSS. Additionally, the mesh STA should maintain synchronization with up to the dot11MeshNbrOffsetMaxNeighbor neighbor STAs that are outside of the MBSS.

Upon receipt of an MLME-MeshNeighborOffsetSyncStart.request, the MLME shall start synchronization using the Neighbor Offset Protocol with the specified peer STA. Upon receipt of an MLME-MeshNeighborOffsetSyncStop.request, the MLME shall stop synchronization with the specified peer STA.

A mesh STA that utilizes the Neighbor Offset Protocol may start its TSF timer independently of other mesh STAs. The mesh STA shall calculate the timing offset value with respect to the neighbor mesh STA as described in 11C.12.2.2.2 (Timing offset calculation). The mesh STA shall adjust its TSF timer based on time stamps received in Beacon or Probe Response frames from neighbor STAs as described in 11C.12.2.2.3 (Clock drift adjustment).

- Timing offset calculation

When dot11MeshActiveSynchronizationProtocol is 0 (Neighbor Offset Protocol), the mesh STA shall update the timing offset value with respect to the neighbor mesh STA based on time stamps from the received Beacon and Probe Response frames as follows:

Toffset = Tt – Tr

where

Toffset is the timing offset value

Tt is the value in the Timestamp field in the received frame

Tr is the frame reception time measured in the mesh STA’s TSF timer

The offset value is represented as twos complement. The unit of the offset value is µs. The mesh STA shall keep the Toffset value calculated from the latest Beacon or Probe Response frame received from each neighbor STA.

A mesh STA may translate the time measured in a neighbor mesh STA’s TSF into the time base of its own TSF as follows:

Tself = Tneighbor – Toffset

where

Tself		 is the translated time in its own TSF

Tneighbor		 is the time measured in the neighbor mesh STA’s TSF

Upon receipt of an MLME-MeshNeighborOffsetMeasure.request, the MLME shall report the measured Toffset to SME by responding with MLME-MeshNeighborOffsetMeasure.confirm. Toffset is used to provide the timing reference of neighbor mesh STAs. These values are needed in order to provide such services as MCCA, MBCA, or power management.

- Clock drift adjustment

When dot11MeshActiveSynchronizationProtocol is 0 (Neighbor Offset Protocol), the mesh STA shall examine the reception time of the Beacon frames from neighbor STAs with which it maintains synchronization and adjust its TSF timer to compensate the relative timing error among neighbor mesh STAs caused by the clock drift. The mesh STA adjusts its TSF so that its TSF counting frequency will be aligned to the most delaying neighbor STAs.

The mesh STA shall operate the following clock drift compensation procedure:

- If the mesh STA does not have a valid Toffset value obtained from the previous Beacon or Probe Response frame reception from a particular neighbor STA, it shall not operate the clock drift compensation for the neighbor STA.

- When the mesh STA receives a Beacon frame or a Probe Response frame from one of the neighbor STAs with which it maintains synchronization, the mesh STA shall calculate the clock drift amount TClockDrift by comparing the Toffset obtained previously for this neighbor STA and the Toffset obtained from the frame reception. 
		TClockDrift = Toffset,1 – Toffset,0 
where TClockDrift is the clock drift amount represented as twos complement in unit of µs, the Toffset,1 is the Toffset obtained from the previous reception, and Toffset,0 is the Toffset obtained from the current frame reception.

- If the received Beacon frame or Probe Response frame contains the Mesh Configuration element and the TBTT Adjusting subfield in the Mesh Configuration field is 1, the mesh STA shall not perform the clock drift compensation based on the received frame and discard the Toffset,1 for this neighbor STA (invalidate the Toffset value obtained from the previous Beacon or Probe Response frame reception).

- The mesh STA shall calculate the TClockDrift value for all neighbor STAs with which it maintains synchronization and pick up the largest TClockDrift value. If the largest TClockDrift is greater than zero, it shall suspend its TSF timer for the duration of the largest TClockDrift. The mesh STA shall suspend its TSF timer frequently enough so that the delay amount within a single beacon period does not exceed 0.08% of its beacon interval.

NOTE—This clock drift compensation procedure does not intend to maintain a strict synchronization. It aims to stop TBTT drifting away among neighbor mesh STAs, allowing some jitter of TSF timer. Since the TSF is adjusted in the slower direction, TSF adjustment does not cause a lost of Beacon frame at neighbor mesh STAs that alternate Awake state and Doze state.

A mesh STA in deep sleep mode may not listen to neighbor mesh STA’s Beacon frame. However, it shall conform to the clock drift compensation procedures and TSF jitter allowance described in this subclause. See Y.3.6 (Synchronization maintenance of mesh STAs in deep sleep mode) for some more guideline.

- Beaconing

- Beacon generation in MBSSs

A mesh STA transmits Beacon frames that are specific to an MBSS. Beacon frames for MBSS, infrastructure BSS, or IBSS are differentiated by the Capability Information field in the Beacon frame as specified in 7.3.1.4 (Capability Information field). A mesh STA that collocates with an AP generates Beacon frames for the MBSS independently of the AP.

The mesh STA shall define a series of TBTTs exactly dot11BeaconPeriod TUs apart. Time zero is defined to be a TBTT with the Beacon frame being a DTIM. At each TBTT, the mesh STA shall schedule a Beacon frame as the next frame for transmission according to the medium access rules specified in Clause 9. The beacon period is included in Beacon and Probe Response frames.

The mesh STA shall start beaconing upon the receipt of the MLME-START.primitive.

- Beacon reception for mesh STA

A mesh STA shall use information from the Timestamp field without regard for the BSSID or Mesh ID, if the mesh STA maintains synchronization with the transmitter of the Beacon frame, to obtain information necessary for synchronization. A mesh STA may use information from the Beacon interval field, the Beacon Timing element, and the MCCAOP Advertisements element without regard for the BSSID or Mesh ID, if the mesh STA maintains synchronization with the transmitter of the Beacon frame, to obtain information necessary for MBCA or MCCA.

A mesh STA in a mesh BSS shall use information that is not in the CF Parameter Set element, the Timestamp field, the Beacon interval field, the Beacon Timing element, or the MCCAOP Advertisements element in received Beacon frames only if the mesh STA maintains mesh peerings with the transmitter of the Beacon frame.

- Mesh Beacon Collision Avoidance (MBCA)

- Overview

Mesh STAs use the Mesh Beacon Collision Avoidance (MBCA) to detect and mitigate collisions among Beacon frames transmitted by other STAs (including mesh STAs, APs, and STAs in an IBSS) on the same channel within the range of 2 hops. MBCA is intended to mitigate hidden node problems with respect to Beacon frames.

NOTE—Beacon frames are essential for passive scan, power management, and MCCA. However, Beacon frames are transmitted without acknowledgement and might collide with other frames. In a mesh BSS, multiple STAs transmit Beacon frames periodically, and mesh STAs might be located out of range of each other. This implies that Beacon frames might suffer from the so-called hidden node problem and might not be received by neighbor STAs. Once Beacon frames from hidden STAs start to collide each other, Beacon frames will keep on colliding if these hidden STAs transmit Beacon frames at the same beacon interval that is a typical operation. MBCA provides a set of rules to mitigate this problem.

When dot11MBCAActivated is true, the mesh STA shall activate the MBCA procedures described in 11C.12.4 (Mesh Beacon Collision Avoidance (MBCA)) and shall set MBCA Enabled subfield in the Mesh Capability field of the Mesh Configuration element to 1.

- Beacon timing advertisement

- Maintenance of the status number

When dot11MBCAActivated is true, the mesh STA shall maintain the status number of the beacon timing information set. The status number, given by a modulo-16 counter, is initialized with 0 and incremented by 1 before transmitting a frame containing the Beacon Timing element when the mesh STA encountered any of the following events since it has updated the status number previously:

- It starts or stops maintaining synchronization with a particular neighbor STA.

- It receives a Beacon frame from a neighbor STA with which it maintains synchronization and the calculated TDelta (see 11C.12.4.2.2) is larger than 255 μs.

- It completes the TBTT adjustment procedure described in 11C.12.4.4.3 (Adjustment procedure).

The mesh STA shall set the Status Number subfield in the Report Control field in the Beacon Timing element to the status number. The Status Number subfield in the Report Control field facilitates the detection of the changes in the beacon timing information set.

- Calculation of neighbor STA’s TBTT

When a Beacon frame is received from one of its neighbor STAs with which the mesh STA maintains synchronization, the mesh STA shall calculate the TBTT of the received Beacon frame as follows:

TTBTT = Tr – (Tt modulo (TBeaconInterval  1024))

where

TTBTT 			is the calculated TBTT

Tr			is the frame reception time measured in the receiving mesh STA’s TSF timer

Tt 			is the value in the Timestamp field in the received frame

TBeaconInterval 			is the value in the Beacon interval field in the received frame

The mesh STA shall extract the second and third least significant octets of the TTBTT and keep the value as an abbreviated TBTT, which represents the time in units of 256 µs.

Further, the mesh STA shall calculate the time difference between the TBTT of the received Beacon frame and the time predicted from the previous TBTT as follows:

TDelta = | TTBTT, 0 – (TTBTT, 1 + (TBeaconInterval NCount)) |

where

TDelta 			is the time difference

TTBTT, 0 		is the TBTT calculated from the received Beacon frame

TTBTT, 1 		is the TBTT calculated for the first time since the latest update of the status number

TBeaconInterval 	is the value in the Beacon interval field in the received Beacon frame

NCount			is the number of TBTTs since TTBTT, 1 is claculated

TDelta is used to maintain the status number described in 11C.12.4.2.1.

- Beacon timing information

The mesh STA shall keep the latest abbreviated TBTT together with the Beacon interval contained in the received frame and the neighbor STA identification, as a beacon timing information with respect to the neighbor STA. When the elapsed time since the latest Beacon frame reception is smaller than 16 s, the beacon timing information is valid.

NOTE—A beacon timing information provides the time reference to a series of the TBTTs of the corresponding STA. Using the beacon timing information, a mesh STA can predict future TBTTs by adding the reported beacon interval to the reported TBTT.

The mesh STA shall collect the valid beacon timing information from each neighbor STA with which it maintains synchronization and keep the collection as the beacon timing information set. The beacon timing information set is advertized to its neighbor mesh STAs through the Beacon Timing element as described in 11C.12.4.2.3 (Transmitter’s procedure).

When the number of valid beacon timing information is large, the beacon timing information set may be divided into multiple tuples of beacon timing information. In such case, a tuple of beacon timing information is included in the Beacon Timing element. (see 11C.12.4.2.3 (Transmitter’s procedure))

- Transmitter’s procedure

When dot11MBCAActivated is true, the mesh STA shall report the TBTT and beacon interval of its neighbor STAs through the Beacon Timing element as described in this subclause.

The Beacon Timing element reports on timing information of the Beacon frames that are received from the neighbor STAs with which the mesh STA maintains synchronization on the operating channel. The mesh STA shall include the Beacon Timing element in Probe Response frames and in TBTT Adjustment Request frames. The mesh STA shall also include the Beacon Timing element in Beacon frames as specified by the attributes of the beacon timing report procedure given by dot11MeshBeaconTimingReportInterval and dot11MeshBeaconTimingReportMaxNum. The Beacon Timing element is present in the Beacon frame when the DTIM Count value in the Beacon frame is zero or equal to an integer multiple of the dot11MeshBeaconTimingReportInterval.

The maximum number of Beacon Timing Information fields contained in a Beacon Timing element is limited to dot11MeshBeaconTimingReportMaxNum for Beacon frames, or is limited by the maximum information element size for other frames.When the number of valid beacon timing information is equal or smaller than the limit, the mesh STA shall include all the beacon timing information in the Beacon Timing element, setting both Beacon Timing Element Number and More Beacon Timing Elements subfield in the Report Control field to 0. When the number of valid beacon timing information exceeds the limit, the mesh STA shall divide the beacon timing information set into multiple tuples and assign each tuple with an index number starting from 0. When the beacon timing information set is divided, the mesh STA shall include one of the successive tuples of beacon timing information in the Beacon Timing element. In such case, the mesh STA shall set the Beacon Timing Element Number subfield in the Report Control field to the index number of the tuple. The mesh STA shall set the More Beacon Timing Elements subfield in the Report Control field to 1 when it has one or more beacon timing information tuples with a larger index number. The mesh STA shall divide the beacon timing information set into no more than N_Info tuples, where N_Info = ceil(number of valid beacon timing information/the maximum number of Beacon Timing Information fields in the Beacon Timing element).

The mesh STA may update the combination of the tuples only when the status number described in 11C.12.4.2.1 is updated. The mesh STA shall include newly updated beacon timing information (i.e., beacon timing information that causes an update of the status number as described in 11C.12.4.2.1 (Maintenance of the status number)) in the tuple with a smaller index number. When the status number is updated, the mesh STA shall include the tuple of beacon timing information indexed as 0 in the Beacon Timing element in the subsequent Beacon frame. Successive tuples shall be transmitted in ascending order of the index number in the successive Beacon frames.

NOTE— The standard does not impose mesh STAs to advertize fragmented beacon timing information set sequentially in its Beacon frames at all times. This implies that the mesh STA can advertise tuples with a smaller index number more frequently, which is useful to notify new beacon timing information efficiently.

When the mesh STA receives a Probe Request frame containing a Beacon Timing element ID in its Request element, it shall respond with a Probe Response frame containing the Beacon Timing element. If all beacon timing information cannot be contained in a Beacon Timing element, the mesh STA shall include multiple Beacon Timing elements containing successive tuples of beacon timing information in the order of the Request element (see Table 7-15) so that all tuples are transmitted.

- Receiver’s procedure

A mesh STA that receives a Beacon Timing element can obtain the beacon reception timing of its neighbor mesh STA. This information is used for its TBTT selection and TBTT adjustment. When dot11MBCAActivated is true, the mesh STA shall operate TBTT selection as described in 11C.12.4.3 (TBTT selection) and TBTT adjustment as described in 11C.12.4.4 (TBTT adjustment).

When a mesh STA receives a Beacon frame containing Beacon Timing element that indicates only a subset of the beacon timing information set is contained, the mesh STA may transmit a Probe Request frame containing a Beacon Timing element ID in its Request Information element to the transmitter of the Beacon Timing element, in order to request the rest of the beacon timing information.

NOTE1—The Report Control field in the Beacon Timing element facilitates the detection of the missing beacon timing information.

NOTE2—Once an entire beacon timing information set is obtained with a particular Status Number, the mesh STA do not need to retrieve beacon timing information as long as the Status Number remains the same as indicated in the previously received Beacon Timing element.

A mesh STA that receives the Beacon Timing element shall record the reported TBTT and its successive TBTTs as neighbor’s essential beacon reception timing if the MSB of the Neighbor STA ID field in the corresponding Beacon Timing Information field is 0. The essential beacon reception timing is used to control the transmission of frames as described in 11C.12.4.5 (Frame transmission across reported TBTT).

A mesh STA can also check if its neighbor mesh STAs received its Beacon frame successfully by checking whether the Beacon Timing elements received from its neighbor mesh STAs contain beacon timing information of the mesh STA. When the Beacon Timing element is received from one of the peer mesh STAs, the mesh STA checks if the MSB of the Neighbor STA ID subfield is set to 0 and the rest of the field matches with the 7 LSBs of the AID value assigned by this peer mesh STA through the mesh peering establishment. When the Beacon Timing element is received from a non-peer mesh STA, the mesh STA checks if the MSB of the Neighbor STA ID subfield is set to 1 and the rest of the field matches with the 7 LSBs of its own MAC address (taking the I/G bit as the MSB). If the matching is verified, the corresponding beacon timing information represents the mesh STA’s beacon reception, which means the neighbor mesh STA receives that Beacon frame correctly.

- TBTT selection

When dot11MBCAActivated is true, the mesh STA shall select its TBTTs and its beacon interval so that its Beacon frames do not collide with Beacon frames transmitted by other STAs in its 2 hop range, using the information obtained from the Beacon Timing element from its neighbor mesh STAs.

Before the mesh STA starts beaconing, it shall obtain the TBTT and beacon interval of its neighbor STAs during the  discovery process (see 11C.2 (Mesh discovery)). The mesh STA shall also collect the beacon timing information contained in the Beacon Timing elements received from its neighbor mesh STAs in order to obtain the TBTT and beacon interval of STAs in 2 hop range. After collecting this information, the mesh STA shall look for the timing of its beacon transmission so that its Beacon frames are likely not to collide with Beacon frames transmitted by other STAs in its 2 hop range. The mesh STA shall update its TSF timer and select its beacon interval to set its TBTTs to the appropriate timing, and then it shall start beaconing using the MLME-START.request primitive.

When dot11MCCAActivated is true, the mesh STA shall choose a DTIM interval with a duration of 2n  100 TU with n a non-negative integer less than or equal to 18.

- TBTT adjustment

- Proactive TBTT adjustment

When dot11MBCAActivated is true, the mesh STA shall check if it does not transmit Beacon frames during the beacon transmissions of other STAs withing its 2 hop rage by parsing the Beacon Timing element. If the Beacon frame is received from a neighbor peer mesh STA that is either in active mode or in light sleep mode, the mesh STA shall also verify if the neighbor peer mesh STA received its Beacon frame as described in 11C.12.4.2.4 (Receiver’s procedure).

When the mesh STA discovers that its Beacon frames repeatedly collide with the Beacon frames of a neighbor or a neighbor’s neighbor and its TBTT appears later than that of colliding STA at the time of collision, it shall start the TBTT scanning procedure described in 11C.12.4.4.3 (Adjustment procedure). If the mesh STA finds an alternative TBTT, it shall start the TBTT adjustment procedure as described in 11C.12.4.4.3 (Adjustment procedure).

- Reactive TBTT adjustment

When a mesh STA discovers that Beacon frames from two or more neighbor mesh STAs are colliding repeatedly or a series of TBTTs are close enough to trigger the consecutive beacon collision, the mesh STA may transmit a TBTT Adjustment Request frame to the neighbor mesh STA of which the TBTT appears last at a particular collision timing in order to request this neighbor mesh STA to adjust its TBTT. The TBTT Adjustment Request frame may be transmitted if the recipient  is a peer mesh STA and has set the MBCA Enabled subfield in the Mesh Capability field of the Mesh Configuration element to 1.

When dot11MBCAActivated is true, the mesh STA that receives a TBTT Adjustment Request frame shall start the TBTT scanning procedure described in 11C.12.4.4.3 (Adjustment procedure), and determine if it can find an appropriate alternative timing for its TBTTs. After the completion of the TBTT scanning procedure, the mesh STA that receives the TBTT Adjustment Request frame shall respond with a TBTT Adjustment Response frame containing the result of the TBTT scanning in the Status Code field. If the mesh STA finds an alternatie TBTT, it shall agree with the request. If it agrees with the request, the Status Code field is set to 0 in the TBTT Adjustment Response frame, and it shall complete the TBTT adjustment procedure described in 11C.12.4.4.3 (Adjustment procedure). If it does not agree with the request, it shall indicate the reason in the Status Code field in the TBTT Adjustment Response frame. A mesh STA can set the Status Code to either 0, 1, or 78 in the TBTT Adjustment Response frame.

- TBTT scanning and adjustment procedure

When a mesh STA is in need of TBTT adjustment, it tries to find an alternative TBTT firstly. The mesh STA shall start the TBTT scanning procedure as follows:

- During the TBTT scanning and adjustment procedure, the mesh STA shall set the TBTT Adjusting field in the Mesh Configuration element to 1 in order to announce that the TBTT adjustment procedure is ongoing.

- The mesh STA collects new beacon timing information. It shall receive Beacon or Probe Response frames from its neighbor STAs with which it maintains synchronization, and obtain the TBTT of its neighbor STAs and the beacon timing information contained in the Beacon Timing elements.

- Using the collected new beacon timing information, the mesh STA shall look for an alternative TBTT that does not cause beacon collision among the STAs in its 2 hop range.

- If an alternative TBTT is not available, the mesh STA terminates the procedure. Upon termination of the procedure, it shall set the TBTT Adjusting field in the Mesh Configuration element to 0. If an alternative TBTT is available, the mesh STA shall start the TBTT adjustment procedure as follows:

- The mesh STA shall suspend its TSF timer for a period of time, no longer than half of the Group Delivery Idle Time (defined in 11C.13.6 (TIM types)) within a single beacon period, to slow its TSF.

- The mesh STA shall adjust TBTT information of the neighbor STAs (see 11C.12.4.2.3 (Beacon timing information)), that are to be contained in the Beacon Timing element, accordingly by subtracting the delay amount.

- When dot11MCCAActivated is true, the mesh STA shall adjust the MCCAOP reservations accordingly by modifying the MCCAOP Offset of each MCCAOP reservation (See 9.9a.3.3 (MCCAOP reservations).)

- The mesh STA shall repeat suspending its TSF timer over multiple beacon periods until its TBTT is set to the alternative TBTT.

- Upon completion of the TBTT adjustment, the mesh STA shall update the status number as described in  11C.12.4.2.1 (Maintenance of the status number) and shall set the TBTT Adjusting field in the Mesh Configuration element to 0.

NOTE 1—Since the TBTT is adjusted by slowing its TSF, TBTT adjustment does not cause a loss of Beacon frames at neighbor mesh STAs that alternate Awake state and Doze state.

NOTE 2—A mesh STA in deep sleep mode might(Ed) interpret its neighbor mesh STA’s TBTT adjustment as a large TSF jitter. When a mesh STA in deep sleep mode observes a large TSF jitter and the received Beacon frame (or Probe Response frame) indicates that the Status Number in the Report Control field in the Beacon Timing element is updated, the mesh STA in deep sleep mode should not take this jitter as clok drift and listen to the next Beacon frame to verify if the clock drift is large.

- Frame transmission across reported TBTT

When dot11MBCAActivated is true, the mesh STA should not extend its transmissions across TBTT of its neighbor STAs with which it maintains synchronization. Further, the mesh STA should not extend its transmissions, other than Beacon frames, across all essential beacon reception timing (see 11C.12.4.2.4 (Receiver’s procedure)) reported from its neighbor mesh STAs with which it maintains synchronization. This operation helps in reducing the hidden STA interference with beacon reception at its neighbor mesh STAs. When both dot11MBCAActivated and dot11MCCAActivated are true, the mesh STA shall not extend its transmissions across TBTT of its neighbor STAs with which it maintains synchronization. Further, the mesh STA shall not extend its transmissions, other than Beacon frames, across all beacon reception timing reported from its neighbor mesh STAs with which it maintins synchronization.

After silencing for dot11MeshAverageBeaconFrameDuration µs from the reported neighbor’s TBTT, the mesh STA may start transmitting frames again.

- Delayed beacon transmissions

A mesh STA may occasionally delay its Beacon frame transmission from its TBTT for a pseudo-random time. This attribute is specified by dot11MeshDelayedBeaconTxInterval, dot11MeshDelayedBeaconTxMinDelay, and dot11MeshDelayedBeaconTxMaxDelay. When dot11MeshDelayedBeaconTxInterval is set to non-zero value, the mesh STA shall delay its Beacon frame transmission from TBTT, once every dot11MeshDelayedBeaconTxInterval. When the mesh STA transmits a Beacon frame with delay from its TBTT, the delay time shall be randomly selected between dot11MeshDelayedBeaconTxMinDelay and dot11MeshDelayedBeaconTxMaxDelay µs.

NOTE—Delayed beacon transmission allows mesh STAs to discover Beacon frames that are transmitted from multiple mesh STAs with TBTTs close to each other. It is recommended to set dot11MeshDelayedBeaconTxMaxDelay to a time longer than the typical duration of Beacon frames.

- MIB Detail

dot11MeshActiveSynchronizationProtocol OBJECT-TYPE

SYNTAX INTEGER { NeighborOffsetProtocol (0), VendorSpecific (255) }

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request.

This attribute specifies the active synchronization protocol."

DEFVAL { NeighborOffsetProtocol }

dot11MeshNbrOffsetMaxNeighbor OBJECT-TYPE

SYNTAX Unsigned32 (1..255)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a capability variable.

Its value is determined by device capabilities.

This attribute specifies the maximum number of neighbor STAs with which the mesh STA maintains synchronization using the Neighbor Offset Protocol."

DEFVAL { 16 }

dot11MBCAActivated OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request.

This attribute specifies whether or not the station activates Mesh Beacon Collision Avoidance mechanisms."

DEFVAL { false }

dot11MeshBeaconTimingReportInterval OBJECT-TYPE

SYNTAX Unsigned32 (1..255)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifies when the Beacon Timing element is present in Beacon frames. The Beacon Timing element is present when the DTIM Count value in the Beacon frame is zero or equal to an integer multiple of the set value."

DEFVAL { 4 }

dot11MeshBeaconTimingReportMaxNum OBJECT-TYPE

SYNTAX Unsigned32 (0..50)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifies the maximum number of the Beacon Timing Information field contained in a Beacon Timing element in the transmitting Beacon frames."

DEFVAL { 16 }

dot11MeshDelayedBeaconTxInterval OBJECT-TYPE

SYNTAX Unsigned32 (0..255)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifies the interval of the delayed beacon transmission for the purpose of MBCA. The value 0 indicates that the delayed beacon transmission is disabled. The value is expressed in units of Beacon Interval."

DEFVAL { 0 }

dot11MeshDelayedBeaconTxMaxDelay OBJECT-TYPE

SYNTAX Unsigned32 (0..65535(CID277))

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifies the maximum delay from a TBTT of delayed beacon transmissions for the purpose of MBCA. The value is expressed in units of microseconds."

DEFVAL { 2048(CID277) }

dot11MeshDelayedBeaconTxMinDelay OBJECT-TYPE

SYNTAX Unsigned32 (0..4023)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifyies the minimum delay time from a TBTT of delayed beacon transmission for the purpose of MBCA. The value is expressed in units of microseconds."

DEFVAL { 0 }

dot11MeshAverageBeaconFrameDuration OBJECT-TYPE

SYNTAX Unsigned32 (0..16383(CID277))

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

This attribute specifies the average duration of the last 16 Beacon frames of other mesh STAs received by this mesh STA. The value is expressed in units of microseconds."

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D8.0, December 2011.

# Comments

Underline and strikeout

Underline and strikeout

underlined

# Text boxes

Abstract

This document provides suggested resolutions to M-BS comments.