## Slide 1: NDP for MU Link Adaptation
Authors:
Date: 2011-1-18
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Introduction
NDP is the only sounding format in 11ac.
Currently the use of NDP is limited to SU operation
Proposal
  Extend definition of use to MU operation
  Introduce metrics to enable DL MU evaluation

## Slide 3: TxVector Settings for NDP
For SU the following TxVector settings are defined:
  LENGTH=0
  NUM_USERS=1 (NDP is a SU packet)
  Group ID is all-one (NDP is a SU packet).
  NUM_STS >=2
    11ac NDPA+NDP sequence only serves the purpose of TxBF/MU.
Proposed MU case:
  LENGTH=0
  NUM_USERS=Nu (NDP now for MU sounding)
  Group ID is set to valid group.
  NUM_STS >=1
    Extend NDP use to 11ac MU Link Adaptation.

## Slide 4: Link Adaptation for MU case
We already have rule on MFB in SU BF (11n): MFB+SNR assumes the same CV will be applied, and Nsts=Nc.
Extended rules for responding to MRQ with NDPA.
Proposal: if the MRQ is in NDPA that requests MU feedback, BF’ee SHALL include the MFB+SNR for MU channel and omit steering matrix data.
  Reason: Provide MU-AP with direct measure of DL channel condition
NDPA
MFB+SNR
NDP
SIFS
SND
Poll
SND
Poll
MFB+SNR
SIFS
SIFS
SIFS
STA Info set to indicate use of GroupID in NDP
MRQ=1
GroupID set to a valid MU group
Pre-coded VHT-LTF fields
Frame format containing DL quality information
MFB+SNR

## Slide 5: Additional MU Metrics
Current MFB+SNR metric of limited value for DL assessment
  Averaging over spatial streams loses channel information
  SNR calculation is undefined, thus implementation dependent
Proposal: Interference Metrics for DL evaluation
Type | Max # of values | Bit resolution
Complete interference | 16 | 6
Per-SS SIR from other users | 12 | 6
Per-User SIR for all SS | 3 | 6
1 SIR from all others | 1 | 8

## Slide 6: Summary of MU metrics benefits
Existing MFB+SNR limited use for MU operation
  Can not help to distinguish if low SNR is from interference
  Limited field availability in VHTC prevents extended definitions
Direct Assist MU operation
  Evaluate effectiveness of precoding matrices
  Minimizes trial-and-error of MU MCS rate selection
  Fine tune MU precoding algorithm
Provides AP valuable info
  Staleness of profiles/precoding matrices
  Level of interference mitigation at STA

## Slide 7: Straw poll #1
Do you support the idea of including MU interference metric feedback for .11ac?
  -Yes
  -No
  -Abstain

## Slide 8: Straw poll #2
Do you support the idea of including an MU-NDP mode to enable MU-DL evaluation?