IEEE P802.11
Wireless LANs

| MIB Contribution |
| --- |
| Date: May 9, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Daniel R. Borges | Apple, Inc. |  | +1 (415) 425-7347 | drborges@apple.com |
| Carlos Cordeiro | Intel Corporation |  | +1 (503) 705-1286 | carlos.cordeiro@intel.com |
| Saishankar Nandagopalan | Tensorcom |  | (858) 337-6652 | nsai@tensercom.com |

Editor: In the Major Section of Annex D, insert the following comment to the end of SMT attributes after dot11HTStationConfigTable:

-- Added for 802.11ad

-- dot11DBandSTAConfigTable		::= { dot11smt <ANA> }(11ad)

Editor: In the Major Section of Annex D, insert the following comment to the end of dot11mac section after dot11ResourceInfoTable:

-- Added for 802.11ad

-- dot11DBandOperationTable		::= { dot11mac <ANA> }(11ad)

-- dot11DBandCountersTable		::= { dot11mac <ANA> }(11ad)

Editor: In the Major Section of Annex D, insert the following comment to the end of dot11phy section after dot11TransmitBeamformingConfigTable:

-- Added for 802.11ad

-- dot11DBandPHYConfigTable		::= { dot11phy <ANA> }(11ad)

-- dot11DBandPHYTxRateTable		::= { dot11phy <ANA> }(11ad)

-- dot11DBandPHYRxRateTable		::= { dot11phy <ANA> }(11ad)

-- dot11DBandBeamformingConfigTable ::= { dot11phy <ANA> }(11ad)

Editor: In the Major Section of Annex D, modify the dot11PhyType object with the following definition.

-- **********************************************************************

-- *    dot11PhyOperation  TABLE

-- **********************************************************************

dot11PHYType OBJECT-TYPE

SYNTAX INTEGER {

fhss(1),

dsss(2),

irbaseband(3),

ofdm(4),

hrdsss(5),

erp(6),

ht(7),

dband(8)

}

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a status variable(#1005).

It is written by the PHY(#1005).

This is an 8-bit integer value that identifies the PHY type supported by the attached PLCP and PMD. Currently defined values

and their corresponding PHY types are:

FHSS 2.4 GHz = 01, DSSS 2.4 GHz = 02, IR Baseband = 03,

OFDM(#1061) = 04, HRDSSS = 05, ERP = 06, HT = 07(11n), DBand = 				08"

::= { dot11PhyOperationEntry 1 }

Editor: After the definition of the dot11HTStationConfigTable, insert the dot11DBandSTAConfigTable as defined below:

-- ********************************************************************

-- * dot11DBandSTAConfigTable TABLE

-- ********************************************************************

dot11DBandSTAConfigTable OBJECT-TYPE

SYNTAX SEQUENCE OF Dot11DBandSTAConfigEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is a table management object.

The dot11DBandSTAConfig Table"

::= { dot11smt <ANA> }

dot11DBandSTAConfigEntry OBJECT-TYPE

SYNTAX Dot11DBandSTAConfigEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is an entry in the dot11DBandSTAConfig Table.

ifIndex - Each IEEE 802.11 interface is represented by an

ifEntry.  Interface tables in this MIB module are indexed

by ifIndex."

INDEX { ifIndex }

::= { dot11DBandSTAConfigTable 1 }

Dot11DBandSTAConfigEntry ::=

SEQUENCE {

dot11MultibandSupportActivated			TruthValue,

dot11DBandCapable						TruthValue,

dot11RelayEnabled						TruthValue,

dot11RSNAProtectedManagementFramesActivated	TruthValue

}

dot11MultibandSupportActivated OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a status variable.

It is written by an external management entity.

Changes take effect as soon as practical in the implementation.

Multiband Support Activated

This attribute, when true, indicates that the capability

of the station to operate in multiple bands is enabled.

The capability is disabled, otherwise. The default value

of this attribute is false."

DEFVAL { false }

::= {  dot11DBandSTAConfigEntry 1 }

dot11DBandCapable OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a capability variable.

It is written by an external management entity.

Its value is determined by device capabilities.

DBand Capable Object

This attribute, when true, indicates the STA is DBand

capable.  This attribute, when false, indicates the STA is not

DBand capable.  The default value of this attribute is false."

DEFVAL { false }

::= { dot11DBandSTAConfigEntry 2 }

dot11RelayEnabled OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a status variable.

It is written by an external management entity.

Changes take effect as soon as practical in the implementation.

This attribute, when true, indicates the DBand STA is Relay

capable.  This attribute, when false, indicates the STA is not

Relay capable.  The default value of this attribute is false."

DEFVAL { false }

::= { dot11DBandSTAConfigEntry 3 }

dot11RSNAProtectedManagementFramesActivated OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a status variable.

It is written by an external management entity.

Changes take effect as soon as practical in the implementation.

If dot11RSNAProtectedManagementFramesEnabled is TRUE, the recipient shall maintain a single replay counter for received unicast Robust Management frames and shall use the PN from the received frame to detect replays."

DEFVAL { false }

::= { dot11DBandSTAConfigEntry 4 }

Editor: After the definition of the dot11DBandPHYConfigTable, insert the dot11DBandBeamformingConfigTable as defined below:

-- ********************************************************************

-- * dot11DBandBeamformingConfig TABLE

-- ********************************************************************

dot11DBandBeamformingConfigTable OBJECT-TYPE

SYNTAX SEQUENCE OF Dot11DBandBeamformingConfigEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is a Table management object.

The dot11DBandBeamformingConfig Table"

::= { dot11phy <ANA> }

dot11DBandBeamformingConfigEntry OBJECT-TYPE

SYNTAX Dot11DBandBeamformingConfigEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is an entry in the dot11DBandBeamformingConfig Table.

ifIndex - Each IEEE 802.11 interface is represented by an

ifEntry.  Interface tables in this MIB module are indexed

by ifIndex."

INDEX { ifIndex }

::= { dot11DBandBeamformingConfigTable 1 }

Dot11DBandBeamformingConfigEntry ::=

SEQUENCE {

dot11MaxBFTime				Unsigned32,

dot11BFTXSSTime				Unsigned32,

dot11MaximalSectorScan			Unsigned32,

dot11ABFTRSSSwitch			Unsigned32,

dot11RSSRetryLimit			Unsigned32,

dot11RSSBackoff				Unsigned32,

dot11BFRetryLimit				Unsigned32,

dot11BFTXSSTime				Unsigned32,

dot11BeamLinkMaintenanceTime		Unsigned32

}

dot11MaxBFTime OBJECT-TYPE

SYNTAX Unsigned32 (1..16)

UNITS "milliseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Maximum Beamforming Time (in units of Beacon Interval)."

DEFVAL { 4 }

::= { dot11DBandBeamformingConfigEntry 1 }

dot11BFTXSSTime OBJECT-TYPE

SYNTAX Unsigned32 (1..256)

UNITS "milliseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Beamforming Transmission ScS Time (in Milliseconds)."

DEFVAL { 4 }

::= { dot11DBandBeamformingConfigEntry 2 }

dot11MaximalSectorScan OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Maximal Sector Scan (in units of Beacon Interval)."

DEFVAL { 8 }

::= { dot11DBandBeamformingConfigEntry 3 }

dot11ABFTRSSSwitch OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

A-BFT Responder Sector Sweep Switch (in units of Beacon Interval)."

DEFVAL { 4 }

::= { dot11DBandBeamformingConfigEntry 4 }

dot11RSSRetryLimit OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Responder Sector Sweep Retry Limit"

DEFVAL { 8 }

::= { dot11DBandBeamformingConfigEntry 5 }

dot11RSSBackoff OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Responder Sector Sweep Backoff"

DEFVAL { 8 }

::= { dot11DBandBeamformingConfigEntry 6 }

dot11BFRetryLimit OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Beamforming Retry Limit"

DEFVAL { 8 }

::= { dot11DBandBeamformingConfigEntry 7 }

dot11BFTXSSTime OBJECT-TYPE

SYNTAX Unsigned32 (1..1024)

UNITS "milliseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Timeout until the initiator restarts ISS (in Milliseconds)."

DEFVAL { 100 }

::= { dot11DBandBeamformingConfigEntry 8 }

dot11BeamLinkMaintenanceTime OBJECT-TYPE

SYNTAX Unsigned32 (0..64000000)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Beam Link Maintenance Time

dot11BeamLinkMaintenanceTime = BeamLink_Maintenance_Unit * BeamLink_Maintenance_Value. Otherwise, the dot11BeamLinkMaintenanceTime is left undefined. An

undefined value of the dot11BeamLinkMaintenanceTime indicates

that the STA does not participate in beamformed link maintenance."

DEFVAL { 0 }

::= { dot11DBandBeamformingConfigEntry 9 }

Editor: After the definition of the dot11ResourceInfoTable, insert the dot11DBandOperationTable as defined below:

-- ********************************************************************

-- * dot11DBandOperation TABLE

-- ********************************************************************

dot11DBandOperationTable OBJECT-TYPE

SYNTAX SEQUENCE OF Dot11DBandOperationEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is a Table management object.

The dot11DBandOperation Table"

::= { dot11mac <ANA> }

dot11DBandOperationEntry OBJECT-TYPE

SYNTAX Dot11DBandOperationEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is an entry in the dot11DBandBeamformingConfig Table.

ifIndex - Each IEEE 802.11 interface is represented by an

ifEntry.  Interface tables in this MIB module are indexed

by ifIndex."

INDEX { ifIndex }

::= { dot11DBandOperationTable 1 }

Dot11DBandOperationEntry ::=

SEQUENCE {

dot11MaxLostBeacons			Unsigned32,

dot11MinBIHeaderDuration		Unsigned32,

dot11PSRequestSuspensionInterval	Unsigned32,

dot11AssocRespConfirmTime		Unsigned32,

dot11BroadcastSTAInfoDuration		Unsigned32,

dot11NbrOfChangeBeacons			Unsigned32,

dot11ImplicitHandoverLostBeacons	Unsigned32,

dot11MinPPDuration				Unsigned32,

dot11SPIdleTimeout				Unsigned32,

dot11QABTimeout					Unsigned32,

dot11ClusterEnableTime				Unsigned32,

dot11PNWarningThreshold				Unsigned32,

dot11BeaconSPDuration				Unsigned32,

dot11PNExhaustionThreshold			Unsigned32,

dot11MaxNumberOfClusteringMonitoringPeriods	Unsigned32,

dot11DBandEcssPolicyDetailUpdateDurationMax	Unsigned32,

dot11DBandEcssClusterReportDurationMin		Unsigned32

}

dot11MaxLostBeacons OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Maximum Number of Lost Beacons"

DEFVAL { 4 }

::= { dot11DBandOperationEntry 1 }

dot11MinBIHeaderDuration OBJECT-TYPE

SYNTAX Unsigned32 (1..100000)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Minimum Beacon Interval Header Duration (in microseconds)"

DEFVAL { 5000 }

::= { dot11DBandOperationEntry 2 }

dot11PSRequestSuspensionInterval OBJECT-TYPE

SYNTAX Unsigned32 (1..64)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

PS Request Suspension Interval (in units of Beacon Interval)"

DEFVAL { 8 }

::= { dot11DBandOperationEntry 3 }

dot11AssocRespConfirmTime OBJECT-TYPE

SYNTAX Unsigned32 (1..8000)

UNITS "milliseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Association Response Confirmation Time (in Milliseconds)."

DEFVAL { 1000 }

::= { dot11DBandOperationEntry 4 }

dot11BroadcastSTAInfoDuration OBJECT-TYPE

SYNTAX Unsigned32 (1..512)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Broadcast STA Information Duration (in units of Beacon Interval)."

DEFVAL { 32 }

::= { dot11DBandOperationEntry 5 }

dot11NbrOfChangeBeacons OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Number of Change Beacons (in units of Beacon Interval)."

DEFVAL { 4 }

::= { dot11DBandOperationEntry 6 }

dot11ImplicitHandoverLostBeacons OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Implicit Handover Lost Beacons (in units of Beacon Interval)."

DEFVAL { 8 }

::= { dot11DBandOperationEntry 7 }

dot11MinPPDuration OBJECT-TYPE

SYNTAX Unsigned32 (1..100000)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

The MinPPDuration subfield indicates the minimum duration of the

PP and GP as part of the dynamic allocation of service period

mechanism (in microseconds)."

DEFVAL { 200 }

::= { dot11DBandOperationEntry 8 }

dot11SPIdleTimeout OBJECT-TYPE

SYNTAX Unsigned32 (1..100000)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

The SPIdleTimeout subfield indicates time during which a STA

expects to receive a frame from its partner STA

(in microseconds)."

DEFVAL { 200 }

::= { dot11DBandOperationEntry 9 }

dot11QABTimeout OBJECT-TYPE

SYNTAX Unsigned32 (1..64000)

UNITS "milliseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Quiet Adjacent BSS Operation Timeout (in milliseconds)"

DEFVAL { 1000 }

::= { dot11DBandOperationEntry 10 }

dot11ClusterEnableTime OBJECT-TYPE

SYNTAX Unsigned32 (1..32)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Frequency with which a non-PCP/non-AP is allowed to retransmit a cluster request element to its PCP/AP (in units of Beacon Interval)."

DEFVAL { 8 }

::= { dot11DBandOperationEntry 11 }

dot11PNWarningThreshold OBJECT-TYPE

SYNTAX Unsigned32 (1..2e48)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Threshold used for generating a warning to the MLME about a potential PN exhaustion (in units of packet number)."

DEFVAL { 2e36 }

::= { dot11DBandOperationEntry 12 }

dot11BeaconSPDuration OBJECT-TYPE

SYNTAX Unsigned32 (1..100000)

UNITS "microseconds"

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

The size of a Beacon SP used for PCP/AP clustering (in microseconds)."

DEFVAL { 600 }

::= { dot11DBandOperationEntry 13 }

dot11PNExhaustionThreshold OBJECT-TYPE

SYNTAX Unsigned32 (1..2e48)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Threshold used for indicating an imminent PN exhaustion (in units of packet number)."

DEFVAL { 2e47 }

::= { dot11DBandOperationEntry 14 }

dot11MaxNumberOfClusteringMonitoringPeriods OBJECT-TYPE

SYNTAX Unsigned32 (1..16)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Number of clustering monitoring periods until determination of the loss of an S-PCP/S-AP."

DEFVAL { 3 }

::= { dot11DBandOperationEntry 15 }

dot11DBandEcssPolicyDetailUpdateDurationMax OBJECT-TYPE

SYNTAX Unsigned32 (10..30000)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Maximum duration in units of TU between attempts by a member PCP/AP in a Centralized PCP/AP cluster to receive a DBand Beacon frame from the S-AP of the Centralized PCP/AP cluster"

DEFVAL { 1000 }

::= { dot11DBandOperationEntry 16 }

dot11DBandEcssClusterReportDurationMin OBJECT-TYPE

SYNTAX Unsigned32 (100..36000000)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME or an external management entity.

Changes take effect as soon as practical in the implementation.

Minimum duration in units of TU between the transmission of interference reports by a member PCP/AP in a Centralized PCP/AP cluster to the S-AP of the Centralized PCP/AP cluster"

DEFVAL { 1000 }

::= { dot11DBandOperationEntry 17 }

-- ********************************************************************

-- * dot11DBandCounters TABLE

-- ********************************************************************

dot11DBandCountersTable OBJECT-TYPE

SYNTAX SEQUENCE OF Dot11DBandCountersEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is a Table management object.

The dot11DBandCountersTable Table"

::= { dot11mac <ANA> }

dot11DBandCountersEntry OBJECT-TYPE

SYNTAX Dot11DBandCountersEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"This is an entry in the dot11DBandCountersTable Table.

ifIndex - Each IEEE 802.11 interface is represented by an

ifEntry.  Interface tables in this MIB module are indexed

by ifIndex."

INDEX { ifIndex }

::= { dot11DBandCountersTable 1 }

Dot11DBandCountersEntry ::=

SEQUENCE {

dot11RSNAStatsGCMPReplays			Unsigned32,

dot11RSNAStatsRobustMgmtGCMPReplays		Unsigned32

}

dot11RSNAStatsGCMPReplays OBJECT-TYPE

SYNTAX Unsigned32 (1..4294967295)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a status variable.

It is written by the SME or an external management entity.

Counter for the number of times an MPDU of type Data is discarded due to PN violation."

DEFVAL { 0 }

::= { dot11DBandCountersEntry 1 }

dot11RSNAStatsRobustMgmtGCMPReplays OBJECT-TYPE

SYNTAX Unsigned32 (1..4294967295)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a status variable.

It is written by the SME or an external management entity.

Counter for the number of times an MPDU of type Management is

discarded due to PN violation."

DEFVAL { 0 }

::= { dot11DBandCountersEntry 2 }

Editor: After the definition of the dot11PhyOperationComplianceGroup2, insert the dot11DBandComplianceGroup as defined below:

-- **********************************************************************

-- *   Groups - units of conformance

-- **********************************************************************

dot11DBandComplianceGroup OBJECT-GROUP

OBJECTS {	dot11MultibandSupportActivated, dot11DBandCapable,

dot11RelayEnabled,

dot11RSNAProtectedManagementFramesActivated

}

STATUS current

DESCRIPTION

"Attributes that configure the DBand Group for IEEE 802.11."

::== { dot11Groups <ANA> }

dot11DBandOperationsComplianceGroup OBJECT-GROUP

OBJECTS {	dot11MaxLostBeacons, dot11MinBIHeaderDuration, dot11PSRequestSuspensionInterval, dot11AssocRespConfirmTime,

dot11BroadcastSTAInfoDuration, dot11NbrOfChangeBeacons,

dot11ImplicitHandoverLostBeacons, dot11MinPPDuration, dot11SPIdleTimeout, dot11QABTimeout, dot11ClusterEnableTime, dot11PNWarningThreshold, dot11BeaconSPDuration, dot11PNExhaustionThreshold,

dot11MaxNumberOfClusteringMonitoringPeriods

}

STATUS current

DESCRIPTION

"Attributes that configure the DBand Operation for IEEE 802.11."

::== { dot11Groups <ANA> }

dot11DBandBeamformingComplianceGroup OBJECT-GROUP

OBJECTS {	dot11MaxBFTime, dot11BFTXSSTime, dot11MaximalSectorScan, dot11ABFTRSSSwitch, dot11RSSRetryLimit, dot11RSSBackoffdot11BFRetryLimit, dot11BFTXSSTime, dot11BeamLinkMaintenanceTime

}

STATUS current

DESCRIPTION

"Attributes that configure the DBand Beaforming functionality

for IEEE 802.11."

::== { dot11Groups <ANA> }

dot11DBandCountersComplianceGroup OBJECT-GROUP

OBJECTS {	dot11RSNAStatsGCMPReplays, dot11RSNAStatsRobustMgmtGCMPReplays

}

STATUS current

DESCRIPTION

"Attributes that are used as counters for a DBand capable Station for IEEE 802.11."

::== { dot11Groups <ANA> }

Editor: Modify the dot11Compliance module-compliance object as defined below.

-- **********************************************************************

-- *   Compliance Statements

-- **********************************************************************

dot11Compliance MODULE-COMPLIANCE

STATUS current

DESCRIPTION

"The compliance statement for SNMPv2 entities that implement the

IEEE 802.11 MIB."

MODULE -- this module

MANDATORY-GROUPS {

dot11SMTbase10,

dot11MACbase3, dot11CountersGroup3,

dot11SmtAuthenticationAlgorithms,

dot11ResourceTypeID, dot11PhyOperationComplianceGroup2,

dot11DBandComplianceGroup }

Editor: After the definition of the dot11TransmitBeamformingGroup, insert the dot11PhyDBandComplianceGroup as defined below:

GROUP dot11DBandComplianceGroup

DESCRIPTION

"Implementation of this group is required when the object

dot11PHYType has the value of DBand.

This group is mutually exclusive to the following groups:

dot11PhyIRComplianceGroup

dot11PhyFHSSComplianceGroup2

dot11PhyOFDMComplianceGroup3

dot11PhyHRDSSSComplianceGroup

dot11PhyERPComplianceGroup

dot11PhyHTComplianceGroup"

GROUP dot11DBandOperationsComplianceGroup

DESCRIPTION

"DBand Operations Compliance Group"

GROUP dot11DBandBeamformingComplianceGroup

DESCRIPTION

"DBand Beamforming Compliance Group"

GROUP dot11DBandCountersComplianceGroup

DESCRIPTION

"DBand Counters Compliance Group

The DBand Counters group is optional."

::= { dot11Compliances 1 }

Editor: Add the following text as the last line for the Description of the dot11PhyDSSSComplianceGroup, dot11PhyIRComplianceGroup, dot11PhyFHSSComplianceGroup2, dot11PhyOFDMComplianceGroup3, dot11PhyHRDSSSComplianceGroup, dot11PhyERPComplianceGroup, and dot11PhyHTComplianceGroup:

dot11DBandComplianceGroup (11ad)

Editor: Add the following text to the list of OPTIONAL-GROUPS in the dot11Compliance Statements.  Add this text after the dot11TransmitBeamformingGroup:

-- dot11DBandCountersComplianceGroup (11ad) }

Editor: After the definition of dot11RMCompliance insert the following text:

-- ********************************************************************

-- * Compliance Statements - DBand (11ad)

-- ********************************************************************

dot11DbandCompliance MODULE-COMPLIANCE (11ad)

STATUS current

DESCRIPTION

"The compliance statement for SNMPv2 entities that implement the

IEEE 802.11 MIB for DBand PHY."

MODULE -- this module

MANDATORY-GROUPS

{

dot11DBandComplianceGroup,

dot11DBandOperationsComplianceGroup,

dot11DBandBeamformingComplianceGroup

}

-- OPTIONAL-GROUPS { dot11DBandCountersComplianceGroup }

::= { dot11Compliances <ANA> }

-- **********************************************************************

-- * End of 802.11 MIB

-- **********************************************************************

END

# Text boxes

Abstract

This document is a contribution to address the open CIDs related to the TGad Management Information Base (MIB).  The following CIDs are addressed with this contribution:

- 2236					// rejected

- 2233					// agreed

- 2234					// agreed

- 2238					// agreed

- 2237 and 2058 (duplicate of 2237)	// agreed