## Slide 1: CVS Request Signaling
Authors:

## Slide 2: Abstract
  CVS in 802.11af Draft 1.0 is a unicast frame that is transmitted from the enabling AP/STA. Several conditions may cause an STA to miss the CVS such as degraded link quality, or wrong MCS used by the enabling STA. To address this scenario, it is useful to have a message for a STA to request a CVS from its enabling AP/STA. This message is sent by an STA that has not recieved the CVS , prior to the CVS interval expiring, to trigger a CVS from the enabling STA.

## Slide 3: Comment ID
  This contribution addresses CID 2
  Sections that are affected:
    6.3 MLME SAP Interface, add 6.3.af7
    8.5.8.1, add 8.5.8.af8
    10.af2.3: Add one paragraph
  Text in: 02-11-0263-01-00af-normative-text-for-cvs-report.doc

## Slide 4: Background
CVS in 802.11af Draft 1.0 is a unicast frame that is transmitted from the enabling AP/STA
Several conditions may cause an STA to miss the CVS
  Degraded link quality.
  Wrong MCS used by the enabling STA
Require a message for a STA to request a CVS from its enabling AP/STA.

## Slide 5: CVS Request IE.
STA sends a CVS request Action frame
  The Category field is set to the value for public
  The Action field is set to indicate a CVSR frame
A MIB dot11CVSResponseTimeout is defined
  This MIB is the time limit for the CVS to be sent from the enabling STA after receiving CVS request.
Once the enabling STA receives the CVS request, AP responds with a secure unicast CVS frame with in dot11CVSResponseTimeout .