## Slide 1: Categories of TGah Use Cases and Straw Polls
Date: 2011-03-08
Authors:

## Slide 2: Abstract
This submission is intended to illicit guidance on how to proceed with the TGah Use Case document. The submission uses categories, from submission 11/286, and fills them out with their original source material. At the end of this submission is a series of straw polls to indicate the level of interest for the use cases.

## Slide 3: Use Case Categories
Use Case 1 : Sensors and meters
Use Case 2 : Backhaul Sensor and meter data
Use Case 3 : Extended range hotspot and cellular offloading
Use Case 4 : Indoor/Outdoor streaming data
Use Case 5 : Electronic Menu & Coupon Distribution
Use Case 6 : Indoor & Outdoor Location
Use Case 7 : AP power saving

## Slide 4: Use Case 1 : Sensors and meters
1a: 11/17r5, slide 7 Smart Grid - Meter to Pole
1b: 11/17r5, slide 9 Intelligent Transport System (ITS)
1c: 11/253 Environmental/Agricultural Monitoring
1d: 11/260r1, slid 4 Industrial process sensors
1e: 11/17r5, slid 17 Healthcare
1f: 11/241r0, slide 3 Healthcare
1g: 11/241r0, slid 5 Home/Building Automation
1h: 11/242r0, slid 2 Home sensors

## Slide 5: Use Case 1a: Smart Grid – Meter to Pole
Wide Area
Gas Meter
Water Meter
Power Meter
Distributed Automation Device
Neighbor Area
Home Area
Wireless communication link
Wired communication link
Proposed infrastructure
Data Collector & Control
IEEE 802.11ah AP
Distributed Automation Device

## Slide 6: Use Case 1a: Smart Grid – Meter to Pole : Requirements
# | Category | Comment
1 | Location | Outdoor, indoor
2 | Environment type | Urban, sub-urban, rural
3 | STA/AP communication | 2-way (meter data & control)
4 | Data rate | 100 kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary
7 | Traffic type | Continuous/periodic/burst
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA (outdoor): 6000 [4], :AP: 1
11 | STA/AP category | STA: fixed (outdoor/indoor), AP: fixed (outdoor)
12 | STA/AP elevation | STA: 1m,..,10m [8], AP: 2m,..,30m [8]
13 | Actors | Meter device (power, gas, water), Distributed Automation Device, IEEE 802.11ah AP

## Slide 7: Use Case 1b: Intelligent Transport System (ITS)
500m
1000m
500m
1000m
0
ITS network A
ITS network B
Logistics
Toll bridge
Toll bridge
Toll bridge
Logistics
Logistics

## Slide 8: Use Case 1b : (ITS): Requirements
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | Urban, sub-urban, rural
3 | STA/AP communication | 2-way (toll data & control)
4 | Data rate | 100 kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Low/high velocity
7 | Traffic type | Burst
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 100, AP: 1
11 | STA/AP category | STA: mobile (outdoor), AP: fixed (outdoor)
12 | STA/AP elevation | STA: 1m,...,2m, AP: 2m,..,5m
13 | Actors | Toll bridge router, on-board unit

## Slide 9: Use Case 1c : Environmental/Agricultural Monitoring
Environmental & Agricultural Monitoring is one of S1G outdoor sensor network use cases
Monitoring data may include:
  Temperature, Humidity, Wind speed/direction
  Water Level
  Pollution information
  Soil Condition
  Plant/crop condition
  Animal/livestock condition and location
  Disaster detection info. (forest fire, flood, …)
  …

## Slide 10: Use Case 1c : Environ./Agri. Mon. : Requirements
Slide 10
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | Rural
3 | STA/AP communication | 2-way (monitoring data and control; mostly monitoring)
4 | Data rate | 100kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary/low
7 | Traffic type | Periodic, event-based
8 | Security requirement | Commercial-grade
9 | Reliability | Commercial-grade
10 | STA/AP capacity | STA: <300 , AP: 1
11 | STA/AP category | STA: fixed/mobile, AP: fixed
12 | STA/AP elevation | STA: 1-2m, AP: 5-10m
13 | Actors | Sensor

## Slide 11: Use Case 1d : Industrial Process Automation Attributes
Automation of industrial process like petroleum refinement, iron and steel, pharmacy, etc [1].
Reliability is the first place.
  Require low PER; <1%
Up to thousands of Input/Output points in the system.
Real-time communication.
  Latency: < hundreds of milliseconds
  Traffic: < ten’s of Kbps per I/O point
Relatively large outdoor area with large metal objects.
  e.g., 2km x 1km
  Mesh network is instrumental [2].

## Slide 12: Use Case 1d: Industrial Process Automation : Requirements
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | rural, rich specular metallic structures
3 | STA/AP communication | Send/receive (Monitoring, Control)
4 | Data rate | <1Mbps *1
5 | BER/PER requirement | PER<1%
6 | Mobility | Stationary, Low velocity
7 | Traffic type | Periodic (0.1s~100s), Burst
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 500 , AP: 10
11 | STA/AP category | STA: fixed, low velocity, AP: fixed
12 | STA/AP elevation | STA: 1-20m, AP: 1-20m
13 | STA-AP Distance | <2km
*1; 500I/O’s x 1packet/s x 64bytes/packet = 32kBytes/s = 256kbit/s => Expected PHY data rate: ~1Mbps

## Slide 13: Use Case 1e : Indoor Healthcare System
Monitor
Monitoring data
Slide 13

## Slide 14: Use Case 1e : Indoor Healthcare System: Requirements
Slide 14
# | Category | Comment
1 | Location | Indoor, outdoor
2 | Environment type | Home, hospital, clinic, elderly care
3 | STA/AP communication | 2-way (healthcare data & control)
4 | Data rate | 100Kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary/low
7 | Traffic type | Periodic/event-based
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA:50, AP: 1
11 | STA/AP category | STA: fixed/mobile (indoor), AP: fixed (indoor)
12 | STA/AP elevation | STA: 1,..,2m, AP: 2m,..,5m
13 | Actors | Heart rate monitor, blood pressure sensor, Electrocardiogram

## Slide 15: Use Case 1f : Healthcare/Fitness
Healthcare and fitness can be categorized as follows
  Hospital/clinic
    Blood pressure
    Heart rate
    Electrocardiogram (ECG)
  Elderly care/independent living
    Fall detection
    Pill bottle monitor
  Personal fitness
    Weight monitor
    Heart rate monitor

## Slide 16: Use Case 1f : Healthcare/Fitness : Requirements
 | Hospital/clinic | Elderly care | Personal fitness
Location | Indoor | Indoor | Indoor
Environment type | Building | Home | Building/home
STA/AP communication | Send (monitor) | Send/receive | Send (monitor)
Mobility | Stationary ~ low (walking ) | Stationary ~ low (walking) | Medium (running/biking)
Traffic type | Periodic: few KBytes every sub-seconds (e.g. blood pressure, ECG, …) Event-based: few 100 bytes per event | Periodic: few 100 bytes every few ~ 10s minutes Event-based: few 100 bytes per event | Periodic: few 100 bytes every minute Event-based: few 100 bytes per event
Security requirement | Higher than Commercial-grade | Commercial-grade | Commercial-grade
STA/AP capacity | STA:<50, AP:1 (multi-story medical center can have higher density) | STA:<50, AP:1 (independent living model can have higher density) | STA: <50, AP:1 (multi-story fitness center can have higher density)
STA/AP category | STA: fixed/mobile, AP: fixed | STA: fixed/mobile, AP: fixed | STA: fixed/mobile, AP: fixed

## Slide 17: Use Case 1g : Home/Building Automation/Control
Light control
Presence detection
Temperature/humidity monitor
HVAC system monitor/control
Consumer electronics/appliances monitor/control
Security/safety
  Door/windows lock/unlock
  Intrusion detection
  Smoke/gas detection

## Slide 18: Use Case 1g : Home/Building Automation/Control : Requirements
Category | Comment
Location | Indoor
Environment type | Home/building
STA/AP communication | Send/receive (monitor/control)
Mobility | Stationary
Traffic type | Periodic: few 100 bytes every few ~ 10s minutes Event-based: few 100 bytes per event
Security requirement | Commercial-grade
STA/AP capacity | STA:50~100, AP:1 (multi-story building can have higher density)
STA/AP category | STA: fixed, AP: fixed

## Slide 19: Use Case 1h : Temperature Sensor Network
19
Traffic Conditions:
Potential interference from overlapping networks using the same frequency bands.
Potential range extension through the use of one repeater between far away sensors and the access points
Use Case:
Sensors are deployed in the home in appropriate locations. A number of sensors likely to be battery operated
Home automation application periodically probes sensors to report temperatures; or sensors pro-actively report changes in temperature beyond a certain threshold; or sensors proactively report temperature readings a scheduled intervals
Pre-Conditions:
User has installed a series of 5 – 20 temperature sensors throughout the home. Most of the sensors are battery operated.
Application:
A home automation system operates its heating / cooling / ventilation system based on temperature readings received from the sensors. The temperature sensors provide updated readings either on a periodic basis, triggered by changes in temperature, or upon request by the home automation system or the end user. Temperature sensor readings are accessible by an authorized user, while being away from home.
The payload data being transmitted is around 50 byte or less no stringent latency or jitter requirements.
Environment:
Typical coverage of a sensor network is an entire home, the maximum number of sensors typically in the 10 – 50 range.
Doc.: IEEE 802.11-11/0301r0

## Slide 20: Use Case 2 : Backhaul Sensor/Meter data
11/14r2, slide 5 Backhaul aggregation of sensors
11/260r1, slide 4 Backhaul aggregation of industrial sensors

## Slide 21: Use Case 2a : Backhaul link for 15.4g
IEEE802.15.4g provides a link for lower traffic leaf sensor with battery power constraints.
IEEE802.11ah is going to provide an appropriate feature
as a backhaul link to accommodate;
  the aggregated traffic of leaf sensors,
  and stream of camera images or surveillance videos.
IEEE802.11ah hopefully performs without degradation of throughput and reliability, even if co-existing with 15.4g.
I&I applications do expect the well managed co-existence.

## Slide 22: Use Case 2b : Backhaul for industrial process automation
1st use case is wireless remote I/O.
2nd use case is wireless backhaul network for wireless sensor / actor network (WSAN).
Wireless Sensor/Actor Network using IEEE802.15.4g PHY
*Low data rate; <200kbps.
*Low power; battery operation for >5years.
15.4g-11ah
Router
11ah AP
2nd use case
Backhaul Network
1st use case:
Wireless Remote I/O
*Aggregate many I/O points
15.4g-11ah
Router
11ah AP
Backbone network
Control Stations
*Execute Feedback Control
Analog I/O, Digital I/O
Analog I/O, Digital I/O

## Slide 23: Use Case 3 : Extended range hotspot and cellular offloading
11/243r0 Outdoor extended range hotspot
11/244r1 Outdoor Wi-Fi for cellular traffic offloading

## Slide 24: Use Case 3a : Extended Range Hotspot
WiFi is being increasingly used for hotzone/hotspot applications around the world
These application can benefit from extended range enabled by use of lower frequency bands
Typical scenarios may include:
  Extended home coverage
  Campus wide coverage
  Shopping malls

## Slide 25: Use Case 3a : Outdoor Extended Range Hotspot : Requirement
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | Urban, Sub-urban
3 | STA/AP communication | Send/receive (monitor & feedback)
4 | Data rate | Up to 10 Mbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Pedestrian
7 | Traffic type | Burst/permanent
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 50, AP: 1
11 | STA/AP category | STA: fixed, AP: fixed
12 | STA/AP elevation | STA: 1-2m, AP: 5-10m

## Slide 26: Use Case 3b : Outdoor Wi-Fi for cellular traffic offloading Motivation
Traffic offloading by 802.11 WLAN is considered as good solution of mobile traffic explosion
However, current 802.11(a, g, n, ac) WLAN have short coverage and assume indoor environment
TGah has large coverage (~1km), so it can be used for mobile traffic offloading in outdoor environment

## Slide 27: Use Case 3b : Outdoor Wi-Fi : Requirements
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | Urban, sub-urban
3 | STA/AP communication | Send/receive (Web browsing, multimedia)
4 | Data rate | Up to 20 Mbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Pedestrian
7 | Traffic type | Burst
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 50 , AP: 1
11 | STA/AP category | STA: nomadic, AP: fixed
12 | STA/AP elevation | STA: 1-2m, AP: 5-10m
13 | Actors | Cellular device, portable smart device

## Slide 28: Use Case 4 : Indoor/Outdoor streaming data
11/17r5, slide 10/11 Outdoor surveillance
11/17r5, slide 12/13 Indoor surveillance
11/17r5, slide 14/15 Home entertainment

## Slide 29: Use Case 4a : Outdoor Surveillance
500m
1000m
500m
1000m
0
Surveillance network A
Surveillance network B
Surveillance
Surveillance
Call 110
Call 110
Surveillance
Call 110

## Slide 30: Use Case 4a : Outdoor Surveillance : Requirements
# | Category | Comment
1 | Location | Outdoor
2 | Environment type | Urban, Sub-urban, rural
3 | STA/AP communication | 2-way (audio/video data & control)
4 | Data rate | 10 Mbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary, low/high velocity
7 | Traffic type | Burst/permanent
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 50, AP: 1
11 | STA/AP category | STA: fixed/mobile (outdoor), AP: fixed (outdoor)
12 | STA/AP elevation | STA: 1m,..,2m, AP: 2m,..,5m
13 | Actors | Surveillance camera, microphone, sensor (light, temperature, movement)

## Slide 31: Use Case 4b : Indoor Surveillance
Surveillance network B
Surveillance network A
Surveillance
Surveillance
Surveillance
Watch dog
Watch dog

## Slide 32: Use Case 4b : Indoor Surveillance : Requirements
# | Category | Comment
1 | Location | Indoor
2 | Environment type | Office, lab, hall, arena
3 | STA/AP communication | 2-way (audio/video data & control)
4 | Data rate | 20 Mbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary
7 | Traffic type | Burst/permanent
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 20, AP: 1
11 | STA/AP category | STA: fixed (indoor), AP: fixed (indoor)
12 | STA/AP elevation | STA: -1m (basement),..,2m, AP: 1m,…,5m
13 | Actors | Surveillance camera, microphone, sensor (light, temperature, movement)

## Slide 33: Use Case 4c : Indoor Media Streaming for Home Entertainment
Bedroom
Hallway
Living room
Study
A/V streaming through a Sub 1GHz link (5/10/20MHz)
A/V player
MP3 player
Slide 33

## Slide 34: Use Case 4c : Indoor Home Entertainment System: Requirements
# | Category | Comment
1 | Location | Indoor
2 | Environment type | Home
3 | STA/AP communication | 2-way (audio/video data & control)
4 | Data rate | 20 Mbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary/low velocity
7 | Traffic type | Burst/permanent
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 20, AP: 1
11 | STA/AP category | STA: mobile/fixed (indoor), AP: fixed (indoor)
12 | STA/AP elevation | STA: -1m (basement),..,2m, AP: 1m,..,2m
13 | Actors | Remote control, TV, MP3player, home gateway, AV player, headphones

## Slide 35: Use Case 5 : Electronic Menu & Coupon Distribution
11/268r0, slide 5/6 Electronic Menu & Coupon Distribution

## Slide 36: Use Case 5a : Scenario Description
Electronic Menu
  When you are driving pass by a restaurant, electronic menu is sent to your iPad (802.11ah STA), and you can check for more detailed info of the menu, and make a reservation
  Once you come for your dinner, you can just order with your iPad
Electronic Coupon distribution
  When you pass by a shopping Mall, the electronic coupon is sent to your iPad (802.11ah STA)

## Slide 37: Use Case 5a: Electronic Menu & Coupon Distribution : Requirements
# | Category | Comment
1 | Location | Outdoor, indoor
2 | Environment type | Urban
3 | STA/AP communication | 2-way (Distribution & Query, Order)
4 | Data rate | 100 kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary/low
7 | Traffic type | Burst/Continuous
8 | Security requirement | High
9 | Reliability | High
10 | STA/AP capacity | STA: 50 , AP: 1
11 | STA/AP category | STA: Mobile, AP: fixed
12 | STA/AP elevation | STA: 1m,..,2m, AP: 2m,..,10m
13 | Actors | Mobile Device, AP

## Slide 38: Use Case 6 : Indoor & Outdoor location
11/268r0, slide 8/9 Indoor & Outdoor location

## Slide 39: Use Case 6a : Scenario Description
Location in Shopping Mall
  When you enter a big shopping mall, a digital map of the shops will be downloaded to your iPad (802.11ah STA), and the APs in the shopping mall will help to position you
  If you want to go directly to some specific shop, you will find the route on your iPad with location from APs
  Similar scenario can be found in Theme Park (Try to find some specific attraction)
Find your car in Public Parking
  When you come back to get your car after shopping, it is possible that you have forget where your car is. You check from your iPad (802.11ah STA) to get locationfrom AP, the AP will try to position your car (with a 802.11ah STA), and display the parking lot and guide you to your car

## Slide 40: Use Case 6a : Indoor and Outdoor Location: Requirements
# | Category | Comment
1 | Location | Indoor/Outdoor(Mall, Parking, Theme Park)
2 | Environment type | Urban
3 | STA/AP communication | 2-way (Electronic Map download, Position Query)
4 | Data rate | 100 kbps
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary/low
7 | Traffic type | Burst/Continuous
8 | Security requirement | Medium
9 | Reliability | High
10 | STA/AP capacity | STA: 50 , AP: N(>3)
11 | STA/AP category | STA: Mobile, AP: fixed
12 | STA/AP elevation | STA: 1m,..,2m, AP: 2m,..,10m
13 | Actors | Mobile Device, AP

## Slide 41: Use Case 7 : AP power saving
11/273r0 AP power saving

## Slide 42: Use Case 7a : AP Power Saving in Smart Grid
11ah STA(*) Meter/sensor
11ah AP(**)
IEEE 802.11ah network
Request:
AP sleep
Response
Slide 42
(*) = IEEE 802.11ah STA with proposed AP power saving support
(**) = IEEE 802.11ah AP with proposed AP power saving support
sleep
t
active
t
11ah STAs
11ah AP
active
sleep
active
Transmission of meter data
Idle period, e.g.,
night time
AP sleep state
Sleep duration
day
day
night
night
day
day
day
night
night
day

## Slide 43: Use Case 7a : Scenario Description: AP Power Saving in Smart Grid
During communication idle periods in Smart Grid
  11ah AP: Request
    AP wants to change from active to sleep mode
  11ah STA: Response
    STA state support: AP active/AP light sleep/AP deep sleep
    STAs high priority messages supported during light sleep mode
Proposed 11ah AP modes (similar to IEEE 802.11s) [6]
  active mode: A link specific power mode in which the AP operates in the Awake state.
  light sleep mode: A link specific power mode in which the AP operates in the Awake or the Doze state and where the AP is expected to receive frames from the STA.
  deep sleep mode: A link specific power mode in which the AP operates in the Doze state and where the AP is not expected to receive frames from the STA.
E.g., utilizing IEEE 802.11v features [7]
Slide 43

## Slide 44: Straw Poll 1
  TGah shall adopt use case category 1 Sensors and meters, in it’s Use Case document.

## Slide 45: Straw Poll 2
  TGah shall adopt use case category 2 Backhaul Sensor and meter data, in it’s Use Case document.

## Slide 46: Straw Poll 3
  TGah shall adopt use case category 3 Extended range hotspot and cellular offloading, in it’s Use Case document.

## Slide 47: Straw Poll 4
  TGah shall adopt use case category 4 Indoor/Outdoor streaming data, in it’s Use Case document.

## Slide 48: Straw Poll 5
  TGah shall adopt use case category 5 Electric Menu & Coupon Distribution, in it’s Use Case document.

## Slide 49: Straw Poll 6
  TGah shall adopt use case category 6 Indoor and Outdoor Location, in it’s Use Case document.

## Slide 50: Straw Poll 7
  TGah shall adopt use case category 7 AP power saving, in it’s Use Case document.

## Slide 51: References
https://mentor.ieee.org/802.11/dcn/11/11-11-0274-02-00ah-tgah-list-of-use-case-submissions.doc
https://mentor.ieee.org/802.11/dcn/11/11-11-0017-05-00ah-proposed-ieee-802-11ah-use-cases.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0241-00-00ah-additional-indoor-use-cases-for-802-11ah.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0014-02-00ah-supplemental-use-case-in-industrial-infrastructural-apps.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0242-00-00ah-tgah-use-case-temperature-sensors.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0243-01-00ah-tgah-additional-outdoor-use-case.ppt

## Slide 52: References cont.
https://mentor.ieee.org/802.11/dcn/11/11-11-0244-01-00ah-tgah-use-case-outdoor-wi-fi-for-cellular-traffic-offloading.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0253-00-00ah-tgah-use-case-outdoor-environment-monitoring.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0260-01-00ah-tgah-use-case-industrial-process-automation.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0268-00-00ah-additional-ieee-802-11ah-use-cases.ppt
https://mentor.ieee.org/802.11/dcn/11/11-11-0273-00-00ah-tgah-use-case-ap-power-saving-in-smart-grid.ppt