IEEE P802.11
Wireless LANs

| Comment Resolution for Transmit Power Limit for Wider Bandwidths |
| --- |
| Date: 2011-03-21 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Daewon Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-7897 | daewon.lee@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1497 | yongho.seok@lge.com |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | illsoo.sohn@lge.com |
| Eunsun Kim | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1860 | esun.kim@lge.com |
| Youhan Kim | Atheros | 1700 Technology Drive, San Jose, CA 95110 | +1-408-830-5835 | youhan.kim@atheros.com |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | +1-408-543-3370 | mfischer@broadcom.com |
| Jae Seung Lee | ETRI | 161 Gajeong-dong, Yuseong-gu, Daejeon, Korea | +82 42 860 1326 | jasonlee@etri.re.kr |
| Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR, 97124, USA | +1 503 724 0893 | robert.j.stacey@intel.com |
| Simone Merlin | Qualcomm | 5665 Morehouse Dr., San Diego, CA 92121 |  | smerlin@qualcomm.com |
| Raja Banerjea | Marvell | 5488 Marvell Lane, Santa Clara CA, 95054 | 1-408-222-3713 | rajab@marvell.com |
| Chunhui (Allan) Zhu | Samsung Electronics | 75 W. Plumeria Dr., San Jose, CA 95131 | +1-408-544-5667 | c.zhu@samsung.com |
| Bo Sun | ZTE Corporation | ZTE Building, #10 South Tangyan Rd., Xi'an, China | 86 29 88724130 | sun.bo1@zte.com.cn |
| Liwen Chu | ST-Ericsson | 2525 Augustine Drive, Santa Clara CA 95054 | +1.408.467.8436 | Liwen.Chu@st.com |
| Edward Au | Huawei Technologies | Huawei Industrial Base, Bantian Longgang, Shenzhen 518129, China | +1 773 782 6875 | edwardau@huawei.com |
| Vish Ponnampalam | Mediatek | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | vish.ponnampalam@mediatek.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGac Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGac Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGac Editor:  Editing instructions preceded by “TGac Editor” are instructions to the TGac editor to modify existing material in the TGac draft.   As a result of adopting the changes, the TGac editor will execute the instructions rather than copy them to the TGac Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

| CID | Commenter Name | Subclause | Page | Line | Comment Type | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 559 | Kim, EunSun | 7.3.2 | 28 | 44 | TR | For 160MHz and 80+80MHz transmission, the wide BW transmission can span across different operating classes (power regimes). The maximum transmit power constraints for transmit bands can be different by regulations. Specifications for the maximum transmit power rules and the method to anounce this limits are required. | Clarify the maximum transmit power limits for 160MHz and 80+80MHz transmission cases. Also, specify a method to announce this information. |
| 1030 | Seok, Yongho | 7.3.2 | 28 | 44 | TR | specification regarding Transmit Power control for wider bandwidth such as 80MHz, 160Mhz, and 80+80Mhz is missing. | as per comment |
| 1031 | Seok, Yongho | 7.3.2 | 28 | 44 | TR | specification regarding channel swithcing for wider bandwidth (80MHz, 160Mhz, and 80+80Mhz) BSS is missing | as per comment |
| 1032 | Seok, Yongho | 7.3.2 | 28 | 44 | TR | specification regarding power constraint element for 160Mhz and 80+80Mhz transmission where the wider BW transmission can span across different operating classes (power regimes) | as per comment |
| 1453 | Lee, Daewon | 7.3.2 | 28 | 44 | TR | missing specification for 80/160MHz Transmit Power control | add TPC for 80/160MHz |
| 1454 | Lee, Daewon | 7.3.2 | 28 | 44 | TR | missing specification for 80/160MHz channel switching | add channel switch for 80/160MHz |
| 1455 | Lee, Daewon | 7.3.2 | 28 | 44 | TR | missing specification for 80/160MHz power constraint element | add power constraint for 80/160MHz |
| 1525 | SOHN, ILLSOO | 7.3.2 | 28 | 44 | TR | Maximum power constraints for 160MHz/80+80MHz are unclear since BW lies across different power regimes. | Clarify how to apply maximum power limit for 160MHz/80+80MHz cases and signaling method. |

Discussion:

With the support of very wide bandwidths in VHT, the transmission signal may be subject to various transmit power constraint given by the regulatory body. For example in US the transmit power for UNII-1 and UNII-2 are different, where the 160MHz transmission signal can be transmitted across these bands.

Figure 1. Example of transmission in different transmit power regulatory domains

There are two components to limiting transmission power for 802.11, the first is the transmit power information given by the Country information element, and the second is power constraint element which give further restrictions on top of the maximum transmit power specified by the Country IE.

Since the VHT transmission can be also transmitted in non-contiguous manner and also support dynamic switching between 20, 40, 80, 160/80+80 MHz bandwidths, we must be able to indicate non-contiguous bands which are backward compatible. Figure 1 shows some examples of how the transmit power may change for different transmission bandwidths.

The Country IE description as it stands is flexible enough to describe contiguous transmit power limits, even though the channel bandwidth may be 80 or even 160MHz. But is not able to describe non-contiguous transmit power limits. For this we propose to use four Channel-power triplets, which indicate the center frequency of the each of the segments in 80+80 MHz transmission bands, and the transmit power limit.

Table 1. Example of Country IE extension to support non-contiguous 80+80 MHz bands

| Name | 1st octet | 2nd octet | 3rd octet |  |
| --- | --- | --- | --- | --- |
| Operating triplet | Operating extension identifier (201) | Operating class | Coverage class | Contiguous band transmit power limit indication |
| Subband triplet | First channel number (1-200) | Number of channels | Maximum transmit power level |  |
| Channel-power triplet | Channel-power identifier (202-255) | Operating class | Coverage class | Non-Contiguous band transmit power limit indication |
| Channel-power triplet | Channel-power identifier (202-255) | Channel number | Maximum transmit power level |  |
| Channel-power triplet | Channel-power identifier (202-255) | Operating class | Coverage class |  |
| Channel-power triplet | Channel-power identifier (202-255) | Channel number | Maximum transmit power level |  |

To show an example out what values would be filled in we show an example in Figure 2 and Table 2.

Figure 2. Example of non-contiguous transmission signal with primary channel at channel 100

Table 2. Example of non-contiguous transmission signal with primary channel at channel 100

| Name | 1st octet | 2nd octet | 3rd octet |
| --- | --- | --- | --- |
| Operating triplet | Operating extension identifier (201) | Operating class (ANA1) | Coverage class |
| Subband triplet | First channel number (100) | Number of channels (4) | Maximum transmit power level (200mW) |
| Channel-power triplet | Channel-power identifier (202) | Operating class (ANA1) | Coverage class |
| Channel-power triplet | Channel-power identifier (202) | Channel number (42) | Maximum transmit power level (80mW) |
| Channel-power triplet | Channel-power identifier (202) | Operating class (ANA2) | Coverage class |
| Channel-power triplet | Channel-power identifier (202) | Channel number (106) | Maximum transmit power level (80mW) |

The power constraint element contains the local maximum transmit power in the current channel. This element can be used in both contiguous and non-contiguous transmission signals, but if the wide band signal is being transmitting in multiple regulatory transmit power limit domains, then we may need to further indicate how differentiate the transmit power limit for smaller bandwidth and large bandwidths. For this we propose to add one element which extends the power constraint element. We propose to extend it by also including bandwidth information so that VHT devices can understand for which bandwidths the local power constraint applies. Since if the operating channel bandwidth is either 20 or 40 MHz, there is no need for this extended power constraint element, we propose only to signal the extended power constraint element if the AP is operating in channel widths lager than 80MHz or above.

Table 3. Power Constraint element

| Element ID | Length | Local Power Constraint |
| --- | --- | --- |
| Octets: 1 | 1 | 1 |

Table 4. Extended Power Constraint element

|  |  | The two fields ‘STA Channel Width’ and ‘Local Power Constraint’ are repeated as needed, as determined by the length field. |
| --- | --- | --- |
| Element ID | Length | STA Channel Width | Local Power Constraint |
| Octets: 1 | 1 | 1 | 1 |

It may be possible to extend the Channel Power Management element used in 11af to inform the transmit power limits but the said information element provides various TV White Space specific functionalities. The functionalities included in the CPM element are signaling of changes of channel availability, signaling of Maximum Transmit Power switching from the regulatory database, and signaling of Channel (and Power) switching. The support of such element with all the functionalities therein in the 5GHz is rather not clear and may cause additional implementation needed for VHT 5GHz only support devices.

To keep the channel switch mechanism simple and considering the VHT is only supported in the 5GHz, we propose to extend the existing transmit power and power capabilities information element to support wider bandwidths.

Proposed Resolution:

Agree in principle to finalize the TBD fields as described in Draft P802.11ac_D0.1 comments 559, 1030, 1031, 1032, 1453, 1454, 1455, and 1525. Acknowledge need for transmit power limit and related functionality for wider bandwidths as described in CID 1378 but reject CID 1378 due to discussion point discussed above.  Also agree to following editing instructions below.

## Editing instructions:

7.2.3.1 Beacon frame format

TGac editor: Insert the Extended Power Constraint element in Table 7-8 Beacon frame body after order 41 and before order Last:

Table 7-8—Beacon frame body

| Order | Information | Notes |
| --- | --- | --- |
| <ANA> | Extended Power Constraint element | The Extended Power Constraint element is present if dot11VHTOptionImplemented attribute is true and STA Channel subfield of the VHT Operation Information field is set to 80MHz or above, and dot11SpectrumManagementRequired is true. |

7.2.3.9 Probe Response frame format

TGac editor: Insert the Extended Power Constraint element in Table 7-15 Probe Response frame body after order 39 and before order Last-l:

Table 7-15—Probe Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| <ANA> | Extended Power Constraint element | The Extended Power Constraint element is present if dot11VHTOptionImplemented attribute is true and STA Channel subfield of the VHT Operation Information field is set to 80MHz or above, and dot11SpectrumManagementRequired is true. |

7.3.2 Information elements

TGac editor: Insert the following row in table 8-50, and renumber the reserved values accordingly:

Table 7-16—Element IDs

| Element | Element ID | Length (in octets) | Extensible |
| --- | --- | --- | --- |
| Extended Power Constraint | < ANA > | 4 - 256 | Yes |

7.3.2.9 Country element

TGac editor: Replace the Figure 7-46 Country element format in section 7.3.2.9 Country element with following figure:

|  | Element ID | Length | Country String | Country Field Triplets | Pad (if needed) |
| --- | --- | --- | --- | --- | --- |
| Octets: | 1 | 1 | 3 | variable | 0 or 1 |

Figure 7-46—Country element format

TGac editor: Change second paragraph of 7.3.2.9 as shown:

The element ID for this element is set to the value for Country, specified in Table 7-26 (Element IDs). The length of the element is variable, as the element may contain more than one triplet comprising the First Channel Number, Number of Channels, and Maximum Transmit Power Level fields and referred to as subband triplets. Alternatively, where dot11OperatingClassesRequired is true and the first octet of a Country Field Triplet First Channel Number/Operating Extension Identifier octet has a positive integer value of 201 or greater, then that triplet comprises the Operating Extension Identifier, Operating Class, and Coverage Class fields. Together they are referred to as an operating triplet. Alternatively, where dot11OperatingClassesRequired is true and the first octet of a Country field triplet has a positive integer value greater than 201, then that triplet comprises the Non-contiguous Extension Identifier, Operating Class/Channel Number, and Coverage Class/Maximum Transmit Power Level fields. Together they are referred to as a channel-power triplet. The minimum length of the element is 8 octets. The format of the Country field triplets is shown in Table 7-46a. Within the Country Field triplets field, Channel Power Triplets shall be positioned after the Subband Triplets and the Operating Triplets if Subband Triplets and Operating Triplets exist within the Country field triplet field.

Table 7-46a—Country field triplets

| Name | 1st octet | 2nd octet | 3rd octet |
| --- | --- | --- | --- |
| Channel Power Triplet | Non-contiguous Extension Identifier (202-255) | Operating Class/Channel Number | Coverage Class/Maximum Transmit Power Level |
| Operating Triplet | Operating Extension Identifier (201) | Operating Class | Coverage Class |
| Subband Triplet | First Channel Number (1-200) | Number of Channels | Maximum Transmit Power Level |

TGac editor: Change first sentence of fourth paragraph of 7.3.2.9 as shown:

The First Channel Number/Operating Extension Identifier/Non-contiguous Extension Identifier field is 1 octet in length.

TGac editor: Insert the following paragraph before last paragraph of 7.3.2.9 as shown:

The Non-contiguous Extension Identifier field has a positive value greater than 201. If the two consecutive Non-contiguous Extension Identifier octet out of the two triplets has a same value, then the first triplet comprises the Non-contiguous Extension Identifier, Operating Class, and Coverage Class fields, and the second triplet comprises the Non-contiguous Extension Identifier, Channel Number, and Maximum Transmit Power Level. Together they are referred to as a Channel Power triplet. The Operating Class in the Channel Power triplet indicates the operating class of the 80MHz segment in the non-contiguous 160MHz channel. The Channel Number in the Channel Power triplet indicates the center frequency of the 80MHz segment in the non-contiguous 160MHz channel. The non-contiguous 160MHz channel transmit power level is indicated by two sets of Channel Power triplet, which comprises of the four consecutive triplets all with the same Non-contiguous Extension Identifier. The two Maximum Transmit Power Level in the two sets of Channel Power triplet shall be identical, where a Maximum Transmit Power Level indicates the Maximum Transmit Power Level of the entire non-contiguous 160MHz channel.

TGac editor: Change the following section 7.3.2.15 Power Constraint element as follows:

7.3.2.15 Power Constraint element

The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current primary 20MHz and primary 40MHz channel. The format of the Power Constraint element is shown in Figure 7-52 (Power Constraint element format).

TGac editor: Insert the following section 7.3.2.15a after section 7.3.2.15 Power Constraint element:

7.3.2.15a Extended Power Constraint element

The Extended Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in each of the operating channel bandwidths. The format of the Power Constraint element is shown in Figure 7-52a (Extended Power Constraint element format).

|  |  |  | These two fields are repeated, as determined by the Length field |
| --- | --- | --- | --- |
|  | Element ID | Length | STA Channel Width | Local Power Constraint |
| Octets: | 1 | 1 | 1 | 1 |

Figure 7-52a—Extended Power Constraint element format

The STA Channel Width field is coded with the identical coding and meaning as STA Channel Width subfield of the VHT operational Information element fields in section 7.3.2.62 (VHT Operation element). The unspecified values in the STA Channel Width field are reserved.

The Local Power Constraint field is coded as an unsigned integer in units of decibels. The local maximum transmit power for a channel is thus defined as the maximum transmit power level specified for the channel in the Country element minus the local power constraint specified for the channel (from the MIB) in the Power Constraint element.

The Extended Power Constraint element is included in Beacon frames, as described in 7.2.3.1 (Beacon frame format), and Probe Response frames, as described in 7.2.3.9 (Probe Response frame format). The use of Extended Power Constraint elements is described in 11.8.2 (Specification of regulatory and local maximum transmit power levels).

TGac editor: Change the following section 11.8.2 as follows:

11.8.2. Specification of regulatory and local maximum transmit power levels

A STA shall determine a regulatory maximum transmit power for the current channel. The STA shall use the minimum of the following:

— Any regulatory maximum transmit power received in a Country element from the AP in its BSS or another STA in its IBSS and

— Any regulatory maximum transmit power for the channel in the current regulatory domain known by the STA from other sources.

A STA shall determine a local maximum transmit power for the current channel by selecting the minimum of the following:

— Any local maximum transmit power received in the combination of a Country element and a Power Constraint element and an Extended Power Constraint element from the AP in its BSS or another STA in its IBSS and

— Any local maximum transmit power for the channel regulatory domain known by the STA from other sources.

The Local Power Constraint field of any transmitted Power Constraint element and Extended Power Constraint element shall be set to a value that allows the mitigation requirements to be satisfied in the current channel.

Any calculation of the local maximum transmit power for the channel shall ensure the mitigation requirements for the channel in the current regulatory domain can be satisfied. The conservative approach is to set the local maximum transmit power level equal to the regulatory maximum transmit power level minus the mitigation requirement. However, it may be possible to satisfy the mitigation requirement using a higher local maximum transmit power level. A lower local maximum transmit power level may be used for other purposes (e.g., range control, reduction of interference).

The regulatory and local maximum transmit powers may change in a STA during the life of a BSS. However, network stability should be considered when deciding how often or by how much these maximums are changed. The regulatory and local maximum transmit powers shall not change during the life of an IBSS.

An AP in a BSS and a STA in an IBSS shall advertise the regulatory maximum transmit power for that STA’s operating channel in Beacon frames and Probe Response frames using a Country element. An AP in a BSS and a STA in an IBSS shall advertise the local maximum transmit power for that STA’s operating channel in Beacon frames and Probe Response frames using the combination of a Country element and a Power Constraint element and an Extended Power Constraint element.

Where TPC is being used for radio measurement without spectrum management, the inclusion of a Power Constraint element and an Extended Power Constraint element in Beacon and Probe Response frames shall be optional.

# Text boxes

Abstract

Submission for Draft P802.11ac_D0.1 comment resolution. The document addresses various comments related to transmit power limit configuration for wider bandwidth such as 80MHz, 160MHz, and non-contiguous 80+80Mhz channel bandwidths.

Submission addresses Draft P802.11ac_D0.1 comments 559, 1030, 1031, 1032, 1453, 1454, 1455, and 1525.