## Slide 1: Usage Cases for 802.11ah
Date: 2011-03-14
Authors:

## Slide 2: Summary
There are more than 10 usages cases for 802.11ah and the number is still growing
  Outdoor applications out number Indoor applications
The breadth of the usage cases present challenges for protocol design
  The outdoor application has distance up to 100 times longer than that of indoor
  The data rate for video streaming is more than a 100 times higher than metering application
  The power requirement is different for mobile/handheld and AC powered STA.
  The number of STAs is ranging from 10’s to 1000’s
What can we do to address the diverse requirements from the potpourri of usage cases?
  11/0286r0 “Categories of TGah Use Cases” and 11/0301 “Categories of TGah Use Cases and Straw Polls” are seeking consensus on the same issue

## Slide 3: Summary – Proposed Applications
Outdoor
  Smart Grid - 100 kbps
  Intelligent Transport System (ITS) - 100 kbps
  Outdoor Surveillance System - 10 Mbps
  Outdoor Wi-Fi - 20 Mbps
  Outdoor Extended Range Hotspot - Up to 10 Mbps
  Industrial Process Automation - <1Mbps *1
  Environmental / Agricultural Monitoring - 100kbps
Indoor
  Indoor Healthcare System - 100Kbps
  Indoor Surveillance System - 20 Mbps
  Home Entertainment System - 20 Mbps

## Slide 4: Outdoor or Indoor – Scope Definition
The scope of the PAR is for fixed, outdoor, point to multi point applications
  5.2 Scope of Proposed Standard:
    This amendment defines …
    This amendment also adds support for:
      transmission range up to 1 km
      data rates > 100 kbit/s
    while maintaining the 802.11 WLAN user experience for fixed, outdoor, point to multi point applications.
PAR only mentioned indoor as a possibility
  17.5.1 Broad Market Potential
    a) Broad sets of applicability. There are a number of license-exempt bands below 1 GHz suitable for indoor/outdoor applications. For instance, the 902-928 MHz ISM band is available in the U.S.
Shall PAR be updated or only consider usage cases for outdoor applications?

## Slide 5: Outdoor and Indoor – Requirements
The channel model for outdoor applications is different from indoor applications
The severity of OBSS interferences is higher for outdoor application
  Does a better OBSS mitigation scheme is required for the outdoor application?
  Certification for outdoor application must be different form the indoor application
Target application date rate is either below 100Kb or above 10Mb
  Mixing high data rate with low data applications that have very different traffic patterns will compromise system performance

## Slide 6: Outdoor and Indoor – Requirements
Number of STAs per AP has major affect on at least the following procedures
  the association process
  The security process (I mean setup, tear down, key exchange and update)
  The channel access
  There are similar technologies address high rate indoor applications.
    What ah can provide while the others can’t
  Should we burden a spec with such diverse requirements?
    The complexity will lengthen the schedule for the development of the specification

## Slide 7: The Reduced Requirements for 11ah Target Applications
  Longer distance
    The range is greater than 100m and is up to 1 Km
  Lower data rate application
    Per STA data rate is around 100K per duty cycle.
    The channel bandwidth can be higher, up to 20Mb
      Reducing power consumption of STA by reduce the transmission time
      Increase the number of STAs supported by an AP
  Fixed location STA (or very low mobility)
    Maximum tolerable Doppler should be < 50 Hz