## Slide 1: Pedestrian Model
Date: 2011-03-14
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com

## Slide 2: Abstract
This presentation shows a pedestrian model in crowded area for TGai.

## Slide 3: General Model
Transmission range of AP: r [m]
Area Occupied by 1 person
a*b [m2]
All persons move at v[m/s] to the same direction
a[m]
b[m]

## Slide 4: Arrival/Departure Rate
Arrival/Departure Rate:
  Arrival/Departure rate depends on the area that crosses the border of cell at a unit time. So,
  Arrival/Departure rate = 2rv/ab [persons/s]

## Slide 5: Practical Model
Hitoshi Morioka, ROOT INC.
Slide 5
But usualy the corridor is narrower than the cell diameter.
Arrival/Departure Rate: wv/ab
Corridor Width: w [m]

## Slide 6: Walking Speed References
Survey by Prof. Richard Wiseman (Univ. of Hertfordshire) and British Council (2007)
  Fastest City (Singapore): 10.55s/20m = 113.7m/min = 1.90m/s
Official walking speed used in real estate ads. in Japan
  80m/min = 1.33m/s
Escalator
  30m/min = 0.5m/s

## Slide 7: Example Arrival/Departure Rate
Corridor Width: 30m
Very Crowded (but slow)
  a: 0.5m
  b: 1m
  v: 0.5m/s
  Arrival/Departure rate: 30*0.5/0.5*1= 30 persons/s = 1800 persons/min
Not so crowded (but fast)
  a: 2m
  b: 2m
  v: 1.5m/s
  Arrival/Departure rate: 30*1.5/22= 11.25 persons/s = 675 persons/min

## Slide 8: Questions & Comments

## Slide 9: Straw Poll 1
Do you believe that this pedestrian model is appropriate in train station use cases?
Yes:
No:
More Discussion:

## Slide 10: Straw Poll 2
Do you believe that these parameters is appropriate?
Yes:
No:
More Discussion: