## Slide 1: Path Loss and Delay Spread Models for 11ah
Date: 2011-03-14
Authors:
Slide 1

## Slide 2: Summary
Part 1
  Discussion of Walfisch-Ikegami Path Loss Model
  Example Path Loss Calculation
  Conclusions
Part 2
  Simple Channel Models for PHY link evaluation

## Slide 3: Part 1

## Slide 4: Walfisch-Ikegami Path Loss Model
Frequency f (800...2000 MHz)
Height of the transmitter htx (4...50 m)
Height of the receiver hrx (1...3 m)
Distance d (20...5000 m)
Mean value of building heights hroof
Mean value of widths of streets w
Mean value of building separation b

## Slide 5: WI Model NLOS Path Loss
NLOS path loss consists of
  Free space loss
  Rooftop-to-street diffraction
  Multi-screen loss – consider antenna is below/above building height
Rooftop-to-street diffraction
Multi-screen loss

## Slide 6: Example Path Loss Calculation (Medium Size City, Suburban Center)
Path loss more sensitive to height when distance is long
10~20 dB additional loss if antenna below roof
To reach 1 km, antenna gain, lower sensitivity phy, etc required
Chart: Distance (m)
| 250 | 500 | 750 | 1000
AP Ant=4, C Ant=1 | 112.2 | 129.1 | 137.5 | 143.5
AP Ant=8, C Ant=1 | 114.63 | 127.9 | 135.2 | 140.3
AP Ant=12, C Ant=1 | 107.25 | 118.7 | 125.4 | 130.1
AP Ant=16, C Ant=1 | 100.62 | 112.1 | 118.8 | 123.5
Chart: Distance (m)
| 250 | 500 | 750 | 1000
AP Ant=8, C Ant=2 | 113.4 | 126.7 | 134.07 | 139.3
AP Ant=8, C Ant=4 | 110.1 | 123.9 | 131.42 | 136.8
AP Ant=8, C Ant=6 | 105.1 | 119.6 | 127.6 | 133.2
AP Ant=8, C Ant=8 | 94.5 | 111.3 | 120.6 | 127.3
AP Antenna height from 4 to 16 m
Client Antenna height from 2 to 8 m
Below Roof
Above Roof
1 Watt EIRP -(-88dBm) Sensitivity

## Slide 7: Conclusion Part 1
WI path loss model is discussed
An example path loss, and sensitivity to antenna heights is presented
Antenna gain, lower sensitivity phy, other improvements are required to reach1 km

## Slide 8: Part 2

## Slide 9: Introduction
Contribution 11/251r0 (Outdoor Channel Models for 802.11ah) recommends re-using 3GPP Channel Models in IEEE 802.11ah.
  3GPP models are valid for most frequency ranges being considered for 11ah
  Similar outdoor usage scenarios
Leveraging on 3GPP’s channel modeling approach has a number of advantages
  Saves time and effort in 11ah
  Well tested/verified and used in extensive amount of simulations
In this contribution
  provide a further discussion on path loss and
  propose to adopt a further set of simple channel models for PHY design/verification
    Again following 3GPP’s approach

## Slide 10: System vs. Link Evaluation
The proposal made in 11/251r0 was to adopt 3GPP channel model used for “system-level” evaluation
  Spatial aspect of the channel are modeled in detail
  Path-loss modeled using extended COST 231 model
  Model based on a very large number of parameters
In 11ah the above model will be useful to evaluate system throughout, latency, MU-MIMO performance etc.
However for the purpose of designing and evaluating the PHY (preambles, coding and modulation, repetition etc) simple channel models should be adopted
  to evaluate single links (between BS and STA)
  capturing multi-path delay, fading and Doppler spread
This approach will speed up PHY design and allow us to easily ensure simulations are consistent

## Slide 11: Our Proposal
PHY link simulations for 11ah use channel models used by 3GPP (for WCDMA link simulations):
  Pedestrian A (Ped-A)
  Pedestrian B (Ped-B) and
  Vehicular A (Veh-A)
Above models have following characteristics
  Models SISO links
  Number of paths and path delay are fixed for each model
  Path assumed to be mutually independent and Rayleigh distributed
  Doppler spread applied
Advantages
  sufficiently models fundamental channel characteristics
  easy to generate
  few parameters means models are easily reproduced consistently

## Slide 12: Channel Model Summary
Path # | Ped-A |  | Ped-B |  | Veh-A | 
 | Delay [ns] | Rel. Pow [dB] | Delay [ns] | Rel. Pow [dB] | Delay [ns] | Rel. Pow [dB]
1 | 0 | 0 | 0 | 0.0 | 0 | 0,0
2 | 110 | -9.7 | 200 | -0.9 | 310 | -1.0
3 | 190 | -19.2 | 800 | -4.9 | 710 | -9.0
4 | 410 | -22.8 | 1200 | -8.0 | 1090 | -10.0
5 | -- | -- | 2300 | -7.8 | 1730 | -15.0
6 | -- | -- | 3700 | -23.9 | 2510 | -20.0
Speed: Limit to 3 km/h and/or 30 km/h