## Slide 1: A focused path torwards TGai D1.0
Date: 2011-03-14
Authors:

## Slide 2: Abstract
Focused path towards D1.0 of TGai summarizing scope and assumptions of TGai per PAR & 5C.

## Slide 3: TGai Problem Statement & Scope
FIA SG
TGai FLS
Agreed problem statement: To much time spent in 802.11 link set-up
Four major aspects:
(1) AP discovery, (2) Network Discovery, (3) secure 802.11 link set-up, (4) higher layer (IP addr. Assignment)
(1), (3), and (4) main focus of upcoming TG; (2) addressed by TGu
Biggest potential for performance improvement:
AP discovery & “parallelization of message exchanges” for higher layer protocols
Security: pre-conditions for security scheme strongly influence potential performance gain
Scope: Modifications to the 802.11 MAC to enable fast link set-up
“link” as defined per IEEE 802.11 baseline
Application layer end-to-end- (secure) link set not in scope of TGai
Concurrency in the exchange of higher layer messages during 802.11 link set-up is one approach to reduce the total time spent in link set-up (even if considering appl. Layer end2end links) but: providing schemes for providing concurrent message exchange is enough, TGai does not need to consider a completed link establishment on higher layers (just enable an “early” start of message exchange)

## Slide 4: Definition of Link & Evaluation of Link Set-Up time
STA can access “the Internet”
We had several discussions during SG phase on the definition of “link”. Based on this discussion, the PAR uses language within the context of IEEE 802.11, i.e.:
3.76 link: In the context of an IEEE 802.11 medium access control (MAC) entity, a physical path consisting of exactly one traversal of the wireless medium (WM) that is used to transfer an MAC service data unit (MSDU) between two stations (STAs). [IEEE 802.11-2007]
Given that TGai’s goal is to explore how to use concurrency of higher layer message exchanges during 802.11 link set-up, TGai should agree on an evaluation criteria for comparing proposals which also considers higher layer aspects
  This does not change the scope of TGai
  Based on the discussion during SG phase, TGai should consider for evaluation purposes
    The time when a local (!!!) IP address is assigned to a STA as the end of the link set up
    Open: when to start measuring? When STA enters AP coverage (assuming perfect knowledge for evaluation purposes)?

## Slide 5: A-priori Knowledge vs. Performance
AP / Network Discovery
Secure 802.11 Link Set-Up
Higher Layer Protocol Exchange (IP Addr. Assignment)
Concurrency of higher layer protocol message exchange
Link Set- Up Phase
Increase in A-Priori Knowledge
Increase in Link Set-Up Time
No Assumptions (Today)
Perfect Knowledge
(E.g. location based information on APs’ frequency and coverage)
E.g. RSNA as in IEEE 802.11
E.g. pre-shared keys (i.e. SIM card)
RSNA in combination with improved message exchange
No assumptions on architecture (DHCP Server anywhere in the AP’s subnet)
Strong assumptions (e.g. DHCP Server co-located with AP)
Vender specific cross-layer implementations
Assumptions will influence the acceptance of the 802.11 WG of proposals / the TGai draft.
Assumptions have to be stated per proposal for assessment purposes.
Shall TGai limit assumptions ?

## Slide 6: Way forward: focused towards comprehensive Draft R1.0 to get immediate WG feedback
Ideas for Improvements
Use Cases & Scenarios
Assumptions
Individual Use Case & Scenario Submissions
TGai Use Case Document
Avoid duplication of use cases & scenarios yielding to same requirements.
Represent all interest groups
TGai Technical / Functional Requirements
Optional: Derived assumptions limiting technical proposals
Individual Submissions on selected improvements areas
TGai Draft 1.0
FIA SG
TGai FLS
Keep focused on TGai scope
Address initial areas for improvements 1st

## Slide 7: Summary
TGai has a narrow, well defined focus that was intensively discussed during SG phase
  keep the project targeted
  focus on key working areas as discussed in SG phase
  get feedback from the WG by having Draft 1.0 according to our timeline
Please revisit SG documents if you did not participate in FIA SG; feel free to contact TG Chairs for finding “key documents”

## Slide 8: References
11-10/1152r01: TGai PAR
11-10/1106r01: PAR & 5C Transition from FIA to Fast Initial Link Set-Up
11-10/0965r01: Potential performance improvements with fast initial link set-up