IEEE P802.11
Wireless LANs

| 11ac Sounding Poll frame and VHT MIMO Control fields |
| --- |
| Date: 2011-03-15 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | illsoo.sohn@lge.com |
| Daewon Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-7897 | daewon.lee@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1497 | yongho.seok@lge.com |
| Eunsun Kim | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1860 | esun.kim@lge.com |
| Dongwook Roh | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea |  | dongwook.roh@lge.com |
| Simone Merlin | Qualcomm | 5665 Morehouse Dr., San Diego, CA 92121 | 1-858-845-1243 | smerlin@qualcomm.com |
| Yong Liu | Marvell | 5488 Marvell Lane, Santa Clara CA, 95054 | 1-408-222-8412 | yongliu@marvell.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGac Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGac Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGac Editor:  Editing instructions preceded by “TGac Editor” are instructions to the TGac editor to modify existing material in the TGac draft.   As a result of adopting the changes, the TGac editor will execute the instructions rather than copy them to the TGac Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

| Comment ID | Subclause | Page | Line | Comment Type | Comment | Suggested Remedy |
| --- | --- | --- | --- | --- | --- | --- |
| 28 | 7.2.1.11 | 9 | 12 | TR | NDPA is a control frame; however, there is no definition of subtype in Table 7-1 and should be added. | Add a new subtype for NDPA in Table 7-1. |
| 32 | 7.2.1.12 | 10 | 29 | TR | Sounding Poll is a control frame; however, there is no definition of subtype for Sounding Poll frame in Table 7-1. | Add a new subtype for Sounding Poll frame in Table 7-1. |
| 141 | 7.2.1.12 | 10 | 37 | TR | The Duration field is not defined. | Change to "The Duration field is set as defined in 7.1.4 (Duration/ID field (QoS STA))." |
| 222 | 7.2.1.12 | 10 | 37 | TR | Why is Duration field TBD? Once the sounding sequence is defined, the duration of the sequence can be determined. | Define the duration field. |
| 763 | 7.2.1.12 | 10 | 37 | TR | Add setting of Duration field | as comment |
| 914 | 7.2.1.12 | 10 | 37 | TR | The Duration field is set to TBD. | Replace with: "Duration is set according to 7.1.4.2; Beamformer should set a value long enough to protect the completion of the sounding sequence" |
| 1012 | 7.2.1.12 | 10 | 37 | TR | TBD in Duration field | Find appropriate field design. |
| 1243 | 7.2.1.12 | 10 | 37 | TR | There are two TBDs in this subclause | un-tbd them |
| 1446 | 7.2.1.12 | 10 | 37 | TR | If the sounding response is segmented due to limits of MPDU, the sounding poll frame should contain information regarding segment information | resolve and finalized TBD fields of sounding poll frame |
| 1474 | 7.2.1.12 | 10 | 37 | TR | Duration field can be decided. The duration field of Sounding Poll use same duration protection with the duration of NDPA. If the Duration field in the NDPA is set to the remaining duration of the TXOP, the duration field in sounding poll is set to the remaining duration of the TXOP too. If the Duration field in the NDPA is set to a NAV value at receiving STAs that protects up to the end of any following frame plus any additional overhead frames, the duration field in sounding poll is set to a NAV value at receiving STAs that protects up to the end of any following frame plus any additional overhead frames too. | Defined the Duration field as following: The Duration field is set to as defined in 7.1.4. |
| 223 | 7.2.1.12 | 10 | 44 | TR | Define the additional fields, if any, in the sounding poll frame. If there is no additonal field, remove the statement. | As in comment |
| 764 | 7.2.1.12 | 10 | 44 | TR | Add the "additional fields" | as comment |
| 1013 | 7.2.1.12 | 10 | 44 | TR | In current specification, a Sounding Poll frame may include some additional fields to improve sounding procedures. The following is one suggestion for the usage of new fields. VHT Compressed Beamforming Report field can grow up to approximately 26Kbytes, which is larger than the maximum allowed MPDU limit for management frames. This makes a VHT Compressed Beamforming frame in the form of A-MPDU. Since each MPDUs in the A-MPDU can be checked with individual FCS whether the transmission is success or not, selective retransmission of only failed segments in the A-MPDU can considerably increase the transmission efficiency in sounding procedures. To support the selective retransmission of segments in VHT Compressed Beamforming frame, a new information field which indicates the transmission successes or failures of individual segments need to be added in a Sounding Poll frame. | Add a new Segment Information subfield in the Sounding Poll frame to support selective retransmission of segments in a VHT Compressed Beamforming frame. |
| 1121 | 7.2.1.12 | 10 | 44 | TR | "The Sounding Poll frame may include additional fields TBD." This seems to allow implementers to add fields at will. | Delete statement |
| 1519 | 7.2.1.12 | 10 | 44 | TR | There can be an additonal field for Sounding Poll. Since VHT Compressed Beamforming Report may be segmented in some cases, selective retransmission of segmented Compressed Beamforming Report should make feedback process efficient. To support this retransmission procedure, a new field which indicates the segment information needs to be adopted in Sounding Poll frame. | Include a new field that indicates segment information. |

| 919 | 7.3.1.31 | 13 | 36 | TR | Specify how the absence of the Bemaforming report field is indicated in the VHT MIMO control field | Use a reserved combination (1110) of bits 12-15; this choice is compliant with the proposal presented in a different comment, referred to the indication of the segment numbering |
| --- | --- | --- | --- | --- | --- | --- |
| 1123 | 7.3.1.31 | 13 | 36 | TR | The VHT MIMO Control field needs a way of specifiying null feedback |  |
| 101 | 7.3.1.31 | 13 | 41-46 | TR | The number of bits in the "Channel Width" in Figure 7-3 is not consistant with that of "BW" in VHT-SIG-A. | Set B8 to be reserved (similar to the BW index in VHT-SIG-A), and shift B8-B11 to the right by one bit. Remark: The other MAC frame should follow the same changes. |
| 1124 | 7.3.1.31 | 14 | 28 | TR | The description does not sound accurate: "Number of carriers grouped into one". Is there some averaging going on or are subcarriers just skipped? | Fix description |
| 1125 | 7.3.1.31 | 14 | 33 | TR | The terms "SU-BF" and "MU-BF" are undefined. Also, the description is incomplete since the VHT Compressed Beamforming Report field is also different depending on the setting (the codebook changes). | "Set to 0 to indicate that the feedback is for SU-MIMO Beamforming. For SU-MIMO Beamforming, the VHT Compressed Beamforming Report uses fewer bits phi and psi (see Condebook Information field) and VHT Compressed Beamforming frame does not include the MU Exclusive Beamforming Report field (see ). Set to 1 to indicate that the feedback is for MU-MIMO Beamforming. For MU-MIMO Beamforming, the VHT Compressed Beamforming Report uses more bits for phi and psi and the VHT Compressed Beamforming frame includes the MU Exclusive Beamforming Report field." |

General Discussion:

In sounding procedures, VHT Compressed Beamforming Report field and MU Exclusive Beamforming Report field can grow over the limit of the maximum MPDU limit of a STA. The feedback needs to be segmented in this case and carried in the form of A-MPDU.

As a worst case example, when 8x8 MU-MIMO, 160MHz bandwidth, subcarrier grouping of 1, and  maximum resolution quantization of 9 and 7 is considered. The size of VHT Compressed Beamforming Report field is 26,216 bytes Also, the size of MU Exclusive Beamforming Report field is 936. The total size of Beamforming Report field is 27,152 bytes. Assuming the maximum MPDU size of 3,895 bytes and considering other overhead, the number of segmentation can grow up to 8.

According to the current draft, a transmission failure in one of the segments in an A-MPDU results in entire retransmission of the VHT Compressed Beamforming frame, which makes the sounding procedure very inefficient when link quality is not good. Thus, the selective retransmission of segments in a VHT Compressed Beamforming frame would be a quite reasonable solution.

To support this, the segments in A-MPDU of VHT Compressed Beamforming frame need to be identified individually. This can be simply accomplished by introducing new fields for segment identification in a VHT MIMO Control field. This new field can also be utilized for the indication that a STA doesn’t have a valid feedback. On the other hand, Sounding Poll frame defined in 7.2.1.12 may include new additional fields for advanced sounding procedures. Thus, a new field can be introduced to indicate the selection of segments for retransmission. Considering the individual indication of segments with minimum additional overhead, a bitmap-type definition would be efficient for the new field.

A beamformer can determine which segment is not correctly received using the segment identification in a VHT MIMO Control field of the received VHT Compressed Beamforming frame. The beamformer may request the retransmission of all the segments or may request only the selected segments which have not correctly received using segment retransmission bitmap in Sounding Poll frame. Upon the reception of the Sounding Poll frame with the segment indication, a STA may feedback only selected segments in a VHT Compressed Beamforming frame or STA may retransmit all segments in a VHT Compressed Beamforming frame.

Proposed Resolution:

▶TR CID 28 and 32: The comments are mentioning a missing subtype of Sounding Poll and NDPA frames.

▷ Proposed Response: Agree in principle.

| 28 | 7.2.1.11 | 9 | 12 | TR | NDPA is a control frame; however, there is no definition of subtype in Table 7-1 and should be added. | Add a new subtype for NDPA in Table 7-1. |
| --- | --- | --- | --- | --- | --- | --- |
| 32 | 7.2.1.12 | 10 | 29 | TR | Sounding Poll is a control frame; however, there is no definition of subtype for Sounding Poll frame in Table 7-1. | Add a new subtype for Sounding Poll frame in Table 7-1. |

▶TR CID 141, 222, 763, 914, 1012, 1243, and 1474: The comments are mentioning missing instructions on Duration field which is left TBD.

▷ Proposed Response: Agree in principle. The Duration field can be set as described in Clause 7.1.4.2 (as described in IEEE802.11-11/0346)

| 141 | 7.2.1.12 | 10 | 37 | TR | The Duration field is not defined. | Change to "The Duration field is set as defined in 7.1.4 (Duration/ID field (QoS STA))." |
| --- | --- | --- | --- | --- | --- | --- |
| 222 | 7.2.1.12 | 10 | 37 | TR | Why is Duration field TBD? Once the sounding sequence is defined, the duration of the sequence can be determined. | Define the duration field. |
| 763 | 7.2.1.12 | 10 | 37 | TR | Add setting of Duration field | as comment |
| 914 | 7.2.1.12 | 10 | 37 | TR | The Duration field is set to TBD. | Replace with: "Duration is set according to 7.1.4.2; Beamformer should set a value long enough to protect the completion of the sounding sequence" |
| 1012 | 7.2.1.12 | 10 | 37 | TR | TBD in Duration field | Find appropriate field design. |
| 1243 | 7.2.1.12 | 10 | 37 | TR | There are two TBDs in this subclause | un-tbd them |
| 1474 | 7.2.1.12 | 10 | 37 | TR | Duration field can be decided. The duration field of Sounding Poll use same duration protection with the duration of NDPA. If the Duration field in the NDPA is set to the remaining duration of the TXOP, the duration field in sounding poll is set to the remaining duration of the TXOP too. If the Duration field in the NDPA is set to a NAV value at receiving STAs that protects up to the end of any following frame plus any additional overhead frames, the duration field in sounding poll is set to a NAV value at receiving STAs that protects up to the end of any following frame plus any additional overhead frames too. | Defined the Duration field as following: The Duration field is set to as defined in 7.1.4. |

▶TR CID 1446, 223, 764, 1013, 1121, and 1519: The comments are any mentioning possible additional field in Sounding Poll frame which is left TBD.

▷ Proposed Response: Agree in principle. One suggestion from comments is to add segment information to enable selective retransmission of segments. Discussions details are given above. More details can be found in IEEE802.11-11/0411.

| 1446 | 7.2.1.12 | 10 | 37 | TR | If the sounding response is segmented due to limits of MPDU, the sounding poll frame should contain information regarding segment information | resolve and finalized TBD fields of sounding poll frame |
| --- | --- | --- | --- | --- | --- | --- |
| 223 | 7.2.1.12 | 10 | 44 | TR | Define the additional fields, if any, in the sounding poll frame. If there is no additonal field, remove the statement. | As in comment |
| 764 | 7.2.1.12 | 10 | 44 | TR | Add the "additional fields" | as comment |
| 1013 | 7.2.1.12 | 10 | 44 | TR | In current specification, a Sounding Poll frame may include some additional fields to improve sounding procedures. The following is one suggestion for the usage of new fields. VHT Compressed Beamforming Report field can grow up to approximately 26Kbytes, which is larger than the maximum allowed MPDU limit for management frames. This makes a VHT Compressed Beamforming frame in the form of A-MPDU. Since each MPDUs in the A-MPDU can be checked with individual FCS whether the transmission is success or not, selective retransmission of only failed segments in the A-MPDU can considerably increase the transmission efficiency in sounding procedures. To support the selective retransmission of segments in VHT Compressed Beamforming frame, a new information field which indicates the transmission successes or failures of individual segments need to be added in a Sounding Poll frame. | Add a new Segment Information subfield in the Sounding Poll frame to support selective retransmission of segments in a VHT Compressed Beamforming frame. |
| 1121 | 7.2.1.12 | 10 | 44 | TR | "The Sounding Poll frame may include additional fields TBD." This seems to allow implementers to add fields at will. | Delete statement |
| 1519 | 7.2.1.12 | 10 | 44 | TR | There can be an additonal field for Sounding Poll. Since VHT Compressed Beamforming Report may be segmented in some cases, selective retransmission of segmented Compressed Beamforming Report should make feedback process efficient. To support this retransmission procedure, a new field which indicates the segment information needs to be adopted in Sounding Poll frame. | Include a new field that indicates segment information. |

▶TR CID 919 and 1123: The comments are mentioning the necessity indication of the feedback without VHT Compressed Beamforming Report.

▷ Proposed Response: Agree in principle. One suggestion from comments is that use the reserved bits for segment numbering and reserve one value to indicate null feedback case. The identification of segments can be utilized for advanced sounding procedures such as selective segment retransmission of VHT Compressed Beamforming frame.

| 919 | 7.3.1.31 | 13 | 36 | TR | Specify how the absence of the Bemaforming report field is indicated in the VHT MIMO control field | Use a reserved combination (1110) of bits 12-15; this choice is compliant with the proposal presented in a different comment, referred to the indication of the segment numbering |
| --- | --- | --- | --- | --- | --- | --- |
| 1123 | 7.3.1.31 | 13 | 36 | TR | The VHT MIMO Control field needs a way of specifiying null feedback |  |

▶TR CID 101: The comment is mentioning the necessity of increasing the number of bits for BW indication in Figure 7-3.

▷ Proposed Response: Disagree. There is no reason to change. Two bits are fine as it is.

| 101 | 7.3.1.31 | 13 | 41-46 | TR | The number of bits in the "Channel Width" in Figure 7-3 is not consistant with that of "BW" in VHT-SIG-A. | Set B8 to be reserved (similar to the BW index in VHT-SIG-A), and shift B8-B11 to the right by one bit. Remark: The other MAC frame should follow the same changes. |
| --- | --- | --- | --- | --- | --- | --- |

▶TR CID 1124: The comment is mentioning the exact behavior for grouping of subcarriers.

▷ Proposed Response: Agree in principle. Grouping is defined as “Grouping is a method that reduces the size of the VHT Compressed Beamforming Report field by reporting a single value for each group of Ng adjacent subcarriers” in 7.3.1.32. The sentence needs to be clarified with the reference.

| 1124 | 7.3.1.31 | 14 | 28 | TR | The description does not sound accurate: "Number of carriers grouped into one". Is there some averaging going on or are subcarriers just skipped? | Fix description |
| --- | --- | --- | --- | --- | --- | --- |

▶TR CID 1125: The comment is mentioning the undefined words “SU-BF” and “MU-BF”.

▷ Proposed Response: Agree in principle. Editorial correction required but details on different numbers of feedback bits seems not appropriate in the table. Those should be written in 7.3.1.32 if necessary.

| 1125 | 7.3.1.31 | 14 | 33 | TR | The terms "SU-BF" and "MU-BF" are undefined. Also, the description is incomplete since the VHT Compressed Beamforming Report field is also different depending on the setting (the codebook changes). | "Set to 0 to indicate that the feedback is for SU-MIMO Beamforming. For SU-MIMO Beamforming, the VHT Compressed Beamforming Report uses fewer bits phi and psi (see Condebook Information field) and VHT Compressed Beamforming frame does not include the MU Exclusive Beamforming Report field (see ). Set to 1 to indicate that the feedback is for MU-MIMO Beamforming. For MU-MIMO Beamforming, the VHT Compressed Beamforming Report uses more bits for phi and psi and the VHT Compressed Beamforming frame includes the MU Exclusive Beamforming Report field." |
| --- | --- | --- | --- | --- | --- | --- |

Agree on following edition instruction.

## Editing instructions:

TGac editor: Insert the following row in Table 7-1 (Draft 802.11mb-D4.0):

| Type value | Type description | Subtype value | Subtype description |
| --- | --- | --- | --- |
| 01 | Control | <ANA> | NDPA |
| 01 | Control | <ANA> | Sounding Poll |

7 Frame formats

7.2 Format of individual frame types

7.2.1 Control frames

7.2.1.12 Sounding Poll

TGac editor: Insert the Segment Retransmission field in Table 7-16f as shown:

| Frame Control | Duration | RA | TA | Segment Retransmission Bitmap | FCS |
| --- | --- | --- | --- | --- | --- |

Octets:		2		2		6		6		1	      4

TGac editor: On page 10 line 37, change the paragraph as follows:

The Duration field is set according to 7.1.4.2 Duration/ID field (QoS STA).

TGac editor: On page 10 line 42, insert two new paragraphs as follows:

The Segment Retransmission Bitmap field indicates the segments to be polled in a VHT Compressed Beamforming frame. The bit in position n (n=0 for LSB and n=7 for MSB) is set to 1 when the segment with the Remaining Segment subfield in VHT MIMO Control field set to n is requested. The bit in position n is set to 0 when the segment with the Remaining Segment subfield in VHT MIMO Control field set to n is not requested.

TGac editor: On page 10 line 44, put the sentence in the form of editor’s note.

7.3 Management frame body components

7.3.1 Fields that are not information element

7.3.1.31 VHT MIMO Control field

TGac editor: Change the VHT MIMO Control field in Figure 7-3 as follows:

| B0-B2 | B3-B5 | B6-B7 | B8-B9 | B10 | B11 | B12-B14 | B15 | B16-B17 | B18-B23 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nc Index | Nr Index | Channel Width | Grouping | Codebook Information | Feedback Type | Remaining Segments | First Segment | Reserved | Sounding Sequence |
| Bits: 3 | 3 | 2 | 2 | 1 | 1 | 3 | 1 | 2 | 6 |

TGac editor: Change the third row in Table 7-2 as follows:

| Grouping | Number of carriers for grouping as defined in 7.3.1.32: Set to 0 for Ng = 1 (No grouping) Set to 1 for Ng = 2 Set to 2 for Ng = 4 The value 3 is reserved |
| --- | --- |

TGac editor: Change the sixth row in Table 7-2 as follows:

| Codebook Information | Indicates the size of codebook entries: If Feedback Type is set to 0 Set to 0 for 2 bit for ψ, 4 bits for  Set to 1 for 4 bit for ψ, 6 bits for  If Feedback Type is set to 1 Set to 0 for 5 bit for ψ, 7 bits for  Set to 1 for 7 bit for ψ, 9 bits for  |
| --- | --- |

TGac editor: Insert the following rows before Sounding Sequence row in Table 7-2:

| Subfield | Description |
| --- | --- |
| Remaining Segments | Indicate the remaining segment number for the associated VHT Compressed Beamforming frame. Set to 0 for the last segment of a segmented frame or the only segment of an unsegmented frame. In case of a retransmitted segment, the field is set to the same value associated with the segment in the original transmission. In case of a VHT Compressed Beamforming frame not carrying Compressed Beamforming Report and MU Exclusive Beamforming Report fields, the field is set to all ones. |
| First Segment | Set to 1 for the first segment of a segmented frame or the only segment of an unsegmented frame; set to 0 otherwise. In case of a retransmitted segment, the field is set to the same value associated with the segment in the original transmission. In case of a VHT Compressed Beamforming frame not carrying Compressed Beamforming Report and MU Exclusive Beamforming Report fields, the field is set to 0. |

Premotion:

Do you agree the comment resolutions for CIDs 28, 32, 141, 222, 763, 914, 1012, 1243, 1446, 1474, 223, 764, 1013, 1121, 1519, 919, 1123, 101, 1124, and 1125 as in 11/0378r1, and to be forwarded to the 11ac task group for motion?

- Yes:

- No:

- Abs:

# Text boxes

Abstract

Submission for Draft P802.11ac_D0.1 comment resolution.

In sounding procedures, VHT Compressed Beamforming Report field and MU Exclusive Beamforming Report field can grow up to approximately 26kByts, which makes the MMPDU of VHT Compressed Beamforming frame be segmented and carried in the form of A-MPDU. This enables advanced features such as selective retransmission of segments in a VHT Compressed Beamforming frame to increase transmission efficiency. In return for that, this submission provides modified VHT MIMO Control field including new subfields for segment identification and modified Sounding Poll frame including new subfield for indication of selective segment retransmission.

Submission addresses Draft P802.11ac_D0.1 technical comments 28, 32, 141, 222, 763, 914, 1012, 1243, 1446, 1474, 223, 764, 1013, 1121, 1519, 919, 1123, 101, 1124, and 1125