IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – CID 342, 343, 899, 1332, 1563, 1628 |
| --- |
| Date: March 14, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Minho Cheong | ETRI |  |  | minho@etri.re.kr |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 899 | 22.3.6 | 88 | 4 | TR | Table 22-4—Timing-related constants It will be a good idea if we can put two columns (one for the parameter and one for the description) |  |
| 1563 | 22.3.6 | 88 | 54 | TR | the formula of TL-LTF is wrong | Modify "TGIS" to "TGI2" |
| 342 | 22.3.6 | 88 | 55 | TR | TGIS | TGI2 |
| 1628 | 22.3.6 | 88 | 55 | TR | This equation for T_L_LTF is wrong | this equation needs to be changed into "2x T_DFT + T_GI2" |
| 1332 | 22.3.6 | 88 | 54-55 (Tab | TR | TL-LTF should be a function of TGI2 rather than TGIS | change to "8 µs = 2 x TDFT + TGI2" |
| 343 | 22.3.6 | 89 | 4 | TR | TLSIG = 4 us, yet (22-15) uses TSYM not TLSIG | Suggest writing 4 us = Tsym for TLSIG, TVHT-LTF; also, arguably, TVHT-STF = 5*TDFT/4 |

Response:

CID 342

AGREE IN PRINCIPLE.  Current equation about TL-LTF in D0.1 is wrong. So, TGIS in that equation shall change into TGI2 to make it correct.

CID 1332, 1563, 1628

See CID 342.

CID 899

AGREE IN PRINCIPLE. Putting two columns as suggested in this comments makes this table more readable.

CID 343

AGREE IN PRINCIPLE. There is a little ambiguity about what TSYM really means in the current text (D0.1). In addition to that, (22-71) and (22-76), which are equations for the VHT data transmission and the non-HT duplicate data transmission, use TSYM in these, regardless of whether short GI is used or not, even though TSYM is the symbol duration by D0.1 only when long GI is used. So, I additionally define TSYML for the symbol duration when long GI is used, and set TSYM to be one between TSYML and TSYMS depending on which GI is used.

Proposed Resolution Text:

TGac editor: Replace Table 22-4 by following new Table:

Table 22-4 – Timing-related constants

| Parameter | Description | VHT_CBW20 | VHT_CBW40 | VHT_CBW80 | VHT_CBW 80+80 | VHT_CBW 160 |
| --- | --- | --- | --- | --- | --- | --- |
| NSD | Number of complex data numbers per frequency segment | 52 | 108 | 234 | 234 | 468 |
| NSP | Number of pilot values per frequency segment | 4 | 6 | 8 | 8 | 16 |
| NST | Total number of subcarriers per frequency segment (See NOTE 1) | 56 | 114 | 242 | 242 | 484 |
| NSR | Highest data subcarrier index per frequency segment | 28 | 58 | 122 | 122 | 250 |
| NSeg | Number of frequency segments | 1 | 1 | 1 | 2 | 1 |
| ∆F | Subcarrier frequency spacing | 312.5 kHz |
| TDFT | IDFT/DFT period | 3.2 µs |
| TGI | Guard interval duration | 0.8 µs = TDFT /4 |
| TGI2 | Double guard interval | 1.6 µs = 2 x TGI |
| TGIS | Short guard interval duration | 0.4 µs = TDFT /8 |
| TSYML | Long GI symbol interval | 4 µs = TDFT + TGI = 1.25 x TDFT |
| TSYMS | Short GI symbol interval | 3.6 µs = TDFT + TGIS = 1.125 x TDFT |
| TSYM | Symbol interval | TSYML or TSYMS depending on which GI is used (See NOTE 2) |
| TL-STF | Legacy short training sequence duration | 8 µs = 10 x TDFT /4 |
| TL-LTF | Legacy long training sequence duration | 8 µs = 2 x TDFT + TGI2 |
| TL-SIG | Legacy SIGNAL field duration | 4 µs = TSYML |
| TVHT-SIG-A | VHT SIGNAL A field duration | 8 µs = 2TSYML |
| TVHT-STF | VHT short training field duration | 4 µs = TSYML |
| TVHT-LTF | Duration of each VHT LTF training field | 4 µs = TSYML |
| TVHT-SIG-B | VHT SIGNAL B field duration | 4 µs = TSYML |
|  |  | NOTE 1 : NST = NSD + NSP NOTE 2 : Long GI is used with transmissions of L-SIG, VHT-SIG-A, VHT-STF, VHT-LTF and VHT-SIG-B. Long GI is used with transmissions of VHT-Data when GI_TYPE in TXVECTOR is set to LONG_GI. Short GI is only used with transmissions of VHT-Data when GI_TYPE in TXVECTOR is set to SHORT_GI. |

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D0.1:

CID 342, 343, 899, 1332, 1563, 1628