IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – CID 1648, 1649, 1654, 1655 |
| --- |
| Date: March 14, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Minho Cheong | ETRI |  |  | minho@etri.re.kr |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 1648 | 22.3.11 | 115 | 3 | TR | There is a little ambiguity about whether MU or SU | add "the tail bits (6 N_ES bits for SU and 6 N_ES,u bits for each user u in MU)" |
| 1649 | 22.3.11.1 | 115 | 61 | TR | It may be better to fill the blank in Table 22-12 | Fill this blank with the expression "see Table 17-6ac" |
| 1654 | 22.3.11.5 | 120 | 23 | TR | There are some amguities about the expression in this sentence. | needs to be changed into " "i th bit of output of j th encoder is assigned to k th input bit of i_ss th spatial stream". Delete y_(j)_i because there is no other referrings. |
| 1655 | 22.3.11.5 | 120 | 26 | TR | There is no description about range of k in Equation (22-53) | add in Equation (22-53) "k=0, 1, … , N_CBPSS" |

Response:

CID 1648

AGREE IN PRINCIPLE.  N_ES is only defined for SU case in Table 22-5. In MU case, the number of encoders may be different according to different users, so is it about the number of tail bits.

Proposed Resolution Text:

TGac editor: Replace the first 3 paragraphs in section 22.3.11by the following red-colored text.

### 22.3.11 Data field

The number of OFDM symbols in the Data field is determined by the Length field in L-SIG (see 22.3.9.1.4), the preamble duration and the setting of the Short GI field in VHT-SIG-A (see 22.3.9.2.3).

For both BCC and LDPC, all bits (including the PHY pad bits) shall be encoded.

When BCC encoding is used, the Data field shall consist of the 16-bit SERVICE field, the PSDU, the PHY pad bits and the tail bits (6 NES bits for SU and 6 NES,u bits for each user u in MU). When LDPC encoding is used, the Data field shall consist of the 16-bit SERVICE field, the PSDU and the PHY pad bits. No tail bits are present when LDPC encoding is used.

The padding flow is as follows. The MAC delivers a PSDU that fills the available octets in the data portion of the PPDU for each user u. In the case of BCC, the PHY determines the number of pad bits to add using Equation (22-44) and appends them to the PSDU. The number of pad bits added will always be between 0 and 7 inclusive per each user.

CID 1649

AGREE IN PRINCIPLE. Scrambler initialization is already defined in section 17. So, it is good to fill this blank in Table 22-12 with the expression "see Table 17-6ac" to resolve ambiguity about its function.

Proposed Resolution Text:

TGac editor: Replace section 22.3.11.1 by the following text.

#### 22.3.11.1 SERVICE field

The SERVICE field is as shown in Table 22-12.

Table 22-12--SERVICE field

| Bits | Field | Description |
| --- | --- | --- |
| B0-B6 | Scrambler Initialization | See Table 17-6ac |
| B7 | Reserved | Set to 0 |
| B8-B15 | CRC | CRC calculated over VHT-SIG-B (excluding tail bits) |

The Reserved and CRC fields shall be scrambled.

CID 1654

ACCEPT

CID 1655

ACCEPT

Proposed Resolution Text:

TGac editor: Replace section 22.3.11.5 by the following text.

#### 22.3.11.5 Stream parser

After coding and puncturing, the data bit streams at the output of the FEC encoders are re-arranged into  blocks of  bits. This operation is referred to as “stream parsing” and is described in this section.

The number of bits assigned to a single axis (real or imaginary) in a constellation point in a spatial stream is denoted by Equation .

The sum of these over all streams is:

Consecutive blocks of  bits are assigned to different spatial streams in a round robin fashion.

If multiple encoders are present, the output of a different encoder is used for each round robin cycle, i.e. at the beginning,  bits from the output of first encoder are fed into all spatial streams, and then  bits from the output of next encoder are used, and so on.

i th bit of output of j th encoder is assigned to k th input bit of iss th spatial stream

where k=0, 1, … , NCBPSS-1

and

where

is the largest integer less than or equal to

is the remainder resulting from the division of integer  by integer

For , the first term in Equation  has a value of 0.

For 160 MHz MCSs, if each BCC encoder does not generate integer blocks of S coded bits in each OFDM symbol, then apply the same stream parsing method above until the last integer block (floor(NCBPS/NES/S)) of S bits at each encoder. Assuming that at this point in each OFDM symbol each BCC has M.s (M<NSS) residue bits, take the last M.s bits in the current OFDM symbol from the first encoder and allocate them to the first M spatial streams (s bits to each stream); then take the last M.s bits in the current OFDM symbol from the second encoder and distribute these among M spatial streams, starting from spatial stream M+1, and so on. Note that upon reaching the spatial stream NSS, cycle back to the 1st spatial stream. Repeat till all bits are distributed in the current OFDM symbol.

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D0.1:

CID 1648, 1649, 1654, 1655