IEEE P802.11
Wireless LANs

| Resolution for CID 1145 |
| --- |
| Date: 2011-03-12 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Robert Stacey | Intel Corporation | 2111 NE 25th Ave, Hillsboro, OR 97124 | +1-503-724-0893 | robert.j.stacey@intel.com |

## Comments

| 1145 | Stacey, Robert | 7.3.61.3 | 31 | 45 | TR | Relationship between HT A-MPDU Parameters field and VHT A-MPDU parameters field is not explicit. Require that HT A-MPDU Parameters field match A-MPDU Parameters field upto 64KB and then fix HT value at 64 for longer values. | As suggested |
| --- | --- | --- | --- | --- | --- | --- | --- |

## Discussion

Need to define normative requirements for setting VHT Capabilities and HT Capabilities Maximum A-MPDU Length Exponent.

## Resolution

Include section 9.12.2 from REVmb 7.0 and edit as follows:

### 9.12.2 A-MPDU length limit rules

An A-MPDU pre-EOF padding is defined as

- the portion of the A-MPDU up to but excluding the first A-MPDU subframe that has a Length field equal to 0 and an EOF field equal to 1,

- the entire A-MPDU if no A-MPDU subframes with Length field equal to 0 and EOF field equal to 1 are present.

NOTE—An A-MPDU and an A-MPDU pre-EOF padding include any A-MPDU subframes with Length field equal to 0 and EOF field equal to 0 inserted in order to meet the MPDU start of spacing requirement.

An HT STA indicates a value in the Maximum A-MPDU Length Exponent field in its HT Capabilities element that defines the maximum A-MPDU length that it can receive. A VHT STA indicates a value in the Maximum A-MPDU Length Exponent field in its VHT Capabilities element that defines the maximum length of the A-MPDU pre-EOF padding that it can receive. The encoding of these fields is defined in Table 8-121 (Subfields of the A-MPDU Parameters field) and Table 8-ac19 (Subfields of the A-MPDU Paramters field) respectively.

A VHT STA that sets the Maximum A-MPDU Length Exponent field in its VHT Capabilities element to a value in the range 0 to 3 shall set the Maximum A-MPDU Length Exponent in its HT Capabilties to the same value. A VHT STA that sets the Maximum A-MPDU Length Exponent field in the VHT Capabilties element to a value larger than 3, shall set the Maximum A-MPDU Length Exponent in the HT Capabilties element to 3.

Using these Maximum A-MPDU Length Exponent fields, the STA establishes at association the maximum length of an A-MPDU pre-EOF padding that can be sent to it. An HT STA shall be capable of receiving A-MPDUs of length up to the value indicated by the Maximum A-MPDU Length Exponent field in its HT Capabilties element. A VHT STA shall be capable of receiving A-MPDUs where the A-MPDU pre-EOF padding length is up to the value indicated by the Maximum A-MPDU Length Exponent field in its VHT Capabilties element.

A STA shall not transmit an A-MPDU in a HT_MF or HT_GF format PPDU that is longer than the value indicated by the Maximum A-MPDU Length Exponent field in the HT Capabilities element sent by the intended receiver. A STA shall not transmit an A-MPDU in a VHT format PPDU where the A-MPDU pre-EOF padding length is longer than the value indicated by the Maximum A-MPDU Length Exponent field in the VHT Capabilties element sent by the intended receiver.

# Text boxes

Abstract

This document proposes a resolution for CID 1145 (comment on P802.11ac/D0.1).