IEEE P802.11
Wireless LANs

| Resolution for CID 1151 VHT Channel Width |
| --- |
| Date: 2011-03-12 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Robert Stacey | Intel Corporation | 2111 NE 25th Ave, Hillsboro, OR 97124 | +1-503-724-0893 | robert.j.stacey@intel.com |

## Comment

| 1151 | Stacey, Robert | 7.3.2.62 | 34 | 22 | TR | "STA Channel Width" is bandly named. This is the BSS Channel Width (logically grouped with Center Frequency and other channel definition paramters). Also, the encoding of this field could be better aligned with HT Operation element. | Change name to "Channel Width". Alternate encoding: 20 MHz: VHT Operation Channel Width = 0, HT Operation Channel Width = 0; 40 MHz: VHT Operation Channel Width = 0, HT Operation Channel Width = 1; 80 MHz: VHT Operation Channel Width = 1, HT Operation STA CHannel Width = 1, 160 MHz: VHT Operation Channel Width = 2, HT Operation STA Channel Width = 1; 80+80MHz: VHT Operation Channel Width = 3, HT Operation Channel Width =1 |
| --- | --- | --- | --- | --- | --- | --- | --- |

## Discussion

## Resolution

Edits applied to P802.11ac/D0.2

Change Figure 8-ac14 as shown blow (change name of STA Channel Width field):

|  | STA Channel Width | Channel Center Frequency Segment 1 | Channel Center Frequency Segment 2 |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | 1 |

Figure 8-ac14—VHT Operation Information field

Change the paragraph following Figure 8-ac14 as follows:

The VHT STA gets the primary channel information from the HT Operation element. The subfields of the VHT Operation Information field are defined in Table 8-ac21 (VHT Operation Information subfields).

Change the “STA Channel Width” row in Table 8-ac21 as follows:

Table 8-ac21—VHT Operation Information subfields

| Field | Definition | Encoding |
| --- | --- | --- |
| STA Channel Width | Defines the channel widths that may be used to transmit to the STA. This field together with the STA Channel Width field in the HT Operation element defines the VHT BSS channel width. | Set to 0 for 20 MHz or 40 MHz channel width (The STA Channel Width field in the HT Operation element determines whether the BSS channel width 20 MHz or 40 MHz). Set to 1 for 4080 MHz channel width. Set to 2 for 80160 MHz channel width. Set to 3 for 16080+80 MHz channel width. Set to 4 for 80 + 80 MHz channel width. Otherwise reserved. |

## 10.24 VHT BSS operation

### 10.24.1 Basic VHT BSS functionality

Insert the following as the first and second paragraph of section 10.24.1:

A STA shall include the HT Operation element in frames in which it has includes the VHT Operation element.

A VHT AP indicates the primary channel of the BSS in the Primary Channel field in the HT Operation element. A VHT AP sets the STA Channel Width field in the HT Operation element and the Channel Width field in the VHT Operation element to indicate BSS channel width as shown in Table 10-ac<new>. Permutations not listed in Table 10-ac<new> are reserved and shall not be used by a VHT AP.

Insert new Table 10-ac<new>:

Table 10-ac<new>--VHT BSS channel width

| VHT Operation Channel Width | HT Operation STA Channel Width | VHT BSS channel width |
| --- | --- | --- |
| 0 | 0 | 20 MHz |
| 0 | 1 | 40 MHz |
| 1 | 1 | 80 MHz |
| 2 | 1 | 160 MHz |
| 3 | 1 | 80+80 MHz |

# Text boxes

Abstract

This document proposes a resolution for CID 1151