IEEE P802.11
Wireless LANs

| Resolution to CID 2136 |
| --- |
| Date: 2011-03-15 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Guido R. Hiertz | Philips | Riedel Communications GmbH & Co. KG, Uellendahler Str. 353, 42109 Wuppertal, Germany | +49-202-292-9987 | hiertz@ieee.org |
| Dee Denteneer | Philips | HTC 37; 5656 AE Eindhoven; The Netherlands | +31 40 27 49743 | Dee.Denteneer@philips.com |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6 80200 München, Germany |  | bahr@siemens.com |

Abstract

This document provides resolution to the comment with CID 2136. The latter asks for removal of the term WDS from the IEEE 802.11-2007 standard.

Delete the following definition from 802.11-2007:

Apply the following changes to 802.11-2007:

- On page 22 in Clause 4 delete "WDS   wireless distribution system"

- In Figure 8-39 (Authenticator state machines, part 3) on page 231 in Clause 8.5.6.1 replace "WDS" with "(FromDS==1 AND ToDS == 1)".

- On page 792 in Clause C.2 (Data type and operator definitions for the MAC state machines) replace "synonym sWdsAddLng Integer = 6;" with "synonym sFourAddrAddLng Integer = 6;".

- On page 792 in Clause C.2 (Data type and operator definitions for the MAC state machines) replace "/* octets added for WDS (addr4) */" with "/* octets added for four address frame format (addr4) */".

- On page 792 in Clause C.2 (Data type and operator definitions for the MAC state machines) replace "(sMaxMsduLng + sMacHdrLng + sWdsAddLng + sWepAddLng + sCrcLng)" with "(sMaxMsduLng + sMacHdrLng + sFourAddrAddLng + sWepAddLng + sCrcLng)".

- On page 815 in Clause C.2 (Data type and operator definitions for the MAC state machines) replace "/* Address 4 [WDS-SA] field (6) */" with "/* Address 4 [Four Address frame SA] field (6) */".

- On page 846 in Clause C.3 (State machines for MAC STAs) replace "isWds:= toDs(pdu) and frDs(pdu)" with "isFourAddrFrame:= toDs(pdu) and frDs(pdu)".

- On page 846 in Clause C.3 (State machines for MAC STAs) replace all occurences of "if isWds then sWdsAddLng else 0 fi" with "if isFourAddrFrame then sFourAddrAddLng else 0 fi".

- On page 912 in Clause C.3 (State machines for MAC STAs) replace "dcl isWds Boolean ;" with "dcl isFourAddrFrame Boolean ;".

- On page 912 in Clause C.3 (State machines for MAC STAs) replace "isWds:= toDs(pdu) and frDs(pdu)" with "isFourAddrFrame:= toDs(pdu) and frDs(pdu)"

- On page 912 in Clause C.3 (State machines for MAC STAs) replace "sWepAddLng + sCrcLng - if isWds then sWdsAddLng else 0 fi" with "sWepAddLng + sCrcLng - if isFourAddrFrame then sFourAddrAddLng else 0 fi"

- On page 912 in Clause C.3 (State machines for MAC STAs) replace "if isWds then sWdsAddLng else 0 fi" with "if isFourAddrFrame then sFourAddrAddLng else 0 fi"

- On page 921 in Clause C.4 (State machines for MAC AP) replace all occurences of "wdsAddr" with "APAddr" and replace all occurrences of "'to Wds ?'" with "'to other AP ?'"

- On page 926 in Clause C.4 (State machines for MAC AP) replace "isWds:= toDs(pdu) and frDs(pdu)" with "isFourAddrFrame:= toDs(pdu) and frDs(pdu)".

- On page 926 in Clause C.4 (State machines for MAC AP) replace "if isWds then sWdsAddLng else 0 fi" with "if isFourAddrFrame then sFourAddrAddLng else 0 fi".

- On page 983 in Clause C.4 (State machines for MAC AP) replace "dcl isWds Boolean ;" with "dcl isFourAddrFrame Boolean ;" and replace "isWds:= toDs(pdu) and frDs(pdu)" with "isFourAddrFrame:= toDs(pdu) and frDs(pdu)".

- On page 983 in Clause C.4 (State machines for MAC AP) replace "decryptLng:=length(pdu) - sMacHdrLng - sWepAddLng + sCrcLng - if isWds then sWdsAddLng else 0 fi" with "decryptLng:=length(pdu) - sMacHdrLng - sWepAddLng + sCrcLng - if isFourAddrFrame then sFourAddrAddLng else 0 fi" and replace "if isWds then sWdsAddLng else 0 fi" with "if isFourAddrFrame then sFourAddrAddLng else 0 fi".

References:

IEEE Std 802.11-2007