## Slide 1
Slide 1
Identification Signal for Fixed devices
Date: 2011-03-15
Authors:

## Slide 2: Comments
576, 922 | Kim, Eunsun Seok, Yongho |  | T | Y | According to the FCC rules, fixed TVBDs shall transmit identifying information. The identification signal must conform to a standard established by a recognized industry standards setting organization. The identification signal shall carry sufficient information to identify the device and its geographic coordinates (§ 15.711(d), FCC 10-174). There is no technical description on how to satisfy this requirements | Add device identification and device location information (or something equivalent) in Beacon, enabling signal or probe request/response frame. See forthcoming document 11-11/xxxxr0.
519 | Kafle, Padam | General | T | Y | Fixed STA needs to broadcast their identity and location information while operating in TVWS band as per the FCC's rules. Also, the registration of such devices to database is not covered. | As per the comment

## Slide 3: Abstract
FCC regulation on identification signal
How to implement this regulation into IEEE 802.11af standard

## Slide 4: FCC requirements (§ 15.711(d) )
Fixed TVBD
  Fixed TVBDs shall transmit identifying information
Identification signal
  The identification signal must conform to a standard established by a recognized industry standards setting organization
  The identification signal shall carry sufficient information to identify the device and its geographic coordinates

## Slide 5: Fixed STA operation
Device operation
  A fixed STA is a registered STA that broadcasts its registered location its identifying information, which is sufficient to identify the device and its registered location, and in some regulatory domains is restricted from enabling other STAs

## Slide 6: Fixed STA operation
Device operation
  A fixed STA shall transmit identifying information in a Beacon frame, Probe Response frame or Public Action frame.
  In US, the identifying information should include FCC identification number (FCC ID), device serial number and device location of fixed STA, which are identical with the information provided in the process of Channel Query.

## Slide 7: Identifying information of fixed STA
Identifying information in 802.11af may include:
  Country-Specific
  Device Identification Info (E.3.1.2)
    FCC ID
    Device Serial Number
  Device Location Info (E.3.1.3)

## Slide 8: Identifying information of fixed STA
Proposed Information Element Format
 | Element ID | Length | Device Identification Information | Device Location Information
Octets: | 1 | 1 | Variable | Variable

## Slide 9: References
FCC 10-174
IEEE P802.11af Draft 1.0