## Slide 1
Slide 1
Identification Signal for Fixed devices
Date: 2011-03-16
Authors:

## Slide 2: Abstract
In this presentation, an identification signal mechanism for a fixed STA is proposed to meet the commission requirement.

## Slide 3: Comments
Comments
  Comment number 519, 576 and 922 ask that a transmission of identifying information from a fixed device needs to be specified
Proposed Resolution
  Agree technical comments 519, 576 and 922 based on this discussion and editorial instructions in 11/403r0

## Slide 4: FCC requirements (§ 15.711(d) )
Fixed TVBD
  Fixed TVBDs shall transmit identifying information
Identification signal
  The identification signal must conform to a standard established by a recognized industry standards setting organization
  The identification signal shall carry sufficient information to identify the device and its geographic coordinates

## Slide 5: Fixed STA operation
Device operation
  A fixed STA is a registered STA that broadcasts its registered location its identifying information, which is sufficient to identify the device and its registered location, and in some regulatory domains is restricted from enabling other STAs

## Slide 6: Fixed STA operation
Device operation
  A fixed STA shall transmit identifying information in a Beacon frame, Probe Response frame or Public Action frame.
  In US, the identifying information should include FCC identification number (FCC ID), device serial number and device location of fixed STA, which are identical with the information provided in the process of Channel Query.

## Slide 7: Identifying information of fixed STA
Identifying information in 802.11af may include:
  Country-Specific
  Device Identification Info (E.3.1.2)
    FCC ID
    Device Serial Number
  Device Location Info (E.3.1.3)

## Slide 8: Identifying information of fixed STA
Proposed Information Element Format
 | Element ID | Length | Device Identification Information | Device Location Information
Octets: | 1 | 1 | Variable | Variable

## Slide 9: References
FCC 10-174
IEEE P802.11af Draft 1.0