## Slide 1: Use Case Characteristics Discussion
Date: 2011-03-15
Authors:

## Slide 2: Abstract
Discussion of concepts to be used to differentiate use case requirements. In the r0 form of this slide set the names of those characteristics had not yet been determined.

## Slide 3
Note: Need to define or rename high, medium, low.
High = hard to achieve
Low = easy to achieve

## Slide 4: xxx1
Xxx1 is the number of STAs attempting to establish for the first time a link to an AP within an ESS as measured over a one second time interval.
  High: more than 50
  Medium: 10 to 49
  Low: less than 10
Link Attempt Rate 
Rate of STA Entry
Rate of initial link request

## Slide 5: xxx2
Xxx2 is the “busyness” of the wireless medium of the ESS. It is measured as the percentage of time the medium is in use.
  High: More than 50%
  Medium: 10 to 50%
  Low: Less than 10%
Media usage
Channel usage

## Slide 6: xxx3
xxx3 is the time the STA is within the range of an AP within an ESS. This time is the maximum available time for establishing a link and exchanging data.
  High: less than 1 second
  Medium: between 1 and 10 seconds
  Low: more than 10 seconds
STA dwell time
Time Envelope
Available time

## Slide 7: xxx4
Xxx4 is the amount time required to establish for the first time a link to an AP within an ESS. This includes the time for AP/Network discovery and (secure) Association and Authentication
  High: less than 100 ms
  Medium between 100 ms and 2 seconds
  Low: more than 2 seconds
NOTE:
  “link”, “association”, authentication are defined as per 802.11
  We need to agree when to start measuring this time interval (e.g. when the STA enters the coverage of the ESS, etc.)
Link Set-Up Latency
Link Set-Up Time

## Slide 8: xxx5
Xxx5 is the time required by the use case for application information exchange. In order to make the use case work, Xxx5 must be smaller than xxx3 – xxx4 .
  High:
  Medium:
  Low:
Application Time

## Slide 9: References