IEEE P802.11
Wireless LANs

| Enablement procedure for TVWS band |
| --- |
| Date: 2011-04-20 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Padam Kafle | Nokia | 6021 Connection Drive, Irving, TX, 75039 | +1-214-673-6232 | Padam.kafle@nokia.com |
| Mika Kasslin | Nokia | Itämerenkatu 11-13, 00180 Helsinki, Finland | +358-50-4836294 | Mika.kasslin@nokia.com |
| Prabodh Varshney | Nokia | 6021 Connection Drive, Irving, TX, 75039 | +1 469 9512745 | Prabodh.varshney@nokia.com |
| Santosh Abraham | Qualcomm Inc | 5775 Morehouse Dr., San Diego, CA | +1-858 651 6107 | sabraham@qualcomm.com |
| Steve Shellhammer | Qualcomm Inc | 5775 Morehouse Dr., San Diego, CA | +1-858-658-1874 | sshellha@qualcomm.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

Discussion:

In the current 802.11af draft specification D1.0, DSE enablement procedure has been used as a basis for operational control in TVWS band. The DSE procedures specified in Clause 10.12 of the 802.11 baseline specification has been introduced by 802.11y amendment for the operation in 3650-3700 MHz band in US. Although the TVWS band operation also requires operational control of dependent stations, there are many differences in regulatory requirements between TVWS band operation and 3650 MHz band. Hence, the DSE enablement procedures specified in current clause 10.12 of the baseline specification and some changes added from .11af D1.0 have caused difficulty interpreting which of the requirements and procedures are applicable for stations to operate in TVWS band (in particular, FCC 10-174 regulatory requirements).

The network initiation and operational rules for TV band white space devices are controlled by information received from an authorized geo-location database. Hence, it is important to simplify the procedures for network entry and operation. Several comments listed below have asked for clarification or simplification of behaviours expected by stations in TVWS band when operating under the control of an authorized geo-location database. The description and rules proposed by editing instructions in this document address these comments.

| CID | Clause Number(C) | Page(C) | Line(C) | Comment | Proposed Change |
| --- | --- | --- | --- | --- | --- |
| 492 | 8.4.5.1 | 38 | 6-10 | DSE enablement element does not need WSM information in its response. The available channel map is already sent as the response during channel availability query procedure. It will be better idea to decouple channel availability from DSE enablement procedure. | Remove the field. |
| 503 | 10.12.2 | 57 | 13 | DSE enablement and deenablement procedures are not necessary for TVWS band operation, as per the currently available regulations. All that is sufficient is to hear an enabling signal transmitted by an AP before starting any transmissions by client STAs in TVWS band, and continue receiving contact verification signal once a client STA receives available channel map. | Since the "dependent STA" and "Enabling STA" are used in relation to Enabling signal, these terms can still be useful. However, remove the requirements of DSE enablement procedure for a dependent STA while operating in TVWS band. DSE procedures as specified in Clause 10.12 are strictly applicable only for 3650-3700 MHz band operation. There are many conflicting procedures not required in TVWS band. |
| 505 | 10.12.5 | 58 | 26 | The rules specified for dependent STA operation with DSE in this clause in baseline are tailored to 3650-3700 MHz band operation. Many of these rules are not required in TVWS band. The requirements to keep up with listening Enabling signal once every 60 s, and also contact verification signal once every 60 s will be two orthogonal requirements, that adds complexity to dependent STAs in TVWS band. | Either move these details to band specific clauses in Annex, and only provide rules that are necessary for TVWS operation. The DSE procedure for TVWS should be much simpler, and should relate to getting available channel list at the beginning and contact verification signal there after. Suggest to remove legacy procedures from .11y. |
| 512 | E.2.4.1 | 131 | 36-41 | Looks like there are too many classifications of devices for specifying their behaviors in TVWS band, which seems unnecessary. Enabling STA and dependent STA to relate to FCC specific device categories (Fixed, Mode II and Mode I) should be sufficient. 802.11 already has AP STA and non-AP STAs for Master and Client roles, respectively. | suggest to remove "Master STA", "Client STA" and "Registered STA". |
| 528 | 10.12 | 56 | 35- | Definitions of each terminologies (i.e. registered/unregistered STA, enabling STA, dependent STA, fixed STA and dependent AP) are confusing and missing. Description on the operations of registered STA, dependent STA and enabling STA is confusing and is not sufficient. Some operations are missing. | Add the definitions and clarify the operations. |
| 982 | 8.4.5.1 | 38 |  | The DSE Enablement element has same function with the Channel Availability Query element, while the Channel Availability Query element may optionally provide Device Location Information. There's no need to have duplicated elements defined for the same purpose. | Remove the clause. |

Proposed Resolution:

Agree with technical comments 492, 503, 505, 512, 528 and 982 based on the discussion and editorial instructions in document 11/0414r3.

| CID | Clause Number(C) | Page(C) | Line(C) | Comment | Proposed Change |
| --- | --- | --- | --- | --- | --- |
| 162 |  | 58 | 44 | " An enabled dependent STA shall cease transmission within dot11DSERenewalTime (in seconds) if it has not received an enabling signal". It seems that an enabling signal serves the purpose of contact verification. However, Contact Verification is mandatory in Annex E. | need clarificaiton. |
| 322 | 10.12.2 | 57 | 13 | DSE enablement and deenablement procedures are not necessary for TVWS band operation, as per the currently available regulations. All that is sufficient is to hear an enabling signal transmitted by an AP before starting any transmissions by client STAs in TVWS band, and continue receiving contact verification signal once a client STA receives available channel map. | Remove DSE enablement |
| 510 | E.2.4.1 | 131 | 14-15 | The dependent AP term has been used throughout the specification without clear definition or description of its behaviors and requirements. Does the dependent AP only need to hear "Enabling Signal" before its initial transmission, or does it need to undergo DSE Enablement procedure as required by an ordinary dependent STA? Is it a master STA or can it be Client of another Enabling STA is not clear either. | Clarify. The dependent AP has to operate like normal dependent STA in 3650-3700 MHz band as such operation is allowed within the DSE service area created by a single Enabling STA. Similar concept does not seem to apply to FCC's rules on TVWS band. Hence, dependent AP term may not be required here, or its requirements should be clearly stated. |
| 513 | E.2.4.1 | 131 | 57 | "dot11LCIDSERequired" is required to be set "true" for the Fixed or personal/portable AP-STAs as they need to have their LCI information. However, for TVWS operation, it is not required for Client STAs. | Clarify. Suggest to separate dot11DSERequired for dependent STA and dot11LCIDSERequired for Enabling STAs. |
| 529 | 10.12 | 57 | 54 | Definition and behavior of enabling signal are not clear. In page 57, L54, it is said that "the enabling signal is not a Public Action frame, and it not relayed." However, in page 132, L 1-2, "enabling signal is received directly from an enabling STA or a dependent AP,". When it is transmitted from a dependent AP, does it mean that the dependent STA can enable other dependent STA or the enabling signal is relayed? | Clarification is needed.. |
| 553 | 10.12 | 56 | 35- | Definitions of each terminologies, registered/unregistered STA, enabling STA, dependent STA, fixed STA and dependent AP are confusing and missing. Description on the operation of registered STA, dependent STA and enabling STA is confusing and is not sufficient. Some of operations are missing. | Clariy and specify. |
| 578 | 10.12 | 56 | 35- | Definitions of each terminologies, registered/unregistered STA, enabling STA, dependent STA, fixed STA and dependent AP are confusing and missing. Description on the operation of registered STA, dependent STA and enabling STA is confusing and is not sufficient. Some of operations are missing. | Clarify and specify. |
| 579 | 10.12 | 57 | 54 | Definition and behavior of enabling signal are not clear. In page 57, L54, it is said that "the enabling signal is not a Public Action frame, and it not relayed." However, in page 132, L 1-2, "enabling signal is received directly from an enabling STA or a dependent AP,". When it is transmitted from a dependent AP, does it mean that the dependent STA can enable other dependent STA or the enabling signal is relayed? | Clarify. |
| 580 | 10.12.6.1 | 59 | 15-19 | Enabling signal definition described in this sub-clause should be replaced as "inband enabling signal" with appropriate definition. | Clarify. |

Proposed Resolution:

Agree in principle with technical comments 162, 322, 510, 513, 529, 553, 578, 579, 580 based on the discussion and editorial instructions in document 11/0414r3.

## Editing instructions:

3.3 Abbreviations and acronyms

TGaf Editor: Insert the following new acronyms in alphabetical order in page 2:

GDB	Geolocation Database

GDC 	Geolocation database Control

TGaf Editor: Insert the following new subclause before Clause 4:

### 3.2.1 Definitions specific to IEEE 802.11 operation in some regulatory domains

### authorized geolocation database (AGDB): an authorized geolocation database whose operation provides frequencies and transmit power limits in accordance with applicable regulations.

8. Frame formats

8.4 Management frame body components

8.4.5 Registered Location Query Protocol elements

8.4.5.4 RLQP Channel Availability Query element

TGaf Editor: Change the Table 8-191 as follows:

Table 8-191—Reason Result Code field values

| Reason Result Code field value | Description |
| --- | --- |
| 0 | Reserved |
| 1 | Channel Availability List requested |
| 2 | Reserved |
| 3 | Success with the Available Channel List result |
| 4 | Request declined |
| 5 | Request not successful because of Device ID verification failure |
| 6 | Request not successful as one or more parameters have invalid values |
| 7 | Handshake timeout Authorization Deenabled |
| 8-255 | Reserved |

10 MLME

TGaf Editor: Change the title of subclause 10.30 as follows:

#### 10.30 Regulatory Domain Operation Operation under the control of a Geolocation Database

10.30.1 General

TGaf Editor: delete 10.30.1 and insert the following text:

In some regulatory domains, regulatory provisions for the use of the frequencies are enforced under the control of an AGDB before stations are permitted to transmit. Some stations may be able to contact an AGDB to obtain the permissible frequencies and operating parameters before they can begin their transmissions. Such stations may operate as geolocation database controlled (GDC) enabling stations, which must provide their identification, geolocation and other information to the AGDB as specified by regulatory authorities. Other stations, that are not capable to access an AGDB on their own, are permitted to transmit when enabled by a GDC enabling station. Such stations operate as GDC dependent stations.

This clause describes procedures for stations when they are operating under the control of an AGDB to satisfy regulatory requirements. For operation under such restrictions, GDC dependent STAs operate according to the control procedures of a GDC enabling STA that enables their operation.

STAs shall use the GDC procedures defined in this subclause if dot11GDCRequired is true. A summary of STA’s roles with their MIB attributes are shown in Table 10-12 (GDC STA attributes).

Table 10-12: GDC STA attributes

| Role of STAs | dot11AGDBAccessActivated |
| --- | --- |
| GDC enabling STA | True |
| GDC dependent STA | False |

A GDC enabling STA is an STA that is able to access an AGDB and obtain the information about the permitted frequencies and other information for the use in its location. A GDC enabling STA may transmit a GDC enabling signal and may enable operations of GDC dependent STAs.

A GDC dependent STA is a STA that transmits under the control of a GDC enabling STA.

The GDC enablement procedure for GDC dependent STAs, and operating rules for GDC enabling and GDC dependent STA are defined in the following subclauses.

TGaf Editor: Insert the following two subclauses before 10.30.2 (White Space Map):

10.30.2 GDC enabling STA operation

In some regulatory domains, such as licensed bands and shared bands where unlicensed operation is permitted, unlicensed devices are required to operate only on frequencies given by an AGDB. The GDC enabling STA is allowed to give permission for operation of GDC dependent STAs by transmitting GDC enabling signals after it has accessed an AGDB.

A GDC STA shall set dot11AGDBAccessActivated to true after it obtains permissible frequencies and other operating parameters valid for its location from an AGDB.

A GDC enabling STA may be an AP or a non-AP STA.

A GDC enabling STA may transmit a GDC enabling signal in the band using an available frequency to indicate that it offers network service.

The GDC enabling signal is a beacon frame containing a Geodatabase Inband Enabling Signal element. Transmissions of any frames by a GDC dependent STA is conditional upon receiving such an enabling signal directly over the air from a GDC enabling STA.

NOTE—After receiving a GDC enabling signal, a GDC STA that is authorized to form a network may communicate via the enabling STA to contact the AGDB using the available communication link. Once such a STA sends its identification, geolocation and other necessary information to the AGDB and obtains permissible frequencies and other operating parameters for its own use, it can set the dot11AGDBAccessActivated to true. Such a GDC STA is no longer required to remain dependent to the GDC enabling STA, and may operate as GDC enabling STA.

Upon receipt of either of:

1. a public action or protected dual of public action Channel Availability Query (CAQ) frame

2. a GAS Initial Request frame containing a RLQP CAQ element in the Query Request field,

the GDC enabling STA provides a response using a procedure specified in 10.30.6 (CAQ Procedures). In some regulatory domains, the GDC enabling station may be required to have secure authentication or association with the GDC dependent STA before it can send the response to the CAQ request. If required, the GDC enabling STA may contact an AGDB to verify that the requesting GDC dependent STA is authorized to operate in the frequency band.

In some regulatory domains, a GDC enabling STA transmits a contact verification signal to each GDC dependent STA it enabled using procedures defined in 10.30.5 (Contact Verification Signal).

A GDC enabling STA may issue an unsolicited CAQ response with a reason result code Authorization Deenabled to request a GDC dependent STA to cease its transmissions and change its GDC enablement state to unenabled.

An enabling STA may transmit a white space map (WSM) within a Beacon frame, Probe Response frame or White Space Map Announcement frame, as defined in 10.30.4 (White Space Map).

A GDC enabling STA may issue a CPM announcement frame to any of its GDC dependent STAs to request radio operation changed in frequency, channel bandwidth, and/or constrained maximum transmit power, along with other operational parameters.

A GDC enabling STA upon receiving a CSM request frame may respond with a CSM response frame or a GAS Initial Response frame containing a RLQP CSM element to provide schedule information in frequency or channel as defined in 10.12 (Channel Schedule Management).

Upon receiving a Network Channel Control request or a GAS Initial Request frame containing a RLQP Network Channel Control element, a GDC enabling STA issues a Network Channel Control response frame or a GAS Initial Response frame containing a RLQP Network Channel Control element to the dependent STA that requested network channel control following the procedure defined in 10.14.7 (Network Channel Control).

A GDC enabling STA may issue a Operation Channel Status Query to any of its GDC dependent STAs with the Operation Channel Status Query/Response Type field value of the Operation Channel Status Query/Response of the Operation Channel Status Query/Response Public Action Frame, set to 0, to receive a Operation Channel Status Response that identifies the operation channel status of the queried GDC dependent STA.

10.30.3 GDC dependent STA operation

A GDC dependent STA shall set dot11AGDBAccessActivated to false.

A GDC dependent STA is configured with a GDC enablement state variable that may be set to one of the following three states: Unenabled, AttemptingEnablement or Enabled. A GDC dependent STA begins operation by setting its GDC enablement state variable to unenabled, and operate in receive only mode in the band, passively scanning channels for an enabling signal from a GDC enabling STA.

A typical state machine implementation of GDC dependent STA operation with GDC is provided in Figure 10-27 (GDC dependent STA state transition diagram).

A STA with dot11AGDBAccessActivated shall not transmit any frames unless it has received a Beacon frame containing a Geodatabase Inband Enabling Signal element (8.4.2.110) from a GDC enabling STA. The GDC dependent STA shall change its GDC enablement state variable to AttemptingEnablement before it attempts any transmission.

Figure 10-27: GDC dependent STA state transition diagram

A GDC dependent STA that is able to receive a valid enabling signal, but has not been enabled by a GDC enabling STA shall not transmit, except to perform GDC enablement with the GDC enabling STA transmitting the enabling signal, unless such action is mandated to be allowed in the regulatory domain (e.g., emergency services). Before attempting GDC enablement with any one GDC enabling STA, a GDC dependent STA may have detected several GDC enabling STAs, may attempt GDC enablement with one and fail, and then attempt GDC enablement with another.

Before a GDC dependent STA is allowed to start its normal data transmissions in the frequency band, it must obtain the permissible frequencies and other parameters from a GDC enabling STA by performing the following GDC enablement procedure:

- If required by the regulatory domain, the GDC dependent STA shall complete the secure authentication or association using the procedures defined in 10.3 (STA authentication and association).

- The GDC dependent STA sends one of the following:

1. a public action or protected dual of public action CAQ frame

2. a GAS Initial Request frame containing a RLQP CAQ element in the Query Request field as defined in 10.30.6 (CAQ Procedures).

- Based on the input information received from a requesting GDC dependent STA, a GDC enabling STA sends the response to the CAQ request that may authorize the dependent STA to be enabled in the permissible frequencies and other parameters.

- When a GDC dependent STA receives one of the following:

1.   a public action or protected dual of public action CAQ frame

2.   a GAS Initial Response or GAS Comeback Response frame containing a RLQP CAQ element,

from the GDC enabling STA with a reason result code 3 (Success with Available Channel List result) within dot11GDCEnablementTimeLimit, the GDC enablement state variable of the GDC dependent STA is set to enabled. The CAQ Success with Available Channel List response includes WSM information, which indicates the list of available channels in the regulatory domain, as defined in subclauses 10.30.4 (White Space Map) and 10.30.6 (CAQ Procedures).

A GDC dependent STA that has not attained GDC enablement from a GDC enabling STA shall not transmit beyond dot11GDCEnablementTimeLimit (in seconds), measured from the time of the first PHY-TXSTART.request primitive, while attempting to attain GDC enablement. Then, when the GDC enablement attempts fail within the allowed maximum time, it shall not transmit for dot11GDCEnablementFailHoldTime (in seconds), before it can again attempt to attain GDC enablement.

Once in GDC enabled state, the following rules apply to a GDC dependent STA during its operations:

- A GDC dependent STA shall cease all transmissions within dot11ContactVerificationSignalInterval (in seconds) if it has not received a valid Contact verification signal from the same GDC enabling STA that has provided it with the authorized channel list for operation. It then changes its GDC enablement state to unenabled. The procedures for Contact verification signal transmission and reception are defined in 10.30.5 (Contact Verification Signal)

- A GDC dependent STA shall immediately cease all transmission if it receives a CAQ response with a reason result code of Authorization Deenabled from the GDC enabling STA that enabled its operation.

- A GDC dependent STA receiving a channel power management action frame or a GAS Initial Request frame containing a RLQP channel power management element from the GDC enabling STA that enabled its operation or a channel power management element from the AP with which it is associated performs the channel power management procedures (see 10.11 (Channel Power Management (CPM))).

- Before its initial operation, a GDC dependent STA may send a Network Channel Control request frame or a GAS Initial Request frame containing a RLQP Network Channel Control element to the enabling STA that enabled its operation. Upon receipt of the response from the enabling STA, it shall operate using the network channel control procedure defined in 10.14.7 (Network Channel Control).

- A GDC dependent STA returns a Operation Channel Status Response in response to a Operation Channel Status Query, if the request is received from the AP with which it is associated or the GDC enabling STA, from which it is enabled, with a Operation Channel Status Query/Response Public Action Frame, with the Operation Channel Status Query/Response Type field value set to 1, with the Operating Class and the Channel Number fields indentifying the STA's operation channel(s), and with the Constrained Maximum Transmit Power field(s) giving the maximum transmit power allowed on the STA's operation channel(s).

Annex E (normative) Country elements and operating classes

E.2 Band-specific operating requirements

E.2.5 TVWS band in the United States (54 MHz to 698 MHz)

E.2.5.1 General

TGaf Editor: change the sixth paragraph in page 138 as follows:

STAs shall have the following elements set to “true”

- dot11LCIDSEGDCRequired,

- dot11OperatingClassesRequired,

- dot11SpectrumManagementRequired,

- dot11MultiDomainCapabilityActivated,

- dot11ChannelPowerManagementActivated,

- dot11ContactVerificationSignalActivated.

TGaf Editor: change the last paragraph in this subclause and Table E-5 in page 139 as follows:

APs shall set the value of dot11DSETransmitDivisor to 256 000, non-AP STAs shall set the value of dot11DSETransmitDivisor to 256. All GDC dependent STAs shall set the other dot11GDCDSE timer values as shown in Table E-5 (TVWS DSE GDC timer limits).

Table E-5—TVWS GDC DSE timer limits

| Parameter | Seconds |
| --- | --- |
| dot11DSEGDCEnablementTimeLimit | 32 |
| dot11DSEGDCEnablementFailHoldTime | 512 |
| dot11DSERenewalTime dot11ContactVerificationSignalInterval | 60 |

Annex C

(normative)

ASN.1 encoding of the MAC and PHY MIB

C.3 MIB Detail

TGaf Editor: Insert the following entries at the end of dot11StationConfigEntry sequence List:

dot11GDCRequired 			TruthValue,

dot11AGDBAccessActivated		TruthValue,

dot11GDCEnablementTimeLimit		Unsigned32,

dot11GDCEnablementFailHoldTime 	Unsigned32,

TGaf Editor: Insert the following elements after dot11WSSTAType in Annex C as shown:

dot11GDCRequired OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME.

This attribute, when true, indicates that the STA is a geolocation database controlled STA, and operates under the control of a GDB using the GDC procedures.”

DEFVAL { FALSE }

::= { dot11StationConfigEntry <ANA> }

dot11AGDBAccessActivated OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME.

Changes take effect as soon as practical in the implementation.

This attribute, when true, indicates that the STA has obtained permissible frequencies and other operating parameters valid for its location from an authorized geolocation database, otherwise this is set to false.”

DEFVAL { FALSE }

::= { dot11StationConfigEntry <ANA> }

dot11GDCEnablementTimeLimit OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME when the device is initialized.

Changes take effect as soon as practical in the implementation.

dot11GDCEnablementTimeLimit indicates the maximum number of seconds that a GDC dependent STA may transmit in a frequency band under the control of a geolocation database while attaining GDC enablement with a GDC enabling STA. Unless another value is mandated by regulatory authorities, the value is 32 seconds."

DEFVAL { 32 }

::= { dot11LCIDSEEntry <ANA> }

dot11GDCEnablementFailHoldTime OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a control variable.

It is written by the SME when the device is initialized.

Changes take effect as soon as practical in the implementation.

dot11GDCEnablementFailHoldTime indicates the number of seconds that a GDC dependent STA must not transmit in a frequency band under control of a geolocation database when it fails to attain GDC enablement with an GDC enabling STA within dot11GDCEnablementTimeLimit seconds. Unless another value is mandated by regulatory authorities, the value is 512 seconds."

DEFVAL { 512 }

::= { dot11LCIDSEEntry <ANA>}

# Text boxes

Abstract

This submission proposes simplification to enablement procedure for TVWS band.

This document is based on IEEE 802.11afD1.01.

Submission addresses the following CIDs received during the first WG letter ballot on 802.11af D1.0:    162, 322, 492, 503, 505, 510, 512, 513, 528, 529, 553, 578, 579, 580, and 982.