IEEE P802.11
Wireless LANs

| Resolution to CID 2285 |
| --- |
| Date: 2011-03-16 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Guido R. Hiertz | Philips | Riedel Communications GmbH & Co. KG, Uellendahler Str. 353, 42109 Wuppertal, Federal Republic of Germany | +49-202-292-9987 | hiertz@ieee.org |
| Dee Denteneeer | Philips | HTC 37; 5656 AE Eindhoven; The Netherlands | +31 40 27 49743 | Dee.Denteneer@philips.com |

Abstract

This document provides resolution to the comment with CID 2285. The latter asks for clarification about the relation between the ESS and MBSS concept.

5.2.3.1 Extended service set (ESS): The large coverage network

The DS and BSSs allow IEEE Std 802.11 to create a wireless network of arbitrary size and complexity. IEEE Std 802.11 refers to this type of network as the ESS network. An ESS is the union of the infrastructure BSSs connected by a DS. The ESS does not include the DS.

The key concept is that the ESS network appears the same to an LLC layer as an IBSS network. STAs within an ESS may communicate and mobile STAs may move from one BSS to another (within the same ESS) transparently to LLC.

Owing to its distributed nature, a mesh BSS (MBSS) has no central entity like the AP of an infrastructure BSS. Thus, an MBSS cannot be further unified and the ESS concept does not apply to the MBSS therefore.

Nothing is assumed by IEEE Std 802.11 about the relative physical locations of the BSSs in Figure 5-3. All of the following are possible: […]

References:

IEEE Std 802.11-2007