IEEE P802.11
Wireless LANs

| Normative Text for Multiple BSSID |
| --- |
| Date: 2011-03-31 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Yongho Seok | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1-dong, Dongan-gu, Anyang-shi, Korea | +82-31-450-1947 | yongho.seok@lge.com |
| Illsoo Sohn | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1-dong, Dongan-gu, Anyang-shi, Korea | +82-31-450-1882 | illsoo.sohn@lge.com |

Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGac Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGac Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGac Editor:  Editing instructions preceded by “TGac Editor” are instructions to the TGac editor to modify existing material in the TGac draft.   As a result of adopting the changes, the TGac editor will execute the instructions rather than copy them to the TGac Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

Comment on Multiple BSSID:

| 1033 | Seok, Yongho | 7.3.2.46 | 28 | 44 | TR | (Refer to IEEE802.11v D3.0) Non-transmitted BSSID Profile needs to include VHT Capabilities and VHT Operation elements. | Include VHT Capabilities and VHT Operation elements in Non-transmitted BSSID Profile. |
| --- | --- | --- | --- | --- | --- | --- | --- |

Proposed Resolution:

Agree in principle to support the Multiple BSSID of VHT STA as described in Draft P802.11ac_D0.1 comments 1033. Also agree to following editing instructions below.

## Editing instructions:

#### 7.3.2.46 Multiple BSSID element

TGac editor: Change the paragraph defining Non-Transmitted BSSID Profile subelement as follows:

The Non-Transmitted BSSID Profile subelement contains a list of elements for one or more APs which have non-transmitted BSSIDs, and is defined as follows:

— For each non-transmitted BSSID, the Non-transmitted BSSID Capability element (see 7.3.2.67) is the first element included, followed by a variable number of information elements, in the order defined in Table 7-8.

— The SSID and Multiple BSSID-Index subelements are included in the Non-Transmitted BSSID Profile subelement.

— The FBMS Descriptor element is included in the Non-Transmitted BSSID Profile subelement if the Multiple BSSID element is included in a Beacon frame and if the TIM field indicates there are buffered multicast frames for this non-transmitted BSSID.

— The Timestamp and Beacon Interval fields, DS Parameter Set, FH Parameter Set, IBSS Parameter Set, Country, FH Parameters, FH Pattern Table, Channel Switch Assignment, Extended Channel Switch Announcement, Wide Bandwidth Channel Switch, VHT Transmit Power Envelope, Supported Regulatory Classes, IBSS DFS, ERP Information, HT Capabilities, and HT Operation elements, VHT Capabilities and VHT Operation elements are not included in the Non-Transmitted BSSID Profile field; the values of these elements for each non-transmitted BSSID are always the same as the corresponding transmitted BSSID element values.

# Text boxes

Abstract

This document is a normative text proposal for supporting multiple BSSIDs of VHT STA.