IEEE P802.11
Wireless LANs

## TGah Channel Models

Date: April 3, 2011

Authors:

Jim Lansford

CSR, plc; e-Mail: jim.lansford@csr.com

Abstract

This document provides the channel models to be used for the Sub-1GHz Task Group (TGah).

List of Participants

| Jim Lansford (CSR) |  |
| --- | --- |

## Revision History

| Date | Version | Description of changes |
| --- | --- | --- |
| 3-April-11 | 0.1 | Initial strawman |

# 1. Introduction

This document describes channel models for Sub-1GHz bands that will be used as a basis to evaluate proposals for submissions to a Draft Standard.  The channel models address use cases for 802.11ah as approved by the Task Group; the approved use cases may change over time, and this document will be modified to reflect the current use case document.

The PAR and 5C for 802.11ah has a broad scope which encompasses an extensive set of potential channel models.  Quoting Section 5.2 of the PAR [1]:

This amendment defines an Orthogonal Frequency Division Multiplexing (OFDM) Physical layer (PHY) operating in the license-exempt bands below 1 GHz, e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan),  314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA), and enhancements to the IEEE 802.11 Medium Access Control (MAC) to support this PHY, and provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g.

The data rates defined in this amendment optimize the rate vs range performance of the specific channelization in a given band.

This amendment also adds support for:

- transmission range up to 1 km

- data rates > 100 kbit/s

while maintaining the 802.11 WLAN user experience for fixed, outdoor, point to multi point applications.

# 2. Use Cases

The following documents refer to submissions that address the approved use cases:

## 2.1 Sensors and Meters

| Use case | Submission | Description |
| --- | --- | --- |
| 1a | 11/17r5 | Smart Grid - Meter to Pole |
| 1c | 11/253 | Environmental/Agricultural Monitoring |
| 1d | 11/260r1 | Industrial process sensors |
| 1e | 11/17r5 | Healthcare |
| 1f | 11/241r0 | Healthcare |
| 1g | 11/241r0 | Home/Building Automation |
| 1h | 11/242r0 | Home sensors |

## 2.2 Backhaul Sensor/Meter data

| Use case | Submission | Description |
| --- | --- | --- |
| 2a | 11/14r2 | Backhaul aggregation of sensors |
| 2b | 11/260r1 | Backhaul aggregation of industrial sensors |

## 2.3 Extended range Wi-Fi

| Use case | Submission | Description |
| --- | --- | --- |
| 3a | 11/243r0 | Outdoor extended range hotspot |
| 3b | 11/244r1 | Wi-Fi for cellular traffic offloading |

# 3.0 Channel models

[Note: This section will be rewritten as channel model submissions are incorporated and the process evolves toward a final channel modeling document that will be ratified by TGah.]

The use cases for 802.11ah are very broad, and encompass both indoor and outdoor usage.  Outdoor usage can be at a wide variety of antenna heights both for the AP and STA (assuming infrastructure mode, although ad hoc mode is not precluded).  Indoor usage can be both industrial and residential; one of the advantages of operation at frequencies below 1GHz is the potential for good propagation through walls, floors, and ceilings, and the channel models will take this into account.  Mobility is limited in use cases ratified through March 2011; velocities no greater than pedestrian speed are expected, so Doppler shifts should take this into account.  Obviously, both line of sight (LOS) and non-line of sight (NLOS) paths can be expected, and channel models will take both of these into account.  Finally, it is also within scope to consider MIMO systems in the frequency bands, so models that address extensions of the 802.11n channel models [2] to Sub-1GHz frequency bands is entirely appropriate and encouraged.  Similarly, existing 3GPP2 models developed for LTE may be appropriate for some frequency bands within the scope of 802.11ah.  Interference effects

## 3.1 Frequency bands

The scope of the PAR for 802.11ah allows for many different frequency bands to be considered for inclusion, spanning from 314-928MHz.

## 3.2 Outdoor usage

Channel models for outdoor usage, such as meter to pole (Use Case 1a) should take into account antenna heights, and urban/suburban/rural terrain, such as addressed by Hata-Okumura and Bertoni-Walfisch models.

## 3.3 Indoor usage

Channel models for communication between indoor devices, such as industrial process sensors (Use Case 1d) or home sensors (Use Case 1h) are often based on empirical or semi-empirical modeling of attenuation versus distance, often piecewise linear, and may include walls as well as variance bands to indicate expected variations from the mean.  While ray tracing techniques can be very useful in predicting performance in a specific location, it poses difficulty in allowing comparison between competing proposals when used as a tool in downselection, and would only be appropriate if all proposals evaluated the same environment.

Indoor models for 802.11 systems in other frequency bands are mature [2], and submissions to augment these channel models with Sub-1GHz band models are encouraged.

## 3.4 Combined indoor/outdoor usage

Some use cases, such as backhaul (Use Case 2a/2b) or cellular offloading (Use Case 3b) involve communication between indoor devices and outdoor infrastructure (or vice versa).  Channel models for these types of use cases could be covered by extensions to models such as those described above in Sections 3.2 and 3.3.

# 4.0 Channel models for TGah use cases

[Note: This section will be updated to reflect models for each use case, and modified as use cases are added or removed.  Clearly, some of these use cases will have exactly the same channel model as others, so “Same as Use Case x.x” will be expected.]

## 4.1 Channel models for Use Case 1 – Sensors and Meters

### 4.1 a) Smart Grid - Meter to Pole

4.1 b) [undefined use case]

### 4.1 c) Environmental/Agricultural Monitoring

### 4.1 d) Industrial process sensors

### 4.1 e) Healthcare

### 4.1 f) Healthcare

### 4.1 g) Home/Building Automation

### 4.1 h) Home Sensors

## 4.2 Channel models for Use Case 2 – Backhaul Sensor/Meter Data

### 4.2 a) Backhaul aggregation of sensors

### 4.2 b) Backhaul aggregation of industrial sensors

## 4.3 Channel models for Use Case 3 – Extended Range Wi-Fi

### 4.3 a) Outdoor extended range hotspot

### 4.3 b) Wi-Fi for cellular traffic offloading

# Appendices

References

[1]  PAR and 5C for 802.11ah: https://mentor.ieee.org/802.11/dcn/10/11-10-0001-13-0wng-900mhz-par-and-5c.doc

[2] 802.11n Channel Models: https://mentor.ieee.org/802.11/dcn/03/11-03-0940-04-000n-tgn-channel-models.doc

[3]