## Slide 1: Proposed resolutions for WSM type comments
Date: 2011-04-05

## Slide 2: Abstract
This presentation shows proposed resolutions for comments 35, 36, 37, 178, 593, 594,705, which are asking for clear explanation and wording.

## Slide 3: Comments
CID | Page (C) | Line (C) | Clause | Comment | Proposed Change
35 | 29 | 24 | 8.4.2.af1 | The WSM Type field is defined on P29L45, there is no need duplicate its definition. | Remove "If a WSM Type field is set to 1, the following WSM Information field corresponds to a TV band WSM."
36 | 29 | 46 | 8.4.2.af1 | Usage of TV band WSM value is poorly worded. | Change "When a STA accesses TV band database to get the available channels in TVWS, TV band WSM is used." to "The WSM Type field is set to 'TV band WSM' when a STA accesses a TVWS database to get list of the available channels."
37 | 30 | 4 | 8.4.2.af1.1 | "A WSM Type in the WSM element may indicate TV band WSM" only may indicate? Does that mean 'TV band WSM' can be used but with a different encoding of the WSM Information field? | Clarify
178 | 136 | 58 | E.3.1.5 | The WSM Type has to be set to 1 (and not to 0) if the WSM Information contains TV Band WSM. | Change "0" to "1"
593 | 29 | 23-24 | 8.4.2.af1 | The sentence "If a WSM Type field is set to 1, the following WSM Information field corresponds to a TV band WSM." doesn't seem to be necessary/appropriate. | Remove the sentence.

## Slide 4: Comments
CID | Page (C) | Line (C) | Clause | Comment | Proposed Change
594 | 29 | 45-49 | 8.4.2.af1 | Wordsmithing | Change the paragraph to read: "The WSM Type field is set to a number that identifies a type of WSM Information indicates the frequency band where the following WSM Information field is applicable. The values of WSM Types are shown in Table 8-42af1 (WSM Type definition). When a STA accesses TV band database to get the available channels in TVWS, TV band WSM is used. WSM Types for other regulatory domain database reserved. When set to '1', it indicates the WSM Information field of the WSM element contains the available channel list for the operation in the TVWS. Other values are reserved."
705 | 29 | 58 | 8.4.2.af1 | Does WSM Type 1 refer to a TV band database or specifically to a US (United States) TV band database. Should "Reserved" refer to other "regulatory domain databases" or other "regulatory domain TV band databases." The distinction is not clear. | Please clarify the name "TV Band WSM" in Table 8-42af1

## Slide 5: Proposed Resolutions
Agree CID 35, 36, 37, 178, 593, 594
Agree in Principle CID 705

## Slide 6: Comment Resolutions text
TGaf editor: Change the text in 8.4.2.af1 as follows:
The WSM Type field is set to a number that identifies a type of WSM Information. The values of WSM Types are shown in Table 8-42af1 (WSM Type definition). When a STA accesses TV band database to get the available channels in TVWS, TV band WSM is used. If a WSM Type field is set to 1, the following WSM Information field corresponds to a TV band WSM. The format of the WSM Information is determined by the value of WSM Type. WSM Types for other regulatory domain database are reserved.
The WSM Type field is set to a number that identifies a type of WSM Information indicates the frequency band where the following WSM Information field is applicable. The values of WSM Types are shown in Table 8-42af1 (WSM Type definition). The WSM Type field is set to 'TV band WSM' when a STA accesses a TVWS database to get list of the available channels. When set to '1', it indicates the WSM Information field of the WSM element contains the available channel list for the operation in the TVWS. Other values are reserved.

## Slide 7: Comment Resolutions text
TGaf editor: Remove the sub-clause 8.3.4.2.af1:
8.3.4.2.af1.1 TV band WSM
A WSM Type in the WSM element may indicate TV band WSM. The WSM Information field corresponding to a TV band WSM is shown in Table E-af2 (WSM Information field format for a TV band WSM).

## Slide 8: Comment Resolutions text
TGaf editor: Change sub-clause E.3.1 as follows:
E.3 TLV Values
E.3.1 WSM Information Values
The format of the WSM Information and values are shown in Table E-af2. If the value of WSM Type is set to 0 1,