IEEE P802.11
Wireless LANs

| Target Only and PERR Comments (RFI) |
| --- |
| Date: 2011-04-06 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6 80200 München, Germany |  | bahr ed siemens dod com |

Resolved Comments:

Principle: 3071, 3120, 3121, 3122, 3123, 3124, 3126

Instruction to Editor: Change the paragraphs on the Per Target Flags field in clause 7.3.2.113 “PREQ element” as indicated by the WinWord change marks.

7.3.2.113 PREQ element

[…]

The format of the Per Target Flags field is shown in Figure 7-95o158 (Per Target Flags field format).

| B0 | B1 | B2 | B3 B7 |
| --- | --- | --- | --- |
| TO | Reserved | USN | Reserved |
| Bits: 1 | 1 | 1 | 5 |
| Per Target Flags field format |

The Per Target Flags field is set as follows:

- Bit 0: TO (Target Only) subfield: The TO subfield defines which mesh STA responds with a PREP element to the PREQ element containing an individual target address. If TO = 1, only the target mesh STA responds with an individually addressed PREP. If TO = 0, intermediate mesh STAs with active forwarding information to the target mesh STA also respond.

- Bit 1: Reserved.

- Bit 2: USN (Unknown Target HWMP Sequence Number) subfield: The USN subfield indicates whether the Target HWMP Sequence Number field of the corresponding target is interpreted as HWMP sequence number (USN = 0) or not (USN = 1), the latter meaning that a target HWMP sequence number is unknown at the originator mesh STA.

- Bit 3–7: Reserved.

[…]

Instruction to Editor: Change clause 11C.9.3 “On-demand path selection mode” as indicated by the WinWord change marks.

11C.9.3 On-demand path selection mode

If a source mesh STA needs to find a path to a destination mesh STA using the on-demand path selection mode, it broadcasts a PREQ with the path target specified in the list of targets and the metric field initialized to the initial value of the active path selection metric.

When a mesh STA receives a new PREQ, it creates or updates its path information to the originator mesh STA and propagates the PREQ to its neighbor peer mesh STAs if the PREQ contains a greater HWMP sequence number, or the HWMP sequence number is the same as the current path and the PREQ offers a better metric than the current path. Each mesh STA may receive multiple copies of the same PREQ that originated at the originator mesh STA, each PREQ traversing a unique path.

Whenever a mesh STA propagates a PREQ, the metric field in the PREQ is updated to reflect the cumulative metric of the path to the originator mesh STA. After creating or updating a path to the originator mesh STA, the target mesh STA sends an individually addressed PREP back to the originator mesh STA.

If the mesh STA that received a PREQ is the target mesh STA, it sends an individually addressed PREP back to the originator mesh STA after creating or updating a path to the originator mesh STA.

The PREQ provides the TO (Target Only) subfield that allows path selection to take advantage of existing paths to the target mesh STA by allowing an intermediate mesh STA to return a PREP to the originator mesh STA. If the TO (Target Only) subfield is 1, only the target mesh STA responds with a PREP. The effect of setting the TO (Target Only) subfield to 0 is the quick establishment of a path using the PREP generated by an intermediate mesh STA, allowing the forwarding of MSDUs with a low path selection delay. In order to select (or validate) the best path during the path selection procedure, the intermediate mesh STA that responded with a PREP propagates the PREQ with the TO (Target Only) subfield set to 1. This prevents all other intermediate mesh STAs on the way to the target from sending a PREP.

Intermediate mesh STAs create a path to the target mesh STA on receiving the PREP, and also forward the PREP toward the originator. When the originator receives the PREP, it creates a path to the target mesh STA. If the target mesh STA receives further PREQs with a better metric, then the target updates its path to the originator with the new path and also sends a new PREP to the originator along the updated path. A bidirectional, best metric end-to-end path is established between the originator and target mesh STA.

Instruction to Editor: Change clause 11C.9.9.3 “Conditions for generating and sending a PREQ” as indicated by the WinWord change marks.

11C.9.9.3 Conditions for generating and sending a PREQ

A mesh STA shall send a PREQ element in an HWMP Mesh Path Selection frame, as defined in 7.4.15.3 (HWMP Mesh Path Selection frame format), in the following cases:

Case A: Path Discovery (Original Transmission)

All of the following applies:

- The mesh STA needs to establish an on-demand path to one or more targets for which there is no ongoing path discovery initiated by this mesh STA.

- The mesh STA has not sent a PREQ element for the target mesh STAs less than dot11MeshHWMPpreqMinInterval TUs ago. If this is the case, the transmission of the PREQ has to be postponed until this condition becomes true.

- The mesh STA has not made more than (dot11MeshHWMPmaxPREQretries – 1) repeated attempts at path discovery towards the target of the PREQ.

The content of a PREQ element in Case A shall be as shown in Table 11C-9 (Content of a PREQ element in Case A).

| Content of a PREQ element in Case A |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | 26 + N11 (if Bit 6 (AE subfield) in the Flags field = 0) 32 + N11 (if Bit 6 (AE subfield) in the Flags field = 1) |
| Flags | Bit 0: 0 (gate role not applicable) Bit 1: 0 (group addressed) Bit 2: 0 (no proactive PREP applicable) Bit 3–5: Reserved Bit 6: Address Extension (AE) (1 – if external address present, 0 – otherwise) Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element, e.g., dot11MeshHWMPnetDiameter. |
| Path Discovery ID | New unique Path Discovery ID, for instance, previous Path Discovery ID + 1 |
| Originator Mesh STA Address | MAC address of the path originator |
| Originator HWMP Sequence Number | Previous Originator HWMP SN + 1. See 11C.9.8.6 (Limiting the rate of HWMP sequence number increments) |
| Originator External Address | Present only if Bit 6 in Flags field = 1. This value is set to the external address, which is the source address of the MSDU (from outside the mesh BSS) that triggered the path discovery at the originator. |
| Lifetime | The time for which mesh STAs receiving the PREQ consider the forwarding information to be valid, e.g., dot11MeshHWMPactivePathTimeout. |
| Metric | Initial value of active path selection metric |
| Target Count | N (N ≥(CID238) 1) |
| Per Target | Per Target Flags | Bit 0 (TO): dot11MeshHWMPtargetOnly Bit 1: Reserved Bit 2 (USN): 0 if forwarding information for Target Address with valid HWMP sequence number exists, 1 otherwise Bit 3–7: Reserved |
|  | Target Address | MAC address of requested target |
|  | Target HWMP Sequence Number | If Per Target Flags Bit 2 (USN) is 0, the latest HWMP sequence number stored by the originator mesh STA for the target mesh STA from the forwarding information (see 11C.9.8.4 (Forwarding information)). Otherwise, reserved. |

Case B: Path Maintenance (Original Transmission) (optional)

All of the following applies:

- The mesh STA has a path to a given target mesh STA that is not a root mesh STA

- The last PREQ to this target was sent dot11MeshHWMPmaintenanceInterval TUs (or more) ago

The content of a PREQ in Case B shall be as shown in Table 11C-10 (Content of a PREQ element in Case B).

| Content of a PREQ element in Case B |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | 26 + N11 |
| Flags | Bit 0: 0 (gate role not applicable) Bit 1: 0 (group addressed) Bit 2: 0 (no proactive PREP applicable) Bit 3–5: Reserved Bit 6: 0 (no address extension) Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element, e.g., dot11MeshHWMPnetDiameter |
| Path Discovery ID | New unique Path Discovery ID, for instance, previous Path Discovery ID + 1 |
| Originator Mesh STA Address | MAC address of the originator of the PREQ |
| Originator HWMP Sequence Number | Originator HWMP SN + 1. See 11C.9.8.6 (Limiting the rate of HWMP sequence number increments) |
| Originator External Address | Field not present |
| Lifetime | The time for which mesh STAs receiving the PREQ consider the forwarding information to be valid, e.g., dot11MeshHWMPactivePathTimeout. |
| Metric | Initial value of active path selection metric |
| Target Count | N (N ≥(CID238) 1) |
| Per Target | Per Target Flags | Bit 0 (TO): 1 (target only) Bit 1: Reserved Bit 2 (USN): 0 Bit 3–7: Reserved |
|  | Target Address | MAC Address of target mesh STA |
|  | Target HWMP Sequence Number | The latest HWMP sequence number for this target known to the originator mesh STA. |

Case C: Proactive PREQ (original transmission)

All of the following applies:

- The root mesh STA is configured as root mesh STA using proactive PREQs ([dot11MeshHWMProotMode = proactivePREQnoPREP(2)] OR [dot11MeshHWMProotMode = proactivePREQwithPREP(3)]).

- The root mesh STA sent its previous proactive PREQ dot11MeshHWMProotInterval TUs ago.

The contents of a PREQ in Case C shall be as shown in Table 11C-11 (Contents of a PREQ in Case C).

| Contents of a PREQ in Case C |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | 37 |
| Flags | Bit 0: set to 1 if dot11MeshGateAnnouncementProtocol is true, set to 0 otherwise. (mesh gate role) Bit 1: 0 (group addressed) Bit 2: 0 if dot11MeshHWMProotMode = proactivePREQnoPREP(2), 1 if dot11MeshHWMProotMode = proactivePREQwithPREP(3) (proactive PREP) Bit 3–5: Reserved Bit 6: 0 (no address extension) Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element, e.g., dot11MeshHWMPnetDiameter. |
| Path Discovery ID | New unique Path Discovery ID, for instance, previous Path Discovery ID + 1 |
| Originator Mesh STA Address | MAC address of the root mesh STA |
| Originator HWMP Sequence Number | Originator HWMP SN + 1. See 11C.9.8.6 (Limiting the rate of HWMP sequence number increments) |
| Originator External Address | Field not present |
| Lifetime | dot11MeshHWMPactivePathToRootTimeout |
| Metric | Initial value of active path selection metric |
| Target Count | 1 |
| Per Target | Per Target Flags | Bit 0 (TO): 1 Bit 1: Reserved Bit 2 (USN): 1 Bit 3–7: Reserved |
|  | Target Address | Broadcast address |
|  | Target HWMP Sequence Number | 0 |

Case D: Root Path Confirmation (Original Transmission)

One of the following applies:

- The mesh STA has received a RANN and the metric (RANN metricmetric to the transmitter of the RANN) is better than the metric to the root in the current forwarding information.

- The mesh STA has a path to a root mesh STA and the last PREQ to the root mesh STA was sent dot11MeshHWMPconfirmationInterval TUs (or more) ago.

The content of a PREQ element in Case D shall be as shown in Table 11C-12 (Content of a PREQ element in Case D).

| Content of a PREQ element in Case D |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | As required |
| Flags | Bit 0: 0 (gate role not applicable) Bit 1: 1 (individually addressed) Bit 2: 0 (no proactive PREP applicable) Bit 3–5: Reserved Bit 6: 0 (no address extension) Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element, e.g., dot11MeshHWMPnetDiameter |
| Path Discovery ID | Not used |
| Originator Mesh STA Address | MAC address of the originator mesh STA |
| Originator HWMP Sequence Number | Originator HWMP SN + 1. See 11C.9.8.6 (Limiting the rate of HWMP sequence number increments) |
| Originator External Address | Field not present |
| Lifetime | The time for which mesh STAs receiving the PREQ consider the forwarding information to be valid, e.g., dot11MeshHWMPactivePathToRootTimeout. |
| Metric | Initial value of active path selection metric |
| Target Count | 1 |
| Per Target | Per Target Flags | Bit 0 (TO): 1 Bit 1: Reserved Bit 2 (USN): 0 Bit 3–7: Reserved |
|  | Target Address | Root mesh STA MAC Address |
|  | Target HWMP Sequence Number | The latest HWMP sequence number for this target known to the originator mesh STA |

Case E: PREQ Propagation

Case E1 (target count = 1, no PREP generation as intermediate mesh STA):

All of the following applies:

- The mesh STA has received and accepted a PREQ—see 11C.9.9.4.2 (Acceptance criteria)

- dot11MeshForwarding is true

- [The active forwarding information for the Originator Mesh STA was created or updated according to the rules defined in 11C.9.8.4 (Forwarding information)] 
OR 
[{the Originator HWMP Sequence Number of the accepted PREQ = HWMP sequence number in the forwarding information for this originator mesh STA} AND {the mesh STA has not previously received a PREQ with the same Originator Mesh STA Address and the same Path Discovery ID}]

- The Element TTL field is greater than 1—see 11C.9.8.2 (HWMP propagation)

- Target Count = 1

- [The mesh STA is not the target of the PREQ] 
OR 
[the target of the PREQ is the MAC broadcast address (all ones)]

- the mesh STA is not the proxy of the target address

- [The TO (Target Only) subfield of the target in the PREQ is set (TO = 1)] 
OR
[{The TO (Target Only) subfield of the target in the PREQ is not set (TO = 0)} AND {mesh STA has no active forwarding information for the requested target}]

The content of a PREQ element in Case E1 shall be as shown in Table 11C-13 (Content of a PREQ element in Case E1).

| Content of a PREQ element in Case E1 |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | As received |
| Flags | As received |
| Hop Count | As received + 1 |
| Element TTL | As received – 1 |
| Path Discovery ID | As received |
| Originator Mesh STA Address | As received |
| Originator HWMP Sequence Number | As received |
| Originator External Address | As received. This field is only present if Bit 6 of the Flags field (AE subfield) is 1. |
| Lifetime | As received |
| Metric | As receivedown metric toward transmitter of received PREQ |
| Target Count | 1 |
| Per Target | Per Target Flags | As received |
|  | Target MAC Address | As received |
|  | Target HWMP Sequence Number | As received |

Case E2 (target count = 1, PREP generation as intermediate mesh STA):

All of the following applies:

- The mesh STA has received and accepted a PREQ—see 11C.9.9.4.2 (Acceptance criteria)

- dot11MeshForwarding is true

- [The active forwarding information for the Originator Mesh STA was created or updated according to the rules defined in 11C.9.8.4 (Forwarding information)] 
OR 
[{the Originator HWMP Sequence Number of the accepted PREQ = HWMP sequence number in the forwarding information for this originator mesh STA} AND {the mesh STA has not previously received a PREQ with the same Originator Mesh STA Address and the same Path Discovery ID}]

- The Element TTL field is greater than 1—see 11C.9.8.2 (HWMP propagation)

- Target Count = 1

- The mesh STA is not the target of the PREQ

- The mesh STA is not the proxy of the target address

- [The TO (Target Only) subfield of the target in the PREQ is not set (TO = 0)] 
AND 
[mesh STA has active forwarding information for the requested target]

The contents of a PREQ element in Case E2 shall be as shown in Table 11C-14 (Contents of a PREQ element in Case E2).

| Contents of a PREQ element in Case E2 |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | As received |
| Flags | As received |
| Hop Count | As received + 1 |
| Element TTL | As received – 1 |
| Path Discovery ID | As received |
| Originator Mesh STA Address | As received |
| Originator HWMP Sequence Number | As received |
| Originator External Address | As received. This field is only present if Bit 6 of the Flags field (AE subfield) is 1. |
| Lifetime | As received |
| Metric | As receivedown metric toward transmitter of received PREQ |
| Target Count | 1 |
| Per Target | Per Target Flags | Bit 0 (TO): 1 (target only because mesh STA sent a PREP) Bit 1: Reserved Bit 2 (USN): As received Bit 3–7: Reserved |
|  | Target MAC Address | As received |
|  | Target HWMP Sequence Number | As received |

Case E3 (target count > 1):

All of the following applies:

- The mesh STA has received and accepted a PREQ—see 11C.9.9.4.2 (Acceptance criteria)

- dot11MeshForwarding is true

- [The active forwarding information for the Originator Mesh STA was created or updated according to the rules defined in 11C.9.8.4 (Forwarding information)] 
OR 
[{the Originator HWMP Sequence Number of the accepted PREQ = HWMP sequence number in the forwarding information for this originator mesh STA} AND {the mesh STA has not previously received a PREQ with the same Originator Mesh STA Address and the same Path Discovery ID}]

- The Element TTL field is greater than 1—see 11C.9.8.2 (HWMP propagation)

- Target Count > 1

- There is at least one requested target that is neither the recipient MAC address nor an external MAC address proxied by the recipient

The contents of a PREQ element in Case E3 shall be as shown in Table 11C-15 (Contents of a PREQ element in Case E3).

| Contents of a PREQ element in Case E3 |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREQ element |
| Length | 26 + N  11 |
| Flags | As received |
| Hop Count | As received + 1 |
| Element TTL | As received – 1 |
| Path Discovery ID | As received |
| Originator Mesh STA Address | As received |
| Originator HWMP Sequence Number | As received |
| Originator External Address | As received. This field is only present if Bit 6 of the Flags field (AE subfield) is set to 1. |
| Lifetime | As received |
| Metric | As receivedown metric toward the transmitter of the received PREQ |
| Target Count | 1  target count  received target count received target count less the number of requested destinations, for which the processing mesh STA — is the target mesh STA or — is the target proxy mesh gate |
| Per Target #A | Per Target Flags #A | As received |
|  | Target MAC Address #A | As received |
|  | Target HWMP Sequence Number #A | As received |
| Per Target #B | Per Target Flags #B | Bit 0 (TO): 1 (target only because mesh STA sent PREP) Bit 1: As received Bit 2 (USN): As received Bit 3–7: As received |
|  | Target MAC Address #B | As received |
|  | Target HWMP Sequence Number #B | As received |

For the per target fields (Per Target Flags, Target Address, Target HWMP Sequence Number) assume the following:

- Target #A: If target A would have been the only requested target, it would generate a PREQ for propagation according to case E1.

- Target #B: If target B would have been the only requested target, it would generate a PREQ for propagation according to case E2.

Instruction to Editor: Change clause 11C.9.9.4.3 “Effect of receipt” as indicated by the WinWord change marks.

11C.9.9.4.3 Effect of receipt

A mesh STA receiving a PREQ according to the acceptance criteria in 11C.9.9.4.2 (Acceptance criteria) shall record the Path Discovery ID and the Originator Mesh STA Address. The receiving mesh STA shall create or update the active forwarding information it maintains for the originator mesh STA of the PREQ according to the rules defined in 11C.9.8.4 (Forwarding information).

If the active forwarding information for the Originator Mesh STA was created or updated according to the rules defined in 11C.9.8.4 (Forwarding information) or if the Target HWMP sequence number of the PREQ is the same as the HWMP sequence number in the forwarding information for the Target Mesh STA and there has been no record of the Originator Mesh STA and Path Discovery ID, the following applies:

- If the mesh STA is the target of the PREQ or is the proxy of the target MAC address it shall initiate the transmission of a PREP to the originator mesh STA (11C.9.10.3 (Conditions for generating and sending a PREP) Case A). If the PREQ carries an external address (indicated by the AE subfield in the Flags field), the mesh STA shall update its proxy information with the Originator External Address as external address, the PREQ Originator Mesh STA Address as the corresponding proxy, and for the proxy lifetime the longer one of the value of the PREQ Lifetime field and the proxy lifetime if the proxy information already exists (see also 11C.10.4.3 (Proxy update (PXU))).

- If step a) was not applicable for the mesh STA and the AE subfield in the Flags field in the PREQ is 1, the mesh STA may update its proxy information with the Originator External Address as external address, the PREQ Originator Mesh STA Address as the corresponding proxy, and for the proxy lifetime the longer one of the value of the PREQ Lifetime field and the proxy lifetime if the proxy information already exists (see also 11C.10.4.3 (Proxy update (PXU))).

- If the mesh STA has valid forwarding information to any of the requested targets and the TO (Target Only) subfield for such a target is not set (TO = 0), it initiates the transmission of a PREP for each of these targets (see 11C.9.10.3 (Conditions for generating and sending a PREP) Case C).

- If the mesh STA is initiating a PREP transmission on behalf of another target according to step c) (intermediate reply), it shall process all of the following:

- Update the precursor list in its forwarding information for the target mesh STA with the next hop from the forwarding information of the originator mesh STA.

- Update the lifetime for this precursor that is the longer one of the lifetime of the forwarding information of the target mesh STA.

- Update the lifetime of the precursor list entry in case it already exists.

- Update the precursor list in its forwarding information for the originator mesh STA with the next hop toward the target mesh STA.

- Update the lifetime for this precursor that is the longer one of the lifetime of the forwarding information of the originator mesh STA.

- Update the lifetime of the precursor list entry in case it already exists.

- If the received PREQ is a proactive PREQ [target address is set to all ones, TO subfield is set (TO = 1)], the mesh STA generates a proactive PREP to the root mesh STA (see 11C.9.10.3 (Conditions for generating and sending a PREP) Case D) depending on the setting of the Proactive PREP subfield. If the Proactive PREP subfield is 1, a proactive PREP is generated, if it is 0, a proactive PREP is generated only if a bidirectional path to the root mesh STA is required (see Annex Y.6 (Generation of proactive PREPs in proactive PREQ mechanism of HWMP)).

f)	If there are individually addressed targets in the PREQ that have not been processed in step a) or that have been processed in step c) or in step e), the receiving mesh STA shall propagate the PREQ as defined in 11C.9.9.3 (Conditions for generating and sending a PREQ) Case E.

Instruction to Editor: Change Cases C and D in clause 11C.9.10.3 “Conditions for generating and sending a PREP” as indicated by the WinWord change marks.

11C.9.10.3 Conditions for generating and sending a PREP

[…]

Case C: Intermediate reply

A PREP is transmitted if the mesh STA has received a PREQ fulfilling all of the following conditions:

- The TO (Target Only) subfield in the corresponding Per Target Flags field in the PREQ is not set (TO = 0)

- The receiving mesh STA has active forwarding information with:

- A destination that is the same as the Target Address of the PREQ

- An HWMP sequence number that is greater than or equal to the Target HWMP sequence number of the PREQ

- A non-zero lifetime

The content of the generated PREP in Case C shall be as shown in Table 11C-18 (Contents of a PREP element in Case C).

| Contents of a PREP element in Case C |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREP element |
| Length | 31 |
| Flags | Bit 0–5: Reserved Bit 6: Address Extension (AE): 0 Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element |
| Target Mesh STA Address | Target MAC address from the PREQ |
| Target HWMP Sequence Number | HWMP sequence number of the stored forwarding information of the Target of the PREQ |
| Target External Address | Not present |
| Lifetime | As per the PREQ that triggered the transmission of this PREP |
| Metric | Value of path metric taken from the active forwarding information for the target address of the PREQ |
| Originator Mesh STA Address | MAC address of the originator mesh STA |
| Originator HWMP Sequence Number | HWMP Sequence number of the originator mesh STA |

Case D:	Proactive PREP in Proactive PREQ mode

One of the following applies:

- The mesh STA has received a proactive PREQ with the Proactive PREP subfield set to 0 AND the mesh STA needs to establish or update a bidirectional path to the root mesh STA.

- The mesh STA has received a proactive PREQ with the Proactive PREP subfield set to 1.

Note, a proactive PREQ is a PREQ with a Target Address set to all ones and its TO subfield set (TO = 1).

The content of the generated PREP in Case D shall be as shown in Table 11C-19 (Contents of a PREP element in Case D).

| Contents of a PREP element in Case D |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PREP element |
| Length | 31 |
| Flags | Bit 0-5: Reserved Bit 6: Address Extension (AE): 0 Bit 7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element |
| Target Mesh STA Address | MAC address of the mesh STA |
| Target HWMP Sequence Number | HWMP sequence number of the mesh STA |
| Target External Address | Not present |
| Lifetime | Lifetime of the PREQ that triggered the transmission of this PREP |
| Metric | Initial value of active path selection metric |
| Originator Mesh STA Address | MAC address of the root mesh STA (originator mesh STA of the PREQ) |
| Originator HWMP Sequence Number | HWMP sequence number of the root mesh STA (originator HWMP sequence number of the PREQ) |

Instruction to Editor: Change Case B and Case D in clause 11C.9.11.3 “Conditions for generating and sending a PERR” as indicated by the WinWord change marks.

11C.9.11.3 Conditions for generating and sending a PERR

[…]

Case B: Original transmission (missing forwarding information)

The mesh STA has not sent a PERR element less than dot11MeshHWMPperrMinInterval TUs ago and one of the following applies:

- The mesh STA receives an individually addressed frame with a destination address not matching its own MAC address for which it has no forwarding information.

- The mesh STA receives an individually addressed frame with a destination address not matching its own MAC address and dot11MeshForwarding is false.

The contents of a PERR element in Case B shall be as shown in Table 11C-21 (Contents of a PERR element in Case B).

| Contents of a PERR element in Case B |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PERR element. |
| Length | 2 + N  13 |
| Element TTL | The maximum number of hops the element is propagated before being discarded. |
| Number of Destinations | Number of announced destinations with missing forwarding information in the PERR. |
| Flags #1 | Bit 0–5: Reserved Bit 6 (AE): 0 Bit 7: Reserved |
| Destination Address #1 | MAC address of destination with missing forwarding information #1. This is Address 3 of the received individually addressed frame. |
| HWMP Sequence Number #1 | Reserved (0) |
| Reason Code #1 | “MESH-PATH-ERROR-NO-FORWARDING-INFORMATION” (see 7.3.1.7 (Reason Code field)). |
| ... | ... |

[…]

Case D: PERR propagation

The mesh STA has not sent a PERR element less than dot11MeshHWMPperrMinInterval TUs ago and all of the following applies:

- The mesh STA received a PERR from a neighbor peer mesh STA.

- A destination in the PERR is the same as one of the destinations in the active forwarding information of the mesh STA where the next hop is the transmitter of the received PERR, and the forwarding information or the proxy information has been invalidated according to conditions in 11C.9.11.4.3 (Effect of receipt) case b), case c), or case d).

- dot11MeshForwarding is true.

- The Element TTL field in the received PERR element is greater than 1.

The contents of a PERR element in Case D shall be as shown in Table 11C-23 (Contents of a PERR element in Case D).

| Contents of a PERR element in Case D |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the PERR element |
| Length | if AE subfield = 0: 2 + N  13 if AE subfield = 1: 2 + N  19 |
| Element TTL | Element TTL in received PERR element – 1 |
| Number of Destinations | 1  number of destinations in the PERR  received value Received number of destinations less the number of received destinations for which the transmitter of the PERR is not the next hop |
| Flags #1 | As received |
| Destination Address #1 | MAC address of unreachable destination #1, as received |
| HWMP Sequence Number #1 | If Reason Code #1 = “MESH-PATH-ERROR-NO-FORWARDING-INFORMATION” and received value = 0, then HWMP sequence number for Destination Address #1 from the forwarding information after the increment of 11C.9.11.4.3 (Effect of receipt) step b). Otherwise, as received. |
| Destination External Address #1 | As received This field is only present if Bit 6 (AE subfield) of the Flags field #1 is 1. |
| Reason Code #1 | As received |
| ... | ... |

Instruction to Editor: Change clause 11C.9.11.4.3 “Effect of receipt” as indicated by the WinWord change marks.

11C.9.11.4.3 Effect of receipt

The following applies only to a PERR element that was accepted according to the acceptance criteria in 11C.9.11.4.2 (Acceptance criteria):

- The mesh STA creates a list of unreachable destinations consisting of those destinations from the received PERR for which the next hop in the local active forwarding information is the transmitter of the PERR. Step b) through step e) are applied to the destinations in this list.

- If the Reason Code is “MESH-PATH-ERROR-NO-FORWARDING-INFORMATION” and the HWMP Sequence Number is 0, the receiving mesh STA increments the HWMP sequence number in the forwarding information of the listed unreachable destination by 1 and invalidates the forwarding information.

- If the Reason Code is “MESH-PATH-ERROR-NO-FORWARDING-INFORMATION” and the HWMP Sequence Number is 0 or the Reason Code is “MESH-PATH-ERROR-DESTINATION-UNREACHABLE” and the received HWMP sequence number for a listed unreachable destination is higher than the current HWMP sequence number in the forwarding information for that destination, the receiving mesh STA shall consider that destination unreachable and shall set the HWMP sequence number in the forwarding information to the HWMP sequence number received in the PERR and shall invalidate the forwarding information associated with this unreachable destination.

- If the the Reason Code is “MESH-PATH-ERROR-NO-PROXY-INFORMATION”, the receiving mesh STA shall consider the corresponding Destination External Address unreachable and shall invalidate the proxy information associated with this unreachable external destination (proxy mesh gate is the Destination Address of the PERR, external MAC address is the Destination External Address of the PERR).

- A PERR element is propagated according to the conditions defined in 11C.9.11.3 (Conditions for generating and sending a PERR) Case D “PERR propagation.”

Instruction to Editor: Change clause 11C.9.12.3 “Conditions for generating and sending a RANN” as indicated by the WinWord change marks.

11C.9.12.3 Conditions for generating and sending a RANN

A mesh STA sends out a RANN element in an HWMP Mesh Path Selection frame, as defined in 7.4.15.3 (HWMP Mesh Path Selection frame format), in the following cases:

Case A: Original transmission

All of the following conditions apply:

- The mesh STA is configured as a root mesh STA using the proactive RANN mechanism (dot11MeshHWMProotMode = rann(4)).

- The root mesh STA sent its previous RANN dot11MeshHWMPrannInterval TUs ago.

The contents of a RANN element in Case A shall be as shown in Table 11C-24 (Contents of a RANN element in Case A).

| Contents of a RANN element in Case A |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the RANN element |
| Length | 21 |
| Flags | Bit 0: set to 1 if dot11MeshGateAnnouncementProtocol is true, set to 0 otherwise. Bit 1–7: Reserved |
| Hop Count | 0 |
| Element TTL | Maximum number of hops allowed for this element |
| Root Mesh STA Address | MAC address of the root mesh STA |
| HWMP Sequence Number | Last used HWMP sequence number of the root mesh STA + 1 |
| Interval | dot11MeshHWMPrannInterval |
| Metric | Initial value of active path selection metric |

Case B: Propagation

All of the following conditions apply:

- The mesh STA has valid forwarding information to a root mesh STA using the proactive RANN mechanism (dot11MeshHWMProotMode = rann(4))

- The mesh STA sent its previous RANN dot11MeshHWMPrannInterval TUs ago

- dot11MeshForwarding is true

- The Element TTL field is greater than 1—see 11C.9.8.2 (HWMP propagation)

The contents of a RANN element in Case B shall be as shown in Table 11C-25 (Contents of a RANN element in Case B).

| Contents of a RANN element in Case B |
| --- |
| Field | Value |
| Element ID | Value given in Table 7-26 (Element IDs) for the RANN element |
| Length | As received |
| Flags | As received |
| Hop Count | As received + 1 |
| Element TTL | As received – 1 |
| Root Mesh STA Address | As received |
| HWMP Sequence Number | As received |
| Interval | As received |
| Metric | As receivedown link metric toward the transmitting mesh STA |

Instruction to Editor: Change clause 11C.9.13 “Considerations for support of STAs without mesh functionality” as indicated by the WinWord change marks.

11C.9.13 Considerations for support of STAs without mesh functionality

The verification, by the AP collocated with the mesh STA, of disjunct MAC addresses between a non-AP STA without mesh functionality and mesh STAs during authentication/association of the non-AP STA without mesh functionality (see 11.3.3 (Additional mechanisms for an AP collocated with one or more mesh STA(s))) may be done by issuing a PREQ for the MAC address of the non-AP STA without mesh functionality by the mesh STA collocated with the AP. The TO (Target Only) subfield of the Per Target Flags field of the PREQ shall be set to 1.

The MAC address of the non-AP STA already exists in the MBSS if the AP with mesh functionality receives a PREP for the MAC address of the non-AP STA and it can be derived from the PREP that the requested MAC address is originated from a mesh STA. (The AE subfield of the Flags field of the PREP is set to 0, see 7.3.2.114 (PREP element).)

References:

IEEE 802.11s WLAN Mesh Networking, Draft Standard D10.0, March 2011

# Text boxes

Abstract

This submission proposes resolutions to some sponsor ballot comments related to the Target Only flag and the PathError element. Some cleanup is also done as well as a few editorial things.