IEEE P802.11
Wireless LANs

| Mesh STA broadcst transmission rule remedy proposal |
| --- |
| Date: 2011-04-14 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6 80200 München, Germany |  | bahr ed siemens dod com |

## Summary of the intention of this document

- Make use of efficient TXOP for group addressed frames transmitted by mesh STAs.
Particularly, allow multiple frames transmission without backoff among MPDUs belong to the same AC, bounded by the TXOP limit.

- This suggested change resolves comments (see below) from previous ballots.

Comment:

Backoff after every single group addressed frame transmission sounds like very heavy and resource consuming operation. Is the backoff really needed after every transmitted group addressed frame? In mesh BSS, it is very likely that there are many small size broadcast traffic, regardless of management or data, and it could be useful to have more efficient delivery scheme.

Proposed change:

Please consider the possibility to transmit multiple group addressed frames in the same EDCA TXOP as in infrasrtucture network. Mesh operation can be more efficient than IBSS. Also, random backoff does not help minimizing collisions in a hidden node scenario.

## Suggested changes to the draft spec

Apply the following changes.
Corresponding changes to D10.0 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor. Please update the part indicated by the “Track Changes” only.

- HCF

- HCF contention-based channel access (EDCA)

- EDCA TXOPs

Change the sixth paragraph in 9.9.1.2 as follows:

It should be noted, that when transmitting multiple frames in a TXOP using acknowledgment mechanisms other than Normal Ack, a protective mechanism should be used (such as RTS/CTS or the protection mechanism described in 9.13 (Protection mechanisms)). A QoS AP or a mesh STA may send group addressed frames without using any protection mechanism. In a QoS IBSS, group addressed frames shall be sent one at a time, and backoff shall be performed after the transmission of each of the group addressed frames. In an MBSS, a mesh STA may send multiple group addressed frames in a TXOP without performing backoff once the TXOP is obtained, and bounded by the TXOP limit.

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D10.0, March 2011.

# Text boxes

Abstract

This document provides suggested resolution to CID XXXX.