## Slide 1: Discussion for 11ah Functional Requirements
Date: 2011-04-11
Authors:

## Slide 2: Abstract
This submission is a preliminary submission for discussions on the functional requirements for TGah.

## Slide 3: Revisit 11ah PAR&5C
5.2 Scope of Proposed Standard:
  an Orthogonal Frequency Division Multiplexing (OFDM) Physical layer (PHY) operating in the license-exempt bands below 1 GHz, e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA)
  and enhancements to the IEEE 802.11 Medium Access Control (MAC) to support this PHY, and provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g.
  The data rates defined in this amendment optimize the rate vs. range performance of the specific channelization in a given band.
  This amendment also adds support for:
    transmission range up to 1 km
    data rates > 100 kbit/s
  while maintaining the 802.11 WLAN user experience for fixed, outdoor, point-to-multi point applications.

## Slide 4: Revisit 11ah PAR&5C (2)
5.4 Purpose of Proposed Standard:
  The purpose of this amendment defines operation of license-exempt 802.11 wireless networks in frequency bands below 1 GHz excluding the TV White Space bands.
5.5 Need for the Project:
  Equipment ships today that utilize the IEEE 802.11 protocols in frequency bands below 1 GHz, primarily used in outdoor applications. However, the IEEE 802.11 standard does not specify channel width and center frequencies for these bands. This amendment will establish standard channel widths and center frequencies for OFDM PHY operations below 1 GHz. The changes primarily will be done in new regulatory classes (requiring extending annex I and J of IEEE 802.11-2007).

## Slide 5: Revisit 11ah PAR&5C (3)
17.5.2 Compatibility
  IEEE 802 defines a family of standards. All standards shall be in conformance with the IEEE 802.1 Architecture, Management, and Interworking documents as follows: 802 Overview and Architecture, 802.1D, 802.1Q, and parts of 802.1f. If any variances in conformance emerge, they shall be thoroughly disclosed and reviewed with 802.
  Each standard in the IEEE 802 family of standards shall include a definition of managed objects that are compatible with systems management standards.
  Compatibility with IEEE 802 requirements will result from keeping the MAC SAP interface the same as for the existing 802.11 standard. The proposed amendment shall introduce no 802.1 architectural changes. The MAC SAP definition shall not be altered, ensuring that all LLC and MAC interfaces are compatible to and in conformance with the IEEE 802.1 Architecture, Management and Internetworking standards. New managed objects shall be defined as necessary in a format and structure consistent with existing 802.11 managed objects.

## Slide 6: Revisit 11ah PAR&5C (4)
17.5.4 Technical Feasibility
  For a project to be authorized, it shall be able to show its technical feasibility. At a minimum, the proposed project shall show:
  a) Demonstrated system feasibility. Equipment that utilizes IEEE 802.11 OFDM radio modulations running at 20 MHz, 10 MHz and 5 MHz are in use today in the 902-928 MHz ISM band.

## Slide 7: Revisit 11ah PAR&5C (5)
17.5.4.1 Coexistence of 802 wireless standards specifying devices for unlicensed operation
  A working group proposing a wireless project is required to demonstrate coexistence through the preparation of a Coexistence Assurance (CA) document unless it is not applicable. The Working Group will create a CA document as part of the WG balloting process. If the Working Group elects not to create a CA document, it will explain to the EC the reason the CA document is not applicable.
  The working group will create a CA document and specifically reference IEEE P802.15.4g as part of the WG balloting process

## Slide 8: Revisit 11ah Use Cases
Use Case 1 : Sensors and meters
  1a: 11/17r5, slide 7 Smart Grid - Meter to Pole
  1c: 11/253, Environmental/Agricultural Monitoring
  1d: 11/260r1, slid 4 Industrial process sensors
  1e: 11/17r5, slid 17 Healthcare
  1f: 11/241r0, slide 3 Healthcare
  1g: 11/241r0, slid 5 Home/Building Automation
  1h: 11/242r0, slid 2 Home sensors
Use Case 2 : Backhaul Sensor and meter data
  2a: 11/14r2, slide 5 Backhaul aggregation of sensors
  2b: 11/260r1, slide 4 Backhaul aggregation of industrial sensors
Use Case 3 : Extended range Wi-Fi
  3a: 11/243r0 Outdoor extended range hotspot
  3b: 11/244r1 Outdoor Wi-Fi for cellular traffic offloading

## Slide 9: Revisit 11ah Use Cases (2)
Data rate (aggregated)
  100Kbps(others), <1Mbps(1d), <10Mbps(3a), <20Mbps(3b)
STA/AP capacity
  6000(1a), 300(1c), 500(1d), 100(1g), <50(others)
Other features
  Stronger Reliability (1d) : PER<1%
  Real time comm. (1d) : latency < hundreds of milliseconds
  Large outdoor coverage (1d) : < 2km
  Coexistence with 15.4g (2a) : performs without degradation of throughput and reliability, even if co-existing with 15.4g.
  Battery operation (2b) : battery operation over 5 years

## Slide 10: Meaning of Functional Requirements
11ah Functional requirements
  These requirements are derived from the document “11-10-0001-13-0wng-900mhz-par-and-5c”.
  TGah amendment must address the functional requirements defined in functional requirements document.
  As defined in Selection Procedure document(0238r2), 11ah functional requirements document also include evaluation methodology (network simulation scenarios)

## Slide 11: Issues to be discussed
Bands
  Available bands are quite different for each country. e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA)
  And it is not possible to define common band which is applicable to all the countries
  How to set a minimal supported band?
    Minimal common band in 900MHz (e.g. Korea band)
    US band
    A set of multiples in 900MHz (US band & Japan band)
    A set of multiples (US band & Europe band & one China band (700))

## Slide 12: Issues to be discussed (2)
Coverage
  While 1km range is enough for most of use cases, use case 1d needs wider coverage up to 2km (it is based on 2km x 1km area with many metallic walls).
  In addition, wider coverage may be much more beneficial to use case (3a) and (3b).
  So, it is not a bad idea to extend coverage up to 2km

## Slide 13: Issues to be discussed (3)
Data rate
  PAR says data rates are supported > 00Kbps
  100Kbps is applied to most of use cases
  Only (1d), (3a), (3b) specifies data rate over 100Kbps.
  So, current description in PAR may be still valid in functional requirements document regarding aggregated throughput
  How about per-link throughput?
    Currently per-link throughputs have range as follows
      Minimum available is about 17bps (=100Kbps/6000) , for use case (1a)
      Maximum available is about 400Kbps(= 20Mbps/50), for use case (3b)
    Do we need some description on maximum or minimum allowable per-link throughput in functional requirements document?

## Slide 14: Issues to be discussed (4)
Coexistence with IEEE802.15 and IEEE802.15.4g
  There is already a specific use case (2a) which needs coexistence with 15.4g
  PAR document describes “provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g”
  5C document describes need to make a coexistence assurance document which is meant for 15.4g as follows:
    The working group will create a CA document and specifically reference IEEE P802.15.4g as part of the WG balloting process
  So, coexistence with IEEE802.15 and IEEE802.15.4g is inevitable

## Slide 15: Issues to be discussed (5)
WLAN user experience
  PAR says “maintaining the 802.11 WLAN user experience for fixed, outdoor, point-to-multi point applications.”
  5C says “Compatibility with IEEE 802 requirements will result from keeping the MAC SAP interface the same as for the existing 802.11 standard. The proposed amendment shall introduce no 802.1 architectural changes. The MAC SAP definition shall not be altered, ensuring that all LLC and MAC interfaces are compatible to and in conformance with the IEEE 802.1 Architecture, Management and Internetworking standards. New managed objects shall be defined as necessary in a format and structure consistent with existing 802.11 managed objects.”
  So, from current PAR & 5C, no chances on existing 802.11 standard is allowed

## Slide 16: Issues to be discussed (6)
Number of associations
  While most of use cases only need 50~100 STAs, use case (1a) needs 6000 STA/AP capacity
  Currently, number of associations is limited to 2007
  With 2007 associations, the max size of the TIM is 251 octets.
  So, it needs to be changed into over 6000 to cover smart grid use case, which is one of the original 11ah applications.

## Slide 17: Issues to be discussed (7)
Power saving
  Low throughput devices may desire larger sleep time, generally 15 minutes and in some extreme cases less a day.
  Most of 11ah devices may be expected to have very long battery duration time.
  Do we need some description about power saving features (e.g., battery life, duty cycle) in functional requirements documents?

## Slide 18: Issues to be discussed (8)
OBSS
  With larger number of clients, especially in an outdoor environments, it is more probable to have hidden nodes and overlapped BSS effect.
  To take into consideration these, do we need some description in functional requirements document?
    e.g.) 11ah BSS shall not degrade performance of existing OBSSs

## Slide 19: Issues to be discussed (9)
Others
  Welcome to other suggestions & discussions

## Slide 20: About Evaluation Methodology
This will be added in 11ah functional requirements document as a chapter
  Including PHY performance, comparison criteria, traffic models and network simulation scenarios as in 11ac functional requirements document
  In 11ah, we have 11 use cases. It is not possible to define simulation scenarios case-by-case because it is too burdensome.
  So, network simulation scenarios are chosen to represent 11ah-specific applications well and have a detailed information for network simulation (coordinates of every STAs, applied channel models, applied rate distributions, MSDU size, and so on)

## Slide 21: How to choose simulation scenarios
It should be taken to represent 11ah-specific application very well.
For simplicity in simulation work, not more than 4 scenarios are appropriate

## Slide 22: Revisit 11n simulation scenarios
It was not possible to define simulation scenarios for every use cases
So, usage model was derived from multiple use cases as a mixture of use cases to represent its 11n-specific applications well
During this mapping process, by imposed impact factor (derived by many straw polls), there’ve been discussions on which use case is more appropriate for a member of specific defined usage model

## Slide 23: Revisit 11n simulation scenarios
The score relates to the results reported in [4] from the vote on 21 July 2003. This scores 3 for high, 2 for medium and 1 for low priority. The "Devn" column shows the weighted absolute deviation in the votes (0 shows complete agreement and 1 shows complete disagreement).
Part of Table 5 - Use Case Definitions (in 11-03-0802-23-000n-usage-models)
Number | Covered by model # | Use case | Application | Environment | Score | Devn.
1 | 1, 3, 4, 5, 6, 7 | One personal phone everywhere – home, office. Each person has a phone that works everywhere, home, office – same number. An extension of the cell phone into the office building. This includes cordless phone over VoIP. | VOIP integrated with other wireless WAN technologies | Residential, Enterprise – large and small, conference room | 2.12 | 0.84
2 | 1 | Multiplayer Internet gaming anywhere within the home / Internet Café. | Interactive gaming (console to internet), internet gaming (controller to console) | Residential/small enterprise (internet cafes) | 1.69 | 0.77
3 | 1 | Multiple TVs running throughout the home getting their content from a single remotely located AV-server/AP/set top box. Local control of the content (changing channels, etc). | HDTV, SDTV, VoD control channel | Residential | 2.87 | 0.23

## Slide 24: Revisit 11n simulation scenarios (from 802.11-09/0096r0)
11n developed typical usage models and objective comparison criteria to ensure that all technical solutions met certain standard
11n usage model defined environments, applications, uses cases, usage models, represented by simulation scenarios
  There were 9 environments, 21 applications, 39 use cases, 17 usage models, 11 simulation scenarios
  Simulations were important in quantifying the performance of a feature
  But in the end the task group focused on only three (or four) simulation scenarios
  And it was up to those performing simulations to modify the applications to saturate the system
11n comparison criteria document included many categories requiring detailed documentation by the proposal teams
  Categories include marketability, backward compatibility and coexistence with legacy devices, performance measurements at the MAC SAP, MAC changes, PHY rates and preambles, channelization, spectral efficiency, PHY performance and changes
  In the end the task group focused mainly on throughput simulations
  Physical layer impairment scenarios were very useful in adding realism to PHY simulations

## Slide 25: Revisit 11n simulation scenarios (from 802.11-08/1323r0)
Application – a source or sink of wireless data that relates to a particular type of user activity.
Examples: Streaming video. VOIP.
Environment – The type of place a WLAN system is deployed in. Initial examples: home, large office.
Use case – A use case is a description of how an end user uses a system that exercises that system’s deployment of WLAN. A use case includes an application in a deployment environment with details regarding the user activity and both sides of the link.
Examples: Watching television remote from the cable or set-top box within the home. Talking on the telephone remote from one’s desk at work.
Usage Model – A specification of one or more applications and environments from which a simulation scenario can be created once the traffic patterns of the applications are known. Usage models are created to "cover" use cases.
Simulation Scenario – A simulation scenario is a description of a usage model that supports simulation. A simulation scenario includes details needed for simulation. Types of details to be included are descriptions that link the usage model to the simulation scenario: environment linked to a channel model, position of the AP (console or ceiling mounted), position of STAs w.r.t. AP, uplink and downlink traffic (# packets, size of packets, interference (number and types of users on the same WLAN channel – adjacent cells, the same cell, number and types of users on alternate channels, BT, baby monitors, GPRS or other systems). A simulation scenario is created from a Usage Model by characterizing the traffic profile of the applications and possibly merging multiple applications together to reduce simulation time.
Slide 25

## Slide 26: Revisit 11n simulation scenarios (from 802.11-08/1323r0)
Understanding and defining the application, environment, channel model, use case, usage model and simulation scenario are all necessary to create comparative results from 802.11 TGn proposals.
Channel models have been defined in TGn channel modeling documents, with 6 channel models. Each environment will map to a pair of channel models..
Each use case involves the use of one or more applications and is defined for one or more environments. It represents a single type of use of a system using the technology.
Each application reflects a source or sink of data. They will eventually be characterized in terms of a traffic profile that allows a simulation of the application to be created.
Each usage model contains a representative mixture of applications and channel models designed to adequately cover the important use cases. There is a many to many mapping between use cases and usage models (i.e., the same use case may contribute to multiple usage models and the same usage model may include applications from multiple use cases).
There will be a one-to-one mapping between usage models and simulation scenarios. The usage model is a marketing-oriented description of a "reasonable mixture" covering the important use cases. The simulation scenario fills in any technical details necessary to fully define the simulation inputs not present in the usage model.
Slide 26

## Slide 27: Revisit 11ac simulation scenarios
New Demand in TGac evaluation (from that of 11n)
TGac Evaluation shall satisfy these
  Compliance to VHTL6 PAR
    Point-to-point (500Mbps) & point-multipoint link test (1Gbps)
      Source and sink
      UDP traffic, with infinite offered load
      select PHY channel model for each system performance functional requirement
  Compliance to VHT-specific Usage models

## Slide 28: High-Quality Video Service Requirements (from 802.11-09/0161r2)
Slide 28
Video Compression |  | Description | Rate, Mbps | Packet Error Rate | Jitter, ms | Delay,ms
Uncompressed | 720p | (RGB): 1280x720 pixels, 24bits/pixels,60frames/s | 1300 | 1e-8 | 5 | 5
 | 1080i | (RGB): 1920x1080/2pixels, 24bits/pixels,60frames/s | 1300 | 1e-8 |  | 
 | 1080p | (YCrCb): 1920x1080 pixels, 12bits/pixels,60frames/s | 1500 | 1e-8 |  | 
 | 1080p | (RGB): 1920x1080 pixels, 24bits/pixels,60frames/s | 3000 | 1e-8 |  | 
Lightly Compressed |  | Motion JPEG2000 H.264 | 150 70 - 200 | 1e-7 1e-7 / 8 | 10 20 | 10 20
Compressed |  | Blu-ray™ | 50 | 1e-7 | 20 | 20
 |  | HD MPEG2 | 20 | 3e-7 | 20 | 20
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 28

## Slide 29: Usage Model Mapping to Operating Bands (from 802.11-09/0161r2 and 08/0451r0)
Slide 29
Category | # | Usage model
1. Wireless Display | 1a | Desktop Storage & Display
 | 1b | Projection to TV or projector in conf room (lightly compressed video)
 | 1c | In room gaming (lightly compressed video)
 | 1d | Streaming from camcorder to display (lightly compressed video)
 | 1e | Broadcast TV field pick up
2. Distribution of HDTV | 2a | Lightly compressed video streaming around the home
 | 2b | Compressed video streaming around home
 | 2c | Intra large vehicle (e.g. airplane) applications
 | 2d | Wireless networking for small office
 | 2e | Remote medical assistance
3. Rapid upload/download | 3a | Rapid sync-n-go file transfer
 | 3b | Picture by picture viewing
 | 3c | Airplane docking
 | 3d | Movie content download to car
 | 3e | Police / surveillance car upload
4. backhaul | 4a | Multi-media mesh backhaul
 | 4b | Point-to-point backhaul
5. Outdoor campus / auditorium | 5a | Video demos / tele-presence in auditorium
 | 5b | Public safety mesh
6. Manufacturing floor | 6a | Manufacturing floor automation
This table is from TGac usage model document (09/0161r2)
Usage model mapping to operating bands
by 08/0451r0
Red mainly matches to TGac usages.
Orange mainly matches to both TGac and TGad usages.
Black mainly matches to TGad usages.
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 29

## Slide 30: Usage Model Mapping to Operating Bands
It is seen that TGac usage models are mainly focused on
  lightly-compressed video in a residential environment
  P2MP compressed video (e.g. blue-ray) in a large office
  P2P high-speed backhaul
Slide 30

## Slide 31: Usage Model Mapping to Channel Model (for reference)
Slide 31
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 31

## Slide 32: Revisit 11ac simulation scenarios
It can be seen that theses scenarios can easily be derived
  lightly-compressed video with the use of channel B
  P2MP compressed video (e.g. blue-ray) with the use of channel D
  P2P high-speed backhaul with the use of channel E
Slide 32

## Slide 33: Revisit 11ac simulation scenarios
It is also possible for these scenarios to be derived with minimum modifications to one of conventional TGn simulation scenarios.
  Locations of AP and STAs : modification is not needed
  High-speed data services supporting high-quality video : only items which need to be modified
    For example, HDTV, SDTV => light-compressed video (MPEG2000)
  Residual services with low data rate such as Internet access, MP3 audio, VoIP and so on : modification is not needed
Slide 33

## Slide 34: Suggestion on 11ah simulation scenario
11ah use cases can be easily divided by 3 groups
  Use Case category 1 (sensors and meters)
  Use Case category 2 (backhaul sensor and meter data)
  Use Case category 3 (extended range Wi-Fi)

## Slide 35: Suggestion on 11ah simulation scenario (2)
Imposing impact factor on each detailed use cases to define simulation scenarios (similar to 11n method) may be too burdensome.
If we can agree, setting 3~4 simulation scenarios may be desirable:
  Use Case category 1 (sensors and meters)
    Outdoor (or mixture of indoor/outdoor) with extremely large number of nodes
    Indoor with moderately large number of nodes
  Use Case category 2 (backhaul sensor and meter data)
    Backhaul network is not easy to simulate because it also needs 15.4g devices needs to be taken into consideration
  Use Case category 3 (extended range Wi-Fi)
    Outdoor with moderately high data rate

## Slide 36: Summary
This is a preliminary submission for discussions on the 11ah functional requirements and its evaluation methodology

## Slide 37: Appendix
11-10-0001-13-0wng-900mhz-par-and-5c
11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document
11-11-0239-02-00ah-proposed-selection-procedure
11-09-0451-16-00ac-tgac-functional-requirements-and-evaluation-methodology
11-03-0813-13-000n-functional-requirements
11-09-0376-00-00ac-proposal-for-tgac-evaluation-methodology
11-10-1045-00-0s1g-possible-mac-changes
11-03-0802-23-000n-usage-models