IEEE P802.11
Wireless LANs

| Setting of DTIM Interval for MCCA |
| --- |
| Date: 2011-05-10 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6 80200 München, Germany |  | bahr ed siemens dod com |

Information to Editor: The following changes are based on IEEE 802.11s D11.01.

Instruction to Editor: Change the text of clause 9.9a.3.1 “General” as indicated by the WinWord change marks.

9.9a.3.1 General

MCF controlled channel access (MCCA) is an optional access method that allows mesh STAs that implement MCCA to access the WM at selected times with lower contention than would otherwise be possible. This standard does not require all mesh STAs to use MCCA. MCCA might be used by a subset of mesh STAs in an MBSS. However, MCCAOP reservations shall only be set up among mesh STAs that have dot11MCCAActivated true and operate on the same channel. The performance of MCCA might be impacted by STAs that do not respect MCCAOP reservations.

MCCA enabled mesh STAs use management frames to make reservations for transmissions. The mesh STA transmitting an MCCA Setup Request frame to initiate a reservation is the MCCAOP owner of the MCCAOP reservation defined in this setup. The receivers of the MCCA Setup Request frame are the MCCAOP responders. The MCCAOP owner and the MCCAOP responders advertise this MCCAOP reservation to their neighbors via an MCCAOP advertisement. The MCCA enabled neighbor mesh STAs that could cause interference to transmissions during these reserved time periods, or that would experience interference from them, shall not initiate a transmission during these reserved time periods. During its MCCAOP, the MCCAOP owner obtains a TXOP by winning an instance of EDCA contention. Because of its reservation, the MCCAOP owner experiences no competition from other MCCA enabled neighbor mesh STAs. At the start of an MCCAOP, the EDCAF of the MCCAOP owner replaces the AIFSN, CWmin, and CWmax value of its dot11EDCATable with MCCA access parameters.

In order to use MCCA, a mesh STA maintains synchronization with its neighboring mesh STAs. Mesh STAs that use MCCA shall use a common DTIM interval or DTIM intervals that are multiples where the factors are a power of 2. Mesh STAs that use MCCA should use a DTIM interval with a duration of 2n  100 TU with n being a non-negative integer less than or equal to 17. Additionally, a mesh STA shall track the reservations of its neighboring mesh STAs.

NOTE1—The DTIM interval of this form has been chosen to ensure that the starting times of the reservations do not change relative to each other between consecutive DTIM intervals. The restriction that n be less than or equal to 17 has been chosen to be compatible with the maximum DTIM interval and so that the range of the MCCAOP Offset in the reservation, see 7.3.2.106.2 (MCCAOP Reservation field), is compatible with the maximal DTIM interval length.

NOTE2—Choosing a different DTIM interval than 2n ( 100 TU with 0 ( n ( 17 may lead in some situations to a performance degradation of MCCA due to starting times of the reservations that change relative to each other between consecutive DTIM intervals. Such situations arise when two mesh BSS (or two parts of the same mesh BSS) with mesh STAs with dot11MCCAActivated equal to true have a different DTIM interval and they overlap. Therefore, a different DTIM interval than 2n ( 100 TU with 0 ( n ( 17 should be only chosen in controlled network environments and measure should be in place to deal with such situations.

Instruction to Editor: Change the text of clause 11C.2.8 “Establishing or becoming a member of a mesh BSS” as indicated by the WinWord change marks.

11C.2.8 Establishing or becoming a member of a mesh BSS

The Mesh Formation Info field in the Mesh Configuration element is available to assist scanning mesh STAs in choosing the mesh BSS of which to become a member. The details of the usage of this information are beyond the scope of this standard.

NOTE1—Selection of the mesh BSS of which the scanning mesh STA becomes a new member is outside the scope of this standard. That is, the mesh STA might freely select the mesh BSS of a candidate peer mesh STA of which it becomes a new member.

After the determination of the active mesh profile, the mesh STA may establish a new mesh BSS or become a new member to an existing mesh BSS.

When dot11MBCAActivated is true, the mesh STA shall perform the TBTT selection procedure described in 11C.12.4.3 (TBTT selection) using TimeStamp, Local Time, Beacon Period, and Beacon Timing in the BSSDescription parameter given by the MLME-SCAN.confirm primitive, before starting its beaconing.

When dot11MultiDomainCapabilityEnabled(REVmb:Activated) is true, the mesh STA shall not establish or become a member of a mesh BSS, unless a properly formed Beacon frame including a Country element is constructed, and dot11CountryString has been set.

A mesh STA shall include a Country element in its Beacon frames if either dot11MultiDomainCapabilityEnabled, dot11SpectrumManagementRequired, or dot11RadioMeasurementEnabled is true. See 7.2.3.1 (Beacon frame format) for the description of a properly formed Beacon frame.

The mesh STA establishes a new mesh BSS by activating a mesh profile that is different from any mesh profile discovered during the scanning of mesh BSSs (see 11C.2.6 (Scanning mesh BSSs)). When dot11MCCAActivated is true, the mesh STA should choose a DTIM interval with a duration of 2n ( 100 TU with n a non-negative integer less or equal to 17.

NOTE2—Choosing a different DTIM interval than 2n ( 100 TU with 0 ( n ( 17 may lead in some situations to a performance degradation of MCCA due to starting times of the reservations that change relative to each other between consecutive DTIM intervals. Such situations arise when two mesh STAs with dot11MCCAActivated is true have chosen independently from each other a different DTIM interval when establishing a new mesh BSS and their mesh BSSs overlap. Therefore, a different DTIM interval than 2n ( 100 TU with 0 ( n ( 17 should be only chosen in controlled network environments and measure should be in place to deal with such situations.

The mesh STA becomes a new member of an existing mesh BSS by activating the same mesh profile as received from a candidate peer mesh STA of this mesh BSS (see 11C.2.6 (Scanning mesh BSSs) and 11C.2.7 (Candidate peer mesh STA)). When dot11MCCAActivated is true, the mesh STA shall choose its DTIM interval according to one of the following rules:

- The DTIM interval of the mesh STA is set to the DTIM interval of one of the candidate peer mesh STAs of this mesh BSS from that the mesh STA received Beacon frames or Probe Response frames with the MCCA Enabled subfield of the Mesh Capability field of the Mesh Configuration element equal to 1.

- The DTIM interval of the mesh STA is set to a multiple of the DTIM interval of one of the candidate peer mesh STAs of this mesh BSS from that the mesh STA received Beacon frames or Probe Response frames with the MCCA Enabled subfield of the Mesh Capability field of the Mesh Configuration element equal to 1. The factor is a power of 2.

- The DTIM interval of the mesh STA is set to a fraction of the DTIM interval of one of the candidate peer mesh STAs of this mesh BSS from that the mesh STA received Beacon frames or Probe Response frames with the MCCA Enabled subfield of the Mesh Capability field of the Mesh Configuration element equal to 1. The divisor is a power of 2.

- If the mesh STA did not receive Beacon frames or Probe Response frames with the MCCA Enabled subfield of the Mesh Capability field of the Mesh Configuration element equal to 1 from any of the candidate peer mesh STAs of this mesh BSS, the mesh STA should choose a DTIM interval with a duration of 2n ( 100 TU with n a non-negative integer less or equal to 17. See also Note 2.

In either case, the mesh STA shall start beaconing using the START primitive. Upon receipt of the MLME-START.request primitive, the mesh STA shall initialize and start its TSF timer as specified by its active synchronization method as described in 11C.12.2 (Extensible synchronization framework), and begin transmitting Beacon frames as described in 11C.12.3 (Beaconing).

If the mesh STA has become a new member of an existing mesh BSS, it should establish a mesh peering with one or more candidate peer mesh STAs of this mesh BSS (see 11C.2.9 (Establishing mesh peerings)) in order to form the MBSS.

After establishing or becoming a member of an MBSS, the mesh STA may continue the discovery procedure described in 11C.2.6 (Scanning mesh BSSs) to discover other candidate peer mesh STAs.

References:

IEEE 802.11s Draft Standard D11.01, May 2011

Kazuyuki Sakoda, “P802.11s sponsor ballot 4th recirc comments”, 11-11/0703

Michael Bahr, “Need and Proposal for Flexible Setting of DTIM Interval in MCCA”, 11-11/0687r1

Michael Bahr, “Setting of DTIM Interval for MCCA”, 11-11/0554r0

# Text boxes

Abstract

This submission provides proposed text for the resolution of comments CIDs 4039, 4040, 4041, 4042, 4056, 4057, 4058, 4059, 4060, 4116, 4117, 4118, 4119 on the setting of the DTIM interval in MCCA. See also submission 11-11/0687 for background information.