## Slide 1: Proposed resolutions for WSM type comments
Date: 2011-04-26

## Slide 2: Abstract
This presentation shows proposed resolutions for comments 68, 100, 181 and 1128, which are asking for clear and explicit explanation on Map ID value

## Slide 3: Comments
CID | Page (C) | Line (C) | Clause | Comment | Proposed Change
68 | 65 | 14 | 10.af2.2 | "circularly increased by 1." what does that mean? Do you mean modulo some base? | Clarify
100 | 65 | 15 | 10.af2.2 | "circularly increased" what does "circularly increased" mean? | I think I know what you mean, but I would like to see a more explicit phrase instead.
181 | 138 | 17 | E.3.1.5 | How to you handle the situation if the counter "wraps around", i.e. if a device received a map version 128 and the map is udated afterwards reverting to version 0 ? | Add text to the amendment assuring that the most recent version of the map is always used by a device even if incrementing the map version by 1 yields to a wrap around / reset to 0
1128 | 65 | 15 | 10.af2.2 | "shall be circularly increased by 1." the operation of circular increase has not been defined. | Define this or reword to avoid undefined terms.

## Slide 4: Proposed Resolutions
CID 68, 100, 1128 ask for clear description on the Map ID value and update of the version. CID 181 says that additional text is required in order to assure that the most recent map is always used by the STA.
Agree CID 68, 100, 181 and 1128

## Slide 5: Comment Resolutions text
TGaf editor: Change the text in 10.af2.2 as follows:
10.af2 Regulatory Domain Operation
10.af2.1 General
10.af2.2 White Space Map
If the WSM Type is 1, then whenever the enabling STA transmit the updated WSM, the value of the Map version bits shall be circularly increased by 1. The value of the Map version bits shall be increased by 1 (modulo ) whenever the enabling STA transmits the updated WSM. The most recently received WSM shall be used by the WSM receiving STAs. If the Type bit in the Map ID field is set to 1, the following channel list is a full channel list and if the Type bit is set to 0, the following channel list is a partial channel list. If a STA receives several WSMs with the same Map version and the Type bit is set to 0, the STA should construct the whole channel list using the multiple WSMs having the same Map version.

## Slide 6: Comment Resolutions text
TGaf editor: change the following clauses after Annex E.2 as follows:
E.3 TLV Values
E.3.1 WSM Information Values
Table E-af3 – Map ID value field
Name | Type | Length (bits) | Value | Scope
Type | <ANA>.2.1 | 1 | Type bit is one bit in length and indicates whether the following channel list is a full channel list or a partial channel list. If the Type bit is set to 1, the following channel list is a full channel list and if the Type bit is set to 0, the following channel list is a partial channel list. | WSM, US
Map version | <ANA>.2.2 | 7 | Map version is 67 bits in length and identifies the version of WSM. When the available channel information from the TV band database is updated and the corresponding WSM is updated, then the Map version is incremented by 1 (modulo ) and the default bit value of the Map version is 0000000. The most recently received WSM shall be used by the WSM receiving STAs. | WSM, US