IEEE P802.11
Wireless LANs

| Resolution text for MIB comments |
| --- |
| Date: 2011-05-12 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Eunsun Kim | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1, Dongan, Anyang, Korea | +82-31-450-1860 | esun.kim@lge.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

Discussion:

This document is submitted to resolve technical comments 161, 1147, 1278 and 1282, which are related to the MIBs parameters.

In IEEE 802.11af D1.0, dot11ContactVerificationSignalInterval is not defined but dot11ContactVerificationInterval is defined instead. Therefore, it is proposed to change dot11ContactVerificationInterval as dot11ContactVerificationSignalInterval. Therefore, it is proposed to agree technical comments 161 and 1282.

CID 1278 says to delete several MIB variables because they are defined but not used in the draft. Hence, it is proposed to agree technical comments 1278 and delete them.

CID 1146 asks to change the parameter type to unsigned 32 according to the C.1 recommendations.

Proposed Resolution:

Agree CID 161, 1147and 1282 based on the discussion and editing instructions in this document.

Agree in principle CID 1278 based on the discussion and editing instructions in this document.

| CID | Commenter | Page(C) | Line(C) | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- | --- | --- |
| 161 | Emily, Qi | 65 | 65 | 10.af2.3 | dot11ContactVerificationSignalInterval is not defined. | define it or change it. |
| 1147 | Stephens, Adrian | 106 | 28 | C.3 | Please review C.1 recommendations. The IETF recommend that INTEGER is reserved for enumeration values. Ditto 109.21 | Change type to Unsigned32. |
| 1278 | Yee, Jung | 103 | 30 | C.3 | parameters dot11TVWSMapEnabled, dot11TVWSMapPeriod, dot11TVWSMapValidTime, dot11RLSImplemented, dot11RLSActivated not used | delete |
| 1282 | Yee, Jung | 103 |  | C.3 | dot11ContactVerificationSignalInterval is not defined in MIB. |  |

## Editing instructions:

Annex C

(normative)

ASN.1 encoding of the MAC and PHY MIB

TGaf editor: Delete parameters dot11TVWSMapEnabled, dot11TVWSMAPPeriod,  dot1TVWSMAPValidTime and dot11RLSSImplemented and their corresponding definitions as follows:

TGaf editor: Change parameters dot11ContactVerificationInterval and dot11WhiteSpaceMapValidTime as follows:

Dot11StationConfigEntry::=

SEQUENCE {

. . .

dot11RobustAVStreamingImplemented TruthValue,

dot11TVWSMapActivated TruthValue,

dot11TVWSMapPeriod Unsigned32,

dot11TVWSMapValidTime INTEGER,

dot11RLSSImplemented TruthValue,

dot11RLSSActivated TruthValue,

dot11WhiteSpaceMapActivated TruthValue,

dot11ContactVerificationSignalActivated TruthValue,

dot11ContactVerificationSignalInterval Unsigned32,

dot11WhiteSpaceMapPeriod Unsigned32,

dot11WhiteSpaceMapValidTime INTEGER Unsigned32,

dot11ChannelPowerManagementActivated TruthValue,

dot11ChannelScheduleManagementActivated TruthValue,

dot11WSSTAType INTEGER

}

dot11TVWSMapEnabled OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive or

MLME-JOIN.request primitive.

This attribute, when true, indicates that the station

capability for White Space Map is enabled. false indicates

the station has no White Space Map capability or

that the capability is present but is disabled."

DEFVAL { false }

::= { dot11StationConfigEntry <ANA> }

dot11MultibandSupportEnabled OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive or

MLME-JOIN.request primitive.

This attribute, when true, indicates that the station

capability for Multi-band Operation is enabled. false indicates

the station has no Multi-band Operation capability or

that the capability is present but is disabled."

DEFVAL { false }

::= { dot11StationConfigEntry <ANA> }

dot11TVWSMapPeriod OBJECT-TYPE

SYNTAX Unsigned32(1..255)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive.

This attribute specifies the number of beacon intervals that

elapse between transmission of Beacon frames containing

a White Space Map element.”

"

DEFVAL { 1 }

::= { dot11StationConfigEntry <ANA> }

dot11TVWSMapValidTime OBJECT-TYPE

SYNTAX Integer (1..65535)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive.

This attribute specifies the amount of time in units of seconds that

a White Space Map element is valid from the TV bands database access time."

DEFVAL { 600 }

::= { dot11StationConfigEntry <ANA> }

TGaf editor: Change the parameter type of dot11WhiteSpaceMapValidTime to Unsigned32 as follows:

dot11WhiteSpaceMapValidTime OBJECT-TYPE

SYNTAX Integer Unsigned 32 (1..65535)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive.

This attribute specifies the amount of time in units of seconds that

a White Space Map element is valid for a

dot11WhiteSpaceMapValidTime from the transmission of the beacon frame containing WSM element.

."

DEFVAL { 600 }

::= { dot11StationConfigEntry <ANA> }

TGaf editor: Change the parameter dot11ContactVerificationInterval to dot11ContactVerificationSignalIntervel as follows :

dot11ContactVerificationSignalInterval OBJECT-TYPE

SYNTAX Unsigned32(1..255)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This is a control variable.

It is written by an external management entity.

dot11ContactVerificationSignalInterval indicates the maximum number of seconds that a dependent STA may receive the Contact Verification Signal frame.

Unless another value is mandated by regulatory authorities, the value is 60 seconds.”

DEFAL { 60 }

::= { dot11StationConfigEntry <ANA> }

# Text boxes

Abstract

This document is to propose resolution for technical comments 161, 1147, 1278 and 1282 that are related to the MIBs parameters.

This document is based on IEEE 802.11af D1.01.