IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – 172 |
| --- |
| Date: May 03, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Liwen | STMicroelectronics |  |  | Liwen.chu@st.com |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 172 | 9.9.1.4 | 53 | 1 | TR | This paragraph does not deal with the following scenarios or should be improved for the following scenarios: 1), RTS/CTS protected TXOP, 2), CTS-to-self protected TXOP, 3), VHT BSS without overlapping BSS and overlapping BSSes have same primary channel. | Change the draft to deal with 3 scenario mentioned in comment column. |

Discussion of comment 172:

The current 11ac

or narrower than the CH_BANDWIDTH parameter in TXVECTOR of the initial frame in the first non-HT duplicate frame exchange in the same TXOP.

These rules can avoid collision after EIFS+backoff  since neighbor STA may not set NAV if non-RTS/CTS non-HT duplicate frame exchange are not used in a TXOP protection.

11ac draft has already defined the frame bandwidth rules in a RTS/CTS protected TXOP as following “For VHT STAs, if the response frame to the initial frame is a(#1282) CTS frame, the bandwidth indicated in the CTS frame determines the bandwidth obtained for the TXOP.” (D0.1 P523 L59). This does not cover multiple RTS/CTS in a TXOP.

But 11ac draft 0.1 is silent on how to select the frame bandwidth rules in a CTS-to-self protected TXOP.

9.19.2.4 Multiple frame transmission in an EDCA TXOP

TGac editor: please add the paragraphes in 11ac draft 0.1, section 9.19.2.4:

If a TXOP is protected by non-HT or non-HT duplicate RTS/CTS, the TXOP holder shall set the CH_BANDWIDTH parameter in TXVECTOR of a PPDU to be the same or narrower than the CH_BANDWIDTH parameter in RXVECTOR of the last received CTS in the same TXOP.

If a TXOP is protected by non-HT or non-HT duplicate CTS-to-Self, the TXOP holder shall set the CH_BANDWIDTH parameter in TXVECTOR of a PPDU to be the same or narrower than the CH_BANDWIDTH parameter in TXVECTOR of the initial CTS-to-Self in the same TXOP.

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D0.1:

172