IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – 178, 172 |
| --- |
| Date: May 03, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Liwen | STMicroelectronics |  |  | Liwen.chu@st.com |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 178 | 22.3.9.2.6 | 110 | 35 | TR | 16 bits Length in units of 4 octets can describe max A-MPDU length defined in 11ac specification (1,048,575). Why do you need the length of Length field more than 16 bits? | Clarify it. |

Discussion of comment 178:

Proposed resolution: counter

In section 22.3.9.2.6, VHT SIG –B is defined as following:

| Field | MU Allocation (bits) | SU Allocation (bits) |
| --- | --- | --- |
|  | 20MHz | 40MHz | 80MHz 160MHz 80+80MHz | 20MHz | 40MHz | 80MHz 160MHz 80+80MHz |
| Length | B0-B15 (16) | B0-B16 (17) | B0-B18 (19) | B0-B16 (17) | B0-B17 (18) | B0-B19 (20) |

The maximal PSDU length in section 22.3.9.2.6 is 220*4-1=4194303 octets. This is defined by PHY maximum data rate and VHT L-SIG capacity.

In subclause 7.4a.1 and Table 22-1, the A-MPDU/VHT PSDU maximum length for a VHT format PPDU excluding EOF delimiters and EOF Pad is defined as 1,048,575 octets. This is restricted by maxmum VHT A-MPDU supported by blockAck mechanism and maximal A_MSDU/MPDU size.

Bigger PHY layer maximal PSDU length makes future extention easier.

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 172 | 9.9.1.4 | 53 | 1 | TR | This paragraph does not deal with the following scenarios or should be improved for the following scenarios: 1), RTS/CTS protected TXOP, 2), CTS-to-self protected TXOP, 3), VHT BSS without overlapping BSS and overlapping BSSes have same primary channel. | Change the draft to deal with 3 scenario mentioned in comment column. |

Discussion of comment 172:

The current 11ac

or narrower than the CH_BANDWIDTH parameter in TXVECTOR of the initial frame in the first non-HT duplicate frame exchange in the same TXOP.

These rules can avoid collision after EIFS+backoff  since neighbor STA may not set NAV if non-RTS/CTS non-HT duplicate frame exchange are not used in a TXOP protection.

11ac draft has already defined the frame bandwidth rules in a RTS/CTS protected TXOP as following “For VHT STAs, if the response frame to the initial frame is a(#1282) CTS frame, the bandwidth indicated in the CTS frame determines the bandwidth obtained for the TXOP.” (D0.1 P523 L59). This does not cover multiple RTS/CTS in a TXOP.

But 11ac draft 0.1 is silent on how to select the frame bandwidth rules in a CTS-to-self protected TXOP.

Propose resolution: counter

9.19.2.4 Multiple frame transmission in an EDCA TXOP

TGac editor: please chang  the 10th paragraph in 11ac draft 0.1, section 9.19.2.4 as following:

A TXOP is obtained after a STA transmitting an initial frame successfully receives a response frame. If the initial frame is a data frame with bandwidth indication, the bandwidth indicated in the data frame determines the bandwidth obtained for the TXOP. If the initial frame is a non-HT format data frame, the bandwidth ob tained for the TXOP is 20MHz. For VHT STAs, if the response frame to the initial frame is a(#1282) CTS frame, the bandwidth indicated in the CTS frame determines the bandwidth obtained for the TXOP. When a TXOP is obtained for a bandwidth that is greater than 20MHz, the STA may transmit PPDUs using CH_BANDWIDTH that are up to and including the bandwidth obtained for the TXOP. During the TXOP, the STA shall not transmit PPDUs using CH_BANDWIDTH greater than the obtained bandwidth for the TXOP. If a TXOP is protected by non-HT or non-HT duplicate RTS/CTS, the TXOP holder shall set the CH_BANDWIDTH parameter in TXVECTOR of a PPDU to be the same or narrower than the CH_BANDWIDTH parameter in RXVECTOR of the last received CTS in the same TXOP.

TGac editor: please add thefollowing paragraph to the end of 11ac draft 0.1, section 9.19.2.4:

If a TXOP is protected by non-HT or non-HT duplicate CTS-to-Self, the TXOP holder shall set the CH_BANDWIDTH parameter in TXVECTOR of a PPDU to be the same or narrower than the CH_BANDWIDTH parameter in TXVECTOR of the initial CTS-to-Self in the same TXOP.

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D0.1:

178, 172