## Slide 1: Comments on 238r13
Date: 2011-05-02
Authors:
Name | Affiliations | Address | Phone | email
Jihyun Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1860 | Jihyun1220.lee@lge.com
Eunsun Kim |  |  |  | 
Yongho Seok |  |  |  | 

## Slide 2: Abstract
This presentation contains comments on “11-11-0238-13-00ai-use-case-reference-list-for-TGai”

## Slide 3: Correction of expected values according to the description of the traits
Tokyo Central Train Station:
  Mobile devices perform Internet access while entering or leaving a very crowded train station. There is the possibility of the person running, not just walking. Another\ example of this this kind of crowding is the Marathon scenario, where there are more than a thousand participants moving through a city and associating with numerous, uncoordinated hotspots
  For a pedestrian case, coverage interval value of less than 10 sec. does not seem quite feasible
    Does everyone run as fast as Usain Bolt? His 100m world record is 9.72 sec…
  Due to unexpected pedestrian route choice, more than 2 sec. seems more reasonable
Trait | Expected Value | Difficulty designation
Link-Attempt Rate | 100s/second | High
Media Load | 50% | High
Coverage Interval | Less than 10 sec More than 2 sec | Med Low to medium
Link Setup Time | 100 ms | High

## Slide 4: Correction of expected values according to the description of the traits
Station arrival
  A train with no Wi-Fi access arrives at a station and the passengers want to connect to the AP. A small number (less than 25%) of the passengers will remain in the AP range when the train leaves, 90 seconds after arrival.
  According to the definition of coverage interval, the expected value of coverage interval should be more than 10 sec., 90 sec in this particular scenario.
  I do not see any difference from Passenger in-transit case. Link setup time should be less than 2 sec. possibly 100ms
Trait | Expected Value | Difficulty designation
Link-Attempt Rate | 100s | High
Media Load | 50+ | High
Coverage Interval | 10 seconds 90 seconds | Low
Link Setup Time | More than 2 sec Less than 2 sec | Low Medium to high

## Slide 5: Correction of expected values according to the description of the traits
Passenger In-transit access
  The train is a mobile AP which the passengers connect to whilst travelling. The turnover of STAs accessing the AP will be about 25% every 3 to 5 minutes. Users will not log off when leaving the train.
  According to the definition of coverage interval, the expected value of coverage interval should be more than 10 sec., 3 to 5 minutes in this particular scenario.
Trait | Expected Value | Difficulty designation
Link-Attempt Rate | 100s | High
Media Load | 50+ | High
Coverage Interval | 10 sec more than 3 to 5 min | Low
Link Setup Time | 100 ms | High

## Slide 6: Correction of expected values according to the description of the traits
Station Lobby
  STAs will arrive in a fairly constant rate and want instant access to schedules, status, and optimal transit routes. The transactions may include ticket purchase.
  Same as Tokyo Central Train Station case, coverage interval less than 10 sec. seems infeasible.
Trait | Expected Value | Difficulty designation
Link-Attempt Rate | 100s/second | High
Media Load | 50% | High
Coverage Interval | Less than 10 sec More than 2 sec | Med Low to medium
Link Setup Time | 100 ms | High

## Slide 7: Expected values of use case traits
Link setup time
  Vague definition
    the amount time required to establish for the first time a link to an AP within an ESS
    It is not clear if this means average link setup time or maximum tolerable link setup time for a STA
  It is not clear how to estimate or calculate expected value of link setup time
Coverage interval
  Vague definition
    The time the STA is within the range of an AP within an ESS
    It is not clear if it includes hand-off time within an ESS
  It is not clear how to estimate expected value of coverage interval