IEEE P802.11
Wireless LANs

| Resolution for CID 1322 |
| --- |
| Date: 2011-05-09 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Robert Stacey | Intel Corporation | 2111 NE 25th Ave, Hillsboro, OR 97124 | +1-503-724-0893 | robert.j.stacey@intel.com |

## Comments

| 1322 | Stephens, Adrian | General |  |  | TR | There is no MIB | Add a MIB. |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1317 | Stephens, Adrian | 22.4.2 | 153 | 3 | TR | There's a TBD | resolve it |
| 542 | Hart, Brian | 22.4.2 | 153 | 13 | TR | and append "but shall not be updated by the PLME" for clarity | As in comment |
| 477 | Hart, Brian | 22.4.2 | 153 | 24 | TR | To get RX-side power saving benefits from the partial AID, the PHY should be configured with its own partial AID | Add a partial AID MIB variable |
| 1318 | Stephens, Adrian | 22.4.2 | 153 | 29 | TR | OK, so this interface tells the PHY where its first segment channel is and how wide it is. But when the TXVECTOR specifies a transmitted PPDU channel width of less than the bandwidth indicated in this table, how does the PHY determine which bits of the full channel width to use? | Specify this algorithm somewhere in the PHY. May need to tell the phy the location of the primary channel to achieve this. |
| 995 | Seok, Yongho | 22.4.2 | 153 | 3,25 | TR | No specifications on TBD | Clarify TBD. |

## Discussion

We need a MIB and to clean up the section 22.4.2 PHY MIB.

## Resolution

1322: AGREE. MIB added.

1377: AGREE. Reference to Annex C

542: AGREE. As suggested.

477: DISAGREE. Partial AID filtering is implementation dependent. Only Tx side needs to be specified.

1318: DISAGREE. Subchannel use is implicit in the channelization.

995: AGREE. First TBD is referfence to Annex C, second TBD on PHY type is <ANA> per MIB.

22.4.2 PHY MIB

VHT PHY MIB attributes are defined in Annex C with specific values defined in Table 22-23 (VHT PHY MIB attributes). The “Operational semantics” column in Table 22-23 (VHT PHY MIB attributes)(#97) contains two types: static and dynamic.

— Static MIB attributes are fixed and cannot be modified for a given PHY implementation.

— Dynamic MIB attributes are interpreted according the MAX-ACCESS field of the MID attribute.

When MAX-ACCESS is set to read-only, the MIB attribute value may be updated by the PLME and read from the MIB attribute by management entities. When MAX-ACCESS is set to read-write, the MIB attribute may be read and written by management entities but shall not be updated by the PLME.

Table 22-23—VHT PHY MIB attributes

| Managed Object | Default value/range | Operational semantics |
| --- | --- | --- |
| dot11PHYOperationTable |
| dot11PHYType | VHT (<ANA>) | Static |
| dot11PHYHTTable |
| dot11CurrentPrimaryChannel | Implementation dependent | Dynamic |
| dot11CurrentSecondaryChannel | Implementation dependent | Dynamic |
| dot11FortyMHzOperationImplemented | False/Boolean | Static |
| dot11FortyMHzOperationActivated | False/Boolean | Dynamic |
| dot11NumberOfSpatialStreamsImplemented | Implementation dependent | Static |
| dot11NumberOfSpatialStreamsActivated | Implementation dependent | Dynamic |
| dot11HTGreenfieldOptionImplemented | False/Boolean | Static |
| dot11HTGreenfieldOptionActivated | False/Boolean | Dynamic |
| dot11ShortGIOptionInTwentyImplemented | False/Boolean | Static |
| dot11ShortGIOptionInTwentyActivated | False/Boolean | Dynamic |
| dot11ShortGIOptionInFortyImplemented | False/Boolean | Static |
| dot11ShortGIOptionInFortyActivated | False/Boolean | Dynamic |
| dot11LDPCCodingOptionImplemented | False/Boolean | Static |
| dot11LDPCCodingOptionActivated | False/Boolean | Dynamic |
| dot11TxSTBCOptionImplemented | False/Boolean | Static |
| dot11TxSTBCOptionActivated | False/Boolean | Dynamic |
| dot11RxSTBCOptionImplemented | False/Boolean | Static |
| dot11RxSTBCOptionActivated | False/Boolean | Dynamic |
| dot11BeamFormingOptionImplemented | False/Boolean | Static |
| dot11BeamFormingOptionActivated | False/Boolean | Dynamic |
| dot11PhyVHTTable |
| dot11CurrentChannelBandwidth | Implementation dependent | Dynamic |
| dot11CurrentChannelCenterFrequencyIndex1 | Implementation dependent | Dynamic |
| dot11CurrentChannelCenterFrequencyIndex2 | Implementation dependent | Dynamic |
| dot11VHTChannelWidthOptionImplemented | Implementation dependent | Static |
| dot11VHTShortGIOptionIn80Implemented | False/Boolean | Static |
| dot11VHTShortGIOptionIn80Activated | False/Boolean | Dynamic |
| dot11VHTShortGIOptionIn160and80p80Implemented | False/Boolean | Static |
| dot11VHTShortGIOptionIn160and80p80Activated | False/Boolean | Dynamic |
| dot11VHTLDPCCodingOptionImplemented | False/Boolean | Static |
| dot11VHTLDPCCodingOptionActivated | False/Boolean | Dynamic |
| dot11VHTTxSTBCOptionImplemented | False/Boolean | Static |
| dot11VHTTxSTBCOptionActivated | False/Boolean | Dynamic |
| dot11VHTRxSTBCOptionImplemented | False/Boolean | Static |
| dot11VHTRxSTBCOptionActivated | False/Boolean | Dynamic |
| dot11TransmitBeamformingConfigTable |
| dot11ReceiveStaggerSoundingOptionImplemented | False/Boolean | Static |
| dot11TransmitStaggerSoundingOptionImplemented | False/Boolean | Static |
| dot11ReceiveNDPOptionImplemented | False/Boolean | Static |
| dot11TransmitNDPOptionImplemented | False/Boolean | Static |
| dot11ImplicitTransmitBeamformingOptionImplemented | False/Boolean | Static |
| dot11CalibrationOptionImplemented | Implementation dependent | Static |
| dot11ExplicitCSITransmitBeamformingOptionImplemented | False/Boolean | Static |
| dot11ExplicitNonCompressedBeamformingMatrixOptionImplemented | False/Boolean | Static |
| dot11ExplicitTransmitBeamformingCSIFeedbackOptionImplemented | Implementation dependent | Static |
| dot11ExplicitNoncompressedBeamformingFeedbackOptionImplemented | Implementation dependent | Static |
| dot11ExplicitCompressedBeamformingFeedbackOptionImplemented | Implementation dependent | Static |
| dot11NumberBeamFormingCSISupportAntenna | Implementation dependent | Static |
| dot11NumberNonCompressedBeamformingMatrixSupportAntenna | Implementation dependent | Static |
| dot11NumberCompressedBeamformingMatrixSupportAntenna | Implementation dependent | Static |
| dot11SUBeamformerOptionImplemented | False/Boolean | Static |
| dot11SUBeamformeeOptionImplemented | False/Boolean | Static |
| dot11MUBeamformerOptionImplemented | False/Boolean | Static |
| dot11MUBeamformeeOptionImplemented | False/Boolean | Static |
| dot11VHTNumberSoundingDimensions | Implementation dependent | Static |
| dot11BeamformeeNTxSupport | Implementation dependent | Static |

802.11ac Editor: Add the MIB to Annex C with editing instructions based on the difference the REVmb 8.0 MIB and the MIB included in this document.

## Diff on edited MIB relative to REVmb 8.0

86a87

> 	--  dot11VHTStationConfigTable 		::= { dot11smt <ANA> }

134a136

> 	--  dot11PhyVHTTable 		::= { dot11phy <ANA> }

318c320,321

< 		dot11BSSBroadcastNullCount	Unsigned32

---

> 		dot11BSSBroadcastNullCount	Unsigned32,

> 		dot11VHTOptionImplemented	TruthValue,

1982a1986,1996

> dot11VHTOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates whether the entity is VHT Capable."

> 	::= { dot11StationConfigEntry 136}

>

12605a12620,12750

> -- * dot11VHTStationConfig TABLE

> -- **********************************************************************

> dot11VHTStationConfigTable OBJECT-TYPE

> 	SYNTAX SEQUENCE OF Dot11VHTStationConfigEntry

> 	MAX-ACCESS not-accessible

> 	STATUS current

> 	DESCRIPTION

> 		"Station Configuration attributes. In tabular form to allow for multiple instances on an agent."

> 	::= { dot11smt <ANA> }

>

> dot11VHTStationConfigEntry OBJECT-TYPE

> 	SYNTAX Dot11VHTStationConfigEntry

> 	MAX-ACCESS not-accessible

> 	STATUS current

> 	DESCRIPTION

> 		"An entry (conceptual row) in the dot11HTStationConfig Table.

>

> 		ifIndex - Each IEEE 802.11 interface is represented by an ifEntry. Interface tables in this MIB module are indexed by ifIndex."

> 	INDEX { ifIndex }

> 	::= { dot11VHTStationConfigTable 1 }

>

> Dot11VHTStationConfigEntry ::=

> 	SEQUENCE {

> 		dot11MaxMPDULength			INTEGER,

> 		dot11VHTMaxRxAMPDUFactor 		Unsigned32,

> 		dot11VHTControlFieldSupported		TruthValue,

> 		dot11VHTTXOPPowerSaveOptionImplemented	TruthValue,

> 		dot11VHTRxMCSMap			OCTET STRING,

> 		dot11VHTRxHighestDataRateSupported	Unsigned32,

> 		dot11VHTTxMCSMap			OCTET STRING,

> 		dot11VHTTxHighestDataRateSupported	Unsigned32

> 		}

>

> dot11MaxMPDULength OBJECT-TYPE

> 	SYNTAX INTEGER { short(3895), medium(7991), long(11454) }

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates the supported maximum MPDU size."

> 	DEFVAL { short }

> 	::= { dot11VHTStationConfigEntry 1 }

>

> dot11VHTMaxRxAMPDUFactor OBJECT-TYPE

> 	SYNTAX Unsigned32 (0..7)

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates the maximum length of A-MPDU that the STA can receive. The Maximum Rx A-MPDU defined by this field is equal to 2^(13+dot11VHTMaxRxAMPDUFactor) -1 octets."

> 	DEFVAL { 0 }

> 	::= { dot11VHTStationConfigEntry 2 }

>

> dot11VHTControlFieldSupported OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the station implementation is capable of receiving the VHT Control field."

> 	DEFVAL { false }

> 	::= { dot11VHTStationConfigEntry 3 }

>

> dot11VHTTXOPPowerSaveOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the station implementation is capable of TXOP Power Save operation."

> 	DEFVAL { false }

> 	::= { dot11VHTStationConfigEntry 4 }

>

> dot11VHTRxMCSMap OBJECT-TYPE

> 	SYNTAX OCTET STRING (SIZE(8))

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		Each octet represents the highest MCS supported (for Rx) on the number of streams represented by the octet index. A value 0 indicates that MCSs 0-7 are supported. A value 1 indicates that MCSs 0-8 are supported. A value 2 indicates that MCSs 0-9 are supported. A value 3 indicates no support for that number of spatial streams."

> 	::= { dot11VHTStationConfigEntry 5 }

>

> dot11VHTRxHighestDataRateSupported OBJECT-TYPE

> 	SYNTAX Unsigned32

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		Represents the highest data rate in Mb/s that the STA is capable of receiving."

> 	::= { dot11VHTStationConfigEntry 6 }

>

> dot11VHTTxMCSMap OBJECT-TYPE

> 	SYNTAX OCTET STRING (SIZE(8))

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		Each octet represents the highest MCS supported (for Tx) on the number of streams represented by the octet index. A value 0 indicates that MCSs 0-7 are supported. A value 1 indicates that MCSs 0-8 are supported. A value 2 indicates that MCSs 0-9 are supported. A value 3 indicates no support for that number of spatial streams."

> 	::= { dot11VHTStationConfigEntry 7 }

>

> dot11VHTTxHighestDataRateSupported OBJECT-TYPE

> 	SYNTAX Unsigned32

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		Represents the highest data rate in Mb/s that the STA is capable of transmitting."

> 	DEFVAL { 0 }

> 	::= { dot11VHTStationConfigEntry 8 }

>

> -- ********************************************************************

> -- * End of dot11VHTStationConfigTable TABLE

> -- ********************************************************************

>

> -- **********************************************************************

14610c14755,14756

< 		ht(7) }

---

> 		ht(7),

> 		vht(<ANA>) }

14620c14766

< 		OFDM = 04, HRDSSS = 05, ERP = 06, HT = 07"

---

> 		OFDM = 04, HRDSSS = 05, ERP = 06, HT = 07, VHT = <ANA>"

16600c16746,16753

< 		dot11NumberCompressedBeamformingMatrixSupportAntenna	Unsigned32 }

---

> 		dot11NumberCompressedBeamformingMatrixSupportAntenna	Unsigned32,

> 		dot11VHTSUBeamformeeOptionImplemented	TruthValue,

> 		dot11VHTSUBeamformerOptionImplemented	TruthValue,

> 		dot11VHTMUBeamformeeOptionImplemented	TruthValue,

> 		dot11VHTMUBeamformerOptionImplemented	TruthValue,

> 		dot11VHTNumberSoundingDimensions 	Unsigned32,

> 		dot11VHTBeamformeeNTxSupport 		Unsigned32

> 		}

16794a16948,17019

> dot11VHTSUBeamformeeOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the STA supports the SU Beamformee role."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 15 }

>

> dot11VHTSUBeamformerOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the STA supports the SU Beamformer role."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 16 }

>

> dot11VHTMUBeamformeeOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the STA supports the MU Beamformee role."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 17 }

>

> dot11VHTMUBeamformerOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the STA supports the MU Beamformer role."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 18 }

>

> dot11VHTNumberSoundingDimensions OBJECT-TYPE

> 	SYNTAX Unsigned32 (1..8)

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates the number of antennas used by the beamformer when sending beamformed tansmissions."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 19 }

>

> dot11VHTBeamformeeNTxSupport OBJECT-TYPE

> 	SYNTAX Unsigned32 (1..8)

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates the number of beamformer transmit antennas the beamformee supports."

> 	DEFVAL { false }

> 	::= { dot11TransmitBeamformingConfigEntry 20 }

>

16802a17028,17247

> -- **********************************************************************

> -- * dot11 Phy VHT TABLE

> -- **********************************************************************

>

> dot11PhyVHTTable OBJECT-TYPE

> 	SYNTAX SEQUENCE OF Dot11PhyVHTEntry

> 	MAX-ACCESS not-accessible

> 	STATUS current

> 	DESCRIPTION

> 		"Entry of attributes for dot11PhyVHTTable. Implemented as a table indexed on ifIndex to allow for multiple instances on an Agent."

> 	::= { dot11phy <ANA> }

>

> dot11PhyVHTEntry OBJECT-TYPE

> 	SYNTAX Dot11PhyVHTEntry

> 	MAX-ACCESS not-accessible

> 	STATUS current

> 	DESCRIPTION

> 		"An entry in the dot11PhyHTEntry Table. ifIndex - Each IEEE 802.11 interface is represented by an ifEntry. Interface tables in this MIB module are indexed by ifIndex."

> 	INDEX {ifIndex}

> 	::= { dot11PhyVHTTable 1 }

>

> Dot11PhyVHTEntry ::=

> 	SEQUENCE {

> 		dot11VHTChannelWidthOptionImplemented		INTEGER,

> 		dot11CurrentChannelBandwidth			INTEGER,

> 		dot11CurrentChannelCenterFrequencyIndex1	Unsigned32,

> 		dot11CurrentChannelCenterFrequencyIndex2	Unsigned32,

> 		dot11VHTShortGIOptionIn80Implemented		TruthValue,

> 		dot11VHTShortGIOptionIn80Activated		TruthValue,

> 		dot11VHTShortGIOptionIn160and80p80Implemented	TruthValue,

> 		dot11VHTShortGIOptionIn160and80p80Activated	TruthValue,

> 		dot11VHTLDPCCodingOptionImplemented		TruthValue,

> 		dot11VHTLDPCCodingOptionActivated		TruthValue,

> 		dot11VHTTxSTBCOptionImplemented			TruthValue,

> 		dot11VHTTxSTBCOptionActivated			TruthValue,

> 		dot11VHTRxSTBCOptionImplemented			TruthValue,

> 		dot11VHTRxSTBCOptionActivated			TruthValue

> 	}

>

> dot11VHTChannelWidthOptionImplemented OBJECT-TYPE

> 	SYNTAX INTEGER { contiguous80(0), contiguous160(1), noncontiguous80plus80(2) }

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute indicates the channel widths supported: 20/40/80 MHz, 20/40/80/160 MHz or 20/40/80/160/80+80 MHz."

> 	DEFVAL { contiguous80 }

> 	::= { dot11PhyVHTEntry 1 }

>

> dot11CurrentChannelBandwidth OBJECT-TYPE

> 	SYNTAX INTEGER { cbw20(0), cbw40(1), cbw80(2), cbw160(3), cbw80p80(4) }

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		This attribute determines the operating channel width."

> 	DEFVAL { cbw20 }

> 	::= { dot11PhyVHTEntry 2 }

>

> dot11CurrentChannelCenterFrequencyIndex1 OBJECT-TYPE

> 	SYNTAX Unsigned32 (0..200)

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		In 20 MHz, 40 MHz, 80 MHz and 160 MHz channels, denotes the channel center frequency.

> 		In 80+80 MHz channels, denotes the center frequency of the primary segment."

> 	DEFVAL { 0 }

> 	::= { dot11PhyVHTEntry 3 }

>

> dot11CurrentChannelCenterFrequencyIndex2 OBJECT-TYPE

> 	SYNTAX Unsigned32 (0..200)

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		In 80+80 MHz channels, denotes the center frequency of the secondary segment.

> 		Undefined for 20 MHz, 40 MHz, 80 MHz and 160 MHz channels."

> 	DEFVAL { 0 }

> 	::= { dot11PhyVHTEntry 4 }

>

> dot11VHTShortGIOptionIn80Implemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the device is capable of receiving 80 MHz short guard interval packets."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 3 }

>

> dot11VHTShortGIOptionIn80Activated OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the reception of 80 MHz short guard interval packets is enabled."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 4 }

>

> dot11VHTShortGIOptionIn160and80p80Implemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the device is capable of receiving 160 MHz and 80+80 MHz short guard interval packets."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 5 }

>

> dot11VHTShortGIOptionIn160and80p80Activated OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the reception of 160 MHz and 80+80 MHz short guard interval packets is enabled."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 6 }

>

> dot11VHTLDPCCodingOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the LDPC coding option for VHT packets is implemented."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 7 }

>

> dot11VHTLDPCCodingOptionActivated OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		This attribute, when true, indicates that the LDPC coding option for VHT packets is enabled."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 8 }

>

> dot11VHTTxSTBCOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the device is capable of transmitting VHT frames using STBC."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 9 }

>

> dot11VHTTxSTBCOptionActivated OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		This attribute, when true, indicates that the entity's capability for transmitting VHT frames using STBC is enabled."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 10 }

>

> dot11VHTRxSTBCOptionImplemented OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-only

> 	STATUS current

> 	DESCRIPTION

> 		"This is a capability variable.

> 		Its value is determined by device capabilities.

>

> 		This attribute, when true, indicates that the device is capable of receiving VHT frames using STBC."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 11 }

>

> dot11VHTRxSTBCOptionActivated OBJECT-TYPE

> 	SYNTAX TruthValue

> 	MAX-ACCESS read-write

> 	STATUS current

> 	DESCRIPTION

> 		"This is a control variable.

> 		It is written by an external management entity.

> 		Changes take effect as soon as practical in the implementation.

>

> 		This attribute, when true, indicates that the entity's capability for receiving VHT frames using STBC is enabled."

> 	DEFVAL { false }

> 	::= { dot11PhyVHTEntry 12 }

>

>

> -- **********************************************************************

> -- * End of dot11PhyVHT TABLE

> -- **********************************************************************

>

20656a21102,21114

> dot11VHTTransmitBeamformingGroup OBJECT-GROUP

> 	OBJECTS {

> 		dot11VHTSUBeamformeeOptionImplemented,

> 		dot11VHTSUBeamformerOptionImplemented,

> 		dot11VHTMUBeamformeeOptionImplemented,

> 		dot11VHTMUBeamformerOptionImplemented,

> 		dot11VHTNumberSoundingDimensions,

> 		dot11VHTBeamformeeNTxSupport }

> 	STATUS current

> 	DESCRIPTION

> 		"Attributes that configure VHT transmit beamforming for IEEE 802.11."

> 	::= { dot11Groups 52 }

>

20770c21228,21229

< 		dot11PSMPOptionImplemented }

---

> 		dot11PSMPOptionImplemented,

> 		dot11VHTOptionImplemented }

21149a21609,21612

> 	GROUP dot11VHTTransmitBeamformingGroup

> 	DESCRIPTION

> 		"The dot11VHTTransmitBeamformingGroup group is optional."

>

21168a21632

> 	--	dot11VHTTransmitBeamformingGroup

## MIB

# Text boxes

Abstract

This document proposes a resolution for CID 1322 (comment on P802.11ac/D0.1).

Editing instructions based on P802.11ac/D0.3.