IEEE P802.11
Wireless LANs

| Comment Resolution for Basic VHT BSS functionality |
| --- |
| Date: 2011-05-04 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | Illsoo.sohn@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1497 | yongho.seok@lge.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGac Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGac Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGac Editor:  Editing instructions preceded by “TGac Editor” are instructions to the TGac editor to modify existing material in the TGac draft.   As a result of adopting the changes, the TGac editor will execute the instructions rather than copy them to the TGac Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

| CID | Subclause | Page | Line | Comment Type | Comment | SuggestedRemedy | Proposed Resolution |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1205 | 11.20.1 | 62 | 6 | TR | The first three paras can be simplified without loss. | Replace with: "A VHT STA that is a member of a VHT BSS shall not transmit a PPDU that does not use the primary 20 MHz channel of the BSS." | Disagree. |
| 182 | 11.20.1 | 62 | 17 | TR | "A VHT STA shall not transmit a 160 MHz VHT PPDU using a 160 MHz channel that cannot be used to setup a VHT 160 MHz BSS." This sentence may not be necessary. | Better relate to adjacent 80+80MHz transmissions. | Agree in principle |
| 1204 | 11.20.1 | 62 | 17 | TR | "A VHT STA shall not transmit a 160 MHz VHT PPDU using a 160 MHz channel that cannot be used to setup a VHT 160 MHz BSS." - "cannot be used to setup" is not a defined condition or term. Ditto at line 22 | Replace with something using defined terms. | Agree in principle |
| 796 | 11.20.1 | 62 | 10-11 | TR | Why emphasize on the primary 20MHz channel only? For 40/80MHz PPDU, primary 40/80 channel is the only valid transmission channel | change it to "A VHT STA that is a member of a VHT 40 MHz, 80 MHz, 160 MHz or 80+80 MHz BSS shall transmit a 40 MHz PPDU using the primary40 MHZ channel", or remove the sentence (11.20.2 presents detailed rules already) | Agree in principle |
| 69 | 11.20.1 | 62 | 17-22 | TR | The phrase of "cannot be used to setup" is not clear. | Specify the conditions when a channel "cannot be used to setup" a VHT 160 MHz or 80+80 MHz BSS. | Agree in principle |

Proposed Resolution:

Agree in principle to CID 182, 1204, 796, 69 and disagree to CID 1205. Proposed text changes are described in the following Editing Instructions section.

## Editing instructions:

TGac editor: Modify basic VHT BSS functionality section as the following:

10.24 VHT BSS operation

10.24.1 Basic VHT BSS functionality

A VHT STA that is a member of a VHT BSS shall not transmit a 20 MHz VHT PPDU that does not use the primary 20 MHz channel of the BSS, except for a 20 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

A VHT STA that is a member of a VHT 40 MHz, 80 MHz, 160 MHz or 80+80 MHz BSS shall not transmit a 40 MHz VHT PPDU that does not use the primary 20 40 MHz channel of the BSS, except for a 40 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

A VHT STA that is a member of part of a VHT 80 MHz, 160 MHz or 80+80 MHz BSS shall not transmit an 80 MHz VHT PPDU that does not use the primary 20 80 MHz channel of the BSS, except for an 80 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

A VHT STA shall not transmit a 160 MHz VHT PPDU using a 160 MHz channel that cannot be used to setup a VHT 160 MHz BSS, except for a 160 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

A VHT STA shall not transmit an(#70) 80+80 MHz VHT PPDU using two nonadjacent 80 MHz channels if either channel cannot be used to setup a VHT 80 MHz BSS, except for a 80+80 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

A VHT STA that is a member of 160 or 80+80 MHz BSS shall not transmit an 160 or 80+80 MHz VHT PPDU that does not use the primary 80 MHz channel and the secondary 80MHz of the BSS, except for an 160 or 80+80 MHz VHT PPDU transmission on an off-channel TDLS direct link(#169).

# Text boxes

Abstract

Submission for Draft P802.11ac_D0.3 comment resolution. The document addresses various comments related to Basic VHT BSS functionality.

Submission addresses Draft P802.11ac_D0.1 comments 69, 182, 796, 1204 and 1205.