IEEE P802.11
Wireless LANs

| Comment resolutions regarding to network channel control reason result code |
| --- |
| Date: 2011-01-12 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Chen Sun | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 | +81 45 847 5062 | sun@nict.go.jp |

| CID | Clause | Page | Line | Comment | Proposed Change | Resolution |
| --- | --- | --- | --- | --- | --- | --- |
| 196 | 8.4.5.4 | 41 | 14 | Reference to Table 8-134 seems to be wrong. The referenced Table does not list Reason Result Codes. | Replace with correct reference. | SAME: 896, 557, 605, 626 Agree in principle with the commenter that the sentence refers to a wrong table. The Network channel control is not the DSE procedure. To resolve this comment a new Table 8-45af3, has been added. See MS Word file IEEE 802.11af-11/0648r0 for the editor’s instructions. |
| 202 | 8.5.8.af2 | 44 | 65 | Reference to Table 8-134 seems to be wrong. The referenced Table does not list Reason Result Codes. | Replace with correct reference. |  |
| 557 | 8.4.5.4 | 41 | 11-12 | It is said that the Reason Result Code field in a Network Channel Control element is used to indicate that a "DSE Enablement frame was generated", however, the reason result should be the reason that a Network Channel Control frame was generated. Does it meant that Network Channel Control exchange procedure is the same as DSE Enablement procedure? | Remove Network Channel Control element or provide a clear behavior of Network Channel Control element. |  |
| 605 | 8.4.5.4 | 41 | 11-12 | It is said that the Reason Result Code field in a Network Channel Control element is used to indicate that a "DSE Enablement frame was generated", however, the reason result should be the reason that a Network Channel Control frame was generated. Does it meant that Network Channel Control exchange procedure is the same as DSE Enablement procedure? | Remove Network Channel Control element or provide a clear behavior of Network Channel Control element. |  |
| 626 | 8.4.5.4 | 41 | 11-12 | It is said that the Reason Result Code field in a Network Channel Control element is used to indicate that a "DSE Enablement frame was generated", however, the reason result should be the reason that a Network Channel Control frame was generated. Does it meant that Network Channel Control exchange procedure is the same as DSE Enablement procedure? | Provide a clear behavior of Network Channel Control element or remove Network Channel Control element. |  |
| 896 | 8.4.5.4 | 41 | 11-12 | It is said that the Reason Result Code field in a Network Channel Control element is used to indicate that a "DSE Enablement frame was generated", however, the reason result should be the reason that a Network Channel Control frame was generated. Does it meant that Network Channel Control exchange procedure is the same as DSE Enablement procedure? | Remove Network Channel Control element or provide a clear behavior of Network Channel Control element. |  |

8.4.5.4 Network Channel Control element

TGaf Editor: Revise the 5th paragraph of this subclause as follows.

The Reason Result Code field is used to indicate the reason that a DSE Enablement Network Channel Control frame was generated. The length of the Reason Result Code field is 1 octet. The reason result codes that have been allocated are shown in Table 8-134 Table 8-45af3.

TGaf Editor: Insert Table 8-45af3 as shown:

Table 8-45af3—Reason result code field values

| Reason Result Code field value | Name | Description |
| --- | --- | --- |
| 0 |  | Reserved |
| 1 |  | Reserved |
| 2 |  | Network channel request |
| 3 | SUCCESS | Success |
| 4 | REFUSED | Request declined |
| 5 | INVALID_PARAMETERS | Request not successful as one or more parameters have invalid values |
| 6 | TOO_MANY_SIMULTANEOUS_REQUESTS | Network channel request denied because the enabler is unable to handle additional dependent STAs |
| 7-255 |  | Reserved |

8.5.8.af2 Network Channel Control frame format

TGaf Editor: Revise the 7th paragraph of this subclause as follows.

The Reason Result Code field is used to indicate the reason that a DSE Enablement Network Channel Control frame was generated. The length of the Reason Result Code field is 1 octet. The reason result codes that have been allocated are shown in Table 8-134 Table 8-45af3.

# Text boxes

Abstract

This document presents resolution to comments 196, 202, 557, 605, 626, 896.