IEEE P802.11
Wireless LANs

| LB176 Proposed Resolutions for Clause 10.ae1 |
| --- |
| Date: 2011-05-06 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | +1 408 543 3370 | mfischer@broadcom.com |
| Michael Montemurro | Research in Motion | 4701 Tahoe Blvd, Mississauga, ON. CANADA. L4W 0B4 | +1 905 629 4746 | mmontemurro@rim.com |

Discussion of proposed changes:

| 3063 | Hunter, David | 10.ae1.2 | 34 | 3 |  | A bit of broken English, plus the implication (by using "every") that a single classification applies to all QMF frames. | Replace "classification by transmitting STA for every QMF frame" with "classification made by the transmitting STA for each QMF frame". | P – editor to make changes found in 11-11-0679r0 under the heading CID 3063 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

CID 3063, 3008, 3124, 3095, 3064

SEE ALSO CID 3137

10.ae1.2 Quality-of-Service Management Frame Policy Advertisement and Configuration Procedures

QMF policies are exchanged and implemented between two QMF STAs. QMF policy is communicated through the QMF Policy element as described in 8.4.2.ae1 (Quality-of-ServiceManagement Frame Policy element). A STA shall not transmit a QMF Policy element with both the Individually Addressed and Group Addressed subfields set to 0 in any of the included QACM subfields.

A non-AP QMF STA shall use the default QMF policy for transmissions of QMF frames to a peer QMF STA if it has not received a QMF policy from that STA. A non-AP QMF STA shall always apply the QMF policy received from a peer QMF STA.

The ACI classification for each QMF frame that is transmitted by a non-AP QMF STA is governed by the QMF policy  The ACI classification for each QMF frame that is transmitted by a QMF AP is governed by the QMF policy configured at that AP.

| 3064 | Hunter, David | 10.ae1.2 | 34 | 10 |  | This requirement implies that the transmitter shall use whatever policy it receives, from whatever source. | At the end of the sentence insert "from the receiving QMF STA". | P – insert “from a peer QMF STA.” |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3065 | Hunter, David | 10.ae1.2 | 34 | 14 |  | Assuming this "can" does not mean "may", the sentence is clearer if reworded. The current sentence is also run-on. | Replace "can be reconfigured, for example, vendor-specific" with "is reconfigurable. For example, vendor-specific". | P – Editor to change "can be reconfigured, for example, vendor-specific" to "can be reconfigured between peer STAs. For example, vendor-specific" and change “may” to “can” – see CID 3096 |
| 3096 | Montemurro, Michael | 10.ae1.2 | 34 | 14 |  | This should be qualified to say that it happens between peer STAs. | Change "can be reconfigured" to "can be reconfigured between peer STAs" | P – see CID 3065 |
| 3066 | Hunter, David | 10.ae1.2 | 34 | 16 |  | The description "the complete QMF policy or the partial QMF policy" implies that there is only one of each. The form of this sentence is better supported by using "complete QMF policy" and "partial QMF policy as mass terms. | Replace "the complete QMF policy or the partial QMF policy" with "complete QMF policy and partial QMF polidy". | P – as per the comment without the spelling error |
| 3008 | Chu, Liwen | 10.ae1.2 | 34 | 3 |  | "The ACI classification by transmitting STA for every QMF frame is governed by the QMF policy obtained from the receiving STA." Is this true if transmitting STA is an AP? | Clarify it. | P - editor to make changes found in 11-11-0679r1 under the heading CID 3008 |
| 3124 | Ptasinski, Henry | 10.ae1.2 | 34 | 3 |  | Incomprehensible sentence. | Change to “The ACI classification used by a transmitting STA for” | P - editor to make changes found in 11-11-0679r1 under the heading CID 3124 |
| 3138 | Stephens, Adrian | 10.ae1.2.1 | 34 | 19 |  | "State 1 and State 2 management frames" - there is no such thing. | Consider replacing "State" with "Class" | A |
| 3095 | Montemurro, Michael | 10.ae1.2 | 34 | 3 |  | Change " by transmitting" to "for the transmitting" | As in comment. | P - editor to make changes found in 11-11-0679r1under the heading CID 3095 |
| 3068 | Hunter, David | 10.ae1.2.1 | 35 | 16 |  | Values of fields are written as numerals. | Replace "zero" with "0" on lines 16 and 32, and on lines 18 and 36 replace "one" with "1". | P - editor to make changes found in 11-11-0679r1 under the heading CID 3068 |
| 3069 | Hunter, David | 10.ae1.2.1 | 35 | 16 |  | "Beacon frame". | Replace "beacon frame" with "Beacon frame". | P - editor to make changes found in 11-11-0679r1 under the heading CID 3069 |
| 3104 | Pandey, Santosh | 10.ae1.2.1 | 35 | 36 |  | This paragraph seems to have a lot of overlap from the 3rd paragraph of this subclause | Suggest deleting this paragraph after - Moving 2nd sentence from this paragraph "The associated QMF STA … " after the second sentence in second paragraph of this subclause - Moving the last sentence from this paragraph " If the AP rejects … " after the last sentence in the fifth paragraph of this subclause - Adding "A QMF AP may send an unsolicited QMF Policy frame to an associated QMF STA with status code set to 0 (Successful)." at the end of 3rd paragraph of this subclause | P - editor to make changes found in 11-11-0679r1 under the heading CID 3104 |

CID 3068, 3069, 3104

10.ae1.2.1 QMF policy communication in a BSS, IBSS or MBSS

A QMF Policy frame is sent by a QMF STA to configure a QMF policy at a peer QMF STA in a BSS, IBSS or MBSS. A QMF Policy Change frame is sent by a QMF STA to request a change to its QMF Policy for the peer QMF STA in a BSS, IBSS, or MBSS.

A non-AP QMF STA operating in a BSS shall not transmit a QMF Policy frame to an AP. A STA may send a QMF Policy Change frame to request a change in the QMF policy at a peer STA. A non-AP QMF STA that receives a QMF Policy Change frame may either accept or reject the request. An associated non-AP QMF STA may send a QMF Policy Change to the QMF AP in its BSS only if the most recently received Extended Capabilities element from the AP has its QMFReconfigurationActivated subfield equal to 1. If the AP rejects the request, the associated QMF STA shall not request the same policy reconfiguration from the AP within the lifetime of its association.

An AP shall respond to a QMF Policy Change frame received from an associated STA by transmitting a QMF Policy frame. If the QMFReconfigurationActivated subfield is 0 in the Extended Capabilities element in the Beacon frame, an AP that receives a QMF Policy Change frame from an associated STA shall respond with a QMF Policy frame, with the current QMF Policy element and status code set to 37 (The request has been declined). If the QMFReconfigurationActivated subfield is 1 in the Extended Capabilities element in the Beacon frame, an AP that receives a QMF Policy Change frame from an associated STA shall evaluate the QMF Policy included in the frame, and shall respond to the request with the resulting QMF Policy element and status code set to 0 (Successful) if it accepts the policy change, or 37 (The request has been declined) if it rejects the policy change. A QMF AP may send an QMF Policy frame with status code set to 0 (Successful) to an associated QMF STA without having first received a QMF Policy Change frame from that STA.

If an accept status is received in a QMF Policy frame within dot11QMFPolicyChangeTimeout of having transmitted a QMF Policy Change frame to the STA that transmitted the QMF Policy frame, then the receiver of the QMF Policy Change frame shall transmit any subsequently queued management frames to the STA that transmitted the QMF Policy Change frame in accordance with the changes to the QMF policy that were indicated in the QMF Policy frame.

If a reject status is received as a response to a QMF Policy Change frame, then the configuration change request is rejected and the STA continues to transmit Management frames in accordance with the previously configured QMF policy. The requesting STA shall not retry the same configuration change request within dot11QMFPolicyChangeTimeout from the time the requesting STA received the rejection frame.

If the requesting STA does not receive a QMF Policy frame in response to a QMF Policy Change frame within dot11QMFPolicyChangeTimeout, then the requesting STA shall continue to transmit frames according to the previously configured QMF policy.

If a QMF STA has received an Extended Capabilities element with the QMFReconfigurationActivated subfield equal to 0 or has not received an Extended Capabilities element from a destination QMF STA, the QMF STA shall not transmit a QMF Policy Config Request frame to the destination QMF STA.

References:

# Text boxes

Abstract

This document provides proposed resolutions for comments to clause 10.ae1 from LB176 (TGae D3.0 LB).