IEEE P802.11
Wireless LANs

| Mesh power management |
| --- |
| Date: 2011-05-10 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |
| Jarkko Kneckt | Nokia Corporation | Itämerenkatu 11 – 13, 00180 Halsinki Finland | +358-50-4821550 | Jarkko.Kneckt(at)Nokia.com |

## Summary of the intention of this document

- In D11.0, power management for mesh STA contains many ambiguities. This submission is trying to clarify the following points:

  - Operation of “peer-specific mesh power mode” and related terminologies.

  - Operation of “non-peer mesh power mode” and related terminologies.

  - Refine the text in defining frame fields format

- Potential discussion tpics:

  - Change “link-specific” to “peer-specific” in clause 11C.13 globally.

## Suggested changes to the draft spec

Apply the following changes.
Corresponding changes to D11.0 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor, except the amendment to the existing text in the base standard.

Instruction to the TGs editor: amend the following text and table as indicated by “track changes”t.

- Definitions

active mode: A mesh power mode in which the mesh station (STA) operates in the Awake state for the corresponding neighbor mesh STA.

deep sleep mode: A mesh power mode in which the mesh station (STA) operates either in the Awake state or in the Doze state, and is not expected to receive Beacons from the corresponding neighbor mesh STA.

light sleep mode: A mesh power mode in which the mesh station (STA) operates either in the Awake state or in the Doze state, and is expected to receive Beacon frames from the corresponding neighbor peer mesh STA.

mesh peer service period (MPSP): (CID148)A contiguous period of time during which one or more individually addressed frames are transmitted between two peer mesh stations (STAs) with at least one of those mesh STAs operating in light sleep or deep sleep mode(CID140). A mesh peer service period is directional and may contain one or more TXOPs. A mesh STA may have multiple mesh peer service periods ongoing in parallel. No more than one mesh peer service period may be set up in each direction with each peer mesh STA.

mesh power mode: The activity level identifier of a mesh station (STA) set per mesh peering or seen from non-peer neighbor STAs. A lower activity level enables a mesh STA to reduce its power consumption.

MPSP owner: A mesh STA that is the owner of the mesh peer service period. It obtains TXOPs, transmits individually addressed frames to the recipient mesh STA in the mesh peer service period and terminates the mesh peer service period.

non-peer mesh power mode: The activity level identifier of a mesh station (STA) toward non-peer neighbor mesh STAs. Two non-peer mesh power modes are defined: active mode and deep sleep mode.

peer-specific mesh power mode: The activity level identifier of a mesh station (STA) set per mesh peering. Three mesh power modes are defined: active mode, light sleep mode, and deep sleep mode.

- Mesh power management

A mesh STA can manage the activity level of its links per mesh peering. A mesh STA sets each of its mesh peerings to either active mode, light sleep mode, or deep sleep mode. The mesh STA tracks the power mode of each of its neighbor peer mesh STAs, and delivers the frames based on the rules defined in 11C.13 (Power save in a mesh BSS).

- Power Management field

Change 7.1.3.1.6 as follows:

The Power Management field is 1 bit in length and is used to indicate the power management mode of a STA. The value of this field remains constant in each frame from a particular STA within a frame exchange sequence. The value indicates the mode in which the station will be after the successful completion of the frame exchange sequence.

In an infrastructure BSS or in an IBSS the following applies:

A value of 1 indicates that the STA will be in PS mode. A value of 0 indicates that the STA will be in active mode. This field is always set to 0 in frames transmitted by an AP.

In an MBSS the following applies:

A value of 0 in group addressed frames, in management frames transmitted to non-peer STAs, and in Probe Response frames indicates that the mesh STA’s all peer-specific mesh power modes and non-peer mesh power mode will be active mode. A value of 1 in group addressed frames, in management frames transmitted to non-peer STAs, and in Probe Response frames indicates that the mesh STA’s non-peer mesh power mode will be deep sleep mode.

A value of 0 in individually addressed frames transmitted to a peer mesh STA indicates that the mesh STA’s peer-specific mesh power mode for the recipient mesh STA will be active mode A value of 1 in individually addressed frames transmitted to a peer mesh STA, except Probe Response frames, indicates that the mesh STA’s peer-specific mesh power mode for the recipient mesh STA will be either light sleep mode or deep sleep mode. When the QoS Control field is present in the frame, the Mesh Power Save Level subfield in the QoS Control field indicates whether the mesh STA will be in light sleep mode or in deep sleep mode for the recipient mesh STA as specified in 7.1.3.5.10 (Mesh Power Save Level subfield).

The mesh power mode transition rules are described in 11C.13.3 (Mesh power mode indications and transitions).

- More Data field(changed per CID126)

Insert the following paragraph after the fourth paragraph of 7.1.3.1.7:

The More Data field is set to 1 in individually addressed frames transmitted by a mesh STA to a peer mesh STA that is either in light sleep mode or in deep sleep mode for the corresponding mesh peering, when additional BUs remain to be transmitted to this peer mesh STA.

Insert the following paragraph to the end of 7.1.3.1.7:

The More Data field is set to 1 in group addressed frames transmitted by a mesh STA when additional group addressed BUs remain to be transmitted. The More Data field is set to 0 in group addressed frames transmitted by a mesh STA when no more group addressed BUs remain to be transmitted.

- EOSP (end of service period) subfield

Insert the following paragraph to the end of 7.1.3.5.2:

The mesh STA uses the EOSP subfield to indicate the end of the current mesh peer service period (MPSP) in which it operates as the owner. The mesh STA sets the EOSP subfield to 1 in its transmission and retransmissions of the MPSP’s final frame to end an MPSP, and sets it to 0 otherwise. See 11C.13.9.4 (Termination of a mesh peer service period) for details.

- Mesh Power Save Level subfield

The Mesh Power Save Level field is 1(CID123) bit in length and indicates whether the mesh STA’s peer-specific mesh power mode will be deep sleep mode or light sleep mode after the successful completion of the frame exchange sequence.

When the Power Mangement field in the Frame Control field in the frame is 1, the following applies:

In individually addressed Mesh Data frames a value of 0 indicates that the mesh STA’s peer-specific mesh power mode for the recipient mesh STA will be light sleep mode (see 11C.13.8.3 (Operation in light sleep mode)). In individually addressed Mesh Data frames a value of 1 indicates that the mesh STA’s peer-specific mesh power mode for the recipient mesh STA will be deep sleep mode (see 11C.13.8.4 (Operation in deep sleep mode)).

In group addressed Mesh Data frames a value of 0 indicates that none of the peer-specific mesh power modes of the mesh STA will be deep sleep mode. In group addressed Mesh Data frames a value of 1 indicates that at least one of the peer-specific mesh power modes of the mesh STA is deep sleep mode.

The Mesh Power Save Level subfield is reserved if the Power Management field in the Frame Control field is 0.

- Receiver Service Period Initiated (RSPI) subfield

The Receiver Service Period Initiated (RSPI) subfield is 1(CID123) bit in length. The subfield is set to 0 to indicate that the mesh peer service period, of which the receiver of this frame is owner, is not initiated. The subfield is set to 1 to indicate that the mesh peer service period, of which the receiver of this frame is owner, is initiated. The use of the(CID122)  RSPI subfield is described in 11C.13.9.2 (Initiation of a mesh peer service period). The RSPI subfield is reserved in group addressed frames.

- Mesh Capability

The Mesh Capability field comprises a set of values indicating whether a mesh STA is a possible candidate for mesh peering establishment. The details of the Mesh Capability field are shown in Figure 7-95o132 (Mesh Capability field).

| B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Accepting Additional Mesh Peerings | MCCA Supported | MCCA Enabled | Forwarding | MBCA Enabled | TBTT Adjusting | Mesh Power Save Level | Reserved |
| Bits: 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Mesh Capability field |

The Accepting Additional Mesh Peerings subfield is set to 1 if the mesh STA is willing to establish additional mesh peerings with other mesh STAs and set to 0 otherwise (i.e., the Accepting Additional Mesh Peerings subfield is set in accordance with dot11MeshAcceptingAdditionalPeerings). When the Mesh Configuration element is included in the Mesh Peering Open frame and in the Mesh Peering Confirm frame, the Accepting Additional Mesh Peerings subfield is set to 1.

The MCCA Supported subfield is set to 1 if the mesh STA implements MCCA and set to 0 otherwise (i.e., the MCCA Supported subfield is set in accordance with dot11MCCAImplemented).

The MCCA Enabled subfield is set to 1 if the mesh STA is using the MCCA and set to 0 otherwise (i.e., the MCCA Enabled subfield is set in accordance with dot11MCCAActivated).

The Forwarding subfield is set to 1 if the mesh STA forwards MSDUs and set to 0 otherwise (i.e., the Forwarding subfield is set in accordance with dot11MeshForwarding).

The MBCA Enabled subfield is set to 1 if the mesh STA is using MBCA, and is set to 0 otherwise (i.e., the MBCA Enabled subfield is set in accordance with dot11MBCAActivated). (See 11C.12.4 (Mesh beacon collision avoidance (MBCA)).)

The TBTT Adjusting subfield is set to 1 while the TBTT adjustment procedure is ongoing, and is set to 0 otherwise. (See 11C.12.4.4.3 (TBTT scanning and adjustment procedures).)

The Mesh Power Save Level subfield is set to 1 if any of the peer-specific mesh power modes is deep sleep mode and set to 0 otherwise. The Mesh Power Save Level subfield is reserved when the Power Management field in the Frame Control Field is set to 0.  See 7.1.3.5.10.

- Power save in a mesh BSS

- General

A mesh STA may leverage mesh power mode to reduce its power consumption. A mesh STA manages each of its mesh peerings with peer-specific mesh power mode as described in 11C.13.2.1 (Peer-specific mesh power modes). A mesh STA may set independent mesh power mode to each of its mesh peerings. A mesh STA also manages a non-peer mesh power mode as described in 11C.13.2.2 (Non-peer mesh power mode). When a mesh STA is in light sleep mode or in deep sleep mode for a mesh peering, the mesh STA shall maintain its mesh awake window as described in 11C.13.6 (Mesh awake window).

A mesh STA shall have the capability to buffer frames and track the peer-specific mesh power modes that are set by each peer mesh STAs for the mesh peerings with the mesh STA, as described in 11C.13.7 (Power save support). A mesh STA shall use mesh peer service periods for individually addressed frame transmissions to neighbor peer mesh STAs that are either in light sleep mode or in deep sleep mode for the corresponding mesh peering, as described in 11C.13.9 (Mesh peer service periods). A mesh STA transmits group addressed frames after the Beacon frame containing DTIM when any of its peer mesh STAs is in light sleep mode or deep sleep mode for the mesh peering with the mesh STA (see 11C.13.4 and 11C.13.5). These capabilities are referred to as support for power save.

- Mesh power modes

A mesh STA is in one of two different power states, Awake or Doze, as defined in 11.2.1.1.

The manner in which a mesh STA transitions between power states is determined by the combination of peer-specific mesh power modes and a non-peer mesh power mode. A mesh STA shall be in Awake state if any of the conditions specified in 11C.13.8.5 (Conditions for Doze state) is not fulfilled. A mesh STA maintains peer-specific mesh power modes for each of its mesh peerings as described in 11C.13.2.1 (Peer-specific mesh power modes). A mesh STA may have a different peer-specific mesh power mode for each mesh peering. A mesh STA maintains a non-peer mesh power mode for non-peer mesh STAs that is described in 11C.13.2.2 (Non-peer mesh power modes). An example illustration of the use of peer specific and non-peer mesh power modes is shown in Figure 11C-5 (An example of mesh power mode usage).

- Peer-specific mesh power modes

The peer-specific mesh power mode specifies the activity level of the mesh STA on the corresponding mesh peering. Three mesh power modes are defined: active mode, light sleep mode, and deep sleep mode. Each peer-specific mesh power modes are defined as follows:

- Active mode: The mesh STA shall be in Awake state all the time.

- Light sleep mode: The mesh STA alternates between Awake and Doze states, as specified in 11C.13.8.3 (Operation in light sleep mode). The mesh STA shall listen to all the Beacon frames from the corresponding peer mesh STA.

- Deep sleep mode: The mesh STA alternates between Awake and Doze states, as specified in 11C.13.8.4 (Operation in deep sleep mode). The mesh STA may choose not to listen to the Beacons from the corresponding peer mesh STA.

The combination of the Power Management field in the Frame Control field and the Mesh Power Save Level subfield in the QoS Control field contained in Mesh Data frame indicates the peer-specific mesh power mode in use as shown in the Table 11C-31 (Mesh power mode definition).

| Peer-specific mesh power mode definition |
| --- |
| Activity level | Peer-specific mesh power mode | Power Management field | Mesh Power Save Level subfield |
| Highest Lowest | Active mode | 0 | Reserved |
|  | Light sleep mode | 1 | 0 |
|  | Deep sleep mode | 1 | 1 |

An example of mesh power mode usage

- Non-peer mesh power modes

The non-peer mesh power mode indicates the mesh power mode of the mesh STA toward the non-peer mesh STAs. Two non-peer mesh power modes are defined: active mode and deep sleep mode. The non-peer mesh power mode is indicated by the Power Management field in the Frame Control field in group addressed frames, management frames transmitted to non-peer neighbor STAs, and in Probe Response frames. When the Power Management field in the Frame Control field is set to 1, the non-peer mesh power mode is deep sleep mode. When the Power Management field in the Frame Control field is set to 0, the non-peer mesh power mode is active mode.

The non-peer mesh STAs may send Probe Request and Mesh Peering Open Request frames to the mesh STA that sets non-peer mesh power mode to deep sleep mode only during the mesh awake window of the mesh STA.

- Mesh power mode indications and transitions

- General

When a mesh STA is in active mode for a mesh peering, it shall set the Power Management field in the Frame Control field to 0 in all individually addressed Mesh Data or QoS Null frames transmitted to the corresponding peer mesh STA.

When a mesh STA is in light sleep mode for a mesh peering, it shall set the Power Management field in the Frame Control field to 1 and the Mesh Power Save Level subfield in the QoS Control field to 0 in all individually addressed Mesh Data or QoS Null frames transmitted to the corresponding peer mesh STA.

When a mesh STA is in deep sleep mode for a mesh peering, it shall set the Power Management field in the Frame Control field to 1 and the Mesh Power Save Level subfield in the QoS Control field to 1 in all individually addressed Mesh Data or QoS Null frames transmitted to the corresponding mesh STA.

When a mesh STA is in deep sleep mode for any of its mesh peerings, the Mesh Power Save Level subfield in the QoS Control field in group addressed Mesh Data frames and the Mesh Power Save Level subfield in the Mesh Capability field in the Mesh Configuration element shall be set to 1. When a mesh STA is not in deep sleep mode for any of its mesh peerings, these subfields shall be set to 1.

To change peer-specific mesh power modes, a mesh STA shall inform its peer mesh STAs through a successful frame exchange initiate by the mesh STA. The Power Management field in the Frame Control field and the Mesh Power Save Level subfield in the QoS Control field of the frame sent by the mesh STA in this exchange indicates the peer-specific mesh power mode that the STA shall adopt upon successful completion of the entire frame exchange.

The algorithm to trigger the change of peer-specific mesh power mode is beyond the scope of this standard.

The non-peer mesh power mode is determined by peer-specific mesh power modes of the mesh STA. When a mesh STA is in light sleep mode or deep sleep mode for at least one mesh peering, it shall set the non-peer mesh power mode to deep sleep mode.

When a mesh STA is in active mode for non-peer STAs, it shall set the Power Management field in the Frame Control field to 0 in all group addressed frames, management frames transmitted to non-peer STAs, and in Probe Response frames.

When a mesh STA is in deep sleep mode for non-peer STAs, it shall set the Power Management field in the Frame Control field to 1 in all group addressed frames, management frames transmitted to non-peer STAs, and in Probe Response frames.

- Transition to a higher activity level

A mesh STA may use group addressed or individually addressed Mesh Data or QoS Null frames to change its mesh power mode to a higher activity level, for example; from deep sleep to light sleep or to active mode; or from light sleep to active mode.

Individually addressed frames may be used to temporarily raise the activity level of the mesh STA for a mesh peering. This is useful in cases when a link temporarily requires efficient data transmission with the peer mesh STA and the mesh STA desires to be able to transit back to lower activity level without performing the mesh power mode transition signaling with all peer mesh STAs.

- Transition to a lower activity level

A mesh STA shall use acknowledged individually addressed Mesh Data or QoS Null frames to change its peer-specific mesh power mode to a lower activity level, for example; from active mode to light or deep sleep mode; or from light sleep to deep sleep mode.

- TIM transmissions in an MBSS

The TIM element identifies the peer mesh STAs in light sleep mode or deep sleep mode for which traffic is pending and buffered in the reporting mesh STA. This information is coded in a partial virtual bitmap, as described in 7.3.2.6 (TIM element). In addition, the TIM contains an indication whether group addressed traffic is pending. Every neighbor peer mesh STA is assigned an AID by the reporting mesh STA as part of the mesh peering establishment process (see 11C.3.1 (General)). The mesh STA shall identify those peer mesh STAs for which it is prepared to deliver buffered MSDUs and MMPDUs by setting bits in the TIM's partial virtual bitmap that correspond to the appropriate AIDs.

- TIM types

There are two different TIM types: TIM and DTIM. A mesh STA shall transmit a TIM with every Beacon frame. Every DTIMPeriod, a TIM of type DTIM is transmitted with a Beacon frame. After transmitting a Beacon containing a DTIM, the mesh STA shall send the buffered group addressed MSDUs and MMPDUs, before transmitting any individually addressed frames. The More Data field of each group addressed frame shall be set to indicate the presence of further buffered group addressed MSDUs and MMPDUs. The mesh STA sets the More Data field to 0 in the last transmitted group addressed frame following the transmission of the DTIM Beacon.

When a mesh STA expects to receive a group addressed frame and CCA is IDLE for the duration of the PHY specific Group Delivery Idle Time, the receiving mesh STA may assume that no more frames destined to group addresses will be transmitted and may return to Doze state. The Group Delivery Idle Time is identical to the TXOP Limit for AC_VI specified by the default EDCA Parameter Set shown in Table 7-37.

- Mesh awake window

A mesh STA shall be in Awake state when its mesh awake window is active. A mesh awake window is active after the Beacon and Probe Response frames containing the Mesh Awake Window element. A mesh STA shall include the Mesh Awake Window element in its DTIM Beacon frames and may include the Mesh Awake Window element in its TIM Beacon and Probe Response frames. A mesh STA that operates in light sleep mode or deep sleep mode for any of its mesh peer-specific mesh power mode shall include the Mesh Awake Window element in its Beacon frame if the Beacon frame indicates buffered traffic for at least one peer mesh STA. The start of the mesh awake window is measured from the end of the Beacon or Probe Response transmission. The duration of the mesh awake window period is specified by dot11MeshAwakeWindowDuration. A mesh STA shall set the Mesh Awake Window field in the Mesh Awake Window element to dot11MeshAwakeWindowDuration. If the Mesh Awake Window element is not contained in the Beacon frame of a mesh STA, the duration of the mesh awake window period following this Beacon is zero.

If the mesh STA that has its mesh awake window active transmits frames destined to group addresses, the duration of the mesh awake window is extended by an additional PostAwakeDuration. The PostAwakeDuration follows the group address frame, and the mesh STA that has its mesh awake window active shall stay in Awake state until it has transmitted all of its group addressed frames and the PostAwakeDuration has expired. The PostAwakeDuration is equal to duration of the mesh awake window.

Peer mesh STAs may send a frame to the mesh STA that is in light or deep sleep mode for the corresponding mesh peerings when the mesh awake window of the light or deep sleep mode mesh STA is active. A successfully transmitted peer trigger frame initiates a mesh peer service period as described in 11C.13.9 (Mesh peer service periods) that allows contiguous frame transmissions.

Non-peer mesh STAs may send class 1 or class 2 frames, such as Probe Request or Mesh Peering Open frames, to the mesh STA that is in deep sleep mode for non-peer mesh STAs when the mesh awake window of the deep sleep mode mesh STA is active.

- Power save support

As described in 11C.13.2 (Mesh power modes), a mesh STA indicates its peer-specific mesh power mode for each mesh peering and obtains the peer-specific mesh power modes of its peer mesh STAs on the corresponding link. A mesh STA shall not arbitrarily transmit frames to mesh STAs operating in a light or deep sleep mode, but shall buffer frames and only transmit them at designated times.

A mesh STA shall only transmit frames to a mesh STA operating in a light or deep sleep mode if the recipient mesh STA is in the Awake state as defined in 11C.13.8.3 (Operation in light sleep mode), 11C.13.8.4 (Operation in deep sleep mode), and 11C.13.9 (Mesh peer service periods); otherwise, the mesh STA shall buffer frames.

As described in 11C.13.4 (TIM transmissions in an MBSS), a mesh STA indicates the presence of buffered traffic in TIM elements for all peer mesh STAs that operate in light or deep sleep mode toward the mesh STA. The mesh STA sets the bit for AID 0 (zero) in the bit map control field of the TIM element to 1 when group addressed traffic is buffered, according to 7.3.2.6 (TIM element). As described in 11C.13.5 (TIM types), a mesh STA transmits its group addressed frames after its DTIM Beacon if any of its peer mesh STA is in light or deep sleep mode toward the mesh STA.

As described in 11C.13.9 (Mesh peer service periods), mesh peer service periods are used for frame transmissions towards a mesh STA that operates in light or deep sleep mode. Mesh peer service periods are not used in frame exchanges towards active mode mesh STAs.

A mesh STA may initiate a mesh peer service period with a peer mesh STA in deep or light sleep mode by transmitting a peer trigger frame when the mesh awake window of the peer mesh STA is active.

- Operations in each mesh power mode

- General

Detailed operations of mesh STA in each mesh power mode are described in the following subclauses. Figure 11C-6 (Mesh power management operation) depicts example power state transitions of mesh STAs, when three mesh STAs are in the mesh power modes shown in the Figure 11C-5 (An example of mesh power mode usage).

Mesh power management operation

- Operation in active mode

If a mesh STA is in active mode for a mesh peering or for non-peer mesh STAs, it shall be in Awake state. Mesh peer service periods are not used in frame exchanges toward active mode mesh STAs.

Active mode mesh STA may receive peer trigger frames from a peer mesh STA in light or deep sleep mode at all times when there is no mesh peer service period ongoing between the peer mesh STAs.

- 11C.13.8.3 Operation in deep sleep mode

If a mesh STA is in deep sleep mode for non-peer mesh STAs, it shall enter the Awake state prior to every TBTT of its own and shall remain in Awake state after the Beacon transmission for the duration of the mesh awake window and the duration of its group addressed frame transmissions, whichever occurs later. The mesh STA may receive frames when its mesh awake window is active as described in 11C.13.6 (Mesh awake window).

When a frame initiating a mesh peering management procedure, an authentication procedure, or a passive scanning procedure, the mesh STA in deep sleep mode for non-peer mesh STAs shall operate in Awake state at least until the completion of the mesh peering management procedure once it is initiated (see 11C.3 (Mesh peering management (MPM)) and 11C.5 (Authenticated mesh peering exchange (AMPE))), until the completion of the authentication procedure once it is initiated (see 11C.3.1 (General) and 11C.3.3 (Mesh authentication)), or the transmission of the Probe Response frame upon the reception of Probe Request frame.

If the mesh STA receives a peer trigger frame initiating a mesh peer service period from a peer mesh STA, the mesh STA shall remain in Awake state until the mesh peer service period is terminated as defined in 11C.13.9.4 (Termination of a mesh peer service period).

The mesh STA may return to Doze state after its mesh awake window if no frame initiating a response transaction or a mesh peer servie period is received during the mesh awake window.

NOTE—When a mesh STA is in light sleep mode or in deep sleep mode for a mesh peering, it sets its non-peer mesh power mode to deep sleep mode. This implies that a mesh STA operating in light sleep mode or in deep sleep mode for a mesh peering is required to conform to the rules described in 11C.13.8.3 (Operation in deep sleep mode).

11C.13.8.4 Additional operation in light sleep mode for a mesh peering

If a mesh STA is in light sleep mode for a mesh peering, it shall enter the Awake state prior to every TBTT of the corresponding peer mesh STA to receive Beacon frame from the peer mesh STA. The mesh STA may return to the Doze state after the Beacon reception from the peer mesh STA, to which it indicated to be in light sleep mode, if the peer mesh STA did not indicate buffered individually addressed or group addressed frames. If an indication of buffered individually addressed frames is received, the light sleep mode mesh STA shall send a peer trigger frame with RSPI field set to 1 to initiate a mesh peer service period with the mesh STA that transmitted the Beacon frame (see 11C.13.9.2 Initiation of a mesh peer service period). If an indication of buffered group addressed frames is received, the light sleep mode mesh STA shall remain Awake state after the DTIM Beacon reception to receive successive group addressed frames The mesh STA shall remain Awake state until the More Data field of a received group addressed frame is set to 0 or if no group addressed frame is received within the PHY specific Group Delivery Idle Time. (See 11C.13.5 (TIM types).)

11C.13.8.5 Additional operation in deep sleep mode for a mesh peering

A mesh STA operating in deep sleep mode for a mesh peering might not receive Beacon frames from the corresponding peer mesh STA as long as it maintains synchronization with the peer mesh STA. The logic of how the mesh STA in deep sleep mode maintains synchronization among neighbors is beyond the scope of this standard. Guidance for the synchronization maintenance by the mesh STA in deep sleep mode is given in Annex Y.3.6 (Synchronization maintenance of mesh STAs in deep sleep mode).

11C.13.8.6 Conditions for Doze state

A mesh STA may enter Doze state if all following conditions are fulfilled:

- The mesh STA operates in light sleep mode or deep sleep mode for all of its mesh peerings, as described in 11C.13.8.3 (Operation in light sleep mode) or 11C.13.8.4 (Operation in deep sleep mode)

- The mesh STA has no mesh peer service period ongoing, as described in 11C.13.9 (Mesh peer service periods)

- The mesh STA has no pending transaction of mesh peering management, authentication, nor passive scanning

- The mesh awake window indicated by the mesh STA has expired, as described in 11C.13.6 (Mesh awake window)

- The mesh STA has terminated its group addressed frames delivery sequence after its DTIM Beacon, as described in 11C.13.5 (TIM types)

Guidance for using the power save in mesh BSS and default parameter values are given in Annex Y.3 (Power save parameters selection).

- Mesh peer service periods

- General

Mesh peer service periods are used for individually addressed frame exchanges between neighbor peer mesh STAs in which at least one of the mesh STAs is in light or deep sleep mode for the corresponding mesh peering. A mesh peer service period is a contiguous period of time during which one or more individually addressed frames are transmitted between two peer mesh STAs. Within a mesh peer service period, a mesh STA may obtain multiple TXOPs. A mesh peer service period is directional. One mesh STA is the owner of the mesh peer service period. It obtains TXOPs in order to transmit Data frames or Management frames to the recipient in the mesh peer service period. At the end of the frame transmissions, the owner of the mesh peer service period terminates the mesh peer service period. The other mesh STA operates as the recipient of the mesh peer service period and does not obtain TXOPs for transmitting Data frames or Management frames to the owner of the mesh peer service period. A mesh STA may have multiple mesh peer service periods concurrently toward multiple neighbor peer mesh STAs. At most, one mesh peer service period is set up in each direction with each peer mesh STA.

A mesh peer service period is initiated by a peer trigger frame. Two mesh peer service periods may be initiated with a peer trigger frame. This enables both the transmitter and the receiver of the peer trigger frame to become the owner of a mesh peer service period. An example mesh peer service period between two mesh STAs in light or deep sleep mode is shown in Figure 11C-7 (Mesh peer service period). The numbering on the left-hand-side describes the phase of the operation: 1 indicates the Initiation phase, 2 indicates the data transmission phase, and 3 indicates the termination phase of the mesh peer service period.

Mesh peer service period

- Initiation of a mesh peer service period

A Mesh Data frame or a QoS Null frame that requires acknowledgement are used as a peer trigger frame. The RSPI and the EOSP subfields in the QoS Control field control the initiation of a mesh peer service period. Table 11C-32 (Mesh peer service period triggering with RSPI and EOSP field combinations in peer trigger frame) lists how mesh peer service periods shall be initiated with different combinations of RSPI and EOSP field values.

Mesh peer service periods are not used in frame transmission toward active mode mesh STAs.

| Mesh peer service period triggering with RSPI and EOSP field combinations in peer trigger frame |
| --- |
| RSPI | EOSP | Mesh peer service period triggering |
| 0 | 0 | One mesh peer service period is initiated. The transmitter of the trigger frame is the owner in the mesh peer service period. |
| 0 | 1 | No mesh peer service period is initiated. |
| 1 | 0 | Two mesh peer service periods are initiated. Both mesh STAs are owners in a mesh peer service period. |
| 1 | 1 | One mesh peer service period is initiated. The receiver of the trigger frame is the owner in the mesh peer service period. |

The mesh peer service period may be initiated in the following cases:

- A mesh STA in light or deep sleep mode receives a peer trigger frame during its mesh awake window as described in 11C.13.6 (Mesh awake window)

- A mesh STA in active mode receives a peer trigger frame from the peer mesh STA in light or deep sleep mode as described in 11C.13.8.2 (Operation in active mode)

- A mesh STA receives a peer trigger frame from the peer mesh STA in light sleep mode as described in 11C.13.8.3 (Operation in light sleep mode)

In addition, when a mesh STA uses MCCA with a neighbor peer mesh STA while in a light sleep mode for the corresponding mesh peering, a scheduled service period begins at the each MCCAOP start time as described in 11C.13.10 (MCCA use by power saving mesh STA). A mesh STA in a light or deep sleep mode shall enter the Awake state prior to the start time of scheduled service period.

- Operation during a mesh peer service period

During the mesh peer service period, the owner and the recipient of the mesh peer service period shall operate in Awake state.The mesh peer service period may contain one or more TXOPs.

Reverse Direction Grant (RDG) shall not be used when the receiver of the TXOP operates in light or deep sleep mode for the link and the mesh peer service period toward the TXOP holder is not ongoing.

- Termination of a mesh peer service period

The mesh peer service period is terminated after a successfully acknowledged QoS Null or Mesh Data frame with the EOSP subfield set to 1 from the owner of the mesh peer service period.

If the mesh STA does not receive an acknowledgement to a frame that requires an acknowledgement and that is sent with the EOSP subfield set to 1, the mesh STA shall retransmit that frame at least once within the same mesh peer service period—subject to applicable retry or lifetime limit. The maximum number of retransmissions within the same mesh peer service period is the lesser of the Max Retry Limit and the MIB attribute dot11MeshSTAMissingAckRetryLimit.

NOTE—If an Ack to the retransmission of this last frame in the same mesh peer service period is not received, the mesh STA might use the next mesh peer service period to further retransmit that frame subject to the applicable retry or lifetime limit.

- MCCA use by power saving mesh STA

When dot11MCCAActivated is true and the mesh STA establishes MCCAOPs, the mesh STA shall be in active mode or light sleep mode towards the neighbor peer mesh STAs with which it has established MCCAOPs.

A scheduled mesh peer service period begins at the MCCAOP start time, if the MCCAOP responder operates in light sleep mode for the MCCAOP owner. The MCCAOP owner is the owner of the scheduled mesh peer service period. The MCCAOP responder is the recipient of the scheduled mesh peer service period. Scheduled mesh peer service periods are not used if the MCCAOP responder is in active mode for the MCCAOP owner.

The scheduled mesh peer service period continues until it is successfully terminated by the acknowledged QoS Null or Mesh Data frame with the EOSP subfield set to 1 from the owner of the mesh peer service period to the recipient of the mesh peer service period as described in 11C.13.9 (Mesh peer service periods).

- Power save parameters selection

- General

Power save mechanisms enable mesh STA operation in Doze state. In Doze state a mesh STA may set the transceivers off. The power save mechanism may adjust the mesh power mode of a mesh STA for various reasons that are beyond the scope of the standard, including but not limited to traffic load or scanning and network maintenance needs.

This annex specifies recommendations on how a mesh STA selects mesh power modes based on traffic load, recommendations on how to do scanning in mesh BSSs that may contain mesh STAs in light or deep sleep mode, and recommended default values for power save related parameters.

- Selecting the mesh power mode based on traffic load

A mesh STA may adjust its mesh power mode based on the traffic load or the QoS requirements of the forwarded traffic. If a mesh STA has high traffic load or a mesh STA is congested, the mesh STA should operate in active mode on the corresponding link to reduce delays or overhead that may be created by the operation in light or deep sleep mode.

A mesh STA may consider staying in active mode for all peer mesh STAs, even if only a single link is congested. When mesh STA operates in active mode, the mesh STA may receive frames at any time and mesh peer service periods may be triggered on demand, as in case of an AP that receives a trigger frame at times controlled by a non-AP STA.

If traffic load is moderate or low and best effort data is transmitted, a mesh STA may consider staying in light sleep mode for all or some mesh peerings. The mesh STA in light sleep mode for a mesh peering receives Beacons from the peer mesh STA with periodic indication of buffered traffic.

If traffic load is low or no traffic is transmitted, a mesh STA may consider staying in deep sleep mode for a mesh peering. The mesh STA does not need to wake up to receive a Beacon from the peer mesh STA to which it is in deep sleep mode.

The mesh STA may use deep sleep mode to control the number of times it enters the Awake state to receive Beacon frame from a peer mesh STA. If the mesh STA is in deep sleep mode for all of its mesh peering, the mesh STA needs only to remain in Awake state during its own Beacon transmission and mesh awake window.

The mesh STA that forwards real time traffic (AC3 or AC2 with EDCA) should be in active mode for the corresponding link. A mesh STA forwarding real time traffic with EDCA may stay in light or deep sleep mode for the corresponding link, if the mesh STA is capable of initiating mesh peer service periods frequently and the other forwarding peer mesh STAs are in active mode. Poor handling of the mesh power modes may result to delays and inappropriate QoS of the forwarded MSDUs.

- Scanning of mesh BSSs

A mesh BSS may have mesh STAs that alternate Awake state and Doze state.. With active scanning only devices in Awake state at the transmission time of Probe Request frame may be found. However, with passive scanning also mesh STAs in light or deep sleep mode for a mesh peering can be found.

Since mesh STAs in light or deep sleep mode may transmit Beacons at long intervals, a mesh STA seeking for candidate mesh STAs for a new mesh peerings should perform passive scanning relatively for a longer time compared to passive scanning in BSS infrastructure mode. Mesh STAs in light or deep sleep mode with long DTIM interval might not be discovered with short scanning durations. Mesh STAs that operate in light or deep sleep mode for a mesh peering may use a short DTIM interval, if they intend to establish new mesh peerings.

- Default parameters

The following are the recommended default values for power save related parameters for mesh STAs:

| Default parameters for mesh STAs that intend to operate in light or deep sleep mode for mesh peerings |
| --- |
|  | For moderate power save | For aggressive power save |
| Beacon period | 200 TU | 800 TU |
| DTIM Period | 4 | 1 |
| Mesh awake window | 10 TU | 10 TU |

A mesh STA that is eager to conserve power and likely to remain in deep sleep mode with most of the mesh peerings should utilize the value from aggressive power save parameters.

Although mesh STAs may utilize individual parameters regardless of the parameters used by neighbor mesh STAs or peer mesh STAs, each implementer should recognize balance between the power save efficiency and delay in the service initiation.

- MSDU forwarding in an MBSS containing mesh STAs in light or deep sleep mode

The battery powered mesh STAs should avoid forwarding MSDUs, to avoid power consumption and possible additional delays and inefficiencies that power save mechanisms may cause. If a light or deep sleep mode mesh STA forwards MSDUs, it should select its mesh power mode based on the traffic load and the traffic type as described in Y.3.2 (Selecting the mesh power mode based on traffic load).

The mesh STAs that desire to save power may select the light or deep sleep mode for a mesh peering as follows:

- mesh STAs that are “mains powered” may apply light or deep sleep mode if they do not have MSDUs to forward

- mesh STAs that are “battery powered” and desire to minimize the power consumption may freely use all mesh power modes

Mesh STAs that are in light or deep sleep mode for a mesh peering may degrade the corresponding link metric value. The use of worse metric values reduces the probability of a link being used for MSDU forwarding. If the mesh STA will operate in active mode for the link in forwarding path, it should apply the link metric value without degradation.

- Synchronization maintenance of mesh STAs in deep sleep mode

A mesh STA in deep sleep mode might not receive Beacon frames from the corresponding peer mesh STA, but the mesh STA is required to  maintain synchronization among neighbor peer mesh STAs. Neighbor offset synchronization method imposes the maintenance of TSF offset values between neighbor peer mesh STAs, which generally requires the reception of Beacon frame or Probe Response frame. The simplest way to maintain the synchronization is that the mesh STA in deep sleep mode for a mesh peering listens to the corresponding peer mesh STA’s Beacon frame for certain periods and check the TSF offset value.

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D11.0, April 2011.

[1] Draft Specification.  doc.: IEEE P802.11-REVmb/D8.0, March 2011.

# Comments

Need to list  a complete set of CIDs here.

Change the Mesh STA A is in  active mode mesh power mode towards mesh STA B

To:

Mesh STA A is in active node peer-specific mesh power mode towards mesh STA B

May want to refine here.

Is it necessary to state “in light sleep mode or deep sleep mode” here?

Moved to later subclause describing “operation in deepsleep mode”

Un???

# Text boxes

Abstract

This document provides suggested resolution to CID 4001, 4002, 4079, 4080, 4081, 4082, 4083.