IEEE P802.11
Wireless LANs

| Mesh beaconing and synchronization |
| --- |
| Date: 2011-05-09 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |

## Summary of the intention of this document

- Resolves comments regarding to M-BS category

## Suggested changes to the draft spec

Apply the following changes.
Corresponding changes to D11.01 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor, except the amendment to the existing text in the base standard.

Instruction to the TGs editor: amend the following text and table as indicated by “track changes”t.

- Mesh neighbor offset synchronization

- Introduction

This mechanism manages the neighbor offset synchronization method with the specified neighbor STA.

- MLME-MESHNEIGHBOROFFSETSYNCSTART.request

- Function

This primitive requests to start the neighbor offset synchronization method with the specified neighbor STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETSYNCSTART.request(

PeerMACAddress

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to start the neighbor offset synchronization method. |

- When generated

This primitive is generated by the SME to start the neighbor offset synchronization method with the specified neighbor STA.

- Effect of receipt

On receipt of this primitive, the MLME commences the neighbor offset synchronization method and the calculation of the TSF timer offset value. The MLME subsequently issues an MLME-MESHNEIGHBOROFFSETSYNCSTART.confirm that reflects the results of this request.

- MLME-MESHNEIGHBOROFFSETSYNCSTART.confirm

- Function

This primitive reports the results of a mesh neighbor offset synchronization request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETSYNCSTART.confirm(

PeerMACAddress,

ResultCode,

TSFOffsetValue

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the neighbor offset synchronization is requested. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, TOO_MANY_NEIGHBORS, or NOT_SUPPORTED | Indicates the result of the mesh neighbor offset synchronization request. |
| TSFOffsetValue | Integer | –263 to (263–1) | Indicates the TSF offset value with the specified neighbor STA, expressed in twos complement in µs. Valid only if the ResultCode is SUCCESS. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MESHNEIGHBOROFFSETSYNCSTART.request and report the TSF offset value.

- Effect of receipt

The SME is notified of the results of the mesh neighbor offset synchronization request.

- MLME-MESHNEIGHBOROFFSETCALCULATE.request

- Function

This primitive requests a calculation result of the TSF timer offset value for the specified neighbor STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETCALCULATE.request(

PeerMACAddress

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to report the TSF offset value. |

- When generated

This primitive is generated by the SME to order a calculation of the TSF timer offset value with the specified neighbor STA.

- Effect of receipt

On receipt of this primitive, the MLME receives a Beacon or Probe Response frame and calculate the TSF timer offset value from the received frame. The MLME tries to receive a Beacon frame immediately after the issue of MLME-MESHNEIGHBOROFFSETCALCULATE.request even if the mesh STA does not listen to the Beacon frame from the specified neighbor STA regularly (i.e., in deep sleep mode toward the specified neighbor STA). The MLME subsequently issues an MLME-MESHNEIGHBOROFFSETCALCULATE.confirm that reflects the results of this request.

- MLME-MESHNEIGHBOROFFSETCALCULATE.confirm

- Function

This primitive reports the results of a mesh neighbor offset calculation request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETCALCULATE.confirm(

PeerMACAddress,

ResultCode,

TSFOffsetValue

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the Neighbor Offset Measure is requested. |
| ResultCode | Enumeration | SUCCESS, TIMEOUT, INVALID_PARAMETERS, or NOT_SUPPORTED | Indicates the result of the mesh neighbor offset calculation request. |
| TSFOffsetValue | Integer | –263 to (263–1) | Indicates the TSF offset value with the specified neighbor STA, expressed in twos complement in µs. Valid only if the ResultCode is SUCCESS. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MESHNEIGHBOROFFSETCALCULATE.request to report a TSF offset value .

- Effect of receipt

The SME is notified of the results of the mesh neighbor offset calculation request.

- MLME-MESHNEIGHBOROFFSETSYNCSTOP.request

- Function

This primitive requests to stop the neighbor offset synchronization method with the specified neighbor STA.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETSYNCSTOP.request(

PeerMACAddress

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to stop the neighbor offset synchronization method. |

- When generated

This primitive is generated by the SME to stop the maintenance of the neighbor offset synchronization method with the specified neighbor STA.

- Effect of receipt

On receipt of this primitive, the MLME stops the neighbor offset synchronization method with the specified peer. The MLME subsequently issues an MLME-MESHNEIGHBOROFFSETSYNCSTOP.confirm that reflects the results of this request.

- MLME-MESHNEIGHBOROFFSETSYNCSTOP.confirm

- Function

This primitive reports the results of a neighbor offset synchronization method stop request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-MESHNEIGHBOROFFSETSYNCSTOP.confirm(

PeerMACAddress,

ResultCode,

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Valid individual MAC address | Specifies the address of the peer MAC entity to which the Neighbor Offset Stop is requested. |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, or NOT_SUPPORTED | Indicates the result of the mesh neighbor offset synchronization stop request. |

- When generated

This primitive is generated by the MLME as a result of an MLME-MESHNEIGHBOROFFSETSYNCSTOP.request.

- Effect of receipt

The SME is notified of the results of the mesh neighbor offset synchronization stop request.

- Synchronization and beaconing in MBSSs

- TSF for MBSSs

A mesh STA shall initialize and update its TSF timer depending on its active synchronization method. Each mesh STA shall maintain a TSF timer as described in 11.1.2, and conform to the TSF timer accuracy as described in 11.1.2.4.

- Extensible synchronization framework

- General

This standard introduces an extensible framework to enable the implementation of multiple synchronization methods for mesh STAs. Within the extensible synchronization framework, the neighbor offset synchronization method is defined as the default mandatory synchronization method in order to enable minimal synchronization capabilities and interoperability between mesh STAs that use MCCA, MBCA, or operate in light or deep sleep mode. The framework allows to integrate other synchronization methods for MBSSs. A vendor may implement any synchronization method using this framework to meet special application needs. Although a mesh STA may include multiple implementations of synchronisation methods, only one synchronization method shall be used by a mesh STA at a time and all the mesh STAs in an MBSS use the same synchronisation method. The active synchronization method is controlled by the SME and given to the MLME by dot11MeshActiveSynchronizationMethod.

Mesh STAs shall announce the active synchronization method using the Synchronization Method Identifier field in the Mesh Configuration element in their Beacon and Probe Response frames.

- Neighbor offset synchronization method

- General

When dot11MeshActiveSynchronizationMethod is neighborOffsetSynchronization (1), the mesh STA shall use the neighbor offset synchronization method as its active synchronization method, and maintain the timing offset value between its own TSF timer and the TSF timer of each neighbor STA with which it synchronizes. The mesh STA shall set the Synchronization Method Identifier field in the Mesh Configuration element to 1.

The mesh STA shall maintain synchronization with all of its neighbor peer mesh STAs. The mesh STA should maintain synchronization with up to dot11MeshNbrOffsetMaxNeighbor neighbor mesh STAs that are in the same MBSS. Additionally, the mesh STA should maintain synchronization with up to dot11MeshNbrOffsetMaxNeighbor neighbor STAs that are outside of the MBSS.

Upon receipt of an MLME-MESHNEIGHBOROFFSETSYNCSTART.request primitive, the MLME shall start synchronization using the neighbor offset synchronization method with the specified peer STA. Upon receipt of an MLME-MESHNEIGHBOROFFSETSYNCSTOP.request primitive, the MLME shall stop synchronization using the neighbor offset synchronization method with the specified peer STA.

A mesh STA that utilizes the neighbor offset synchronization method may start its TSF timer independently of other mesh STAs. The mesh STA shall calculate the timing offset value with respect to the neighbor STA, with which it maintains synchronization, as described in 11C.12.2.2.2 (Timing offset calculation). The mesh STA shall adjust its TSF timer based on time stamps received in Beacon or Probe Response frames from neighbor STAs, with which it maintains synchronization, as described in 11C.12.2.2.3 (Clock drift adjustment).

When the mesh STA alternates Awake state and Doze state, it may not listen to the Beacon frames of a neighbor mesh STA, with which it maintains synchronization, at all times. However, it shall conform to the clock drift compensation procedures and TSF jitter allowance as described in 11C.12.2.2.3 (Clock drift adjustment). See Y.3.6 (Synchronization maintenance of mesh STAs in deep sleep mode) for more guideline.

- Timing offset calculation

When dot11MeshActiveSynchronizationMethod is neighborOffsetSynchronization (1), the mesh STA shall calculate the timing offset value with respect to the neighbor STA with which it maintains synchronization. The calculation of the timing offset value is based on time stamps from the received Beacon and Probe Response frames as follows:

Toffset = Tt – Tr

where

Toffset is the timing offset value

Tt is the value in the Timestamp field in the received frame

Tr is the frame reception time measured in the TSF timer of the mesh STA

The offset value is represented as a signed integer. The unit of the offset value is µs. The mesh STA shall keep the Toffset value calculated from the latest Beacon or Probe Response frame received from each neighbor STA with which it maintains synchronization.

A mesh STA may translate the time measured in the TSF of the neighbor STA into the time base of its own TSF as follows:

Tself = Tneighbor – Toffset

where

Tself		 is the translated time in its own TSF

Tneighbor		 is the time measured in the TSF timer of the neighbor STA

Upon receipt of an MLME-MESHNEIGHBOROFFSETCALCULATE.request primitive, the MLME shall receive a Beacon or Probe Response frame from the specified neighbor STA, calculate the Toffset from the received frame, and report the calculated Toffset to the SME by responding with an MLME-MESHNEIGHBOROFFSETCALCULATE.confirm primitive. Toffset is used to provide the timing reference of neighbor STAs.

- Clock drift adjustment

When dot11MeshActiveSynchronizationMethod is neighborOffsetSynchronization (1), the mesh STA shall examine the reception time of the Beacon frames from neighbor STAs with which it maintains synchronization and adjust its TSF timer to compensate the relative timing error among neighbor mesh STAs caused by the clock drift. The mesh STA adjusts its TSF so that its TSF counting will be aligned to the most delaying neighbor STA.

When the mesh STA receives a Beacon frame or a Probe Response frame from one of the neighbor STAs with which it maintains synchronization, the mesh STA shall perform the following measurement procedure:

- The mesh STA checks if the transmitter of the Beacon frame or Probe Response frame is in the process of the TBTT adjustment (see 11C.12.4.4.3 (TBTT scanning and adjustment procedures)). If the received frame contains the Mesh Configuration element and the TBTT Adjusting subfield in the Mesh Configuration field is 1, the mesh STA shall invalidate the Toffset value for this neighbor STA and shall not perform the following steps.

- The mesh STA checks if it has a valid Toffset value obtained from the previous Beacon or Probe Response frame reception from the transmitter of the received frame. If it does not have the valid Toffset value, it shall not perform the following steps.

- The mesh STA calculates the clock drift amount TClockDrift by comparing the Toffset,p,the offset value obtained previously for this neighbor STA, and the Toffset,c, the offset value obtained from the current frame reception. 
		TClockDrift = Toffset, p – Toffset, c 
where TClockDrift is the clock drift amount in µs represented as a signed integer.

- The mesh STA shall compare the TClockDrift value with the TMaxClockDrift, the largest TClockDrift value obtained from other neighbor STA within this beacon period. If the TClockDrift value for this neighbor STA is greater than the TMaxClockDrift value, the mesh STA replaces the TMaxClockDrift value with the TClockDrift value, in order to determine the largest TClockDrift value among neighbor STAs.

When the previous TClockDrift values have been stable for a neighbor mesh STA, the mesh STA may substitute the previous TClockDrift value for the TClockDrift value in the measurement procedure and process the step d), at the time of a TBTT of the neighbor STA, without receiving a Beacon frame.

Before the mesh STA transmits a Beacon frame, it shall perform the following adjustment procedure:

- The mesh STA checks if the current TMaxClockDrift value is greater than zero. If the TMaxClockDrift value is greater than zero, it shall continue the following steps. Otherwise, it shall initialize the TMaxClockDrift with zero and shall not perform the following step.

- If the TMaxClockDrift value is smaller than 0.04% of its beacon interval, the mesh STA shall adjust its TSF timer so that the next TBTT will be delayed for the duration of the TMaxClockDrift and initialize the TMaxClockDrift value with zero. Otherwise, it shall adjust its TSF timer so that the next TBTT will be delayed for the duration of 0.04% of its beacon interval and subtract the value of 0.04% of its beacon interval from the TMaxClockDrift.

The mesh STA may adjust its TSF timer only to slow the counting. The mesh STA may adjust its TSF timer within the range of 0.04% in a beacon period.

When the delay amount at each beacon periods are not stable, the mesh STA should listen to neighbor STA’s Beacon frames frequently. An implementation may circumvent the potential jitter of the TSF timer introduced by the adjustment procedure by adopting additional adjustment to the TMaxClockDrift, which is beyond the scope of the standard, as long as the mesh STA’s TSF counting is aligned to the most delaying neighbor STA without introducing unnecessary delay of its TSF counting.

NOTE—This clock drift compensation procedure does not intend to maintain a strict synchronization. It aims to stop TBTT drifting away among neighbor mesh STAs, allowing some jitter of TSF timer.

- Beaconing

- Beacon generation in MBSSs

A mesh STA transmits Beacon frames that are specific to an MBSS. Beacon frames for MBSS, infrastructure BSS, or IBSS are differentiated by the Capability Information field in the Beacon frame as specified in 7.3.1.4 (Capability Information field). A mesh STA that collocates with an AP generates Beacon frames for the MBSS independently of the AP.

The mesh STA shall define a series of TBTTs exactly dot11BeaconPeriod TUs apart. Time zero is defined to be a TBTT with the Beacon frame being a DTIM. At each TBTT, the mesh STA shall schedule a Beacon frame as the next frame for transmission according to the medium access rules specified in Clause 9. The beacon period is included in Beacon and Probe Response frames.

The mesh STA shall start beaconing upon the receipt of the MLME-START.request primitive.

- Beacon reception for mesh STA

A mesh STA shall use information from the Timestamp field without regard for the BSSID or Mesh ID in order to obtain information necessary for synchronization, if the mesh STA maintains synchronization with the transmitter of the Beacon frame. A mesh STA may use information from the Beacon interval field and the Beacon Timing element without regard for the Mesh ID in order to obtain information necessary for MBCA, if the mesh STA maintains synchronization with the transmitter of the Beacon frame and dot11MBCAActivated is true. A mesh STA may use information from the MCCAOP Advertisement Overview element and MCCAOP Advertisement element without regard for the Mesh ID in order to obtain information necessary for MCCA, if the mesh STA maintains synchronization with the transmitter of the Beacon frame and dot11MCCAActivated is true.

A mesh STA in a mesh BSS shall use information that is not in the CF Parameter Set element, the Timestamp field, the Beacon interval field, the Beacon Timing element, the MCCAOP Advertisement Overview element, or the MCCAOP Advertisement element in received Beacon frames only if the mesh STA maintains a mesh peering with the transmitter of the Beacon frame.

- Mesh beacon collision avoidance (MBCA)

- Overview

Mesh STAs use the mesh beacon collision avoidance (MBCA) protocol to detect and mitigate collisions among Beacon frames transmitted by other STAs (including mesh STAs, APs, and STAs in an IBSS) on the same channel within the range of 2 hops. MBCA mitigates hidden node problems with respect to Beacon frames.

NOTE—Beacon frames are transmitted without acknowledgement and might collide with other frames. In a mesh BSS, multiple STAs transmit Beacon frames periodically, and mesh STAs might be located out of range of each other. This implies that Beacon frames might suffer from the so-called hidden node problem and might not be received by neighbor STAs. Once Beacon frames from hidden STAs start to collide, Beacon frames will keep on colliding if these hidden STAs transmit Beacon frames at the same beacon interval that is a typical operation. MBCA provides a set of rules to mitigate this problem.

When dot11MBCAActivated is true, the mesh STA shall set the MBCA Enabled subfield in the Mesh Capability field of the Mesh Configuration element to 1.

MBCA is composed of beacon timing advertisements, TBTT selection, and TBTT adjustment. When dot11MBCAActivated is true, the mesh STA advertises the TBTT and beacon interval of its neighbor STAs through the Beacon Timing element as described in 11C.12.4.2 (Beacon timing advertisement). Upon reception of the Beacon Timing element, the mesh STA obtains the beacon timing information of its neighbor mesh STAs and uses this information for its TBTT selection and TBTT adjustment as described in 11C.12.4.3 (TBTT selection) and 11C.12.4.4 (TBTT adjustment). The mesh STA may also perform additional procedures described in 11C.12.4.5 (Frame transmission across reported TBTT) and 11C.12.4.6 (Delayed Beacon transmissions).

When dot11MBCAActivated is true, the mesh STA that alternates Awake state and Doze state should listen to Beacon frames from its neighbor STAs, with which it maintains synchronization, often, in order to advertise and obtain the recent TBTT information.

- Beacon timing advertisement

- General

When dot11MBCAActivated is true, the mesh STA shall contain Beacon Timing element in Beacon and Probe Response frames in order to advertise its beacon timing information. The mesh STA calculates the TBTT of its neighbor STAs with which it maintains synchronization as described in 11C.12.4.2.3 (Calculation of neighbor STA’s TBTT), and composes beacon timing information as described in 11C.12.4.2.4 (Beacon timing information). The mesh STA collects the beacon timing information from each neighbor STA with which it maintains synchronization. The collection of the beacon timing information is termed “beacon timing information set”. The mesh STA contains whole or part of the beacon timing information set in the Beacon Timing element as described in 11C.12.4.2.5 (Transmitter’s procedure). The mesh STA also maintains the status number of the beacon timing information set and contains the status number in the Beacon Timing element as described in 11C.12.4.2.2 (Maintenance of the status number). The receiver of the Beacon Timing element uses the received beacon timing information as described in 11C.12.4.2.6 (Receiver’s procedure).

- Calculation of neighbor STA’s TBTT

When a Beacon frame is received from one of its neighbor STAs with which the mesh STA maintains synchronization, the mesh STA shall calculate the TBTT of the received Beacon frame as follows:

TTBTT = Tr – (Tt modulo (TBeaconInterval  1024))

where

TTBTT 			is the calculated TBTT

Tr			is the frame reception time measured in the TSF timer of the receiving mesh STA

Tt 			is the value in the Timestamp field in the received frame

TBeaconInterval 			is the value in the Beacon interval field in the received frame

The TTBTT is used as described in 11C.12.4.2.4 (Beacon timing information).

Further, the mesh STA shall calculate the time difference between the TBTT of the received Beacon frame and the time predicted from the past TBTT as follows:

TDelta = | TTBTT, c – (TTBTT, p + (TBeaconInterval  NCount)) |

where

TDelta 			is the time difference

TTBTT, c 			is the TBTT calculated from the received Beacon frame

TTBTT, p 			is the TBTT calculated for the first time after the latest status number update (see 11C.12.4.2.2 (Maintenance of the status number))

TBeaconInterval 			is the value in the Beacon interval field in the received Beacon frame

NCount			is the number of TBTTs since TTBTT, p has been calculated

TDelta is used to maintain the status number described in 11C.12.4.2.2 (Maintenance of the status number).

- Beacon timing information

The mesh STA shall keep the latest TTBTT together with the Beacon interval contained in the received frame and the identifier of the neighbor STA as the beacon timing information with respect to the neighbor STA. When the elapsed time since the latest Beacon frame reception is smaller than 524 288 TU, the beacon timing information is valid.

NOTE—The beacon timing information provides the time reference for a series of the TBTTs of the corresponding STA. Using the beacon timing information, a mesh STA is able to predict future TBTTs by adding the reported beacon interval to the reported TBTT.

The mesh STA shall collect the valid beacon timing information from each neighbor STA with which it maintains synchronization and keep the collection as the beacon timing information set. The beacon timing information set is advertised to its neighbor mesh STAs through the Beacon Timing element as described in 11C.12.4.2.5 (Transmitter’s procedure).

When the amount of neighbors, for which valid beacon timing information is kept, is large, the beacon timing information set may be divided into multiple tuples of beacon timing information. In such case, a tuple of beacon timing information is included in the Beacon Timing element (see 11C.12.4.2.5 (Transmitter’s procedure)).

- Maintenance of the status number

The mesh STA shall maintain the status number of the beacon timing information set. The status number is set to a value from a single modulo-16 counter, starting at 0 and incrementing by 1 for each transmission of a frame containing the Beacon Timing element after the mesh STA encountered any of the following events:

- It starts or stops maintaining synchronization with a neighbor STA.

- It receives a Beacon frame from a neighbor STA with which it maintains synchronization and the calculated TDelta (see 11C.12.4.2.3 (Calculation of neighbor STA’s TBTT)) is larger than 255 μs.

- It completes the TBTT adjustment procedure described in 11C.12.4.4.3 (TBTT scanning and adjustment procedures).

The mesh STA shall set the Status Number subfield in the Report Control field in the Beacon Timing element to the status number. The Status Number subfield in the Report Control field facilitates the detection of the changes in the beacon timing information set.

- Transmitter’s procedure

When dot11MBCAActivated is true, the mesh STA shall report the TBTT and beacon interval of its neighbor STAs through the Beacon Timing element as described in this subclause.

The Beacon Timing element reports on timing information of the Beacon frames that are received from the neighbor STAs with which the mesh STA maintains synchronization on the operating channel. The mesh STA shall include the Beacon Timing element in Probe Response frames and in TBTT Adjustment Request frames. The mesh STA shall also include the Beacon Timing element in Beacon frames as specified by dot11MeshBeaconTimingReportInterval and dot11MeshBeaconTimingReportMaxNum. The Beacon Timing element is present in a Beacon frame when the DTIM Count value in the Beacon frame is zero or equal to an integer multiple of dot11MeshBeaconTimingReportInterval.

The maximum number of Beacon Timing Information fields contained in a Beacon Timing element is limited to dot11MeshBeaconTimingReportMaxNum for Beacon frames, or is limited by the maximum information element size for other frames. When the number of neighbors, for which valid beacon timing information is kept, is equal or smaller than the limit, the mesh STA shall include all the beacon timing information in a single Beacon Timing element, setting both Beacon Timing Element Number and More Beacon Timing Elements subfield in the Report Control field to 0. When the number of neighbors, for which valid beacon timing information is kept, exceeds the limit, the mesh STA shall divide the beacon timing information set into multiple tuples and assign each tuple with an index number starting from 0. When the beacon timing information set is divided, the mesh STA shall include the successive tuples of beacon timing information in the Beacon Timing elements. In this case, the mesh STA shall set the Beacon Timing Element Number subfield in the Report Control field to the index number of the tuple. The mesh STA shall set the More Beacon Timing Elements subfield in the Report Control field to 1 when it has one or more beacon timing information tuples with a larger index number. The mesh STA shall divide the beacon timing information set into no more than N_Info tuples, where N_Info = ceil(number of valid beacon timing information / maximum number of Beacon Timing Information fields in the Beacon Timing element).

The mesh STA may update the combination of the tuples only when the status number described in 11C.12.4.2.2 (Maintenance of the status number) is updated. The mesh STA shall include newly updated beacon timing information (i.e., beacon timing information that causes an update of the status number as described in 11C.12.4.2.2 (Maintenance of the status number)) in the tuple with a smaller index number. When the status number is updated, the mesh STA shall include the tuple of beacon timing information indexed as 0 in the Beacon Timing element in the subsequent Beacon frame. Successive tuples shall be transmitted in ascending order of the index number in the successive Beacon frames.

NOTE— The standard does not impose mesh STAs to advertise a fragmented beacon timing information set sequentially in its Beacon frames at all times. This implies that the mesh STA might advertise tuples with a smaller index number more frequently, which is useful to notify new beacon timing information efficiently.

When the mesh STA receives a Probe Request frame containing a Beacon Timing element ID in its Request element, it shall respond with a Probe Response frame containing the Beacon Timing element. If all beacon timing information cannot be contained in a Beacon Timing element, the mesh STA shall include multiple Beacon Timing elements containing successive tuples of beacon timing information in the order of the Request element (see Table 7-15) so that all tuples are transmitted.

- Receiver’s procedure

A mesh STA with dot11MBCAActivated equal to true that receives a Beacon Timing element obtains the beacon timing information of its neighbor mesh STA and uses it for its TBTT selection and TBTT adjustment as described in 11C.12.4.3 (TBTT selection) and 11C.12.4.4 (TBTT adjustment).

When a mesh STA receives a Beacon frame with a Beacon Timing element that contains only a subset of the beacon timing information set, the mesh STA may transmit a Probe Request frame containing a Beacon Timing element ID in its Request Information element to the transmitter of the Beacon Timing element, in order to request the rest of the beacon timing information.

NOTE 1—The Report Control field in the Beacon Timing element facilitates the detection of the missing beacon timing information.

NOTE 2—Once the entire beacon timing information set with a particular Status Number is obtained, the mesh STA does not need to retrieve beacon timing information as long as the Status Number remains the same.

A mesh STA that receives the Beacon Timing element shall record the reported TBTT and its successive TBTTs as neighbor’s essential Beacon reception timing if the MSB of the Neighbor STA ID field in the corresponding Beacon Timing Information field is 0. The essential Beacon reception timing is used to control the transmission of frames as described in 11C.12.4.5 (Frame transmission across reported TBTT).

A mesh STA can also check if its neighbor mesh STAs received its Beacon frame successfully by checking whether the Beacon Timing elements received from its neighbor mesh STAs contain beacon timing information of the mesh STA. When the Beacon Timing element is received from one of the peer mesh STAs, the mesh STA checks if the MSB of the Neighbor STA ID subfield is set to 0 and the rest of the field matches with the 7 LSBs of the AID value assigned to the mesh STA through the mesh peering establishment. When the Beacon Timing element is received from a non-peer mesh STA, the mesh STA checks if the MSB of the Neighbor STA ID subfield is set to 1 and the rest of the field matches with the 7 LSBs of its own MAC address (taking the I/G bit as the MSB). If the matching is verified, the corresponding beacon timing information represents the correct Beacon reception by the neighbor mesh STA.

If a Beacon frame is received from a neighbor peer mesh STA that is either in active mode or in light sleep mode, the Beacon Timing element is present in the frame, and all beacon timing information is contained in the Beacon Timing element, the mesh STA shall verify whether the neighbor peer mesh STA received its Beacon frame. If the Beacon Timing element does not contain beacon timing information of the mesh STA or the Neighbor TBTT subfield of the corresponding beacon timing information does not reflect the recent TBTT of the mesh STA, the mesh STA considers the previous Beacon frame was not received by the neighbor peer mesh STA.

- TBTT selection

When dot11MBCAActivated is true, the mesh STA performs the TBTT selection described herein before it starts beaconing (see 11C.2.8 (Establishing or becoming a member of a mesh BSS)). The mesh STA selects its TBTTs and its beacon interval so that its Beacon frames do not collide with Beacon frames transmitted by other STAs in its 2 hop range.

Before the mesh STA starts beaconing, it performs scanning and discovered neighbor STAs are reported through an MLME-SCAN.confirm primitive (see 11C.2.6 (Scanning mesh BSSs)). Using TimeStamp, Local Time, and Beacon Period in the BSSDescription parameter provided by the MLME-SCAN.confirm primitive, the mesh STA shall obtain the TBTT and beacon interval of its neighbor STAs operating on the same channel as the mesh STA starts to operate. The mesh STA shall also collect the beacon timing information contained in the Beacon Timing elements received on the channel through Beacon Timing in the BSSDescription parameter provided by the MLME-SCAN.confirm primitive, in order to obtain the TBTT and beacon interval of STAs in 2 hop range. After obtaining this information, the mesh STA shall look for a timing of its Beacon transmissions so that its Beacon frames are likely not to collide with Beacon frames transmitted by other STAs in its 2 hop range. The mesh STA shall update its TSF timer and select its beacon interval to set its TBTTs to the appropriate timing, and then it shall start beaconing using the MLME-START.request primitive.

- TBTT adjustment

- Self-determined TBTT adjustment

When dot11MBCAActivated is true, the mesh STA checks if it does not transmit Beacon frames during the beacon transmissions of other STAs within its 2 hop range using the Beacon Timing element received from its neighbor peer mesh STA.

When the mesh STA discovers that its Beacon frames repeatedly collide with the Beacon frames of a neighbor or a neighbor’s neighbor and its TBTT comes later than the TBTT of the colliding STA at the time of collision, it shall perform the TBTT scanning procedure described in 11C.12.4.4.3 (TBTT scanning and adjustment procedures). If the mesh STA finds an alternative TBTT, it shall start the TBTT adjustment procedure as described in 11C.12.4.4.3 (TBTT scanning and adjustment procedures).

- Requested TBTT adjustment

When a mesh STA discovers that Beacon frames from two or more neighbor STAs are colliding repeatedly or a series of TBTTs are close enough to trigger frequent Beacon collisions, the mesh STA may transmit a TBTT Adjustment Request frame to the neighbor mesh STA of which the TBTT comes last at a particular collision timing in order to request this neighbor mesh STA to adjust its TBTT. The TBTT Adjustment Request frame may be transmitted only if the following conditions hold:

- The recipient of the TBTT Adjustment Request frame is a peer mesh STA and has set the MBCA Enabled subfield in the Mesh Capability field of the Mesh Configuration element to 1.

- The other colliding STA does not include the Mesh Configuration element in its Beacon frames or the TBTT Adjusting field in the Mesh Configuration element is 0.

When dot11MBCAActivated is true, the mesh STA that receives a TBTT Adjustment Request frame shall perform the TBTT scanning procedure described in 11C.12.4.4.3 (TBTT scanning and adjustment procedures), and determine if it can find an appropriate alternative timing for its TBTTs. After the completion of the TBTT scanning procedure, the mesh STA that receives the TBTT Adjustment Request frame shall respond with a TBTT Adjustment Response frame containing the result of the TBTT scanning in the Status Code field. If the mesh STA finds an alternative TBTT, it shall agree with the request. If it agrees with the request, the Status Code field is set to 0 in the TBTT Adjustment Response frame, and it shall complete the TBTT adjustment procedure described in 11C.12.4.4.3 (TBTT scanning and adjustment procedures). If it does not agree with the request, it shall indicate the reason in the Status Code field in the TBTT Adjustment Response frame. A mesh STA may set the Status Code to either 0, 1, or 78 in the TBTT Adjustment Response frame.

- TBTT scanning and adjustment procedures

When a mesh STA is in need of TBTT adjustment, it tries to find an alternative TBTT first. The mesh STA shall perform the TBTT scanning procedure as follows:

- The mesh STA checks if its beacon timing information and collected neighbor’s beacon timing information are sufficiently new. If the mesh STA did not receive a Beacon frame from a neighbor STA with which it maintains synchronization at the latest TBTT, it shall receive a Beacon or Probe Response frame from the neighbor STA and obtain the TBTT of the neighbor STA and the beacon timing information contained in the Beacon Timing element.

NOTE 1—This is particularly important if the mesh STA is in deep sleep mode for a neighbor peer mesh STA.

- Using the latest TBTT of its neighbor STAs and the latest beacon timing information of neighbor mesh STAs, the mesh STA shall look for an alternative TBTT that does not cause Beacon collision among the STAs in its 2 hop range.

If an alternative TBTT is not available, the mesh STA terminates the procedure. If an alternative TBTT is available, the mesh STA shall start the TBTT adjustment procedure as follows:

- The mesh STA shall set the TBTT Adjusting field in the Mesh Configuration element to 1 in order to announce that the TBTT adjustment procedure is ongoing.

- The mesh STA shall suspend its TSF timer for a period of time, no longer than half of the Group Delivery Idle Time (defined in 11C.13.5 (TIM types)) within a single beacon period, to slow its TSF.

- The mesh STA shall adjust TBTT information of the neighbor STAs (see 11C.12.4.2.4 (Beacon timing information)), that are to be contained in the Beacon Timing element, accordingly by subtracting the delay amount.

- When dot11MCCAActivated is true, the mesh STA shall adjust the MCCAOP reservations accordingly by modifying the MCCAOP Offset of each MCCAOP reservation. See 9.9a.3.3 (MCCAOP reservations).

- The mesh STA shall repeat suspending its TSF timer over multiple beacon periods until its TBTT is set to the alternative TBTT.

- Upon completion of the TBTT adjustment, the mesh STA shall update the status number as described in 11C.12.4.2.2 (Maintenance of the status number) and shall set the TBTT Adjusting field in the Mesh Configuration element to 0.

NOTE 2—A mesh STA in deep sleep mode might interpret its neighbor mesh STA’s TBTT adjustment as a large TSF jitter. When a mesh STA in deep sleep mode observes a large TSF jitter and the Status Number in the Report Control field in the Beacon Timing element of the received Beacon frame (or Probe Response frame) has been updated, the mesh STA in deep sleep mode should not take this jitter as clock drift and listen to the next Beacon frame to verify if the clock drift is large.

- Frame transmission across reported TBTT

When dot11MBCAActivated is true, the mesh STA should not extend its transmissions across TBTT of its neighbor STAs with which it maintains synchronization. Further, the mesh STA should not extend its transmissions, other than Beacon frames, across all essential Beacon reception timing (see 11C.12.4.2.6 (Receiver’s procedure)) reported from its neighbor mesh STAs with which it maintains synchronization. This operation helps in reducing the hidden STA interference with Beacon reception at its neighbor mesh STAs. When both dot11MBCAActivated and dot11MCCAActivated are true, the mesh STA shall not extend its transmissions across TBTT of its neighbor STAs with which it maintains synchronization. Further, the mesh STA shall not extend its transmissions, other than Beacon frames, across all Beacon reception timing reported from its neighbor mesh STAs with which it maintains synchronization.

After silencing for dot11MeshAverageBeaconFrameDuration µs from the reported neighbor’s TBTT, the mesh STA may start transmitting frames again.

- Delayed Beacon transmissions

A mesh STA may occasionally delay its Beacon frame transmission from its TBTT for a pseudo-random time. This attribute is specified by dot11MeshDelayedBeaconTxInterval, dot11MeshDelayedBeaconTxMinDelay, and dot11MeshDelayedBeaconTxMaxDelay. When dot11MeshDelayedBeaconTxInterval is set to non-zero value, the mesh STA shall delay its Beacon frame transmission from TBTT, once every dot11MeshDelayedBeaconTxInterval. When the mesh STA transmits a Beacon frame with delay from its TBTT, the delay time shall be randomly selected between dot11MeshDelayedBeaconTxMinDelay and dot11MeshDelayedBeaconTxMaxDelay µs.

NOTE—Delayed Beacon transmission allows mesh STAs to discover Beacon frames that are transmitted from multiple mesh STAs with TBTTs close to each other. It is recommended to set dot11MeshDelayedBeaconTxMaxDelay to a time longer than the typical duration of Beacon frames.

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D11.01, May 2011.

[1] Draft Specification.  doc.: IEEE P802.11-REVmb/D8.0, March 2011.

# Comments

Move 11C12.4.2.2 (Maintenance of the status number) is relocated after the clause describing beacon timing information.

This subclause is moved from above. (make copy and paste here)

# Text boxes

Abstract

This document provides suggested resolution to CID 4003, 4004, 4005, 4006, 4007, 4008, 4009, 4010, 4011, 4012, 4013, 4014, 4015, 4016, 4017, 4018, 4019, 4020, 4051, 4052, and 4084.