## Slide 1: Data Rate Requirement Of WiFi Offloading in TGah
Date: 2011-05-10
Authors:

## Slide 2: WiFi Offloading
3GPP Consider WiFi Offloading a User Feature [1],[2],[3],[4],[5]
  Standardization of 3GPP system to WLAN interworking also started since Rel-6
  Starting from Rel-8, the development of 3GPP Evolved Packet System (EPS) also considers interactions with non-3GPP access networks including WiFi network
TGah User case Category 3 [6]
  Current 802.11(a, g, n, ac) WLAN have short coverage and mostly used in indoor environment
  TGah has large coverage (~1km), can be used for mobile traffic offloading in outdoor environment

## Slide 3: Data Rate of Cellular Networks
Standard | Family | Downlink (Mbit/s) | Uplink (Mbit/s)
WiMAX | 802.16 | 128 (20MHz) | 56 (20MHz)
LTE | UMTS/4G | 100 (20MHz) | 50 (20 MHz)
UMTS W-CDMA HSDPA+HSUPA HSPA+ | UMTS/3G | 0.384 14.4 56 | 0.384 5.76 22
UMTS-TDD | UMTS/3G | 16 | 
EV-DO 1x Rev. 0 EV-DO 1x Rev.A EV-DO Rev.B | CDMA2000 | 2.45 3.1 4.9xN | 0.15 1.8 1.8xN
EDGE Evolution | GSM | 1.6 | 0.5

## Slide 4: Increase Data Rate Requirement for User Category 3
Requirements given in [1]:
  Data rate (Aggregate BSS PHY rate):20 Mbps
  Mobility: Pedestrian
  STA/AP capacity: STA: 50 , AP: 1
Should the highest data rate be increased in order to be comparable to the next generation cellular system ?
  For a 5MHz channels, increasing aggregate BSS data rate means MIMO technology is required.

## Slide 5: Reference
[1] GAN (Generic Access Network, TS 43.318 etc.)
[2] EGAN (Enhanced GAN, TR 43.902 etc.)
[3] IP Flow Mobility and Seamless WLAN Offload (TS 23.261 etc.)
[4] I-WLAN (Interworking Wireless LAN, TS 23.234 etc.)
[5] Support of non-trusted non-3GPP access network in EPS (TS 23.402 etc.)
[6] “Potential Compromise for 802.11ah Use Case Document”, Rolf de Vegt, Qualcomm