IEEE P802.11
Wireless LANs

| LB171 D1.01 comment resolution (MAC CSM frame format) |
| --- |
| Date: 2011-05-01 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zhou Lan | NICT | 3-4,Hikarino-oka, Yokosuka, 239-0847, Japan | +81-46-847-5097 | lan@nict.go.jp |
| Chen Sun | NICT |  |  |  |
| Yohannes Alemseged | NICT |  |  |  |
| Hiroshi Harada | NICT |  |  |  |

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

# MAC CSM related comments

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 187 | 33.54 | 8.4.2.af4 | "... Any secured container ..." not specific enough. | Name the alternatives (apart from the public action frame) to transfer the Channel Schedule Management element |
| 339 | 33.54 | 8.4.2.af4 | Please define secured container and how it operates. | As per comment. |
| 413 | 33.54 | 8.4.2.af4 | Is "any secured container" defined? | Does this simply mean "encrypted"? What else is a "secured container"? |
| 562 | 33.54 | 8.4.2.af4 | should explicitly describe secured containers in this section. Too ambiguous | explain all secured contains. |
| 596 | 33.54 | 8.4.2.af4 | "Channel Schedule Management element is transmitted in the public action frame or any secured container to indicate the channel scheduel change." What is "any secured container"? | Clarify or remove "any secured contatiner". |
| 669 | 33.54 | 8.4.2.af4 | description of any secured container should be provided. | clarify or remove any secured container |
| 760 | 33.54 | 8.4.2.af4 | what is a "secured container"? | clarify |
| 887 | 33.54 | 8.4.2.af4 | "Channel Schedule Management element is transmitted in the public action frame or any secured container to indicate the channel scheduel change." What is "any secured container"? | Clarify or remove "any secured contatiner". |

Discussions:

According to the FCC rules, all the channel availability and schedule information should be delivered in a secured manner. The current draft only specifies two methods to deliver the channel schedule information. One is a publication action frame used by GAS protocol, the other is a regular publication frame. Both of them have the protected dual of action frame defined, which can be used when security negation is set up between the stations. So the “secured container” here particularly refers to the “protected dual of action frame”

Proposed resolution:

Agree in principle-replace “secured container” by “protected dual of action frame” with the editorial instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 247 | 33.55 | 8.4.2.af4 | Please explain here what "channel schedule change" represents. | As in comment. |

Discussions:

Channel schedule change actually means channel schedule information. It is not only the updated information of channel schedule. It is better to change to “channel schedule information” for clarification.

Proposed resolution:

Agree in principle-replace “channel schedule change” by “channel schedule information” with the editing instruction in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 287 | 34.21 | 8.4.2.af4 | wrong preposition | change "of generating" to "for transmitting" change "for a query" to "within a query" - but you also need to specify what sort of query and I do not know that now. |

Proposed resolution:

Agree in principle-change the sentence with the editing instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 176 | 36.20 | 8.4.2.af4 | Description of Channel Schedule Descriptor info field missing. | Add a description of the Channel Schedule Description field. Note in this description that the minimal length of the field is 1 octett. Also change the minimal value of the length of the IE in Table 8-51 to "6" |
| 825 | 36.20 | 8.4.2.af4 | Missing description of Channel Schedule Descriptor field. | Add description of Channel Schedule Descriptor field after description of Device Identification Info field. |
| 1076 | 34.06 | 8.4.2.af4 | Try as I might, I found nothing that told me the format of the Channel Schedule description. OK, there were statements of what was in the descriptor, and (curiously) what was not in it, but no structure. | Define the structure and semantics of the Channel Schedule Descriptor field. |

Discussions:

The Channel Schedule Descriptor info field is defined in section 8.2.6.1.4. The reference should be given in this sub clause.

Proposed resolution:

Agree in principle-provide reference with the editing instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 188 | 34.29 | 8.4.2.af4 | Table 8-42af41: usage of result codes 10 -- 255 left open | make result codes 10 -- 255 reserved. Possibly assign a few result codes for vendor specific usage. |
| 744 | 34.26 | 8.4.2.af4 | "Table 8-42af41—Reason Result Code field values" Are values 10-255 reserved? It's better to add a row in this table indicating values 10-255 reserved | Add a row indicating values 10-255 reserved at the end of Table 8-42af41—Reason Result Code field values |
| 964 | 34.26 | 8.4.2.af4 | "Table 8-42af41—Reason Result Code field values" Are values 10-255 reserved? It's better to add a row in this table indicating values 10-255 reserved | Add a row indicating values 10-255 reserved at the end of Table 8-42af41—Reason Result Code field values |

Proposed resolution:

Agree with comment CID 188, 744, 964 based on the discussion and editing instructions in this document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 248 | 35.12 | 8.4.2.af4 | "..channel availability is based on TV channel or WLAN channel." It is not clear here what it means to be based on the "TV channel" and what it means to be based on the "WLAN channel". Are available WLAN channels a subset of available TV channels? How is this decided whether to provide one set of channels or the other one? | As in comment. |

Proposed resolution:

Agree in principle, No change is required. According to the current TGaf draft, all the channel availability and schedule information are provided by RLSS instead of directly from TVWS database. A RLSS can have the function of mapping the channel availability and schedule information from TV channel to WLAN channel. Also RLSS is provided by operator, not regulator, therefore it is up to the operator to decide to provide the whole set of WLAN channel schedule information or only a set of channel schedule information based on the situation of operation, traffic load, interference etc.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 530 | 35.00 | 8.4.2.af4 | What's the difference between Channel Availability Starting Time and the time that the channel is available? | Clarify. |
| 537 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |
| 606 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |
| 897 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |

Discussions:

"Channel Availability Starting Time" is the name of the field, and the content is the instant time that the channel becomes available. In order to avoid confusion, change "Channel Availability Starting Time" to "Channel Availability Starting Time field".

Proposed resolution:

Agree in principle-replace “Channel Availability Starting Time” by “Channel Availability Starting Time field” with the editing instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 532 | 41.41 | 8.4.5.5 | According to current text in 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 593 | 41.41 | 8.4.5.5 | According to current text in 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 558 | 41.41 | 8.4.5.5 | enabling STA should query RLS, not database using RLQP. Conflicting description with 10.af2. | Fix |
| 608 | 41.41 | 8.4.5.5 | According to 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 899 | 41.41 | 8.4.5.5 | According to 10.af2, enabling STA queries RLS using RLQP | database -> RLS |

Discussions:

It is agreed that we don’t define the interface between enabling STA and database. The query of a CSM can be sent to RLSS or another enabling STA. So “database” should be changed to “RLSS or another enabling STA”

Proposed resolution:

Agree in principle-replace “database” by “RLSS or another enabling STA” with the editing instruction in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 761 | 34.53 | 8.4.2.af4 | what is "None WLAN information capability"? | Define |

Discussions:

It means that the RLSS or the enabling STA is not capable of providing schedule information based on WLAN channel. Change to "no capability of providing schedule information on WLAN channel" for clarification.

Proposed resolution:

Agree in principle-Change the phrase to “no capability of providing schedule information on WLAN channel” with the editing instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 829 | 34.12 | 8.4.2.af4 | Are Device Identification Info and Channel Schedule Descriptor always present, even if the request is declined? | Clarify. |

Proposed resolution:

Agree in principle. No change is required. Channel Schedule Descriptor will provide the reason why the request is declined. It has to be present even if the request is declined.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1019 | 41.65 | 8.4.5.5 | It does not make sense to descrive the 'value as variable' | Remove ", and the value is variable" |

Proposed resolution:

Agree with comment CID 1019 based on the discussion and editing instructions in document 802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1077 | 35.56 | 8.4.2.af4 | "The optional Operating Class field is present in the Channel Schedule Descriptor" - if it's optional, how come the statement that it's present? | Remove "optional". Check and correct similar uses in this table. |
| 1232 | 35.00 | 8.4.2.af4 | Table 8-42af42: Operating Class field is not optional |  |

Proposed resolution:

Agree with comment 1077 and 1232 based on the discussion and editing instructions in this document   802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1230 | 35.28 | 8.4.2.af4 | Inconsistent description of Channel Number | only 1 field |

Proposed resolution:

Agree with comment CID 1230 based on the discussion and editing instructions in this document   802.11-11/0754r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 175 | 36.18 | 8.4.2.af4 | Specify the minimal length of the device identification information field (=1). Same applies to the min. length of the channel schedule description. Otherwise, it is not clear, that each information field should be aligned to octett boundaries. This impacts the min. length of the channel schedule management information element (per Table 8-51) which is not correct even for the text as it is. | Insert "The minimal length of the Device Identification Info field is one octett" after "...schedule information." (line 20, page 36). Also change the minimal value of the length of the IE in Table 8-51 to "6" |
| 828 | 27.40 | 8.4.2.1 | length of Channel Schedule Management is incorrect. | Max length should be 257. Min length should be 4 + minimum device identification info length + minimum channel schedule descriptor length. |
| 1055 | 27.40 | 8.4.2.1 | Where does the Length limit of 255 come from? | Justify it or change to 257 |

Proposed resolution:

Agree in principle-change the length value to 257 with the editing instructions in document 802.11-11/0754r1.

## Editing instructions:

8.4 Management frame body components

8.4.2 Information elements

8.4.2.1 General

TGaf Editor: change Table 8-65as following:

Table 8-65—Element IDs

| Element | Element ID | Length of indicated element (in octets) | Extensible |
| --- | --- | --- | --- |
| White Space Map (see 8.4.2.106 (White Space Map element)) | <ANA> | 3 to 255 | Yes |
| DSE Link Identifier (see 8.4.2.107 (DSE Link Identifier element)) | <ANA> | 8 or 14 | Yes |
| Channel Power Management Announcement (see 8.4.2.108 (Channel Power Management Announcement element)) | <ANA> | 3 to 257 |
| Channel Schedule Management (see 8.4.2.109 (Channel Schedule Management element)) | <ANA> | 4 to 255257 |
| Geodatabase Inband Enabling Signal (see 8.4.2.110 (Geodatabase Inband Enabling Signal element)) | <ANA> | 2 |
| Contact Verification Signal (see 8.4.2.111 (Contact Verification Signal element)) | <ANA> | 3 | Yes |

8.4.2.109 Channel Schedule Management element

TGaf Editor: Change the first paragraph of this subclause as following:

The Channel Schedule Management element is transmitted in the public action frame or any secured container a public action frame or a protected dual of public action frame to indicate the channel schedule change information.

TGaf Editor: Change the third paragraph of this subclause as following:

The Reason Result Code field indicates the reason for generating the Channel Schedule Management for a query request of transmitting a query request of channel schedule information. It also indicates the result of a response, whether the query is successful or not, and the reason if it is not successful. The value of this field is defined in Table 8-192 (Reason Result Code field values).

TGaf Editor: after the last paragraph of this sub clause, add the following paragraph:

The Channel Schedule Descriptor field indicates the channels on which the schedule information is request and the channel schedule information on those channels in the response. The value of the field is defined in 8.2.6.1.4 (Channel Schedule Descriptor).

TGaf Editor: change Table 8-193 as following:

Table 8-42af41—Reason Result Code field values

| Reason result code field values | Description |
| --- | --- |
| 0 | Requesting for a new channel schedule information from Registered Location Secure Server. It happens the first time STAs try to obtain channel schedule information from Registered Location Secure Server. |
| 1 | Requesting for an updated channel schedule information from Registered Location Secure Server. It happens when the STAs change locations and have to re-contact the Registered Location Secure Server for updated channel schedule information. |
| 2 | Success with full channel schedule information on the requested channel obtained. |
| 3 | Success with only schedule changes on the requested channel obtained. |
| 4 | Success with no channel schedule changes from last query of the Registered Location Secure Server. |
| 5 | Request declined by the enabling STA for unspecified reason. |
| 6 | Request declined by the enabling STA because of None WLAN information capability no capability of providing schedule information on WLAN channel. |
| 7 | Request declined by Registered Location Secure Server for unspecified reason. |
| 8 | Request declined by Registered Location Secure Server because of None WLAN information capability no capability of providing schedule information on WLAN channel.. |
| 9 | Timeout. |
| 10-255 | Reserved. |

TGaf Editor: change Table 8-193 as following:

Table 8-193—Channel Schedule Management Mode values

| Channel schedule management mode value | Operating class present | Description |
| --- | --- | --- |
| 0 | No | The Channel schedule information is based on the TV channel. The Reason and Result Code field is set to either zero or one. |
| 1 | Yes | The Channel Schedule information is based on the WLAN channel. The Reason and Result Code field is set to either zero or one. |
| 2 | No | The Channel Schedule information provided is based on the TV channel. Channel Availability Starting Time field is present in the Channel Schedule Descriptor and the time that the channel becomes available is provided. |
| 3 | Yes | The channel Schedule information provided is based on the WLAN channel. The Channel Availability Starting Time field is present in the Channel Schedule Descriptor and the time that the channel becomes available is present. |
| 4 | Yes | The Channel Schedule information provided is based on the TV channel. The Channel Availability Starting Time field is NOT present in the Channel Schedule Descriptor. |
| 5 | Yes | The channel Schedule information provided is based on the WLAN channel. The Channel Availability Starting Time field is NOT present in the Channel Schedule Descriptor. |
| 6-255 | Reserved. |

8.4.5.6 RLQP Channel Schedule Management element

TGaf Editor: change the first paragraph as following:

The RLQP Channel Schedule Management element is used by an enabling STA to query the database RLSS or another enabling STA for channel schedule information.

TGaf Editor: change the third paragraph as following:

The Length field indicates the length of the remaining element fields in octets, and the value is variable.

# Text boxes

Abstract

This document contains proposed resolution of some of the comments categorized as MAC CSM in LB171 of P802.11af D1.0, shown in 802.11-11/0277r11. Proposed resolutions are based on 802.11af  draft text D1.01.

This submission provides resolutions for comment CID 187, 339, 413, 562, 596, 669, 760, 887, 247, 287, 176, 188, 744, 964, 248, 825, 1076, 532, 593, 558, 608, 899, 761, 829, 1019, 1077, 1232, 1230, 175, 828, 1055, 218.