IEEE P802.11
Wireless LANs

| PS buffering of Deauthentication and Disassociation frames |
| --- |
| Date: 2011-05-10 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Jouni Malinen | Atheros Communications, Inc. |  |  | jouni.malinen@atheros.com |

Changes on top of REVmb/D8.0:

page 1008

10.3.2.4 Deauthentication--originating STA

Change the note in item b):

NOTE—as the Deauthentication frame is a bufferable MMPDU, the transmission of this frame might be delayed by the operation of a power-saving protocol. The AID and  the PTKSA are maintained (when applicable) until the frame is acknowledged or attempts to transmit the frame are abandoned.

Change item d):

- Once the Deauthentication frame is acknowledged or attempts to transmit the frame are abandoned,.the MLME shall issue an MLME-DEAUTHENTICATE.confirm primitive to inform  the SME of  the deauthentication.

Add a new item between existing items e and f:

If  the STA is contained within an AP, its SME, upon receipt of an MLME-DEAUTHENTICATE.confirm primitive, shall release the AID assigned for the indicated STA, if the state for the indicated STA was State 3 or State 4.

page 1009

10.3.2.5 Deauthentication--destination STA

Change item b):

b)	Upon receiving an MLME-DEAUTHENTICATE.indication primitive, the SME shall:

1)	delete any PTKSA and temporal keys held for communication with the originating STA by using the MLME-DELETEKEYS.request primitive (see 11.4.12 (RSNA security association termination)) and by invoking MLME-SETPROTECTION.request(None),

2)	if the STA is contained within an AP, its SME shall release the AID assigned for the indicated STA and shall inform the DS of the disassociation, if the state for the originating STA was State 3 or State 4.

page 1016

10.3.3.8 AP disassociation initiation procedure

Change note in item a):

NOTE—as the Disassociation frame is a bufferable MMPDU, the transmission of this frame might be delayed by the operation of a power-saving protocol. The AID and  the PTKSA are maintained (when applicable) until the frame is acknowledged or attempts to transmit the frame are abandoned.

Change item c):

c) Once the Disassociation frame is acknowledged or attempts to transmit the frame are abandoned ,the MLME shall issue an MLME-DISASSOCIATE.confirm primitive to inform the SME of the disassociation

Add a new item between existing items d and e:

Upon receiving an MLME-DISSASSOCIATE.confirm primitive, the SME shall release the AID assigned for the indicated STA, if the state for the indicated STA was State 3 or State 4.

page 1016

10.3.3.9 AP disassociation receipt procedure

Add a new item:

e) The SME shall release the AID assigned for the indicated STA.

# Text boxes

Abstract

REVmb/D8.0 CID 12187 identified issues in the Deauthentication and Disassociation procedure on the AP in the case the non-AP STA being disconnected is in power save mode at the time. This submission proposes changes to reorder operations in the Deauthentication and Disassociation procedures to delay releasing of the Association ID (AID) and deletion of the PTKSA (if applicable) to be able to use normal PS buffering procedures and management frame protection for the Deauthentication and Disassociation frames. Transition into State 1 (or State 2) is done immediately to ensure that no further Class 3 frames from the STA or to the STA are accepted during the short period between the moment that the AP starts the Deauthentication/Disassociation procedure and the transmission of the Deauthentication/Disassociation frame.